Source	Marketwire
Date	03/04/2016
Time	05:01:19 AM

Company	 UNIGOLD INC.
Title	Unigold Identifies Potential Vertical Feeder System at the Candelones 
Extension Deposit Intersecting 12.0 metres of 7.46 g/t Au; 1.4% Cu





    CDNX Symbol: UGD











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Unigold Inc.

TSX VENTURE SYMBOL: UGD

March 4, 2016

Unigold Identifies Potential Vertical Feeder System at the Candelones Extension 
Deposit Intersecting 12.0 metres of 7.46 g/t Au; 1.4% Cu


TORONTO, ONTARIO--(Marketwired - March 4, 2016) - Unigold Inc. ("Unigold" or 
the "Company") (TSX VENTURE:UGD) is pleased to announce recent results from 
exploration drilling at the Candelones Extension deposit, within the Company's 
100% owned Neita Concession in the Dominican Republic.

The Company has completed four holes at Target B; the second of three targets 
selected for drill testing (Ref. Figure 1.0). The drilling at Target B included 
four holes, centered on previous hole LP28 (16.4 g/t Au; 26.7 g/t Ag; 0.3% Cu; 
2.4% Zn over 15.0 metres ("m")). Newly discovered mineralization is contained 
with a vertical feeder zone of sulphide matrix-supported angular breccias which 
show clear evidence of multiphase epithermal activity. The best results were 
intersected in hole LP16-100 which identified two, distinct zones of 
enrichment. The first, with elevated lead, zinc and silver grades, assayed 2.43 
g/t Au; 18.8 g/t Ag; 0.2% Cu and 4.3% Zn over 9.5 m at a depth of 291.1 m from 
the collar. The second, with elevated gold and copper grades, assayed 7.46 g/t 
Au; 5.1 g/t Ag; 1.4% Cu and 1.3% Zn over 12.0 m at a depth of 307.5 m from the 
collar. The zonation may reflect excellent preservation of a classic, 
telescoping epithermal system.

Previous drilling at Target A, 200 m east of Target B (ref. Fig 1.0), 
intersected massive to semi-massive sulphides that returned intercepts of 6.19 
g/t Au over 34.9 m, 7.45 g/t Au over 15.7 m and 4.15 g/t Au over 34.0 m (UGD 
PR# 2016-02). Mineralization at this target defined a flat-lying lens of 
massive sulphide. The area between Target A and B was not sufficiently tested 
during historic drilling to draw any conclusions regarding the relationship 
between the newly discovered feeder zone and the massive sulphide lens. It is 
possible that a genetic relationship links the two zones and this must be 
tested and defined in future drill programs.

The gold copper zone at Target B is particularly interesting as it appears to 
define a potential vertical feeder zone whereas the massive sulphides at Target 
A appear to be horizontal and cross-cut stratigraphy. The newly discovered 
vertical feeder system has been defined by drilling over a 100 m vertical 
distance by new hole LP16-100 and previous holes LP28 and LP29 (6.28 g/t Au; 
1.1% Cu over 12.0 m). The feeder appears to be vertical and is estimated to 
have a true horizontal thickness ranging from 6.0 m (LP16-100) to 9.0 m (LP28) 
with a currently defined strike length of 20-25 m. The feeder appears to plunge 
to the east and is open down dip and down plunge.

Joseph Del Campo, Interim President and CEO of Unigold notes: "We are very 
pleased with these latest results. This is the second target we have drill 
tested and it is the second target where we have identified strong evidence for 
vertical feeders and massive sulphides. These results support our suspicion 
that previous drilling, while successful at identifying a multimillion ounce, 
low-grade, stratabound deposit, failed to adequately define high-grade feeder 
zones in this complex epithermal system. The results from Target A and Target B 
have proven that both massive sulphide mineralization and feeder zones both 
exist within the bounds of, and were missed by, previous drilling. The grades 
returned from these two targets are 3 to 4 times higher than the stratabound 
mineralization and are some of the highest grade intercepts returned in the 
history of the project. We are very encouraged with the results received to 
date from Targets A and B. Results are pending from Target C, a further 300 
metres to the west. Target C, hosts the highest grade mineralization from 
historical drilling. We remain very optimistic that our interpretation will 
lead to similar results that should be available by the end of March."

Tables 1.0 and 2.0 summarize the results from the four holes completed at 
Target B. In all cases, the results summarized in Table 2.0 are inclusive of 
the results summarized in Table 1.0.

Table 1.0 - Barite and Quartz-Sulphide Mineralization - Target B - Candelones 
Extension

/T/

----------------------------------------------------------------------------
True
Width
Hole           From      To Interval      Au      Ag      Cu      Zn     (1)
----------------------------------------------------------------------------
(m)     (m)      (m)   (g/t)   (g/t)     (%)     (%)     (m)
----------------------------------------------------------------------------
LP16-97       249.0   264.0     15.0    1.15     1.0     0.0     0.4    15.0
----------------------------------------------------------------------------
LP16-98       245.8   250.6      4.8    7.32    52.0     0.2     2.7     4.8
----------------------------------------------------------------------------
LP16-99       276.6   283.0      6.4    4.23    12.1     0.2     1.7     6.4
----------------------------------------------------------------------------
LP16-100      291.1   333.6     42.5    3.41     6.3     0.5     1.6    33.0
----------------------------------------------------------------------------
including   291.1   300.6      9.5    2.43    18.8     0.2     4.3     8.0
----------------------------------------------------------------------------
and   307.5   319.5     12.0    7.46     5.1     1.4     1.3     8.0
----------------------------------------------------------------------------

/T/

Table 2.0 (2) - Stratabound Mineralization - Target B - Candelones Extension

/T/

----------------------------------------------------------------------------
True
Width
Hole           From      To Interval      Au      Ag      Cu      Zn     (1)
----------------------------------------------------------------------------
(m)     (m)      (m)   (g/t)   (g/t)     (%)     (%)     (m)
----------------------------------------------------------------------------
LP16-97       247.0   340.8     93.8    0.68     1.0     0.0     0.1    93.8
----------------------------------------------------------------------------
LP16-98       245.8   344.6     98.8    1.19     5.0     0.1     0.4    98.8
----------------------------------------------------------------------------
LP16-99       231.5   321.0     89.5    1.06     4.0     0.1     0.4    89.5
----------------------------------------------------------------------------
LP16-100      240.9   366.0    125.1    1.72     2.7     0.2     0.6   125.1
----------------------------------------------------------------------------

(1)  True width is estimated based on current interpretation of the attitude
of the mineralization and the orientation of each drill hole.

(2)  Intervals reported are inclusive of intervals summarized in Table 1.0.

/T/

The Target B area is structurally complex. Extensive faulting and multiple 
intermediate to mafic dikes and/or sills are present. The gold and copper 
enriched feeder system can be observed over a 100 m vertical distance, 
intersected on section by holes LP28 and LP16-100 (75 m vertical separation) 
and by previous hole LP29 (23 m east and 25 m below LP16-100). Hole LP16-97, 75 
m above LP29, did not intersect similar high grade gold and copper 
mineralization, suggesting that the feeder system may have a plunge component. 
Where the feeder intersects the andesite - dacite contact, the dip of the 
contact appears to flatten and massive to semi-massive barite with elevated 
zinc is observed. From the point of intersection, average grades of all metals 
within the stratabound zone decrease down dip to the south whereas to the 
north, in the up dip direction along the contact, metal grades are markedly 
higher within the defined stratabound deposit.

The gold and copper mineralization in holes LP28, 29 and LP16-100 is closely 
associated with late quartz veins that exhibit characteristics consistent with 
sulphide rich epithermal systems (Ref Figure 4.0). LP29 is one of the few holes 
where visible gold has been observed in drill core.

Figures 1.0 to 4.0 are available at the following address: 
http://media3.marketwire.com/docs/1045540_Figures.pdf

Premier Mining Destination - Dominican Republic

The Dominican Republic is host to world-class gold and base metal mines and 
deposits. The government supports development and exploration in the mining 
sector. In addition, the country has well established Mining Laws and 
Environmental Laws. Unigold's wholly owned flagship property, Neita is 
compliant with all mineral and environmental requirements and work is conducted 
to internationally accepted environmental and social standards. The Neita 
concession exploration license was renewed in 2012 and is in good standing.

Unigold intends to acquire new financing in the near future to resume drilling 
in the Dominican Republic to follow up on the promising results achieved to 
date on Targets A and B.

QA/QC

Diamond drilling at the Candelones Project utilizes both HQ and NQ diameter 
tooling. Holes are established using HQ diameter tooling before reducing to NQ 
tooling to complete the hole. The core is received at the on-site logging 
facility where it is, photographed, logged for geotechnical and geological data 
and subjected to other physical tests including magnetic susceptibility and 
specific gravity analysis. Samples are identified, recorded, split by wet 
diamond saw, and half the core is sent for assay with the remaining half stored 
on site. A minimum sample length of 0.3 metres and a maximum sample length of 
1.5 metres are employed with most samples averaging 1.0 metres in length except 
where geological contacts dictate. Certified standards and blanks are randomly 
inserted into the sample stream and constitute approximately 5-10% of the 
sample stream. Samples are shipped to a sample preparation facility in the 
Dominican Republic operated by Bureau Veritas. Assaying is performed at Bureau 
Veritas Commodities Canada Ltd.'s laboratory in Vancouver, B.C. Canada. All 
samples are analyzed for gold using a 50 gram lead collection fire assay fusion 
with an atomic adsorption finish. In addition, most samples are also assayed 
using a 36 element multi-acid ICP-ES analysis method.

Wes Hanson P.Geo., Chief Operating Officer of Unigold, has reviewed and 
approved the contents of this press release.

About Unigold Inc. - Discovering Gold in the Caribbean

Unigold is a Canadian based mineral exploration company traded on the TSX 
Venture Exchange under the symbol UGD, focused primarily on exploring and 
developing its gold assets in the Dominican Republic.

Forward-looking Statements

Certain statements contained in this document, including statements regarding 
events and financial trends that may affect our future operating results, 
financial position and cash flows, may constitute forward-looking statements 
within the meaning of the federal securities laws. These statements are based 
on our assumptions and estimates and are subject to risk and uncertainties. You 
can identify these forward-looking statements by the use of words like 
"strategy", "expects", "plans", "believes", "will", "estimates", "intends", 
"projects", "goals", "targets", and other words of similar meaning. You can 
also identify them by the fact that they do not relate strictly to historical 
or current facts. We wish to caution you that such statements contained are 
just predictions or opinions and that actual events or results may differ 
materially. The forward-looking statements contained in this document are made 
as of the date hereof and we assume no obligation to update the forward-looking 
statements, or to update the reasons why actual results could differ materially 
from those projected in the forward-looking statements. Where applicable, we 
claim the protection of the safe harbour for forward-looking statements 
provided by the (United States) Private Securities Litigation Reform Act of 
1995.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Unigold Inc.
Mr. Joseph Del Campo
Interim President & CEO
416.866.8157
jdelcampo@unigoldinc.com
www.unigoldinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=559706586