Source	MARKET NEWS
Date	03/04/2016
Time	07:32:33 AM

Company	 Terrax Minerals Inc.
Title	Drills 4.05 
M @ 3.49 G/t Au And 7.50 M @ 2.08 G/





    CDNX Symbol: TXR











Press Release





TERRAX MINERALS INC ("TXR-V;TRXXF-0")
- Drills 4.05 M @ 3.49 G/t Au And 7.50 M @ 2.08 G/t Au
- At Mispickel Target, Yellowknife City Gold Project

TerraX Minerals Inc. has received assay results from the 3rd and
4th holes of a four hole drill program testing quartz vein and
replacement style mineralization at the Mispickel target on its Walsh
Lake property of the Yellowknife City Gold Project ("YCG"), immediately
north of Yellowknife in the Northwest Territories. The two holes
reported today were both drilled on the same section, 50 m to the south
of the first two holes, and intersected:

//st

-- 4.05 m @ 3.49 g/t Au in the main zone of hole TWL16-003

-- 7.50 m @ 2.08 g/t Au in the hanging-wall zone of hole TWL16-004

//et

Drilling at Mispickel totaled 384 meters in 4 holes on two parallel
sections approximately 50 meters apart. The two holes on each section
were designed to hit mineralization approximately 20-25 and 40-50
meters below a surface trench sampled by TerraX in 2013, which returned
chip sampling assays across strike on the sulphide-quartz vein zone of
6.0 m @ 7.29 g/t Au (News release of October 30, 2013).

The initial two holes of the program were collared 10 meters north
of the original trench and returned 8.60 m @ 12.87 g/t Au in TWL16-001
and 7.30 m @ 23.60 g/t Au in TWL16-002 in the Main Zone and 11.32 m @
2.14 g/t Au in a Footwall Zone in hole TWL16-001 (see our news release
of February 23 2016). The Main Zone mineralization is characterized by
multiple narrow boudinaged quartz veins with abundant visible gold
within minor replacement style sulphide mineralization (1-2% sulphides)
of the host felsic volcanics and sediments. TWL16-003 intersected the
Main Zone with 4.05 m @ 3.49 g/t Au. This hole intersected the
characteristic style of mineralization in the Main Zone, with narrow
quartz veins and minor sulphidized wall rock. In addition TWL16-003
intersected a strong zone in the hanging wall of the main zone with
increased alteration and sulphide mineralization that resulted in a
continuum of anomalous gold mineralization extending from the Hanging
Wall Zone to the Main Zone, with an overall intercept of 39.00 m @ 0.63
g/t Au in TWL16-003.

TWL16-004, the deeper hole on the section, reported 7.50 m @ 2.08
g/t Auwithin a broader zone of 16.90 m @ 1.25 g/t Au in the Hanging
Wall Zone. TWL16-004 was only drilled to a planned depth of 83 meters,
stopping in mineralized argillites, and thus did not test the Main Zone
down dip from TWL16-003. Although TWL16-004 did not extend to the Main
Zone, the Hanging Wall Zone alone graded 42.25 meters @ 0.66 g/t Au.
The higher total cumulative gold widths and values in hole TWL16-004
were achieved even though the hole did not intersect the Main Zone,
which was responsible for the majority of gold grade in the total
cumulative TWL16-003 intersection. The stronger and wider
mineralization in TWL16-004 indicates the entire Mispickel target area
has potential to grow into a large gold bearing system.

A map and cross section showing the location of drill holes
TWL16-003 and 004 on the Mispickel target area is available on our web
site under "Walsh Lake - 2016 Field Exploration".

The obvious increase in grade and width of zones of mineralization
with depth, and the potential to demonstrate continuity of
mineralization along strike, has resulted in a decision to do more work
in the Mispickel area this winter. A detailed ground magnetic survey
will be carried out initially as magnetic susceptibility readings of
the core have shown a good correlation of gold grade with higher
magnetism. This survey will be completed in the next two weeks. The
drill data from the first four holes, coupled with the magnetic survey,
will provide information on designing an expanded drill program to
extend this new promising area of mineralization. The follow up drill
program could begin in late March with ice road supported access and
lake based drill sites available until the middle of April when the
spring breakup will begin.

The results of drill holes TWL16-003 and TWL16-004 are summarized
below, by zone:

//st
-----------------------------------------------------------------------
-----
Drill                                              From    To Interval    Au
Hole  Dip Azimuth  UTM Location       Zone         (m)   (m)      (m)   g/t
----------------
(NAD 83)
----------------
Easting Northing
---------------------------------------------------------------------------
-
TWL16-
003   -45     270 640291  6945810     Total Zone 18.25 57.25    39.00  0.63

------------------------------------------
Hanging
Wall incl. 24.40 40.70    16.30  0.41

------------------------------------------
Main incl. 49.65 53.70     4.05  3.49

------------------------------------------

------------------------------------------
Footwall       87.10 90.40     3.30  0.29
---------------------------------------------------------------------------
-
TWL16-
004   -65     270 640291  6945810     Total Zone 40.10 83.07    42.97  0.66

------------------------------------------
Hanging
Wall incl. 40.10 57.00    16.90  1.25

---------------------------------
and
incl. 44.50 52.00     7.50  2.08

------------------------------------------
BELOW END OF HOLE - NOT
Main                      INTERSECTED

------------------------------------------

------------------------------------------
BELOW END OF HOLE - NOT
Footwall                      INTERSECTED
---------------------------------------------------------------------------
-
//et

Drill holes were drilled normal to interpreted strike of the zone.
Current interpretations for dip, based on the surface trenching and the
four drill holes, indicate that the true width of TWL16-003 is
approximately 90% of drill intersection widths, and for TWL16-004 is
approximately 65% of drill intersection widths.

Following the Mispickel drilling TerraX mobilized two drills to
its Sam Otto target, 1.5 km to the southwest on the Walsh Lake property
(News release of February 17, 2016) completing nine holes totaling
1,501 meters. The drills were then moved to the Homer Lake target on
the Northbelt property of the YCG and 1,145 meters were drilled in five
holes before moving to the Barney Zone in the Core Gold Area of the
YCG, where drilling is currently underway. Maps showing the location of
the Sam Otto, Homer Lake and Barney target areas on the YCG are
available on our web site under "2016 Field Exploration".

TerraX collected 165 samples for assay from the drilling reported
here. Results ranged from below detection to a high of 12.6 g/t Au.
Drill hole collar locations were surveyed to sub-meter accuracy. Down
hole surveying (Easy Shot) was completed on all holes. TerraX inserts
certified standards and blanks into the sample stream as a check on
laboratory QC. Drill core samples are cut by diamond saw at TerraX's
core facilities in Yellowknife. A halved core sample is left in the
core box. The other half core is sampled and transported by TerraX
personnel in securely sealed bags to ALS Chemex's (ALS) preparation
laboratory in Yellowknife. After sample preparation, samples are
shipped to ALS's Vancouver facility for gold and ICP analysis. Gold
assays of )3 g/t are re-assayed on a 30 gm split by fire assay with a
gravimetric finish. ALS is a certified and accredited laboratory
service. ALS routinely inserts certified gold standards, blanks and
pulp duplicates, and results of all QC samples are reported.

The technical information contained in this news release has been
approved by Joseph Campbell, the President of TerraX, who is a
Qualified Person as defined in "National Instrument 43-101, Standards
of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold ("YCG") encompasses 118 sq km of
contiguous land immediately north and south of the City of Yellowknife
in the Northwest Territories. Through a series of acquisitions, TerraX
now controls one of the six major high-grade gold camps in Canada.
Being within 15 km of the City of Yellowknife, the YCG is close to
vital infrastructure, including transportation, service providers,
hydro-electric power and skilled tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering
23 km of strike length on the southern and northern extensions of the
shear system that hosted the high-grade Con and Giant gold mines. The
project area contains multiple shears that are the recognized hosts for
gold deposits in the Yellowknife gold district, with innumerable gold
showings and high grade drill results this past year that serve to
indicate the project's potential as a world-class gold district. Since
February 2013, TerraX has consolidated the project area by acquiring,
optioning and staking numerous properties including: Northbelt,
Goodwin, Ryan Lake, Walsh Lake, U-Breccia and Southbelt as well as
staking and acquiring additional contiguous lands.

For more information on the YCG project, please visit our web site
at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.

TSX Venture closing price for TXR-V
Date: 2016/03/03
Closing Price: 0.37

TEL:  514-341-0408  Paradox Public Relations
Toll Free: 1-866-460-0408
E-mail: info@paradox-pr.ca
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1606300021TS11606300782-07294220160304