Source	MARKET NEWS
Date	03/07/2016
Time	06:28:38 AM

Company	 Savary Gold Corp.
Title	Adds 
Additional Gold Occurrences to 50+ Discover





    CDNX Symbol: SCA











Press Release





SAVARY GOLD CORP ("SCA-V")
- Adds Additional Gold Occurrences to 50+ Discovered and Documented
- Over The Past Two Years:

Savary Gold Corp. ("Savary") announces newly reviewed grab sample
assay results collected by Delta Gold in 1996 and 1997 over the
Karankasso JV Project in south western Burkina Faso which is currently
65% owned by Savary and 35% owned by Sarama Resources Limited
("Sarama"). A summary of results of these additional zones is presented
below.

-18.2 g/t, 5,21 g/t and 2.82 g/t gold - FDHN Zone, northern end of
new 18 km long mineralization trend

-2.25 g/t, 12.5 g/t, 3.8 g/t and 29.5 g/t gold - Dio Zone -
diorite intrusion-hosted

-5.15 g/t and 1.93 g/t gold - QPT Zone - quartz porphyry volcanic
host

-1.82 g/t, 4.61 g/t, 5.63 g/t, 9.3 g/t, 15.98 g/t, 19.04 g/t and
22.0 g/t gold - Splay 1 Zone

-1.84 g/t, 2.97 g/t, 3.16 g/t, 4.03 g/t, 5.4 g/t, 9.58 g/t, 20.88
g/t and 39.57 g/t - Splay 2 Zone

-1.12 g/t, 5.24 g/t and 13.89 g/t gold - Sera Main S Zone

-1.84 g/t gold - Sera Main SC Zone

"These new occurrences have been thrown into hat with the others
and have been prioritized using our newly developed mineralization
model" stated Don Dudek, President and CEO of Savary. "Those new
targets, which we currently think are the best of the best, will be
tested in our next drill program along with a program designed to add
scope to our currently defined zones. Drilling is planned to commence
in Q2, 2016."

In February, Savary Gold received historic Delta Gold data files
that included results for 1,736 prospecting samples collected in 1996
and 1997. The data also indicated a series of new gold occurrences as
documented above. Some additional gold occurrences are evident in the
data, but, will require site validation.

Over the past two years, Savary Gold has carried out a field and
mapping program that has resulted in a much better understanding of the
geological controls for the gold mineralization and the discovery of an
additional 60+ new gold occurrences.

Zone details

All presented zones are referenced in the attached figure at the
end of this release.

FDHN Zone

The FDHN Zone is located over an artisanal mining site at the
northern end of the newly documented 18 km long DH Trend. The DH trend
was first documented during a site visit to the DH zone in January,
2016. This area was selected for review after satellite images
indicated the presence of artisanal mine shafts and a large area of
surface workings. At the site, numerous 2 to 2.5 metres wide, cemented
to non-cemented shafts, with the deepest reported to extend to 80
metres vertical were observed. In this area, nine, parallel, up to 300
metres long mineralized structures have been subject to shaft-style
artisanal mining. It is expected that the mineralized structures are
made up of multiple mineralized veins, as the artisanal miners along
one of the trends reported that they were mining three, separate narrow
quartz vein zones from one shaft. Only the deepest shafts, along one of
the nine mined structures, return fresh rock, which in this case, is
strongly silicified gabbro. The balance of the shafts, which extend to
approximately 25 metres depth, remain in oxidized saprolitic rock. The
artisanal miners are focussed on the silicified core of the mineralized
structures which is best described as a mixture of quartz vein and
silicified mafic intrusion with trace to 10% granular pyrite. Rocks
peripheral to the core silicified zone, which are discarded in waste
piles, contain trace to 2% coarse grained pyrite and up to 30% coarse
bladed arsenopyrite along with trace to 15% quartz veins; grab samples
of this material returned up to 5.99 g/t gold. Sulphide content is not
directly related to quartz vein percentage and occurs as disseminations
throughout the rock. A large area of shallow artisanal diggings,
surround the area of deeper shafts and extends southward for another
1,300 metres and up to 650 metres east-west. Only one surface exposure
of fresh rock was observed in this area with most shafts displaying
close to two metres of laterite above the saprolitic rock.

Dio Zone

The Dio Zone is located approximately 1,400 metres northeast of
the Kueredougou Zone (open pit Inferred mineral resource of 795,000
tonnes grading 3.31 g/t gold totalling 84,500 ozs gold - Savary news
release November 24, 2015). Grab samples collected over this zone
returned 2.25 g/t, 12.5 g/t, 3.8 g/t and 29.5 g/t gold. The Dio zone is
diorite-intrusion-hosted and is inferred to be located in the same
structurally complex zone that resulted in the emplacement of several
felsic to intermediate intrusions and created the Kueredougou Zone.

QPT Zone

The QPT Zone is located 1.25 km west of the southern end of the
Kueredougou zone. The QPT zone is interpreted to be hosted by a quartz
porphyritic felsic tuff unit that extends from north of the previously
documented Highway QP zone to approximately 1.7 km south of the QPT
zone, a distance of approximately 13 km. This mineralization trend has
been subject to recent intense artisanal mining activity and may
develop into an important target area. Other than for a small survey
over the Highway QP zone this mineralization trend has not been covered
by ground IP (Induced Polarization) surveys; IP surveys have been used
to trace gold mineralized zones along strike and to define new targets
in overburden-covered areas.

Splay 1 Zone

The Splay 1 Zone is located 1.2 km east of the southern end of the
Kueredougou West Zone (open pit Inferred mineral resource of 1,904,000
tonnes grading 2.12 g/t gold totalling 129,700 ozs gold - Savary news
release November 24, 2015). Grab samples collected over the Splay 1
Zone contained 1.82 g/t, 4.61 g/t, 5.63 g/t, 9.3 g/t, 15.98 g/t, 19.04
g/t and 22.0 g/t gold. This zone appears to be a Splay structure off of
the Koure East Sulphide Trend and is associated with the western edge
of a north-northeast-trending, 2.3 km long IP chargeability trend. A
large, 600 meter by 300 meter area of shallow artisanal workings in
cover laterites, lies along the geophysical trend to the south; it is
possible that these workings are sourced from a yet undiscovered
laterite-covered zone that lies along the prospective geophysical
trend. No drill holes have tested this target area.

Splay 2 Zone

The Splay 2 Zone is located approximately 1,000 metres east of the
southern end of the south end of the Kueredougou West Zone. Samples
collected over the Splay 2 Zone contained 1.84 g/t gold, 2.97 g/t gold,
3.16 g/t gold, 4.03 g/t gold, 5.4 g/t gold, 9.58 g/t gold, 20.88 g/t
gold and 39.57 g/t gold. This zone is aligned along a north-northeast
trending IP chargeability high that can be traced for approximately 1.8
km and may correlate with a seven metre RAB intercept that returned
1.04 g/t gold, located approximately 440 metres to the south.

Sera Main S Zone

This new occurrence is the most southerly gold occurrence
identified to date. It is located at the southern end of a 45 kilometre
long gold-in-soil trend and approximately 10 km south of the Serakoro
Main Zone. Twelve Samples collected from this area returned high values
of 1.12 g/t, 13.89 g/t and 5.24 g/t gold. A RAB hole, located
approximately 275 metres to the north, returned 0.79 g/t gold over 2
metres.

Sera Main SC Zone

The Sera Main SC Zone is located approximately 1,000 metres
west-northwest of the Sera Main S Zone. This zone is unique in that it
is the first documented gold occurrence which appears to be hosted by a
regional scale chert horizon that has been intermittently traced for at
least 30 km. In the occurrence area, the trend of the geology is
rotated from north to northwest.

QAQC

Assay samples were sent to Analabs in Ouagadougou, Burkina Faso
and analysed by fire assay. No standards are noted in the sample
streams.

PDAC Convention

Please visit Savary's booth 2550 at the convention.

About Savary Gold

Savary Gold is a Canadian exploration company, along with partner,
Sarama Resources Limited, are focused on exploring and developing the
Karankasso Gold Project in Burkina Faso. The Project properties lie
within the Birimian age, Hounde Greenstone Belt, which hosts Semafo's
Mana mine and additional gold deposits that are presently subject to
extensive exploration efforts (including Endeavour Mining's Hounde
Project, Roxgold's Yaramoko Project, Orezone's Bondi Project and
Sarama's South Hounde Project, which is adjacent to Savary Gold's
property). The Project contains an Inferred open pit constrained
mineral resource of 9.16 million tonnes grading 2.28 g/t gold (Savary
news release November 24, 2015). For additional information please
visit our website at www.savarygold.com.

Don Dudek, P.Geo., President and CEO of the Company and a
qualified person under National Instrument 43-101, has reviewed and
approved the scientific and technical information in this press
release.

SAVARY GOLD CORP.
On behalf of the Board

"Don Dudek"

President & Chief Executive Officer

For more information, please contact:

Don Dudek, President and CEO

T: 647-259-2097

E: info@savarygold.com; www.savarygold.com

Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These
statements are based on current expectations and assumptions that are
subject to risks and uncertainties. Actual results could differ
materially because of factors discussed in the management discussion
and analysis section of our interim and most recent annual financial
statement or other reports and filings with the TSX Venture Exchange
and applicable Canadian securities regulations. We do not assume any
obligation to update any forward-looking statements, except as required
by applicable laws.

(img
src='https://www.thenewswire.com/client_files/tnwaVt2DK_.png' /) @
https://www.thenewswire.com/client_files/tnwaVt2DK.png
Click Image To View Full Size

* Red dots and diamonds - grab samples gold occurrences containing
)1 g/t gold

* Yellow dots and diamonds - grab sample gold occurrences
containing from 0.5 g/t to 1.0 g/t gold

* Purple Stars represent mineralized zones with drill results

* Black stars represent new zones referred to on this release




__________________________________________________
_______________________________________________
TSX Venture closing price for SCA-V
Date: 2016/03/04
Closing Price: 0.05
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1606600013TS11606600931-06272120160307