Source	MARKET NEWS
Date	03/07/2016
Time	06:46:40 AM

Company	 Golden Predator Mining Corp.
Title	3 
Aces Bulk Sampling Progress Report





    CDNX Symbol: GPY











Press Release





GOLDEN PREDATOR MINING CORP ("GPY-V")
- 3 Aces Bulk Sampling Progress Report

Golden Predator Mining Corp. (the "Company") is pleased to
announce that as of March 1, 2016 it has completed drilling, blasting,
excavation, bagging and loading of approximately 550 tons of
gold-quartz vein material from the Sleeping Giant vein bulk sample
program at its 3 Aces Project, Yukon, as previously announced..  This
initial phase began February 16th, 2016 and is expected to conclude by
the end of March 2016. Company geologists elected to continue the
program and expand the original 550 ton targeted bulk sample after
noting good vein continuity and the occurrence of visible gold within
the down-dip continuation of the quartz vein.

The bulk sampling program was designed to extract a minimum of 550
tons of high grade gold-quartz vein from the Sleeping Giant vein. The
vein is exposed at surface and contains coarse visible gold. Bulk
sampling is designed to give an estimate of the actual grade of the
vein given the distribution of coarse gold.  The portion of the vein
extracted in the bulk sample was defined by closely spaced Rotary Air
Blast (RAB) drilling conducted in the summer of 2015.  The results of
that drilling are summarized below and more fully in the Company's news
release dated September 14, 2015.  The 2016 bulk sample program will
assist in designing future drill programs to accurately estimate the
grade of the vein. Processing of the bulk sample will begin during
March and is expected to continue through April.

To view a video overview of the bulk sample program please visit:
https://youtu.be/p6QnmnhyseI. The Company is also exhibiting at the
Prospectors and Developers Conference (PDAC) in Toronto at booth #2650
from March 6th to March 9th, 2016.

//st
Sleeping Giant Zone - RAB Significant Results Table

Hole            From      To Thickness     Au      Au
(ft)    (ft)    (ft)1  oz/t2    g/t3
3ARAB15-01      0.00    2.50      2.50   1.39   47.60
3ARAB15-02      0.00    5.00      5.00   1.51   51.91
3ARAB15-03      0.00    2.50      2.50   1.92   65.75
3ARAB15-04      0.00    2.50      5.00   0.75   25.75
3ARAB15-05      0.00    2.50      2.50   6.84  234.50
3ARAB15-06      0.00    5.00      5.00   2.74   93.98
3ARAB15-07      0.00    5.00      5.00   1.54   52.70
3ARAB15-08      0.00    7.50      7.50   1.93   66.02
3ARAB15-09      2.30    5.00      2.70   1.47   50.55
3ARAB15-10      2.00    5.00      3.00   1.00   34.45
3ARAB15-11      0.00   10.50     10.50   3.17  108.54
including       0.00    2.50      2.50   9.73  333.50
3ARAB15-12      0.00    7.50      7.50   3.04  104.39
including       0.00    2.50      2.50   3.31  113.65
including       5.00    7.50      2.50   5.37  184.25
3ARAB15-13      0.00    7.50      7.50   4.64  158.97
including       0.00    2.50      2.50   8.08  277.00
including       5.00    7.50      2.50   5.32  182.25
//et

Drill intercepts are reported as true thickness intervals. Au
grades are reported in troy ounces per short ton Au grades are reported
in grams per metric tonne

Sleeping Giant Zone

The Sleeping Giant Zone, accessible via an exploration dirt road,
encompasses an area approximately 33,000 m2 defined by float and
outcrops of quartz veins. To date, it contains one of the 3 Aces
property's two preferred continuous quartz veins offering potential for
bulk sampling. The Zone consists of a number of outcropping targets
consisting of gently to moderately dipping gold-bearing quartz veins.
Located along the road cut on the southern part of the Sleeping Giant
Zone, the veins' apparent dip slope is exposed for about 25m along
strike on the north side of the road.

3 Aces Project, Yukon

The 3 Aces property consists of 1,118 contiguous quartz claims
(23,000 hectares) located in southeast Yukon. The property is located
along the all-season Nahanni Range Road which accesses the Cantung Mine
located 40 kilometres to the north.

The 3 Aces property contains a number of quartz veins and vein
zones that cut Cambrian aged limestone, shale, quartz grits and pebble
chert conglomerates of the Hyland Group. Previous sampling and
exploration by Golden Predator (formerly Northern Tiger) has outlined
extensive gold-in-soil anomalies over nine square kilometres, including
numerous high grade gold showings.

The 3 Aces property is located in the traditional territory of the
Kaska Nation. In January 2013, Golden Predator signed an Exploration
Agreement with the Kaska Nation, as represented by the Ross River Dena
Council and the Liard First Nation, with respect to activities within
their traditional territories.

The technical content of this news release has been reviewed and
approved by Mike Burke, P. Geo, Chief Geologist and a Qualified Person
as defined by National Instrument 43-101.

Golden Predator Mining Corp.

Golden Predator Mining Corp., a Canadian gold mineral exploration
company, is focused on advancing the 3 Aces Project and Brewery Creek
project in Canada's North. The Company has undertaken a bulk sampling
at the 3 Aces project, focused on high grade native gold bearing quartz
veins, to define the distribution and grade of gold in the veins.  The
Company's Brewery Creek Project is a past producing heap leach gold
mine with a preliminary economic assessment, next steps include
advancing the project through feasibility and permitting.

For additional information:

Janet Lee-Sheriff
Chief Executive Officer
(214) 304-9552
info@goldenpredator.com
www.goldenpredator.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release. No
stock exchange, securities commission or other regulatory authority has
approved or disapproved the information contained herein. This press
release contains projections and forward-looking information that
involve various risks and uncertainties regarding future events. Such
forward-looking information can include without limitation statements
based on current expectations involving a number of risks and
uncertainties and are not guarantees of future performance. There are
numerous risks and uncertainties that could cause actual results and
the Company's plans and objectives to differ materially from those
expressed in the forward-looking information. Actual results and future
events could differ materially from those anticipated in such
information. These and all subsequent written and oral forward-looking
information are based on estimates and opinions of management on the
dates they are made and are expressly qualified in their entirety by
this notice. Except as required by law, the Company assumes no
obligation to update forward-looking information should circumstances
or management's estimates or opinions change.

Source: Golden Predator Mining Corp (TSX Venture:GPY)
http://www.goldenpredator.com
______________________________________
_______________________________________________
TSX Venture closing price for GPY-V
Date: 2016/03/04
Closing Price: 0.15
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1606600017TS11606601020-06444420160307