Source	MARKET NEWS
Date	03/10/2016
Time	07:36:58 AM

Company	 Midnight Sun Mining Corp.
Title	Drills 
15 Metres Grading 0.73% Copper at Solwezi





    CDNX Symbol: MMA











Press Release





MIDNIGHT SUN MINING CORP ("MMA-V")
- Drills 15 Metres Grading 0.73% Copper at Solwezi Properties

Midnight Sun Mining Corp. (the "Company" or "Midnight Sun")
announces results of recently completed core drilling on the Mitu and
Dumbwa Central areas of its Solwezi copper-cobalt properties in
northwest Zambia. The drill program consisted of 610 meters of HQ core
drilled in 5 holes. Significant mineralization was reported in all
holes including:

* 0.73% copper and 0.017% cobalt over 15.5 meters and 0.56% copper
and 0.015% cobalt over 12.0 meters in hole DC-15-03

o including 0.88% copper and 0.024% cobalt over 6.2 meters;

* 0.38% copper over 24.0 meters in hole DC-15-02

o including 0.55% copper and 0.015% cobalt over 15.1 meters

* 0.17% copper over 20.2 meters in hole DC-15-01

* 0.22% copper and 0.022% cobalt over 15 meters in hole M-15-02

//st
The following table summarizes the assay results of the recently completed
5 drill holes:
Hole #      From    To Interval True width Copper Cobalt
(m)   (m)     (m)         (m)     %      %
DC-15-01      0   20.2    20.2        20.2   0.17      -
and        29.2   32.2       3         2.4   0.29      -
and         118    128      10           8   0.11      -
and         189  195.2     6.2         4.9   0.09      -
DC-15-02      1     25      24          24   0.38      -
including     1   15.1    15.1        15.1  0.554  0.015
DC-15-03      0   15.5    15.5        15.5  0.733   0.17
and          83     98      15          12   0.56  0.015
including    89   96.8     7.8         6.2   0.88  0.024
M-15-01   110.5  146.5*   36.5        29.2      -  0.069
M-15-02    14.8   29.8      15          15  0.223  0.022
and        35.8   41.8       3         2.4   0.12      -
and        41.8   46.8       5           4      -  0.087
and        46.8     50     3.2         2.6  0.125      -
and        55.8   68.3    12.5          10  0.096      -
and          86     91       5           4  0.138      -
and          96  104.8*    8.8           7      -  0.033
//et

* indicates end of hole bottoming in mineralization. True widths are
estimated to be between 100% of reported intervals for all saprolite
intersections and 80% for all others as estimated by cross sectional
analysis.

This drill program targeted two areas, Mitu and Dumbwa Central, on
the Company's Solwezi properties. The Solwezi property is located
approximately 15km southwest of the Kansanshi mine, the largest copper
mine in Africa, which is operated by First Quantum Minerals (FM.T).
Further drilling on MMA's primary Solwezi property target, the 22 Zone,
was deferred until later in 2016 in order to obtain assessment credits
on the adjoining permit. Highlights from previously reported drilling
on the 22 Zone include;

* 5.71% copper over 14.2 meters, including 9.58% copper over 7.2
meters

* 5.08% copper over 8.0 meters; and

* 6.27% copper over 4.5 meters.

Note: The above reported lengths are intercept lengths and not
estimated true widths

"Drilling to date has confirmed the presence of three high
potential zones in the Solwezi area, namely the 22 Zone, Dumbwa Central
and Mitu." commented Bob Sibthorpe, President and CEO. "All three have
potential for surface oxide mineralization and hard rock sulfide
mineralization at depth. The copper grades reported from Dumbwa
Central, DC-15-03 and DC-15-02, approximate the latest resource grade
estimates from Kansanshi and Sentinel, the two closest copper mines.
Hole M-15-02 ended in cupriferous black shale, a unit associated with
some 80% of all copper production in Zambia. This was the first time
that this rock unit has been encountered on the Solwezi permits, and
its presence is very exciting. A program for 2016 including geophysical
and geochemical surveying and follow up drilling is being prepared."

All drilling in this program was carried out by Blu Rock Drilling
and assaying was performed by Genalysis Laboratory Services, an
internationally accredited lab. Minor silver values were associated
with higher grade copper samples.

Qualified Control/Quality Assurance: Samples obtained during core
drilling were transported directly to Genalysis Laboratories in
Chingola, Zambia by Midnight Sun personnel for sample preparation.
Samples were sorted, dried, crushed, and pulped before being sent to
Perth, Australia for final chemical analysis using ICP-MS methods. All
samples returning )20,000 ppm Cu were automatically re-checked by
Genalysis. Genalysis is a fully accredited Laboratory and sample
duplicates, standards and blanks were inserted by Genalysis and
verified by the qualified person.

Qualified Person: Warren Robb, P.Geo, a Qualified Person under NI
43-101, has reviewed and approved the technical data and contents of
this release.

ON BEHALF OF WPC RESOURCES CORP.
Robert Sibthorpe B.Sc.(Geology), M.B.A.
President & CEO

For Further Information Contact:

Al Fabbro
Director
Tel: 604-351-8850

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.

This news release includes certain statements that may be deemed
"forward-looking statements." All statements in this release, other
than statements of historical facts, are forward-looking statements.
Although the Company believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions, such
statements are not guarantees of future performance and actual results
or developments may differ materially from those in the forward-looking
statements. Factors that could cause actual results to differ
materially from those in forward-looking statements include, changes in
market conditions, unsuccessful exploration results, changes in
commodity prices, unanticipated changes in key management personnel and
general economic conditions. Mining exploration and development is an
inherently risky business. Accordingly, the actual events may differ
materially from those projected in the forward-looking statements. This
list is not exhaustive of the factors that may affect any of the
Company's forward-looking statements. These and other factors should be
considered carefully and readers should not place undue reliance on the
Company's forward-looking statements. The Company does not undertake to
update any forward-looking statement that may be made from time to time
by the Company or on its behalf, except in accordance with applicable
securities laws.
______________________________________
_______________________________________________
TSX Venture closing price for MMA-V
Date: 2016/03/08
Closing Price: 0.15
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1606900018TS11606901161-07355120160310