Source	Marketwire
Date	03/02/2017
Time	07:00:58 AM

Company	 STELLAR AFRICAGOLD INC.
Title	Stellar AfricaGold Update on Balandougou Bulk Sample Program





    CDNX Symbol: SPX











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Stellar AfricaGold Inc.

TSX VENTURE SYMBOL: SPX

March 2, 2017

Stellar AfricaGold Update on Balandougou Bulk Sample Program


MONTREAL, QUEBEC--(Marketwired - March 2, 2017) - John Cumming, President and 
Chief Executive Officer of Stellar AfricaGold Inc., (TSX VENTURE:SPX) 
("Stellar" or the "Company") is pleased to announce that preparations for 
Stellar's bulk sample program are on schedule and on budget.

THE BULK SAMPLE PROGRAM

All of the essential preparations for the bulk sample program including 
metallurgical testing, environmental and social impact study, acquisition of 
the pilot plant, and surface stripping and site infrastructure are either 
well-advanced or completed.

As previously announced, the bulk sample program will process 15,000 tons of 
surface oxide mineralization from the B3 Zone of Stellar's 100% owned 52 km2 
Balandougou Project in Guinea where a 72 kg composite sample used for 
metallurgical testing returned an average grade of 3.5 g/t Au. The primary 
objective of the program is to investigate the suitability of the B3 oxide 
mineralization to gold extraction and recovery using gravity separation as the 
sole or primary method of gold recovery. Gravity separation is the most 
environmentally friendly gold extraction method because no chemicals are used 
in the gold extraction process. It is also the most economical solution for 
processing surface oxide deposits.

The B3 shear zone was first discovered by Stellar during a regional and 
detailed soil geochemistry survey done in 2010. A strong NW-SE trending gold 
anomaly approximately 1,150 metres long by 350 metres wide was outlined. The 
geochemical anomaly was subsequently investigated with 76 Reverse Circulation 
drill holes totalling 5050 metres at a 50m grid interval along an 800 metres 
strike length, and then by 16 diamond drill holes totalling 2,350 metres. Using 
an excavator, five trenches at 100 metre intervals to a depth of more than 3 
metres were dug across the B3 zone, and an extensive structural analysis was 
undertaken by AECOM, an independent consultant, to better understand the 
controls of the gold mineralization.

In preparation for the bulk sample program and to qualify the B3 zone oxide 
mineralization for this kind of testing, the Company has initiated or completed 
the following:

/T/

--  Metallurgical testing of B3 oxide mineralization including a four-stage
gravity separation test
--  Environmental and social impact study
--  Engineering design and construction of a 15 tons per hour gravity
separation pilot plant,
--  Construction of surface infrastructure

/T/

METALLURGICAL TEST

Stellar has engaged the Metallurgy and Mineralogy Division of SGS South Africa 
to perform a four-stage gravity recovery test work on a 72-kilogram composite 
sample collected from the mineralized sections of trenches F, G and H across 
the B3 gold structure of the Balandougou Project in Guinea.

The pre-test head grade of the composite sample submitted to SGS was 3.5g/T Au. 
For the test, a 50 kilogram sub-sample was concentrated through four stages of 
gravity separation using consecutively smaller milling sizes. The overall gold 
recovery after gravity separation was 66.2% with 33.8% of the gold remaining in 
the gravity tails. The 33.8% unrecovered gold in the tailings is thought to be 
due to the presence of fine gold particles in the initial sample that were too 
fine to recover using only gravity separation.

To address the issue of fine gold not being recovered by gravity separation, 
the Company requested a bench test using cyanidation on the tailings after 
completion of the last stage of gravity separation to evaluate the suitability 
of a cyanide circuit to process the gravity tailings and increase the gold 
recovery. The cyanidation bench test of the gravity tailings resulted in a 91% 
gold recovery from the tailings over a four-hour leach period.

The combination of the four-stage gravity separation followed by cyanide 
leaching test resulted in a combined gold recovery of 97% of the tested head 
grade.

At this time Stellar does not plan to include a cyanide circuit into its bulk 
sample program but will store all tailings in a manner suitable for 
reprocessing if and when a cyanide circuit is implemented.

ENVIRONMENTAL AND SOCIAL IMPACT STUDY

In September 2016, the Company engaged the Bureau D'Etudes Guineen De 
L'Ingenierie et de L'Environnement SARL (B.E.G.I.E SARL) to conduct a Social 
and Environmental Impact Study, which is a pre-requisite for Stellar's Guinean 
subsidiary to be granted a Semi-Industrial Exploitation Licence. The Guinea 
Environment and Mining Code requires the completion of an environmental and 
social impact study for all mining projects to evaluate the effects of a 
proposed semi-industrial or industrial mining operation on the ecological 
balance and on the quality of life of the neighboring populations as well as, 
if necessary, propose measures to mitigate any identified adverse impacts.

Stellar is pleased to report that following all necessary local consultations 
and having received a positive recommendation, an Environmental Certificate of 
Conformity was awarded to Stellar's subsidiary MGWA-Goldenfrank SARL.

15 TONS PER HOUR PILOT GRAVITY PLANT

Stellar has engaged XKJ Solution, a branch of Henan Xingyang Mining Machinery 
Manufactory of China, for the engineering design and fabrication of a 
15-to-25-ton-per-hour pilot plant to process the 15,000 tons bulk sample. 
Construction of the plant in China is underway with completion scheduled for 
the end of March 2017. The completed pilot plant will be shipped to Guinea by 
sea and the plant is scheduled to be delivered on site by the end of April.

The final design parameters and the fine tuning of the pilot plant were 
according to the results of the SGS Mineral Services four-stage gravity test 
results. The pilot plant was design with all required components including a 
primary and a fine jaw crushers and a ball mill that will discharge -0.2 mm 
size material into two Knelson Concentrators for optimal gold recovery.

SURFACE INFRASTRUCTURE AND STRIPPING

Stellar has engaged CITAG Bureau d'Ingenierie, a local Guinean engineering firm 
that specializes in mine construction, for the mine pit and plant site 
preparation and to supervise surface stripping and infrastructure construction. 
Subject to satisfactory completion of this first engagement CITAG may also be 
awarded the contract to mine the 15,000 tons sample under Stellar Supervision.

The processing of the 15,000 tons sample is scheduled to start in June 2017 and 
continue at a rate of 150 tons per day for approximately 4 months.

GRANT OF INCENTIVE STOCK OPTIONS

The Company has granted 300,000 incentive stock options to three consultants to 
the Company. The options are for a five-year term exercisable at $0.05 per 
share, are fully vested and are granted pursuant and subject to the Company's 
approved Stock Option Plan and such regulatory approvals as may be required. 
The consultants are engaged on a month-to-month basis and the options are 
subject to early termination thirty days following the end of the consultants' 
engagement.

ABOUT STELLAR AFRICAGOLD INC.

Stellar AfricaGold Inc. is a Canadian gold exploration Company based in 
Montreal, Quebec, with operations concentrated mainly in West Africa and in 
Quebec.

The Company is currently developing the promising gold potential of the 
Balandougou project in Guinea, which is at an advanced exploration stage, as 
well as of the Namarana project in Mali.

In Quebec, the Company owns 100% of the Opawica Project in the Chibougamau 
mining camp.

The technical content of this press release has been reviewed and approved by 
independent consultant Greg Isenor, P. Geo, a Qualified Person as defined in NI 
43-101.

On Behalf of the Board

John Cumming, LLM, President & CEO

Forward Looking Statement

This news release contains forward-looking statements. All statements, other 
than of historical fact, that address activities, events or developments that 
the Company believes, expects or anticipates will or may occur in the future 
(including, without limitation, statements regarding expected, estimated or 
planned gold and niobium production, cash costs, margin expansion, capital 
expenditures and exploration expenditures and statements regarding the 
estimation of mineral resources, exploration results, potential mineralization, 
potential mineral resources and mineral reserves) are forward-looking 
statements. Forward-looking statements are generally identifiable by use of the 
words "may", "will", "should", "continue", "expect", "anticipate", "outlook", 
"guidance", "estimate", "believe", "intend", "plan" or "project" or the 
negative of these words or other variations on these words or comparable 
terminology. Forward-looking statements are subject to a number of risks and 
uncertainties, many of which are beyond the Company's ability to control or 
predict, that may cause the actual results of the Company to differ materially 
from those discussed in the forward-looking statements. Factors that could 
cause actual results or events to differ materially from current expectations 
include, among other things, without limitation: changes in the global prices 
for gold, niobium, copper, silver or certain other commodities (such as diesel, 
aluminum and electricity); changes in U.S. dollar and other currency exchange 
rates, interest rates or gold lease rates; risks arising from holding 
derivative instruments; the level of liquidity and capital resources; access to 
capital markets, financing and interest rates; mining tax regimes; ability to 
successfully integrate acquired assets; legislative, political or economic 
developments in the jurisdictions in which the Company carries on business; 
operating or technical difficulties in connection with mining or development 
activities; laws and regulations governing the protection of the environment; 
employee relations; availability and increasing costs associated with mining 
inputs and labour; the speculative nature of exploration and development; 
contests over title to properties, particularly title to undeveloped 
properties; and the risks involved in the exploration, development and mining 
business. Risks and unknowns inherent in all projects include the inaccuracy of 
estimated reserves and resources, metallurgical recoveries, capital and 
operating costs of such projects, and the future prices for the relevant 
minerals. Development projects have no operating history upon which to base 
estimates of future cash flows.

The capital expenditures and time required to develop new mines or other 
projects are considerable, and changes in costs or construction schedules can 
affect project economics. Actual costs and economic returns may differ 
materially from estimates and the Company could fail to obtain the governmental 
approvals necessary for the operation of a project; in either case, the project 
may not proceed, either on its original timing or at all.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Stellar AfricaGold Inc.
Maurice Giroux, VP Exploration
514-866-6299
mgiroux.stellar@gmail.com
www.stellarafricagold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=588881460