Source	CANADA NEWSWIRE
Date	03/02/2017
Time	06:03:56 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Announces Exploration Results from New 100% Owned Odin Copper
Project, Oligocene Porphyry Belt Northern Chile





    CDNX Symbol: MRZ











Press Release




" BC-Mirasol-Odin-Results   03-02 1020
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Announces Exploration Results from New 100% Owned Odin Copper
Project, Oligocene Porphyry Belt Northern Chile@

VANCOUVER, March 2, 2017 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
"Mirasol") is pleased to announce initial exploration results from a new
porphyry copper target at its 100% owned Odin project, located 20 km north of
BHP's La Escondida Copper Mine in Northern Chile.
The Odin Project was staked by Mirasol as part of its ongoing
Atacama-Puna generative program which is focused on prolific mineral belts in
northern Chile and Argentina. Mirasol holds 100 percent of four copper
projects in this region. These total 26,700 hectares and are located along the
world class late Eocene to Oligocene age porphyry-copper belt that hosts many
large-scale copper mines in Northern Chile (Figure 1). The Odin claims cover a
2 sq. km alteration anomaly detected from Landsat satellite imagery, and are
located on the north-south oriented Domeyko fault system, a +700 km long
continent-scale feature that controlled the emplacement of giant
porphyry-copper deposit clusters of this age, including the La Escondida and
Chuquicamata mining districts.
Stephen Nano, Mirasol's CEO commented: "Odin is one of a number of
projects Mirasol has staked as part of the company's Chilean copper
exploration program. The Odin lithocap target represents an intriguing
conceptual exploration target for large-scale porphyry copper mineralization
located on one of the world's premier copper belts, and warrants testing with
systematic electrical geophysical surveys followed by drilling. Mirasol is
actively a seeking strategic joint venture partner to further explore and
developed Odin and Mirasol's other copper projects in its Chilean portfolio".
Previous exploration at Odin by a large copper producer focussed on an
area of structurally hosted copper-oxide mineralization exposed in trenches
and outcrops over 0.5 sq. km. Mirasol does not have access to this previous
exploration data; however, field observations by our geologists have
identified the collars from a number of shallow (estimated ~150 m deep) drill
holes, some trenches and evidence of ground geophysical surveys.
Mirasol's exploration work at Odin includes geological mapping and
rock-chip sampling of the historic trenches and outcrops, and multi-element
geochemistry and alteration mineralogy acquired with portable X-ray
Fluorescence (pXRF) and portable Near Infrared Spectrometers (pIR-Spec) field
analytical equipment: (learn more about these exploration technologies)
Outcropping alteration and mineralization at Odin is developed within a
Carboniferous age east-dipping rhyoltic pyroclastic volcanic unit which
overlies a Carboniferous age intrusive body. Both these rocks are interpreted
to be older basement that are host to the later porphyry copper
mineralization, the age of which needs to be confirmed by radiometric dating,
but is expected to be similar to the late Eocene to Oligocene porphyry
mineralization in the belt.
Mapping of alteration minerals identified in pIR-Spec provide exploration
vectors to distinguish between relatively lower-temperature, intermediate
argillic alteration mineral assemblages associated with oxide copper found in
the trenches, from higher-temperature, advanced argillic and phyllic
alteration assemblages found in the alteration cap, situated in the eastern
portion of the alteration anomaly.
Interpretation of results from Mirasol's trench mapping and chip channel
sampling shows copper oxide mineralization is associated with argillic altered
structures and breccia zones (< 10 m wide) that have assayed up to 0.58% Cu
over 3.3 m (0.1% Cu cut-off) with anomalous Mo up to 185 ppm. Assay results
from the trenches show a general increase in copper grade toward the
alteration cap to the east.
Mirasol has integrated findings from recently published generalized
porphyry models (General Porphyry Model) with its project-specific field
information and has developed a new exploration model for Odin (Figure 2 and
Figure 3). Mirasol's model suggests that the oxide copper mineralization may
be peripheral geochemical leakage from a possibly large, untested porphyry
target centred beneath an unmineralized alteration cap rock in the eastern
portion of the Odin claims. Alteration caps of this type, termed "lithocaps",
are typically devoid of significant mineralization, but can conceal large
mineralized porphyry systems at depth.
Stephen Nano, Vice President of Exploration for the Company, a Qualified
Person under NI 43-101, is responsible for the technical content of this
release.
Quality Assurance/Quality Control of the Odin exploration program:
All previous exploration on the projects was supervised by Mirasol CEO
Stephen C. Nano, who is the Qualified Person under NI 43-101. The technical
interpretations presented here are those of Mirasol Resources Ltd.
Mirasol applies industry standard exploration methodologies and
techniques. All geochemical rock and drill samples are collected under the
supervision of the Company's geologists in accordance with industry practice.
Geochemical assays are obtained and reported under a quality assurance and
quality control (QA/QC) program. Samples are dispatched to an ISO 9001:2008
accredited laboratory in Chile for analysis. Assay results from drill core
samples may be higher, lower or similar to results obtained from surface
samples due to surficial oxidation and enrichment processes or due to natural
geological grade variations in the primary mineralization.
Forward Looking Statements: The information in this news release contains
forward looking statements that are subject to a number of known and unknown
risks, uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward looking statements. Factors
that could cause such differences include: changes in world commodity markets,
equity markets, costs and supply of materials relevant to the mining industry,
change in government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding future
exploration programs, operation plans, geological interpretations, mineral
tenure issues and mineral recovery processes. Although we believe the
expectations reflected in our forward looking statements are reasonable,
results may vary, and we cannot guarantee future results, levels of activity,
performance or achievements. Mirasol disclaims any obligations to update or
revise any forward looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/March2017/02/c3389.html

-0-                           03/02/2017
/For further information: Stephen Nano, President and CEO; or John
Toporowski, Manager of Investor Relations, Tel: +1 (604) 602-9989: Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-