Source	Marketwire
Date	03/01/2017
Time	05:02:01 AM

Company	 ADVANTAGE LITHIUM CORP.
Title	Advantage Lithium JV Surpasses Best Results to Date at Clayton NE: Total 
Composite 426.72 metres of 243.44mg/l Lithium in Brines





    CDNX Symbol: AAL











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Advantage Lithium Corp.

TSX VENTURE SYMBOL: AAL
OTCQX SYMBOL: AVLIF

March 1, 2017

Advantage Lithium JV Surpasses Best Results to Date at Clayton NE: Total 
Composite 426.72 metres of 243.44mg/l Lithium in Brines

Clayton NE drilling maintains 100% success rate and may have hit previously 
untested aquifers

VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 1, 2017) - Advantage Lithium 
Corp. (the "Company" or "Advantage Lithium") (TSX VENTURE:AAL)(OTCQX:AVLIF) and 
its joint venture partner, Nevada Sunrise Gold Corp. ("Nevada Sunrise"), are 
pleased to announce the lithium brine drilling results at the Clayton NE 
project in the Clayton Valley, Nevada. Clayton NE borders the Silver Peak mine, 
operated by Albemarle Corporation ("Albemarle") - North America's only 
producing lithium mine. Hole CNE-17-04, drilled to a total depth of 609.6 
metres (2,000 feet), has intersected multiple aquifer formations, including a 
total composite of 426.72 metres of brine-producing strata averaging 243.44 
milligrams per litre ("mg/l") lithium between a depth of 140.21m to 609.6m 
metres, including a higher-grade interval averaging 274.6 mg/l lithium over 
79.2 metres from a depth of 530.35 metres to 609.6 metres. This hole follows 
successful results from phase one drilling (see news releases dated Nov 1, 
2016, Dec 5, 2016 and Dec 21, 2016).

Highlights

/T/

--  Continued 100% Drilling Success Rate with Strong Lithium Brine Results.
Hole CNE-17-04 has intersected multiple aquifer formations:
--  Total composite of 426.72m of brine producing strata at an average
grade of 243.44 mg/l lithium, including:
--  274.6 mg/l lithium over 79.2 metres (530.35m to 609.6m)
--  Extension of mineralized brine trend to 4.46km. The highly-successful
Phase 1 program defined a 3.43km mineralized trend. The results of Phase
2 drilling to date has extended this trend length to 4.46km.
--  Drilling deeper into potentially untested aquifers. Phase 2 holes are
targeting possible deeper aquifers that may not have been intersected by
previous drilling in the Clayton Valley. Previous hole CNE-16-03, from
the Phase 1 program, was one of the deepest boreholes drilled in the
Clayton Valley and, based on results obtained, may have hit a previously
untested aquifer.
--  Permits/waivers obtained for future development of a lithium brine
resource and wells. In November 2016, waivers were received from the
Nevada Division of Water Resources for 5 of the 6 permitted holes, which
allows for reaming a borehole to a larger diameter well, pump testing,
and flow rate determination in order to provide the necessary technical
information for development of an initial lithium brine resource at
Clayton NE.

/T/

Ross McElroy, Technical Advisor and Director, of Advantage Lithium, commented: 
"We are continuing to see strong grades and brine flow from our drilling at 
Clayton NE and now have a mineralized brine trend that may stretch as far as 
4.46km. These latest results are in line with our previous best hole at the 
project and, once again, we've not only encountered lithium brines relatively 
close to surface but also at greater depths, which suggests we may have again 
hit previously untested aquifers. All-in-all, we are making excellent progress 
towards an initial resource estimate at Clayton NE."

Table 1: Results of Brine Samples for CNE-17-04

/T/

----------------------------------------------------------------------------
Drill
Hole             Aquifer System                  Interval (m)
---------------------------------
From        To        Width
----------------------------------------------------------------------------
CNE-17-04      Salt Aquifer System - A      140.21     146.30      6.10
----------------------------------------------------------------------------
Salt Aquifer System - B      152.40     158.50      6.10
----------------------------------------------------------------------------
Main Ash - A           182.88     188.98      6.10
----------------------------------------------------------------------------
Main Ash - B           195.07     201.17      6.10
----------------------------------------------------------------------------
Tufa Aquifer           201.17     219.46      18.29
----------------------------------------------------------------------------
Lower Aquifer System - A     219.46     249.94      30.48
----------------------------------------------------------------------------
Lower Aquifer System - B     256.03     469.39     213.36
----------------------------------------------------------------------------
Lower Gravel Aquifer       469.39     579.12     109.73
----------------------------------------------------------------------------
Bedrock              579.12     609.60      30.48
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Lithium
Drill          Total Dissolved         Range         Lithium Average
Hole         Solids (TDS) mg/l       (mg/l)          Grade (mg/l)


----------------------------------------------------------------------------
CNE-17-04            230,000              N/A              182.00
----------------------------------------------------------------------------
255,000              N/A              238.00
----------------------------------------------------------------------------
310,000              N/A              310.00
----------------------------------------------------------------------------
175,000              N/A              177.00
----------------------------------------------------------------------------
114,000 - 183,000      63 - 105             89.17
----------------------------------------------------------------------------
118,200 - 154,000      194 - 301           266.80
----------------------------------------------------------------------------
161,000 - 234,000      162 - 274           242.29
----------------------------------------------------------------------------
200,000 - 268,000      223 - 283           260.11
----------------------------------------------------------------------------
219,000 - 242,000      269 - 286           274.00
----------------------------------------------------------------------------

/T/

The Phase 2 drilling program is comprised of a total of approximately 1,800 
metres (5,905 feet) in three reverse circulation ("RC") holes expected to test 
depths of a minimum 600 metres each. Using a similar approach to the successful 
Phase 1 program that hit wide intercepts of lithium brine with strong brine 
flow rates, these new holes are focused on high-priority conductive horizons 
identified and imaged in the 2016 3-D resistivity survey and confirmed by 
drilling to be lithium-bearing brines. All four holes drilled to date are 
adjacent to Silver Peak lithium brine field operation, North America's only 
producing lithium mine, operated by Albemarle Corporation ("Albemarle") in 
close proximity to several of their production wells.

CNE-17-04 was completed to a depth of 609.6 metres (2,000 feet), intersecting 
the base of the Clayton Valley salar sedimentary basin at 579.12 metres (1,885 
feet). Drilling has intersected typical Clayton Valley strata consisting of 
alternating layers of gravel, volcanic ash and clay as well as units consisting 
of carbonate deposits and other evaporites. A total of 80 grab groundwater 
samples were collected as brine-bearing formations were encountered. Table 1 
presents a compiled summary of the depths of the aquifer systems with brine 
interval thickness and associated average lithium grades and TDS 
concentrations. Anomalous lithium results with average concentration of 243.44 
mg/l were obtained from six (6) discrete brine-bearing formations intersected 
over a 469.39 metre section (from 140.21 to 609.6 metres) within the Salt 
Aquifer, Main Ash Aquifer, Tufa Aquifer, Lower Aquifer System, Lower Gravel 
Aquifer, and a possible fractured bedrock aquifer.

Within this section, a 24.38 metre interval composed of compacted, confining 
clay was intersected from depth of 158.50 to 182.88 metres. Water was not 
produced from this unit. This zone is not included in the calculation of total 
average lithium concentrations. Recoverable water was not present in three 
6.1-metre intervals within this 469.39-metre section because of excessive 
fine-grained solids content. The Salt Aquifer System contains two brine-bearing 
zones (A and B as shown in table 1) separated by an unsampled zone from 146.30 
to 152.40 metres. The Main Ash Aquifer contains two brine-bearing zones (A and 
B as shown in Table 1) separated by an unsampled zone from 188.98 to 195.07 
metres. The Lower Aquifer System contains one unsampled zone from 249.94 to 
256.03 metres. These three unsampled zones are not included in the calculation 
of total average lithium concentrations for these aquifers.

The highest-grade results were obtained in the Main Ash Aquifer with a peak 
concentration up to 310 mg/l lithium (182.88 to 201.17 metres), and in the 
deeper Lower Gravel Aquifer, with a peak concentration up to 301 mg/l (219.46 
to 225.55 metres). In addition to brine samples, drill cuttings were collected 
for each 1.5 metre interval and 87 samples have been submitted for analysis. 
Analytical results for the drill cuttings are pending.

Clayton Valley Project Overview

/T/

--  Clayton NE consists of 55 unpatented claims totaling approximately 1,080
acres (437 hectares) located in the Clayton Valley sedimentary salar and
is contiguous to the eastern boundary of Albemarle's Silver Peak
property, North America's only lithium producer;
--  O'Keefe Drilling, of Butte, Montana, has been retained for the Phase 2
program to drill by RC equipment;
--  Several of Albemarle's lithium brine production wells are situated
within approximately 100 metres and less of the Clayton NE western claim
boundary.
--  Clayton NE is subject to an option earn-in agreement where Advantage
Lithium can earn up to a 70% interest in the Project after fulfilling
CDN$3.0 million in exploration expenditures on a package of five lithium
properties optioned from Nevada Sunrise (for further details, see Nevada
Sunrise news release dated June 20, 2016);
--  Nevada Sunrise is the project manager at Clayton NE on behalf of
Advantage Lithium, the operator.

/T/

For further information on Clayton NE, including location maps, see the 
Company's website www.advantagelithium.com.

The technical information in this news release has reviewed and approved on 
behalf of the company by Ross McElroy, P.Geol., Technical Advisor and Director 
for Advantage Lithium Corp., and a "Qualified Person" as defined in NI 43-101.

About Advantage Lithium Corp.

Advantage Lithium Corp. is a resource company specializing in the strategic 
acquisition, exploration and development of lithium properties and is 
headquartered in Vancouver, British Columbia. The common shares of the company 
are listed on the TSX Venture Exchange (TSX VENTURE:AAL), and the company is 
also traded on the OTCQX Best Market in the U.S. (OTCQX:AVLIF). The company has 
signed an LOI, subject to definitive agreement, with lithium producer, 
Orocobre, subject to definitive agreement, to acquire 100% interest in five 
projects in Argentina and a 75% interest in a sixth, called Cauchari. Cauchari 
is host to a near-surface estimated inferred resource of 230 million cubic 
metres of brine at 380 mg/l Lithium that equates to 470,000 tonnes of lithium 
carbonate (LCE), and a large exploration target of 5.6mt to 0.25mt of LCE and 
19mt to 0.9 of KCL. Cauchari is located just 20 km south Orocobre's flagship 
Olaroz Lithium Facility. The Company is also earning an interest from Nevada 
Sunrise Gold Corp., in a portfolio of five lithium brine projects in the 
Clayton and Lida Valley regions of Nevada, USA, including 70% in Clayton NE. In 
addition, the Company has acquired 100% of the Stella Marys lithium brine 
project, immediately adjacent to Orocobre's Salinas Grandes project that hosts 
an inferred, near-surface resource, in Argentina's Lithium Triangle.

Further information about the Company can be found at www.advantagelithium.com.

ADVANTAGE LITHIUM CORP.

David Sidoo, President

Cautionary Statement:

Certain information contained in this press release constitutes 
"forward-looking information", within the meaning of Canadian legislation. 
Generally, these forward-looking statements can be identified by the use of 
forward-looking terminology such as "is expected", "intends", or "has the 
potential to". Forward looking statements contained in this press release may 
include statements regarding the future operating or financial performance of 
Advantage that involve known and unknown risks and uncertainties which may not 
prove to be accurate. Actual results and outcomes may differ materially from 
what is expressed or forecasted in these forward-looking statements. Such 
statements are qualified in their entirety by the inherent risks and 
uncertainties surrounding future expectations. The forward-looking statements 
included in this press release are made as of the date of this press release 
and the Company disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
events or otherwise, except as expressly required by applicable securities 
legislation.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Advantage Lithium Corp.
David Sidoo
President
604.685.9316
Fax: 604.683.1585
info@advantagelithium.com
www.advantagelithium.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=588787387