Source	MARKET NEWS
Date	03/01/2017
Time	05:57:45 AM

Company	 Atlantic Gold Corporation
Title	Further 
First Stage Results From The Resource De





    CDNX Symbol: AGB











Press Release




[200/News Release]AGBVATLANTIC GOLD CORPMAR 01 2017  05:55 AMFurther 
First Stage Results From The Resource Definition Drill --->@NEWS RELEASE
ATLANTIC GOLD CORP ("AGB,AGB-V;SPVEF,SPVVF-0")
- Further First Stage Results From The Resource Definition Drill
- Program At Fifteen Mile Stream

Atlantic Gold Corporation ("Atlantic" or the "Company") is pleased
to report assay results received from a further eighteen holes of the
resource definition diamond drilling program being undertaken at its
Fifteen Mile Stream Gold Project in Nova Scotia, Canada. Drilling is
ongoing with 95 holes for 8,200m of the planned 25,000m having been
drilled to date. The objective of this program is to bring the
resources at the Company's Fifteen Mile Stream deposit to measured and
indicated status and thereby adding to the existing life of mine plan
at the Moose River Consolidated (MRC) gold project.

Drilling Results:

These results continue to reasonably reflect those grades, widths
and disposition of mineralization documented from the 1980s drilling
programs, and which underpin the current inferred resource estimate for
Fifteen Mile Stream (see below). Mineralization occurs within
argillites, greywackes and bedding-parallel quartz veins across the
hinge zone and limbs of an E-W trending anticline. The northern limb of
the anticline dips moderately north, with the southern limb vertical to
overturned (generally steeply north dipping). All holes are therefore
declined to the south and hence true widths vary (see assay table
below) depending on which limb of the anticline is intersected. Free
gold is commonly observed, and in association with pyrrhotite and
arsenopyrite. These results further support our understanding of the
essential continuity of this mineralization, and often across
substantial widths. Its shallow and widespread disposition across a
sub-horizontal anticlinal hinge zone continue to encourage the prospect
for the delineation of open pittable reserves.

The accompanying cross section and drill progress plan can be
viewed here:             http://media3.marketwire.com/docs/atla0224.pdf


Results subsequent of those previously released are tabulated
below. Previous results can be found here: February 10, 2017.

//st
---------------------------------------------------------------------------
-
Depth
Hole id           East      North       Dip        Az.        (m)



---------------------------------------------------------------------------
-
FMS-17-021                 12450      10060        -60        175
91.9
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-022                 13625      10200        -60        175
110
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-023                 12450      10040        -60        175
71
---------------------------------------------------------------------------
-
FMS-17-024                 12450      10020        -60        175
50
---------------------------------------------------------------------------
-
FMS-17-025                 12400      10080        -60        175
110
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-026                 13625      10180        -60        175
101
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-027                 12400      10060        -60        175
92
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-028                 13625      10160        -60        175
92
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
FMS-17-030                 12400      10020        -60        175
50
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-033                 12350      10040        -60        175
101
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
FMS-17-036                 13450      10080        -60        175
152
---------------------------------------------------------------------------
-
FMS-17-047                 13425      10040        -60        175
68
---------------------------------------------------------------------------
-
(incl.
---------------------------------------------------------------------------
-
FMS-17-049                 12850      10040        -60        175
62
---------------------------------------------------------------------------
-
FMS-17-051                 13400      10100        -60        175
170
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
(incl.
---------------------------------------------------------------------------
-
FMS-17-052                 12950      10040        -60        175
62
---------------------------------------------------------------------------
-
FMS-17-053                 12950      10020        -60        175
41
---------------------------------------------------------------------------
-
FMS-17-054                 12950      10080        -60        175
101
---------------------------------------------------------------------------
-
FMS-17-055                 13400      10080        -60        175
131
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-
and
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
Significant Intervals
Hole id           (greater than or equal to0.5g/t Au and up to 3m
internal dilution)

-------------------------------------------------------
From        To       Width     Approx.     Grade
(m)        (m)        (m)     true width  (g/t Au)
(m)
---------------------------------------------------------------------------
-
FMS-17-021                38         39         1          1         69.1
---------------------------------------------------------------------------
-
and     51         54         3         2.5        2.37
---------------------------------------------------------------------------
-
and     66         71         5          4         1.45
---------------------------------------------------------------------------
-
FMS-17-022                83         85         2          2         4.78
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
and    102        110         8          8        1.17!
---------------------------------------------------------------------------
-
FMS-17-023                47         53         6          5         1.86
---------------------------------------------------------------------------
-
FMS-17-024                                                           NSA
---------------------------------------------------------------------------
-
FMS-17-025                39         41         2         1.5       11.97
---------------------------------------------------------------------------
-
and     55         56         1          1         5.26
---------------------------------------------------------------------------
-
and     69         75         6          4         3.75
---------------------------------------------------------------------------
-
and     84         85         1          1         30.0
---------------------------------------------------------------------------
-
and     92         94         2         1.5        1.68
---------------------------------------------------------------------------
-
FMS-17-026                68         83         15         15        0.47
---------------------------------------------------------------------------
-
and     88         92         4          4         1.03
---------------------------------------------------------------------------
-
FMS-17-027                12         16         4          3         0.81
---------------------------------------------------------------------------
-
and     21         25         4          3         0.92
---------------------------------------------------------------------------
-
and     32         52         20         15        2.74
---------------------------------------------------------------------------
-
and     56         61         5          4         1.25
---------------------------------------------------------------------------
-
and     71         75         4          3         1.36
---------------------------------------------------------------------------
-
FMS-17-028                59         67         8          8         0.84
---------------------------------------------------------------------------
-
72         78         6          6         1.27
---------------------------------------------------------------------------
-
FMS-17-030                25         37         12         9         1.39
---------------------------------------------------------------------------
-
and     48         50         2         1.5       2.05!
---------------------------------------------------------------------------
-
FMS-17-033                37         62         25         19        0.90
---------------------------------------------------------------------------
-
and     76         84         8          6         0.96
---------------------------------------------------------------------------
-
FMS-17-036                92        102         10         7         0.92
---------------------------------------------------------------------------
-
FMS-17-047                39         54         15         10        2.56
---------------------------------------------------------------------------
-
(incl.     49         50         1         0.5       23.2)
---------------------------------------------------------------------------
-
FMS-17-049                20         21         1         0.5        4.47
---------------------------------------------------------------------------
-
FMS-17-051                14         26         12         11        0.83
---------------------------------------------------------------------------
-
and     31         39         8          7         1.03
---------------------------------------------------------------------------
-
and     44         60         16         14        0.91
---------------------------------------------------------------------------
-
and     66         69         3         2.5        1.92
---------------------------------------------------------------------------
-
and     77         90         13         11        1.17
---------------------------------------------------------------------------
-
and     94        115         21         15        0.98
---------------------------------------------------------------------------
-
and    128        140         12         8         2.79
---------------------------------------------------------------------------
-
(incl.    136        136         1         0.5        21.2
---------------------------------------------------------------------------
-
FMS-17-052                46         49         3          2         1.64
---------------------------------------------------------------------------
-
FMS-17-053                14         15         1         0.5        13.9
---------------------------------------------------------------------------
-
FMS-17-054                25         26         1          1         9.60
---------------------------------------------------------------------------
-FMS-17-055                8          9          1          1         58.8
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
and     36         42         6          5         0.81
---------------------------------------------------------------------------
-
and     56         70         14         12        2.43
---------------------------------------------------------------------------
-
and     75         81         6          5         1.24
---------------------------------------------------------------------------
-
and     94         96         2         1.5        2.30
---------------------------------------------------------------------------
-
and    100        111         11         8         0.82
---------------------------------------------------------------------------
-

NSA: No significant assays.

! Mineralization to end of hole

The current resource estimate for Fifteen Mile Stream is as follows:



---------------------------------------------------------------------------
-
Category        Tonnes (millions)    Grade (g/t) Au   Contained Au
(oz.)
---------------------------------------------------------------------------
-
FIFTEEN MILE STREAM
---------------------------------------------------------------------------
-
Inferred              11.72               1.55             584,000
Resource
---------------------------------------------------------------------------
-
Resources that are not reserves do not have demonstrated economic viability
---------------------------------------------------------------------------
-
//et

The Mineral Resource estimate for Fifteen Mile Stream is quoted at
a cut-off grade of 0.5g/t. It has an effective date of February 16,
2015 and was prepared as part of a technical report in accordance with
NI 43-101 by Mr. Neil Schofield, a principal of FSSI (Australia) Pty
Ltd, released on April 2, 2015 on SEDAR.

Results and updates from this drilling program will be reported
progressively.

Technical Disclosure

All assays are 50g charge fire assays conducted on whole-sample
pulverized 1m samples of sawn, half NQ core with 1-in-10 duplicate
assays and insertion of standards and blind blanks. Sample preparation
and assaying is conducted at the Sudbury and Vancouver laboratories of
ALS Canada Ltd, an entity having no other relationship with the
Company. Core recovery is estimated for each metre and averages )97%,
excluding occasional voids, usually (2m, representing historic
underground workings. Standards, blanks and duplicate assay results are
acceptable. True width of the mineralization varies according to the
dip of the enclosing stratigraphy. It is therefore noted for each
intersection (see table above).                 The individual drill
hole assay results underlying the mineralized intersections listed in
the table above have been verified by detailed checking against the
original assays sheets. The lengths and average grades of each
intersection have also been checked against the drill hole assay logs.
Wally Bucknell, Director of Exploration to the Company
and a Qualified Person as defined by National Instrument 43-101 ("NI
43-101") has reviewed and approved the contents of this news release.
Further updates will be provided in due course.
On behalf of the Board of Directors, Steven Dean,
Chairman and Chief Executive Officer                 Neither the TSX
Venture Exchange nor its Regulation Services Provider (as that term is
defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward-Looking Statements:                This release contains
certain "forward looking statements" and certain "forward-looking
information" as defined under applicable Canadian and U.S. securities
laws. Forward-looking statements and information can generally be
identified by the use of forward-looking terminology such as "may",
"will", "expect", "intend", "estimate", "anticipate", "believe",
"continue", "plans" or similar terminology. Forward-looking statements
and information are not historical facts, are made as of the date of
this press release, and include, but are not limited to, statements
regarding discussions of future plans, guidance, projections,
objectives, estimates and forecasts and statements as to management's
expectations with respect to, among other things, the activities
contemplated in this news release and the timing and receipt of
requisite regulatory, and shareholder approvals in respect thereof.
Forward-looking statements in this news release include, without
limitation, statements related to proposed exploration and development
programs, grade and tonnage of material and resource estimates. These
forward looking statements involve numerous risks and uncertainties and
actual results may vary. Important factors that may cause actual
results to vary include without limitation, the timing and receipt of
certain approvals, changes in commodity and power prices, changes in
interest and currency exchange rates, risks inherent in exploration
estimates and results, timing and success, inaccurate geological and
metallurgical assumptions (including with respect to the size, grade
and recoverability of mineral reserves and resources), changes in
development or mining plans due to changes in logistical, technical or
other factors, unanticipated operational difficulties (including
failure of plant, equipment or processes to operate in accordance with
specifications, cost escalation, unavailability of materials, equipment
and third party contractors, delays in the receipt of government
approvals, industrial disturbances or other job action, and
unanticipated events related to health, safety and environmental
matters), political risk, social unrest, and changes in general
economic conditions or conditions in the financial markets. In making
the forward-looking statements in this press release, the Company has
applied several material assumptions, including without limitation, the
assumptions that: (1) market fundamentals will result in sustained gold
demand and prices; (2) the receipt of any necessary approvals and
consents in connection with the development of any properties; (3) the
availability of financing on suitable terms for the development,
construction and continued operation of any mineral properties; and (4)
sustained commodity prices such that any properties put into operation
remain economically viable. Information concerning mineral reserve and
mineral resource estimates also may be considered forward-looking
statements, as such information constitutes a prediction of what
mineralization might be found to be present if and when a project is
actually developed. Certain of the risks and assumptions are described
in more detail in the Company's audited financial statements and MD&A
for the year ended December 31, 2015 and for the quarter ended
September 30, 2016 on the SEDAR website at www.sedar.com. The actual
results or performance by the Company could differ materially from
those expressed in, or implied by, any forward-looking statements
relating to those matters. Accordingly, no assurances can be given that
any of the events anticipated by the forward-looking statements will
transpire or occur, or if any of them do so, what impact they will have
on the results of operations or financial condition of the Company.
Except as required by law, the Company is under no obligation, and
expressly disclaim any obligation, to update, alter or otherwise revise
any forward-looking statement, whether written or oral, that may be
made from time to time, whether as a result of new information, future
events or otherwise, except as may be required under applicable
securities laws.

Maryse Belanger (COO)
+1 604 689-5564
______________________________________
_______________________________________________

TSX Venture closing price for AGB-V
Date: 2017/02/28




















TSX Venture closing price for AGB-V
Date: 2017/02/28
Closing Price: 0.97
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1705900020TS11705900829-05552820170301