Source	MARKET NEWS
Date	03/01/2017
Time	06:37:13 AM

Company	 Happy Creek Minerals Ltd.
Title	Completes 2016 Fox Tungsten Exploration





    CDNX Symbol: HPY











Press Release





Completes 2016 Fox Tungsten Exploration --->@NEWS RELEASE
HAPPY CREEK MINERALS LTD ("HPY-V")
- Completes 2016 Fox Tungsten Exploration

Happy Creek Minerals Ltd. (the "Company") is announcing a summary
of exploration work completed in 2016 on its 100% owned Fox tungsten
property, located northeast of 100 Mile House, in south central British
Columbia, Canada.

Between May and October 12, 2016, the Company completed 2,330
metres of drilling in 28 holes, 79 metres of surface chip and channel
sampling, 1.2 km of access trail construction between the BN and Ridley
Creek zones, 61 contour soil samples between the BN and BK zones, and
geological mapping with 23 rock samples collected for assay. A table of
drill and trench results accompany this news release on the Company's
website. Initial exploration and drill results were announced June 27,
September 26, October 24, and October 31, 2016. New results presented
here include additional soil, rock, trench and drill results with a
view to the exploration potential for expanding the current resource as
announced January 26, 2017. Drill and trench results are uncut,
intervals presented are measured down-hole and true widths are
estimated to be 75 to 95 percent of the interval. Tungsten assays are
reported as percent WO3 (tungsten trioxide) as it is the compound for
which prices are based, and is currently reported around US$21.0 per Kg
WO3 while in 2012 it was around US$40.0 per Kg WO3. For reference, a
grade of 0.8% WO3 contains 8.0 kg/tonne of WO3.

David Blann, P.Eng., President and CEO of Happy Creek states:
"During 2016, we increased the Fox's contained tungsten by two and a
half times while being among the highest grade in the industry, and a
good portion occurs in a low-strip, surface-cut setting. The inferred
resource at the BN zone with 1.89 percent WO3 is globally among the
highest grade. In addition, new mineralized prospects found at surface
are closing the gaps between the 708, BN, Ridley Creek and BK zones
that span three kilometres, and the project is thought to hold great
resource potential in the 10 km by 3 km mineral system. With less than
one percent of North America's tungsten consumption mined here, the Fox
is on track to be an important new development project with excellent
grade, size potential and proximity to infrastructure. We look forward
to advancing this project further in 2017."

Resources

On January 26th, 2017, the Company announced resources for the
Ridley Creek and BN zones. Together, these zones now contain 486,000
tonnes grading 0.817% WO3 (Indicated) and 361,000 tonnes grading 1.568%
WO3 (Inferred). For a portion of the Ridley Creek zone, there is
329,000 tonnes of 0.759% WO3 (Indicated) within a pit shell having a
strip ratio of 3.3:1. These grades are thought to be comparable to the
Cantung mine located in the

Yukon/Northwest Territories, regarded as among the highest-grade
deposits in the western world.

Exploration Results Ridley Creek zone

In 2016, contour soil samples were collected at the southeast
corner of the current Ridley Creek resource. In this area of the
deposit, drill hole F11-2 contains 2.20 metres of 2.11% WO3 starting at
7.15 metres and the mineralized zone remains open in extent. The soils
returned positive tungsten values (11-183 ppm W) along strike to the
southeast that suggest the mineralized zone may continue near surface
for 200 metres further in this direction. On the southwest edge of the
current resource, drill hole F16-09 returned several mineralized
intercepts including 3.0 metres of 0.52% WO3. Approximately 150 metres
along strike to the north of the Ridley Creek resource, a chip sample
from the bottom of a 20-metre thick calc-silicate cliff returned 1.5
metres of 3.44% WO3 and the mineralized zone is open in width. These
results suggest there is good potential to expand the near-surface
portion of the Ridley Creek resource in several directions.

BN zone

In 2016, drilling of nine holes at the BN zone together with those
from 2012, have outlined an inferred resource of 254,000 tonnes grading
1.892% WO3. Drill holes F16-19 and F16-20 are the southern-most in this
zone, and returned 6.0 metres of 0.56% WO3 starting at 31.0 metres, and
5.0 metres of 0.97% WO3 starting at 21.0 metres, respectively. These
intercepts are closer to surface than the others further north.
Approximately 150 metres south of these holes and at a lower elevation,
large tabular shaped calc-silicate/skarn boulders were located at
surface and are thought to be near where the zone will daylight to
surface. At the north end of the BN resource, drill holes F16-22
returned 4.0 metres of 1.36% WO3 and F12-27 returned 4.1 metres of
1.78% WO3 at surface while the main resource layer intercept returned
14.8 metres of 4.0% WO3. Starting at 136.0 metres and not included in
the current resource, F12-27 also returned 7.8 metres of 1.77% WO3
(along with 0.64% zinc, 3.0 g/t indium, 6.8 g/t silver and 151 g/t
bismuth) and the three mineralized layers remain open in extent to the
north. On a larger scale, positive tungsten in soil and outcrop located
in 2016 occur in a 1.5 km long zone to the southwest of the drilling.
The 708 prospect is an outcrop with 2.0 metres of 1.52% WO3 that is
open in width. Much of the BN area is underexplored at surface. The BN
target is situated near the contact between the favorable calc silicate
host rock and the Deception stock, which is thought to be an ideal
setting for high-grade tungsten skarn deposits to occur. Together, the
results show excellent potential to expand the current BN resource.

BK zone

Trench sampling performed in 2016 has defined continuity at
surface over a 20 metre strike length with 3.0 metres of 0.97% WO3, 6.0
metres of 0.66% WO3, and between these trenches, 3.4 metres of 3.42%
WO3. The variation in grade of the trenches reflect a complexity to the
mineralized zone. The mineralized zone was traced at surface for
another 80 metres south with a moderate degree of certainty and chip
samples across poorly exposed outcrop returned 2.0 metres of 0.66% WO3,
and 0.60 metres of 0.38% WO3 which remain open in width. A grab sample
containing 1.31% WO3 also occurs. Approximately 120 metres further
south an outcrop containing 0.37% WO3 in a grab sample was collected
and the favorable geology was mapped continuously south to the Ridley
Creek zone.

Fifteen metres southwest of the BK trenches, drill holes F16-11
(vertical) and F16-12 (-60 degrees) are oriented to the southeast and
cut 1.0 metres of 0.46% WO3 and 2.20 metres of 0.66% WO3, respectively,
and both intervals start at 12.5 metres down hole. The mineralized zone
in the trenches is continuous through these drill holes from surface,
while the grade and thickness is lower. Seventeen metres west of the
trenches, drill holes F16-14 (-45 degrees) and F16-15 (-65 degrees) are
oriented to the northeast and returned 5.2 metres of 0.70% WO3 and 6.0
metres of 0.67% WO3, starting at 20.8 and 10.0 metres, respectively.
The mineralized zone remains open in extent with encouraging grade and
thickness. The down hole depths to the top of the zone as compared with
the surface mineralized zone in the trenches suggest post-mineral
folding occurred. Folding of the mineralized zone allows potential for
it to extend at least 50 metres east of the trenches where angular
boulders returned values of 1.12% WO3 and 4.65% WO3. Additional
drilling and trenching of the BK zone is planned to further expand the
known mineralized zone and determine its resource potential.

South Grid zone

The South Grid target is defined by positive tungsten in soil in
an area 1.25 km by 500 metres in dimension and in early 2016, twenty
grab samples collected from widespread outcrop and angular boulders
returned positive tungsten values. Four samples contain from 1.75-5.89%
WO3, five samples contain from 0.35-0.76% WO3 and five samples contain
from 0.12-0.26% WO3. At the end of the 2016 drilling program, three
drill holes were lost or abandoned at a shallow depth due to deep,
sinking mud conditions. The drilling confirmed the favorable calc
silicate zones are up to 16.0 metres in thickness, and dip 25 to 35
degrees southwest. Assays include 2.0 metres of 0.15% WO3 starting at
2.0 metres in F16-27 and the hole was lost at 19.6 metres. Drill hole
F16-28 returned 1.5 metres of 0.13% WO3 starting at 26.5 metres and
this hole was also abandoned. A machine trench cleared off an
eight-metre-long and approximately 0.60 metres wide portion of surface
outcrop and grab samples collected at two metre intervals returned 0.22
- 0.54% WO3. This zone remains open in extent along

strike and width. The South Grid target is thought to be
insufficiently tested and may be compared to exploration at the Ridley
Creek zone, where drilling returned 2.0 metres of 0.124% WO3 that is
located 100 metres from a drill hole containing 26.1 metres of 1.19%
WO3. Additional drill testing of the large scale South Grid is planned.


Associated metals

In addition to tungsten, results continue to indicate values of
zinc, indium, gold, silver and bismuth occur and the Company's previous
metallurgical tests with flotation are encouraging for a separate
concentrate as potential by-product credits. Drill hole F16-03 includes
3.4 metres with 2.19% WO3, 0.46% zinc, 3.0 ppm (parts per million or
grams per tonne) indium, 129 ppb (parts per billion) gold and 456 ppm
bismuth, and F16-17 includes 4.1 metres of 5.1% WO3, 1.04% zinc, 3.9
ppm indium, 97 ppb gold and 301 ppm bismuth. Elevated silver values
were returned in drill hole F16-10 with 2.0 metres of 11.0 g/t silver,
and F16-17 with 2.85 metres containing 0.21% WO3 and 100.0 g/t silver.
The Company is monitoring and tracking the potential credits from
by-products so that they may be included in a future resource estimate.


Plans

The Company is completing reports of work from 2016, updating the
website and permits for an expanded program in 2017. Exploration on the
Fox property continues to find new zones at surface, and drilling
continues to expand mineralized zones with grades among the highest in
the industry. The Company has received approval for additional Federal
NSERC funding in 2017 to continue scientific studies conducted through
the University of British Columbia. Plans for 2017 include further
drilling to increase the size of the project resource base and perform
various engineering and environmental studies with a view to
potentially conducting a preliminary economic assessment.

The Company will be present at the PDAC in Toronto and have booth
2425 (b) on Tuesday March 7th and Wednesday March 8th at the Investors
Exchange.

On behalf of the Board of Directors,

"David E Blann"

David E Blann, P.Eng. President, CEO

FOR FURTHER INFORMATION PLEASE CONTACT: David Blann, President, CEO
Corporate Office:

Phone: 604.662.8310
Email: Info@happvcreekminerals.com Website: www.happvcreekminerals.com

Corporate Communications Ron Birch: Phone: 250-545-0383 Toll Free:
1-800-910-7711

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

David Blann, P.Eng. is a Qualified Person as defined by National
Instrument 43-101 and is responsible for the preparation and approval
of the technical information disclosed in the news release. Drill hole
intervals are down-hole measurements and while true thickness remains
uncertain, they are estimated to be between 75-95 percent of down hole
measurements. Drill core samples are derived from 1A core cut by rock
saw and shipped to, prepared and analyzed at SGS Laboratories in
Burnaby, British Columbia. Drill core and trench samples are digested
and analyzed by aqua regia and ICP-MS as well as peroxide fusion and
ICP-AES for percent tungsten (W), respectively. Over limit samples
greater than 4 percent W are re-analyzed by XRF. Wis multiplied by
1.261 to obtain WO3 (tungsten trioxide) the compound for which tungsten
prices are quoted. ICP-MS results are reported in ppm (parts per
million) or ppb (parts per billion). Samples returning over 4,000 ppm
zinc are assayed to provide percent zinc. For composites, zinc (ppm) is
converted to percent by dividing by 10,000. The Company routinely
inserts blanks, certified standards and duplicate samples within the
submitted drill core batches submitted for assay as part of its quality
control procedures.

This press release contains "forward-looking information" within
the meaning of applicable securities laws, including statements that
address capital costs, recovery, grade, and timing of work or plans at
the Company's mineral projects. Forward-looking information may be, but
not always, identified by the use of words such as "seek",
"anticipate", "plan", "planned", "continue", "expect", "thought to",
"project", "predict", "potential", "targeting", "intends", "believe",
"opportunity", "further" and others, or which describes a goal or
action, event or result such as "may", "should", "could", "would",
"might" or "will" be undertaken, occur or achieved. Statements also
include those that address future mineral production, reserve
potential, potential size or scale of a mineralized zone, potential
expansion of mineralization, potential type(s) of mining, potential
grades as well as to Happy creek's ability to fund ongoing expenditure,
or assumptions about future metal or mineral prices, currency exchange
rates, metallurgical recoveries and grades, favourable operating
conditions, access, political stability, obtaining or renewal of
existing or required mineral titles, licenses and permits, labour
stability, market conditions, availability of equipment, accuracy of
any mineral resources, anticipated costs and expenditures. Assumptions
may be based on factors and events that are not within the control of
Happy creek and there is no assurance they will prove to be correct.
Such forward-looking information involves known and unknown risks,
which may cause the actual results to materially differ, and/or any
future results expressed or implied by such forward-looking
information. Additional information on risks and uncertainties can be
found within Financial Statements, Prospectus and other materials found
on the Company's SEDAR profile at www.sedar.com. Although Happy creek
has attempted to identify important factors that could cause actual
actions, events or results to differ materially from those described in
forward-looking information, there can be no assurance that such
information will prove to be accurate as actual results and future
events could differ materially from those anticipated in such
statements. Happy creek withholds any obligation to update or revise
any forward-looking information, whether as a result of newinformation, future 
events or otherwise, unless required by law.
______________________________________
_______________________________________________
TSX Venture closing price for HPY-V
Date: 2017/02/28
Closing Price: 0.22
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1705900038TS11705901055-06333520170301