Source	Marketwire
Date	03/06/2017
Time	01:01:59 PM

Company	 SEARCH MINERALS INC.
Title	Search Minerals Produces High Purity Mixed Rare Earth Oxide Product From 
the Pilot Plant Operation





    CDNX Symbol: SMY











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Search Minerals Inc.

TSX VENTURE SYMBOL: SMY

March 6, 2017

Search Minerals Produces High Purity Mixed Rare Earth Oxide Product From the 
Pilot Plant Operation


VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 6, 2017) - Search Minerals 
Inc. (TSX VENTURE:SMY) ("Search" or the "Company") is pleased to announce the 
initial results from its pilot plant operation at SGS Laboratories in 
Lakefield, Ontario. The pilot plant project has been completed with some 
further results to be subsequently released.

After processing over 3.0 tonnes of material representative of the Foxtrot 
Deposit, the pilot plant testing has clearly demonstrated the ability to 
produce a high purity mixed rare earth oxide (REO) concentrate. In addition, 
the pilot plant testing has successfully demonstrated the ability to bring 
uranium, thorium, zinc, and iron levels below those thresholds expected by 
refineries that separate mixed REO concentrates into individual rare earth 
elements (REEs).

Pilot Plant Highlights:

/T/

--  Processed over 3.0 tonnes of crushed material from the Foxtrot Deposit
using the patented Search Minerals Direct Extraction Process.
--  Achieved excellent metallurgical results including:
--  Average extractions of 85% neodymium (Nd), 86% praseodymium (Pr),
68% dysprosium (Dy) by acid treatment/water leaching.
--  Average Losses of 2% Nd, 2% Pr and 0.3% Dy through iron removal.
--  Separation of uranium from the rare earths by ion exchange to below
detection limits in solution.
--  Precipitation of +99.9% of the rare earth elements as a mixed
carbonate product containing approx. 35% total rare earth content.
(Average of 5.3% Nd, 1.48% Pr, 0.58% Dy).
--  Demonstration of the re-leaching and purification of the mixed
carbonate product to produce REO material for refining with low Th
(8.6 g/t), U (less than 0.5 g/t) and Zn (64 g/t).
--  The refining of the mixed rare earth carbonate product was performed
in a sulfuric acid medium with careful control of thorium
(precipitation with magnesium carbonate) and zinc (precipitation
with hydrogen sulfide).
--  The final product was formed by oxalic acid precipitation and
calcination.
--  Generated engineering data for all parts of the circuit from sample
preparation to production of the mixed rare earth oxide.
--  Produced environmental samples (leach residues, precipitates, and barren
solutions) for characterization.

/T/

Greg Andrews, President and Chief Executive Officer of Search, states, "The 
results from the pilot plant testing conducted at SGS Laboratories in 
Lakefield, Ontario under the supervision of Search Vice-President of 
Metallurgy, Dr. David Dreisinger have exceeded expectations. The results help 
support a conclusion that our proprietary 'Direct Extraction' metallurgical 
process can produce a high purity mixed rare earth oxide. Furthermore, based on 
close attention to market forecasts, the process has been optimized to 
significantly increase recoveries for our key revenue elements, neodymium (Nd) 
and praseodymium (Pr)."

"We cannot overstate the importance of this achievement," noted Jim Clucas, 
Executive Chairman of Search. "Getting the metallurgy provides greater 
confidence and is a major milestone in the advancement of any REE project. It 
not only takes significant financial resources but significant management 
attention. On behalf of the Board and Management of Search Minerals I would 
like to thank the NunatuKavut Community Council and all our shareholders for 
their ongoing support over the last two years. As well, we'd like to thank the 
Atlantic Canada Opportunities Agency ("ACOA") and the Research & Development 
Corporation of Newfoundland and Labrador ("RDC") for their contribution of 
$1.25M towards this $ 1.9M pilot plant project," Clucas added.

Further Description of Process and Results

The Search Minerals Direct Extraction Process was tested on a sample of Foxtrot 
mineralization at SGS Minerals Lakefield Site. A representative bulk sample of 
Foxtrot mineralization was prepared under the supervision of Dr. Randy Miller 
of Search Minerals for the testing. The material was crushed to -10 mesh 
particle size prior to chemical treatment.

The testing process included: (1) extensive bench scale testing of the new 
sample and optimization of the chemical conditions for rare earth element 
recovery from the Foxtrot material, (2) a 5-day commissioning campaign in 
December 2016 to ensure smooth pilot operation, (3) a 10-day production 
campaign in January 2017 from crushed sample to mixed rare earth carbonate and 
(4) a 4-day refinery campaign to process mixed rare earth carbonate precipitate 
to mixed rare earth oxide.

Primary Leach Circuit

The first part of the pilot plant (to production of mixed rare earth carbonate) 
included these steps:

/T/

1.  Acid/sample mixing in a "PUG" mill.
2.  Acid/sample heating in the METSO HOLOFLITE system.
3.  Holding acid/sample mixture at temperature in a holding furnace
(equivalent to the insulated discharge hopper in the plant).
4.  Water leaching of the acid/sample mixture to dissolve rare earth
elements.
5.  Iron removal (along with aluminum and thorium) by pH adjustment with
magnesium carbonate addition.
6.  Filtration and washing to recover a leach/purification residue and a
clean solution carrying rare earth elements.
7.  Removal of uranium by ion exchange.
8.  Precipitation of rare earth elements as a mixed carbonate by addition of
sodium carbonate.
9.  Thickening and filtration/washing of the mixed rare earth carbonate. The
mixed rare earth carbonate is held as a wet filter cake ready for the
re-leach circuit of the pilot plant, which was operated as a separate
campaign.

/T/

The key results of the Primary Leach Circuit of the pilot plant were as follows:

1. Acid bake and water leach extractions with approximately 140 kg of sulfuric 
acid addition per tonne of ore.

The acid baking and water leach extractions were reported for the period 
January 21, 2017 to January 27, 2017 as follows. The average extractions of the 
critical elements were 85% for Nd, 86% for Pr and 68% for Dy with several 
operating periods exceeding 70% Dy.

/T/

----------------------------------------------------------------------------
Extraction (%)
----------------------------------------------------------------------------
La Ce Pr Nd Sm Eu Gd Tb Dy Ho  Y Er Tm Yb Lu Sc Th  U
----------------------------------------------------------------------------
January 21 AM          88 87 87 87 83 77 78 75 73 70 71 67 65 59 55 13 71 55
----------------------------------------------------------------------------
January 21 PM          89 89 90 89 85 81 80 74 72 70 71 67 65 60 55 15 70 56
----------------------------------------------------------------------------
January 22 AM          87 87 87 86 83 83 78 73 70 68 69 64 61 58 54 14 64 51
----------------------------------------------------------------------------
January 22 PM          83 84 94 83 80 80 75 71 70 67 68 65 63 58 53 15 70 51
----------------------------------------------------------------------------
January 23 AM          84 84 94 84 80 79 74 72 69 67 68 65 63 60 56 17 76 51
----------------------------------------------------------------------------
January 23 PM          82 83 92 82 81 81 75 70 66 68 65 61 63 57 62 20 77 52
----------------------------------------------------------------------------
January 24 AM          84 86 95 84 80 79 73 70 65 68 67 59 61 55 51 NA 77 49
----------------------------------------------------------------------------
January 24 PM          87 88 97 87 83 72 75 73 70 65 67 65 63 56 47 19 82 53
----------------------------------------------------------------------------
January 25 AM          85 85 85 84 81 80 73 68 63 65 66 63 61 53 41 14 79 47
----------------------------------------------------------------------------
January 25 PM          87 87 87 86 82 77 75 69 65 62 67 62 60 55 46 13 76 53
----------------------------------------------------------------------------
January 26 AM          87 87 86 85 80 78 75 71 67 63 68 64 62 59 46 11 77 52
----------------------------------------------------------------------------
January 26 PM          85 85 85 84 80 74 75 71 68 66 68 64 62 58 51 15 77 49
----------------------------------------------------------------------------
January 27 AM          87 87 87 86 84 75 77 71 71 65 69 66 63 57 53 18 79 56
----------------------------------------------------------------------------
Average                86 86 86 85 82 78 75 71 68 67 68 64 62 57 51 11 75 52
----------------------------------------------------------------------------

/T/

2. Iron Removal

The iron removal process is designed to remove the bulk of the iron, aluminum 
and thorium from solution by precipitation with magnesium carbonate while 
minimizing the losses of rare earths to the iron residue. The average removal 
efficiency of impurities was 100% for Fe, 56% for Al and 92% for Th. The losses 
of rare earths by co-precipitation were minimal. The overall recoveries of the 
rare earth elements to solution are summarized below. The average recoveries 
were Nd (83%), Pr (84%) and Dy (68%). When compared to the acid bake and water 
leach extractions, the losses were 2-3% for Nd-Pr and less than 1% for Dy.

/T/

----------------------------------------------------------------------------
Recoveries to Solution after Iron Removal (%)
----------------------------------------------------------------------------
La  Ce  Pr  Nd  Sm  Eu  Gd  Tb  Dy  Ho   Y  Er  Tm  Yb  Lu
----------------------------------------------------------------------------
Average           84  84  84  83  80  76  75  70  68  65  68  64  60  56  49
----------------------------------------------------------------------------

/T/

3. Uranium Ion Exchange

The uranium ion exchange process selectively removes uranium from the iron free 
solution to ensure production of a low uranium mixed rare earth oxide product. 
The uranium was removed to below the detection limit in the solution with 
negligible (less than 0.1%) loss of rare earth elements by co-loading with 
uranium.

4. Precipitation of a Mixed Rare Earth Carbonate Precipitate

The uranium and iron free solution was treated with sodium carbonate solution 
to precipitate the rare earths (and any remaining impurities) as a mixed 
carbonate product. This process was highly efficient and produced a mixed 
carbonate product of the analysis shown below. The first table shows the rare 
earth composition of the precipitate. The second table shows the remaining 
contaminants in the precipitate that must be removed in the refining process 
(the second part of the Search Minerals Direct Extraction Process).

/T/

----------------------------------------------------------------------------
Average Analysis of the Rare Earth Carbonate
Precipitate (%)
----------------------------------------------------------------------------
La     Ce     Pr     Nd     Sm     Eu     Gd     Tb
----------------------------------------------------------------------------
Average                5.83  12.54   1.48   5.32   0.93   0.05    0.7    0.1
----------------------------------------------------------------------------

---------------------------------------------------------------------
Average Analysis of the Rare Earth Carbonate
Precipitate (%)
---------------------------------------------------------------------
Dy     Ho      Y     Er     Tm     Yb     Lu
---------------------------------------------------------------------
Average                0.58   0.11   2.85    0.3   0.04   0.23   0.03
---------------------------------------------------------------------
----------------------------------------------------------------------------
Average Impurity Analysis of the Rare Earth Carbonate Precipitate
----------------------------------------------------------------------------
Th     U    Si    Al    Fe    Mg    Ca    Mn    Cr    Be    Zn
----------------------------------------------------------------------------
(g/t) (g/t)   (%)   (%)   (%)   (%)   (%)   (%)   (%)   (%)   (%)
----------------------------------------------------------------------------
Average      199     1  5.49  5.89  0.34  0.48  1.08  0.35  0.03  0.12   3.1
----------------------------------------------------------------------------

/T/

5. Re-Leach and Refining

The second part of the pilot plant program processed the mixed rare earth 
carbonate product to form a mixed rare earth oxide.

The steps in this process were:

1. Re-leach the mixed carbonate in a weak sulfuric acid solution (change from 
former practice of using hydrochloric acid).

2. Adjust the pH of the solution to remove Fe, Al, Th to low levels.

3. Filter the solid residue produced by the pH adjustment. Note that some REEs 
are precipitated in this process but we have shown on the bench that we can 
treat this residue with strong acid and recycle to the first part of the plant 
(current operation) with negligible losses of REE's.

4. Removal of zinc by sulfide precipitation to produce a 63% Zn stream.

5. Precipitation of REE's by oxalic acid addition to form insoluble RE oxalates.

6. Filtration and washing of RE Oxalates.

7. Calcine the RE Oxalates to produce the approx. 99% pure produce with low 
impurity content for refining.

The re-leaching and pH adjustment process was effective at redissolving the 
rare earth elements from the mixed carbonate and precipitating the iron, 
aluminum and thorium to low levels using magnesium carbonate. This process was 
done with sulfuric acid addition in order to remove the use of hydrochloric 
acid from the Search Minerals Direct Extraction Process.

The precipitate recovered from this part of the process still carries high rare 
earth values which must be recovered and recycled to the first part of the 
Search process for recovery. The initial testing of the re-leaching of this 
precipitate has shown that high extractions (and therefore negligible losses) 
of rare earth elements can be obtained. Further bench scale work on this 
precipitate treatment is being performed by SGS Minerals to confirm the high 
extractions and negligible losses.

The removal of zinc from solution by hydrogen sulfide precipitation was very 
effective to producing a low zinc solution composition for the oxalic acid 
precipitation step.
The initial recovery of a mixed rare earth oxide by oxalic acid precipitation 
and calcination has confirmed the production of a high grade mixed rare earth 
oxide product containing low Th (8.6 g/t), U (less than 0.5 g/t) and Zn (64 
g/t) for refining to individual rare earth elements.

Qualified Person:

Dr. David Dreisinger, Ph.D., P.Eng., is the Company's Vice President, 
Metallurgy and Qualified Person for the purposes of NI 43-101. Dr. Dreisinger 
has reviewed and approved the technical disclosure contained in this news 
release as applicable. The company will endeavour to meet high standards of 
integrity, transparency, and consistency in reporting technical content, 
including geological and assay (e.g., REE) data.

About Search Minerals Inc.

Led by a proven management team and board of directors, Search is focused on 
finding and developing resources within the emerging Port Hope Simpson Critical 
Rare Earth Element (CREE) District of SE Labrador. The Company controls a belt 
70 km long and 8 km wide including its 100% interest in the FOXTROT Project 
which is road accessible and at tidewater. Exploration efforts have advanced 
"Deepwater Fox" and "Fox Meadow" as significant new CREE prospects very similar 
and in close proximity to the original FOXTROT discovery. While the Company has 
identified more than 20 other prospects in the District, its primary objective 
remains development of FOXTROT by confirming proprietary processing technology 
at the pilot plant level (in progress) and delineation of prospects that will 
ensure competitive-low cost production beyond the 14-year mine life 
contemplated in the Preliminary Economic Assessment of FOXTROT completed in 
April 2016. The FOXTROT Project has a low capital cost to bring the initial 
project into production ($152 M), a short payback period and is scalable due to 
Search's proprietary processing technology.

All material information on the Company may be found on its website at 
www.searchminerals.ca and on SEDAR at www.sedar.com

About neo-CREOs (Adamas Intelligence - December 2016)

We consider neodymium, praseodymium, and dysprosium to be neo-CREOs because 
there is a high probability they will be in short supply by 2025, and they are 
vital to NdFeB magnets used widely in renewable power generation, electric 
mobility, and energy-efficient technologies. We consider terbium to be a 
neo-CREO because upon experiencing shortages of dysprosium, consumers in the 
magnet industry will rapidly consume available terbium supplies in its place 
for applications involving renewable power generation, electric mobility and 
energy efficient technologies. Lanthanum is considered a neo-CREO because there 
is a high probability it will be in short supply by 2025 and because it is 
widely used in catalytic converters and rechargeable batteries, and will be 
increasingly used as a thermal stabilizer by producers of poly-vinyl chloride 
(PVC) to minimize lead consumption and improve the energy efficiency of PVC and 
other processing equipment.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

CAUTIONARY STATEMENTS

Regarding "Forward-Looking" Information.

This news release includes certain "forward-looking information" and 
"forward-looking statements" (collectively "forward-looking statements") within 
the meaning of applicable Canadian and United States securities legislation 
including the United States Private Securities Litigation Reform Act of 1995. 
All statements, other than statements of historical fact, included herein, 
without limitation, statements relating the future operating or financial 
performance of the Company, are forward-looking statements.

Forward-looking statements are frequently, but not always, identified by words 
such as "expects", "anticipates", "believes", "intends", "estimates", 
"potential", "possible", and similar expressions, or statements that events, 
conditions, or results "will", "may", "could", or "should" occur or be 
achieved. Forward-looking statements in this news release relate to, among 
other things future events or the Company's future performance, business 
prospects or opportunities. Actual future results may differ materially. There 
can be no assurance that such statements will prove to be accurate, and actual 
results and future events could differ materially from those anticipated in 
such statements. Forward-looking statements reflect the beliefs, opinions and 
projections on the date the statements are made and are based upon a number of 
assumptions and estimates that, while considered reasonable by the respective 
parties, are inherently subject to significant business, economic, competitive, 
political and social uncertainties and contingencies. Many factors, both known 
and unknown, could cause actual results, performance or achievements to be 
materially different from the results, performance or achievements that are or 
may be expressed or implied by such forward-looking statements and the parties 
have made assumptions and estimates based on or related to many of these 
factors. Such factors include, without limitation, general business, economic 
and social uncertainties; litigation, legislative, environmental and other 
judicial, regulatory, political and competitive developments; and those 
additional risks set out in Search's public documents filed on SEDAR at 
www.sedar.com. Although Search believes that the assumptions and factors used 
in preparing the forward-looking statements are reasonable, undue reliance 
should not be placed on these statements, which only apply as of the date of 
this news release and no assurance can be given that such events will occur in 
the disclosed time frames or at all. Except where required by law, Search 
disclaims any intention or obligation to update or revise any forward-looking 
statement, whether as a result of new information, future events, or otherwise.

- 30 -

CONTACT INFO:

Greg Andrews
President and CEO
Tel: 604 998-3432 Ext 2
E-mail: info@searchminerals.ca

or

Paul Snow
Investor Relations
Tel: 709 753-0794
E-mail: psnow@pilotcom.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=589122590