Source	Marketwire
Date	03/16/2017
Time	05:01:07 AM

Company	 ATLANTIC GOLD CORPORATION
Title	Atlantic Gold Reports Additional Results from the Resource Definition 
Drill Program at Fifteen Mile Stream





    CDNX Symbol: AGB











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

March 16, 2017

Atlantic Gold Reports Additional Results from the Resource Definition Drill 
Program at Fifteen Mile Stream

Highlights include: 20M @ 3.35 g/t from 68M, 17M @ 2.26 from 42M, 45M @ 1.12 
g/t from 64M

VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 16, 2017) - Atlantic Gold 
Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is pleased to 
report assay results received from a further 34 holes of the resource 
definition diamond drilling program being undertaken at its Fifteen Mile Stream 
Gold Project in Nova Scotia, Canada. A single rig is presently drilling on the 
property with 110 holes for 10,220m of the planned 25,000m having been drilled 
to date. The objective of this program is to bring the resources at the 
Company's Fifteen Mile Stream deposit to measured and indicated status and 
thereby adding to the existing life of mine plan at MRC.

Drilling Results:

As previously reported these results continue to reflect those grades, widths 
and disposition of gold mineralization documented from the 1980s and 2011 
drilling programs, and which underpin the current inferred resource estimate 
for Fifteen Mile Stream (see below). Mineralization occurs within argillites, 
greywackes and bedding-parallel quartz veins across the hinge zone and limbs of 
the E-W trending Fifteen Mile Stream (FMS) Anticline. The northern limb of the 
anticline dips moderately north, with the southern limb vertical to overturned 
(generally steeply north dipping). All holes are therefore declined to the 
south and hence true widths vary (see assay table below) depending on which 
limb of the anticline is intersected, and also depending on hole declination. 
Free gold is commonly observed, and in association with pyrrhotite and 
arsenopyrite.

The northern limb is more strongly mineralized in the eastern, and dominant, 
Egerton-MacLean zone than in the Hudson zone to the west, and hence drilling 
extends further to the north in the Egerton-MacLean zone. The subvertical 
southern limb is more consistently mineralized across the Egerton-MacLean and 
Hudson zones though mineralization now appears to be subdued in the central 
area between the two zones. As a result of extensive drainage the drilling to 
date has generally been predicated on ready access to dry or "upland" drill 
sites such that at Egerton-MacLean in particular, results to hand are largely 
peripheral to the central part of the deposit as presently known. Drilling from 
wetland sites, and upland sites with restricted access, is about to commence. 
These sites represent the majority of the inferred resources previously 
reported for Fifteen Mile Stream.

The shallow and widespread disposition of mineralization in multiple layers 
across a sub-horizontal anticlinal hinge zone continue to encourage the 
prospect for the delineation of near surface mineralization.

The accompanying cross sections and drilling progress plan can be viewed here:
http://media3.marketwire.com/docs/atla0315.pdf

On the drilling progress plan attention is drawn to the perceived spatial 
relationship between the Egerton-MacLean zone and the Plenty prospect to the 
southwest, and the historical workings in between these zones. The Plenty zone 
is thought to represent a segment of the subvertical southern limb of the FMS 
Anticline faulted into place along the Seigel Fault from an original position 
probably to the north and at depth.

The mineralization intersected in hole FMS-17-073 (8m @ 1.28 g/t from 55m) is 
located south of the Seigel Fault and would seem to represent the eastern limit 
of the Plenty zone as it abuts the Seigel Fault. From this point southwestwards 
to the holes most recently drilled at Plenty is a distance of about 350m, and 
this gap is potentially mineralized. It is further noted that, historically, 
Fifteen Mile Stream and Plenty have been held under different ownerships; this 
is the first time the two prospects can effectively be considered together. 
Drilling is planned here once Fifteen Mile Stream and Cochrane Hill programs 
have been completed.

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017 and March 1, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
Depth(greater than or equal to0.5g/t Au and
Hole id      East North Dip Az.   (m)           up to 3m internal dilution)
---------------------------------------
From  To Width Approx true      Grade
(m) (m)   (m)   width (m)   (g/t Au)
----------------------------------------------------------------------------
FMS-17-029  12400 10040 -60 175    71    7   8     1         0.8       6.77
----------------------------------------------------------------------------
and                                     16  17     1         0.8       3.77
----------------------------------------------------------------------------
and                                     24  26     2         1.6       9.60
----------------------------------------------------------------------------
and                                     35  38     3           2       5.35
----------------------------------------------------------------------------
and                                     50  52     2         1.6       1.60
----------------------------------------------------------------------------
FMS-17-031  13575 10160 -60 175   122   54  71    17          17       1.50
----------------------------------------------------------------------------
FMS-17-032  12350 10020 -60 175    80   15  18     3         2.5       4.56
----------------------------------------------------------------------------
and                                     22  25     3         2.5       2.11
----------------------------------------------------------------------------
and                                     30  41    11           9       1.59
----------------------------------------------------------------------------
FMS-17-034  13575 10140 -60 175    92   31  40     9           9       0.40
----------------------------------------------------------------------------
and                                     44  59    15          15       1.70
----------------------------------------------------------------------------
and                                     65  72     7           7       2.41
----------------------------------------------------------------------------
FMS-17-035  12350 10060 -60 175   101   20  21     1           1       4.03
----------------------------------------------------------------------------
and                                     75  87    12          10       1.24
----------------------------------------------------------------------------
FMS-17-036  13450 10080 -60 175   152   44  58    14          11       1.05
----------------------------------------------------------------------------
and                                     68  69     1         0.8       28.2
----------------------------------------------------------------------------
and                                     92 102    10           7       0.92
----------------------------------------------------------------------------
FMS-17-037  12350 10080 -60 175   122   39  45     6           5       0.79
----------------------------------------------------------------------------
and                                     50  58     8           7       1.53
----------------------------------------------------------------------------
and                                     64  65     1           1       14.1
----------------------------------------------------------------------------
and                                     81  82     1           1       3.33
----------------------------------------------------------------------------
and                                     98 106     8           6       1.02
----------------------------------------------------------------------------
FMS-17-038  13450 10060 -60 175   101    6  10     4           4       1.41
----------------------------------------------------------------------------
and                                     54  79    25          15       0.71
----------------------------------------------------------------------------
FMS-17-039  12800 10060 -60 175    80   47  50     3           2       1.02
----------------------------------------------------------------------------
FMS-17-040  13450 10040 -60 175    80   19  42    23          13       1.54
----------------------------------------------------------------------------
and                                     50  51     1         0.6       6.62
----------------------------------------------------------------------------
FMS-17-041  12800 10040 -60 175    62                          -        NSA
----------------------------------------------------------------------------
FMS-17-042  13425 10080 -60 175   131    5  11     6           5       1.13
----------------------------------------------------------------------------
and                                     44  57    13          11       0.88
----------------------------------------------------------------------------
and                                     67  68     1         0.7       9.81
----------------------------------------------------------------------------
and                                     73  75     2         1.5       1.86
----------------------------------------------------------------------------
and                                     96 103     7           5       0.81
----------------------------------------------------------------------------
FMS-17-043  12800 10020 -60 175    47                          -        NSA
----------------------------------------------------------------------------
FMS-17-044  12850 10080 -60 175   101   69  74     5           5       0.98
----------------------------------------------------------------------------
FMS-17-045  13425 10060 -60 175    92   24  35    11           9       1.35
----------------------------------------------------------------------------
and                                     66  82    16          13       0.80
----------------------------------------------------------------------------
FMS-17-046  12850 10060 -60 175    80   55  58     3           3       1.27
----------------------------------------------------------------------------
FMS-17-048  13425 10100 -60 175   161   22  34    12          11       0.70
----------------------------------------------------------------------------
and                                     49  58     9           8       0.81
----------------------------------------------------------------------------
and                                     64 109    45          40       1.12
----------------------------------------------------------------------------
and                                    118 133    15          11       1.08
----------------------------------------------------------------------------
FMS-17-050  12950 10060 -60 175    80    4   5     1         0.8       21.0
----------------------------------------------------------------------------
and                                     69  73     4           3       1.21
----------------------------------------------------------------------------
FMS-17-057  13400 10060 -60 175   101   45  60    15          12       0.59
----------------------------------------------------------------------------
and                                     68  84    16          10       0.66
----------------------------------------------------------------------------
and                                     88  91     3           2       2.48
----------------------------------------------------------------------------
FMS-17-058  13000 10060 -60 175    80                          -        NSA
----------------------------------------------------------------------------
FMS-17-059  13375 10080 -60 175   140   14  33    19          16       0.72
----------------------------------------------------------------------------
and                                     39  46     7           6       0.95
----------------------------------------------------------------------------
and                                     68  88    20          14       3.35
----------------------------------------------------------------------------
(incl.                                  81  82     1         0.7       29.6)
----------------------------------------------------------------------------
and                                    104 117    13           8       1.46
----------------------------------------------------------------------------
FMS-17-060  13000 10040 -60 175    62                          -        NSA
----------------------------------------------------------------------------
FMS-17-061  13250 10060 -60 175   140   28  29     1         0.7       26.2
----------------------------------------------------------------------------
and                                     86  89     3           2       1.31
----------------------------------------------------------------------------
and                                    118 119     1         0.7       5.11
----------------------------------------------------------------------------
FMS-17-062  13000 10020 -60 175    41                          -        NSA
----------------------------------------------------------------------------
FMS-17-063  13050 10040 -60 175    62   43  52     9           7       1.05
----------------------------------------------------------------------------
FMS-17-064  13050 10080 -60 175    98   88  92     4           3       1.07
----------------------------------------------------------------------------
FMS-17-065  13275 10040 -60 175   110   43  44     1         0.8       11.9
----------------------------------------------------------------------------
and                                     48  55     7           5       1.10
----------------------------------------------------------------------------
FMS-17-066  13050 10060 -60 175    80   67  68     1         0.8       6.12
----------------------------------------------------------------------------
and                                     74  76     2         1.5       1.92
----------------------------------------------------------------------------
FMS-17-067  13275 10020 -60 175    92   42  59    17          10       2.26
----------------------------------------------------------------------------
FMS-17-068  13050 10020 -60 175    41                          -        NSA
----------------------------------------------------------------------------
FMS-17-070  13100 10080 -60 175   101   27  28     1         0.6       4.49 
----------------------------------------------------------------------------
and                                     83  86     3           2       1.74
----------------------------------------------------------------------------
and                                     98  99     1         0.7       27.3
----------------------------------------------------------------------------
and                                     99 100     1         0.7       25.0
----------------------------------------------------------------------------
FMS-17-071  13100 10060 -60 175    80   74  78     4           3       1.53
----------------------------------------------------------------------------
FMS-17-072  13100 10040 -60 175    62   42  47     5           4       7.29
----------------------------------------------------------------------------
(incl.                                  43  44     1         0.8       28.1)
----------------------------------------------------------------------------
and                                     51  56     5           4       5.63
----------------------------------------------------------------------------
(incl.                                  55  56     1         0.8       23.3)
----------------------------------------------------------------------------
FMS-17-073  13275  9980 -60 175    80   55  63     8           6       1.28
----------------------------------------------------------------------------

/T/

NSA: No significant assays.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Category           Tonnes (millions)    Grade (g/t) Au  Contained Au (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource              11.72              1.55             584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

Results and updates from this drilling program will be reported progressively.

Technical Disclosure

All assays are 50g charge fire assays conducted on whole-sample pulverized 1m 
samples of sawn, half NQ core with 1-in-10 duplicate assays and insertion of 
standards and blind blanks. Sample preparation and assaying is conducted at the 
Sudbury and Vancouver laboratories of ALS Canada Ltd, an entity having no other 
relationship with the Company. Core recovery is estimated for each metre and 
averages greater than 97%, excluding occasional voids, usually less than 2m, 
representing historic underground workings. Standards, blanks and duplicate 
assay results are acceptable.

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection (see table above). Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The individual drill hole assay results underlying the mineralized 
intersections listed in the table above have been verified by detailed checking 
against the original assays sheets. The lengths and average grades of each 
intersection have also been checked against the drill hole assay logs.

Wally Bucknell, Director of Exploration to the Company and a Qualified Person 
as defined by National Instrument 43-101 ("NI 43-101") has reviewed and 
approved the contents of this news release.

Further updates will be provided in due course.

On behalf of the Board of Directors,

Steven Dean, Chairman and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements:

This release contains certain "forward looking statements" and certain 
"forward-looking information" as defined under applicable Canadian and U.S. 
securities laws. Forward-looking statements and information can generally be 
identified by the use of forward-looking terminology such as "may", "will", 
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans" or 
similar terminology. Forward-looking statements and information are not 
historical facts, are made as of the date of this press release, and include, 
but are not limited to, statements regarding discussions of future plans, 
guidance, projections, objectives, estimates and forecasts and statements as to 
management's expectations with respect to, among other things, the activities 
contemplated in this news release and the timing and receipt of requisite 
regulatory, and shareholder approvals in respect thereof. Forward-looking 
statements in this news release include, without limitation, statements related 
to proposed exploration and development programs, grade and tonnage of material 
and resource estimates. These forward looking statements involve numerous risks 
and uncertainties and actual results may vary. Important factors that may cause 
actual results to vary include without limitation, the timing and receipt of 
certain approvals, changes in commodity and power prices, changes in interest 
and currency exchange rates, risks inherent in exploration estimates and 
results, timing and success, inaccurate geological and metallurgical 
assumptions (including with respect to the size, grade and recoverability of 
mineral reserves and resources), changes in development or mining plans due to 
changes in logistical, technical or other factors, unanticipated operational 
difficulties (including failure of plant, equipment or processes to operate in 
accordance with specifications, cost escalation, unavailability of materials, 
equipment and third party contractors, delays in the receipt of government 
approvals, industrial disturbances or other job action, and unanticipated 
events related to health, safety and environmental matters), political risk, 
social unrest, and changes in general economic conditions or conditions in the 
financial markets.
In making the forward-looking statements in this press release, the Company has 
applied several material assumptions, including without limitation, the 
assumptions that: (1) market fundamentals will result in sustained gold demand 
and prices; (2) the receipt of any necessary approvals and consents in 
connection with the development of any properties; (3) the availability of 
financing on suitable terms for the development, construction and continued 
operation of any mineral properties; and (4) sustained commodity prices such 
that any properties put into operation remain economically viable. Information 
concerning mineral reserve and mineral resource estimates also may be 
considered forward-looking statements, as such information constitutes a 
prediction of what mineralization might be found to be present if and when a 
project is actually developed. Certain of the risks and assumptions are 
described in more detail in the Company's audited financial statements and MD&A 
for the year ended December 31, 2015 and for the quarter ended September 30, 
2016 on the SEDAR website at www.sedar.com. The actual results or performance 
by the Company could differ materially from those expressed in, or implied by, 
any forward-looking statements relating to those matters. Accordingly, no 
assurances can be given that any of the events anticipated by the 
forward-looking statements will transpire or occur, or if any of them do so, 
what impact they will have on the results of operations or financial condition 
of the Company. Except as required by law, the Company is under no obligation, 
and expressly disclaim any obligation, to update, alter or otherwise revise any 
forward-looking statement, whether written or oral, that may be made from time 
to time, whether as a result of new information, future events or otherwise, 
except as may be required under applicable securities laws.

- 30 -

CONTACT INFO:

Atlantic Gold Corporation
Maryse Bélanger
COO
+1 604 689-5564

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=589705855


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

March 16, 2017

Atlantic Gold Reports Additional Results from the Resource Definition Drill 
Program at Fifteen Mile Stream

Highlights include: 20M @ 3.35 g/t from 68M, 17M @ 2.26 from 42M, 45M @ 1.12 
g/t from 64M

VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 16, 2017) - Atlantic Gold 
Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is pleased to 
report assay results received from a further 34 holes of the resource 
definition diamond drilling program being undertaken at its Fifteen Mile Stream 
Gold Project in Nova Scotia, Canada. A single rig is presently drilling on the 
property with 110 holes for 10,220m of the planned 25,000m having been drilled 
to date. The objective of this program is to bring the resources at the 
Company's Fifteen Mile Stream deposit to measured and indicated status and 
thereby adding to the existing life of mine plan at MRC.

Drilling Results:

As previously reported these results continue to reflect those grades, widths 
and disposition of gold mineralization documented from the 1980s and 2011 
drilling programs, and which underpin the current inferred resource estimate 
for Fifteen Mile Stream (see below). Mineralization occurs within argillites, 
greywackes and bedding-parallel quartz veins across the hinge zone and limbs of 
the E-W trending Fifteen Mile Stream (FMS) Anticline. The northern limb of the 
anticline dips moderately north, with the southern limb vertical to overturned 
(generally steeply north dipping). All holes are therefore declined to the 
south and hence true widths vary (see assay table below) depending on which 
limb of the anticline is intersected, and also depending on hole declination. 
Free gold is commonly observed, and in association with pyrrhotite and 
arsenopyrite.

The northern limb is more strongly mineralized in the eastern, and dominant, 
Egerton-MacLean zone than in the Hudson zone to the west, and hence drilling 
extends further to the north in the Egerton-MacLean zone. The subvertical 
southern limb is more consistently mineralized across the Egerton-MacLean and 
Hudson zones though mineralization now appears to be subdued in the central 
area between the two zones. As a result of extensive drainage the drilling to 
date has generally been predicated on ready access to dry or "upland" drill 
sites such that at Egerton-MacLean in particular, results to hand are largely 
peripheral to the central part of the deposit as presently known. Drilling from 
wetland sites, and upland sites with restricted access, is about to commence. 
These sites represent the majority of the inferred resources previously 
reported for Fifteen Mile Stream.

The shallow and widespread disposition of mineralization in multiple layers 
across a sub-horizontal anticlinal hinge zone continue to encourage the 
prospect for the delineation of near surface mineralization.

The accompanying cross sections and drilling progress plan can be viewed here:
http://media3.marketwire.com/docs/atla0315.pdf

On the drilling progress plan attention is drawn to the perceived spatial 
relationship between the Egerton-MacLean zone and the Plenty prospect to the 
southwest, and the historical workings in between these zones. The Plenty zone 
is thought to represent a segment of the subvertical southern limb of the FMS 
Anticline faulted into place along the Seigel Fault from an original position 
probably to the north and at depth.

The mineralization intersected in hole FMS-17-073 (8m @ 1.28 g/t from 55m) is 
located south of the Seigel Fault and would seem to represent the eastern limit 
of the Plenty zone as it abuts the Seigel Fault. From this point southwestwards 
to the holes most recently drilled at Plenty is a distance of about 350m, and 
this gap is potentially mineralized. It is further noted that, historically, 
Fifteen Mile Stream and Plenty have been held under different ownerships; this 
is the first time the two prospects can effectively be considered together. 
Drilling is planned here once Fifteen Mile Stream and Cochrane Hill programs 
have been completed.

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017 and March 1, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
Depth(greater than or equal to0.5g/t Au and
Hole id      East North Dip Az.   (m)           up to 3m internal dilution)
---------------------------------------
From  To Width Approx true      Grade
(m) (m)   (m)   width (m)   (g/t Au)
----------------------------------------------------------------------------
FMS-17-029  12400 10040 -60 175    71    7   8     1         0.8       6.77
----------------------------------------------------------------------------
and                                     16  17     1         0.8       3.77
----------------------------------------------------------------------------
and                                     24  26     2         1.6       9.60
----------------------------------------------------------------------------
and                                     35  38     3           2       5.35
----------------------------------------------------------------------------
and                                     50  52     2         1.6       1.60
----------------------------------------------------------------------------
FMS-17-031  13575 10160 -60 175   122   54  71    17          17       1.50
----------------------------------------------------------------------------
FMS-17-032  12350 10020 -60 175    80   15  18     3         2.5       4.56
----------------------------------------------------------------------------
and                                     22  25     3         2.5       2.11
----------------------------------------------------------------------------
and                                     30  41    11           9       1.59
----------------------------------------------------------------------------
FMS-17-034  13575 10140 -60 175    92   31  40     9           9       0.40
----------------------------------------------------------------------------
and                                     44  59    15          15       1.70
----------------------------------------------------------------------------
and                                     65  72     7           7       2.41
----------------------------------------------------------------------------
FMS-17-035  12350 10060 -60 175   101   20  21     1           1       4.03
----------------------------------------------------------------------------
and                                     75  87    12          10       1.24
----------------------------------------------------------------------------
FMS-17-036  13450 10080 -60 175   152   44  58    14          11       1.05
----------------------------------------------------------------------------
and                                     68  69     1         0.8       28.2
----------------------------------------------------------------------------
and                                     92 102    10           7       0.92
----------------------------------------------------------------------------
FMS-17-037  12350 10080 -60 175   122   39  45     6           5       0.79
----------------------------------------------------------------------------
and                                     50  58     8           7       1.53
----------------------------------------------------------------------------
and                                     64  65     1           1       14.1
----------------------------------------------------------------------------
and                                     81  82     1           1       3.33
----------------------------------------------------------------------------
and                                     98 106     8           6       1.02
----------------------------------------------------------------------------
FMS-17-038  13450 10060 -60 175   101    6  10     4           4       1.41
----------------------------------------------------------------------------
and                                     54  79    25          15       0.71
----------------------------------------------------------------------------
FMS-17-039  12800 10060 -60 175    80   47  50     3           2       1.02
----------------------------------------------------------------------------
FMS-17-040  13450 10040 -60 175    80   19  42    23          13       1.54
----------------------------------------------------------------------------
and                                     50  51     1         0.6       6.62
----------------------------------------------------------------------------
FMS-17-041  12800 10040 -60 175    62                          -        NSA
----------------------------------------------------------------------------
FMS-17-042  13425 10080 -60 175   131    5  11     6           5       1.13
----------------------------------------------------------------------------
and                                     44  57    13          11       0.88
----------------------------------------------------------------------------
and                                     67  68     1         0.7       9.81
----------------------------------------------------------------------------
and                                     73  75     2         1.5       1.86
----------------------------------------------------------------------------
and                                     96 103     7           5       0.81
----------------------------------------------------------------------------
FMS-17-043  12800 10020 -60 175    47                          -        NSA
----------------------------------------------------------------------------
FMS-17-044  12850 10080 -60 175   101   69  74     5           5       0.98
----------------------------------------------------------------------------
FMS-17-045  13425 10060 -60 175    92   24  35    11           9       1.35
----------------------------------------------------------------------------
and                                     66  82    16          13       0.80
----------------------------------------------------------------------------
FMS-17-046  12850 10060 -60 175    80   55  58     3           3       1.27
----------------------------------------------------------------------------
FMS-17-048  13425 10100 -60 175   161   22  34    12          11       0.70
----------------------------------------------------------------------------
and                                     49  58     9           8       0.81
----------------------------------------------------------------------------
and                                     64 109    45          40       1.12
----------------------------------------------------------------------------
and                                    118 133    15          11       1.08
----------------------------------------------------------------------------
FMS-17-050  12950 10060 -60 175    80    4   5     1         0.8       21.0
----------------------------------------------------------------------------
and                                     69  73     4           3       1.21
----------------------------------------------------------------------------
FMS-17-057  13400 10060 -60 175   101   45  60    15          12       0.59
----------------------------------------------------------------------------
and                                     68  84    16          10       0.66
----------------------------------------------------------------------------
and                                     88  91     3           2       2.48
----------------------------------------------------------------------------
FMS-17-058  13000 10060 -60 175    80                          -        NSA
----------------------------------------------------------------------------
FMS-17-059  13375 10080 -60 175   140   14  33    19          16       0.72
----------------------------------------------------------------------------
and                                     39  46     7           6       0.95
----------------------------------------------------------------------------
and                                     68  88    20          14       3.35
----------------------------------------------------------------------------
(incl.                                  81  82     1         0.7       29.6)
----------------------------------------------------------------------------
and                                    104 117    13           8       1.46
----------------------------------------------------------------------------
FMS-17-060  13000 10040 -60 175    62                          -        NSA
----------------------------------------------------------------------------
FMS-17-061  13250 10060 -60 175   140   28  29     1         0.7       26.2
----------------------------------------------------------------------------
and                                     86  89     3           2       1.31
----------------------------------------------------------------------------
and                                    118 119     1         0.7       5.11
----------------------------------------------------------------------------
FMS-17-062  13000 10020 -60 175    41                          -        NSA
----------------------------------------------------------------------------
FMS-17-063  13050 10040 -60 175    62   43  52     9           7       1.05
----------------------------------------------------------------------------
FMS-17-064  13050 10080 -60 175    98   88  92     4           3       1.07
----------------------------------------------------------------------------
FMS-17-065  13275 10040 -60 175   110   43  44     1         0.8       11.9
----------------------------------------------------------------------------
and                                     48  55     7           5       1.10
----------------------------------------------------------------------------
FMS-17-066  13050 10060 -60 175    80   67  68     1         0.8       6.12
----------------------------------------------------------------------------
and                                     74  76     2         1.5       1.92
----------------------------------------------------------------------------
FMS-17-067  13275 10020 -60 175    92   42  59    17          10       2.26
----------------------------------------------------------------------------
FMS-17-068  13050 10020 -60 175    41                          -        NSA
----------------------------------------------------------------------------
FMS-17-070  13100 10080 -60 175   101   27  28     1         0.6       4.49 
----------------------------------------------------------------------------
and                                     83  86     3           2       1.74
----------------------------------------------------------------------------
and                                     98  99     1         0.7       27.3
----------------------------------------------------------------------------
and                                     99 100     1         0.7       25.0
----------------------------------------------------------------------------
FMS-17-071  13100 10060 -60 175    80   74  78     4           3       1.53
----------------------------------------------------------------------------
FMS-17-072  13100 10040 -60 175    62   42  47     5           4       7.29
----------------------------------------------------------------------------
(incl.                                  43  44     1         0.8       28.1)
----------------------------------------------------------------------------
and                                     51  56     5           4       5.63
----------------------------------------------------------------------------
(incl.                                  55  56     1         0.8       23.3)
----------------------------------------------------------------------------
FMS-17-073  13275  9980 -60 175    80   55  63     8           6       1.28
----------------------------------------------------------------------------

/T/

NSA: No significant assays.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Category           Tonnes (millions)    Grade (g/t) Au  Contained Au (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource              11.72              1.55             584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

Results and updates from this drilling program will be reported progressively.

Technical Disclosure

All assays are 50g charge fire assays conducted on whole-sample pulverized 1m 
samples of sawn, half NQ core with 1-in-10 duplicate assays and insertion of 
standards and blind blanks. Sample preparation and assaying is conducted at the 
Sudbury and Vancouver laboratories of ALS Canada Ltd, an entity having no other 
relationship with the Company. Core recovery is estimated for each metre and 
averages greater than 97%, excluding occasional voids, usually less than 2m, 
representing historic underground workings. Standards, blanks and duplicate 
assay results are acceptable.

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection (see table above). Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The individual drill hole assay results underlying the mineralized 
intersections listed in the table above have been verified by detailed checking 
against the original assays sheets. The lengths and average grades of each 
intersection have also been checked against the drill hole assay logs.

Wally Bucknell, Director of Exploration to the Company and a Qualified Person 
as defined by National Instrument 43-101 ("NI 43-101") has reviewed and 
approved the contents of this news release.

Further updates will be provided in due course.

On behalf of the Board of Directors,

Steven Dean, Chairman and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements:

This release contains certain "forward looking statements" and certain 
"forward-looking information" as defined under applicable Canadian and U.S. 
securities laws. Forward-looking statements and information can generally be 
identified by the use of forward-looking terminology such as "may", "will", 
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans" or 
similar terminology. Forward-looking statements and information are not 
historical facts, are made as of the date of this press release, and include, 
but are not limited to, statements regarding discussions of future plans, 
guidance, projections, objectives, estimates and forecasts and statements as to 
management's expectations with respect to, among other things, the activities 
contemplated in this news release and the timing and receipt of requisite 
regulatory, and shareholder approvals in respect thereof. Forward-looking 
statements in this news release include, without limitation, statements related 
to proposed exploration and development programs, grade and tonnage of material 
and resource estimates. These forward looking statements involve numerous risks 
and uncertainties and actual results may vary. Important factors that may cause 
actual results to vary include without limitation, the timing and receipt of 
certain approvals, changes in commodity and power prices, changes in interest 
and currency exchange rates, risks inherent in exploration estimates and 
results, timing and success, inaccurate geological and metallurgical 
assumptions (including with respect to the size, grade and recoverability of 
mineral reserves and resources), changes in development or mining plans due to 
changes in logistical, technical or other factors, unanticipated operational 
difficulties (including failure of plant, equipment or processes to operate in 
accordance with specifications, cost escalation, unavailability of materials, 
equipment and third party contractors, delays in the receipt of government 
approvals, industrial disturbances or other job action, and unanticipated 
events related to health, safety and environmental matters), political risk, 
social unrest, and changes in general economic conditions or conditions in the 
financial markets.
In making the forward-looking statements in this press release, the Company has 
applied several material assumptions, including without limitation, the 
assumptions that: (1) market fundamentals will result in sustained gold demand 
and prices; (2) the receipt of any necessary approvals and consents in 
connection with the development of any properties; (3) the availability of 
financing on suitable terms for the development, construction and continued 
operation of any mineral properties; and (4) sustained commodity prices such 
that any properties put into operation remain economically viable. Information 
concerning mineral reserve and mineral resource estimates also may be 
considered forward-looking statements, as such information constitutes a 
prediction of what mineralization might be found to be present if and when a 
project is actually developed. Certain of the risks and assumptions are 
described in more detail in the Company's audited financial statements and MD&A 
for the year ended December 31, 2015 and for the quarter ended September 30, 
2016 on the SEDAR website at www.sedar.com. The actual results or performance 
by the Company could differ materially from those expressed in, or implied by, 
any forward-looking statements relating to those matters. Accordingly, no 
assurances can be given that any of the events anticipated by the 
forward-looking statements will transpire or occur, or if any of them do so, 
what impact they will have on the results of operations or financial condition 
of the Company. Except as required by law, the Company is under no obligation, 
and expressly disclaim any obligation, to update, alter or otherwise revise any 
forward-looking statement, whether written or oral, that may be made from time 
to time, whether as a result of new information, future events or otherwise, 
except as may be required under applicable securities laws.

- 30 -

CONTACT INFO:

Atlantic Gold Corporation
Maryse Bélanger
COO
+1 604 689-5564

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=589705855