Source	Marketwire
Date	03/16/2017
Time	10:16:05 AM

Company	 WEST KIRKLAND MINING INC.
Title	West Kirkland Mining Reports New Gold Intercepts at Three Hills and Hill 
of Gold at the Hasbrouck Gold Project, Nevada





    CDNX Symbol: WKM











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: West Kirkland Mining Inc.

TSX VENTURE SYMBOL: WKM
OTCQB SYMBOL: WKLDF

March 16, 2017

West Kirkland Mining Reports New Gold Intercepts at Three Hills and Hill of 
Gold at the Hasbrouck Gold Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 16, 2017) - West Kirkland 
Mining Inc. (TSX VENTURE:WKM) (OTCQB:WKLDF) ("West Kirkland" or the "Company") 
today announces new gold bearing intercepts from a 2017 exploration drilling 
program. Drilling was performed east of the Three Hills pit and at the 
newly-leased Hill of Gold deposit which, together with the Hasbrouck Mine, form 
the Hasbrouck Gold Project.

DRILLING AT THREE HILLS

Holes TH17R-001, TH17R-002, AND TH17R-003 are within the Three Hills Mine 
permitted pit outline. Intercepts are outside the reserve boundary and will be 
evaluated for targeting resource and reserve expansion.

/T/

----------------------------------------------------------------------------
Length                       AuEq
Hole No.    From (m) To (m)      (m) Au (g/t) Ag (g/t)    (g/t)
----------------------------------------------------------------------------
THREE HILLS  TH17R-001        162    165        3      0.6      1.6      0.7
---------------------------------------------------------------
TH17R-002         93    139       46      0.6      1.9      0.6
---------------------------------------------------
165    169        5      0.5      4.2      0.5
---------------------------------------------------------------
TH17R-003        134    146       12      0.5      3.7      0.5
---------------------------------------------------------------
TH17R-004        143    146        3      0.6      1.5      0.6
---------------------------------------------------------------
TH17R-007         24     26        2      1.1      1.0      1.1
---------------------------------------------------
53     56        3      0.6      0.7      0.6
----------------------------------------------------------------------------
AuEq grade is (gold grade) +( silver grade multiplied by $16.89 divided by
$1,200)

/T/

Three Hills is part of the Hasbrouck Gold Project which includes Three Hills, 
Hasbrouck, and now Hill of Gold deposits. Hasbrouck Gold Project Proven and 
Probable Reserves are 45.3 million tons containing 762,000 ounces gold and 10.6 
million ounces silver:

/T/

----------------------------------------------------------------------------
Hasbrouck Gold Project Mineral Reserves
June 3, 2015, Mine Development Associates (1, 2)
----------------------------------------------------------------------------
Three Hills Mineral         K tons       Grade                Grade
Reserves                      Ore (oz Au/ton)  K oz Au (oz Ag/ton)  K oz Ag
----------------------------------------------------------------------------
0.005 opt
Au cutoff      Proven            -           -        -           -        -
-------------------------------------------------------------
Probable      9,653       0.018      175           -        -
-------------------------------------------------------------
P&P           9,653       0.018      175           -        -
----------------------------------------------------------------------------
Hasbrouck Mine Mineral
Reserves
----------------------------------------------------------------------------
Variable cutoff
grade(3)      Proven        6,242       0.020      127       0.410    2,562
-------------------------------------------------------------
Probable     29,374       0.016      461       0.273    8,007
-------------------------------------------------------------
P&P          35,617       0.017      588       0.297   10,569
----------------------------------------------------------------------------
Total Hasbrouck Gold
Project Mineral Reserves
----------------------------------------------------------------------------
Variable cutoff
grade(3)      Proven        6,242       0.020      127       0.410    2,562
-------------------------------------------------------------
Probable     39,028       0.016      635       0.205    8,007
-------------------------------------------------------------
P&P          45,270       0.017      762       0.233   10,569
----------------------------------------------------------------------------
Notes:
1)  The estimation and classification of Proven and Probable Mineral
Reserves have been prepared by Thomas L. Dyer, P.E., of Mine Development
Associates following CIM standards
2)  Mineral Reserves are estimated based on $1,225/oz gold and $17.50/oz
silver
3)  Cutoff grades used for Mineral Reserves are: Three Hills 0.005 oz
Au/ton, Hasbrouck Upper Siebert 0.008 oz Au/ton, and Hasbrouck Lower
Siebert 0.007 oz Au/ton

/T/

DRILLING AT HILL OF GOLD

Exploration at Hill of Gold is directed at defining an open pit that can add 
life to the permitted Three Hills Mine. Historical metallurgical work at Hill 
of Gold indicates that mineralization is oxidized and amenable to heap leach at 
1.5 inch crush for an 80% gold recovery. The Hill of Gold host rocks and 
geological setting are similar to the Three Hills deposit.

The hole West Kirkland drilled at Hill of Gold has been successful in expanding 
the gold zone defined by historical drilling of 29,926 feet from 83 reverse 
circulation holes and 6 core holes.

/T/

----------------------------------------------------------------------------
From           Length                       AuEq
Hole No.       (m)  To (m)      (m) Au (g/t) Ag (g/t)    (g/t)
----------------------------------------------------------------------------
HILL OF GOLD  HoG17-001      0.0   103.6    103.6      0.5      8.0      0.6
----------------------------------------------------------------------------
AuEq grade is (gold grade) +( silver grade multiplied by $16.89 divided by
$1,200)

/T/

In late 2016, West Kirkland entered a lease on the Hill of Gold deposit with 
the option to acquire a 100% interest. Hill of Gold is located equidistant 
between the Three Hills and Hasbrouck Mines and is now being explored as a 
possible source of ore for processing at the fully-permitted Three Hills Mine 
heap leach facility.

Further drilling will be targeted up-dip towards surface from this initial gold 
bearing intercept.

ABOUT THE HASBROUCK GOLD PROJECT

Hasbrouck Gold Project consists of two all-oxide gold-silver deposits eight 
kilometers apart. Both deposits will be mined in open pits having low stripping 
ratios and minimal pre-stripping should the project proceed to production.

West Kirkland's independent consultants, Mine Development Associates, produced 
an updated Pre-feasibility Study in September 2016 which is available on SEDAR 
and at www.wkmining.com. All necessary permits to construct and operate the 
Three Hills Mine are in hand, and work to obtain permits for the Hasbrouck Mine 
is ongoing, with submission of a Plan of Operation to the Bureau of Land 
Management (BLM) targeted for Q4, 2017.

QUALIFIED PERSON

R. Michael Jones P.Eng, CEO for West Kirkland Mining is a non-independent 
Qualified Person as defined by NI 43-101. He has reviewed the information 
contained in this news release and has verified the data by hiring qualified 
geologists and engineers and has completed a review of the detailed technical 
information. Mineral Reserve information in this news release has been 
developed and approved by Thomas L. Dyer, P.E., of Mine Development Associates 
following CIM standards.

QUALITY ASSURANCE/QUALITY CONTROL

West Kirkland Mining utilizes a well-documented system of inserting blanks and 
standards into the assay stream and has a strict chain of custody. Assays are 
completed at independent laboratories which have internal quality assurance and 
quality control systems and procedures. Assays were performed by ALS Chemex 
Labs Ltd., by fire assay and ICP methods.

ABOUT WEST KIRKLAND MINING INC.

West Kirkland owns a 75% interest in the Hasbrouck Gold Project in Tonopah, 
Nevada. A Pre-feasibility Study with construction-level drawings and all 
federal and state permits for the phase-one Three Hills Mine provides a 
ready-to-construct project. Drilling for potential expansion is underway. West 
Kirkland also holds a 60% interest in the open pit heap-leach TUG Gold Project 
in Utah in joint venture with Newmont.

/T/

On behalf of West Kirkland Mining Inc.
"R. Michael Jones"
Chief Executive Officer

/T/

For further information, please see the Company's website at www.wkmining.com 
or contact us by email at info@wkmining.com.

Disclaimer for Forward-Looking Information

This press release contains forward-looking information or forward-looking 
statements (collectively "forward-looking information") within the meaning of 
applicable securities laws. Forward-looking information is typically identified 
by words such as: "believe", "expect", "anticipate", "intend", "estimate", 
"postulate" and similar expressions, or are those, which, by their nature, 
refer to future events. Forward-looking information in this news release 
includes, without limitation, the completion of the Prefeasibility Study, the 
project approach of the Prefeasibility Study and exploration and all 
information under the heading "Prefeasibility Study Detail", including the 
Prefeasibility Study budget. Although West Kirkland believes that such timing 
and expenses as set out in this press release are reasonable, it can give no 
assurance that such expectations and estimates will prove to be correct. The 
Company cautions investors that any forward-looking information provided by the 
Company is not a guarantee of future results or performance, and that actual 
results may differ materially from those in forward-looking information as a 
result of various factors, including, but not limited to, the state of the 
financial markets for the Company's equity securities, the state of the market 
for gold or other minerals that may be produced generally, variations in the 
nature, quality and quantity of any mineral deposits that may be located, the 
Company's ability to obtain any necessary permits, consents or authorizations 
required for its activities, to raise the necessary capital or to be fully able 
to implement its business strategies and other risks associated with the 
exploration and development of mineral properties. The reader is referred to 
the Company's public filings for a more complete discussion of such risk 
factors and their potential effects which may be accessed through the Company's 
profile on SEDAR at www.sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

West Kirkland Mining Inc.
Investor Relations
(416) 884-3556
rbruggeman@wkmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=589742052