Source	Marketwire
Date	03/23/2017
Time	05:31:27 AM

Company	 SALAZAR RESOURCES LIMITED
Title	Salazar intersects 14.43 metres (13.07m true) averaging 2.65 g/t gold, 
10.58 g/t silver, 1.32% copper, 6.63% zinc at its Curipamba Project





    CDNX Symbol: SRL











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Salazar Resources Limited

TSX VENTURE SYMBOL: SRL
FRANKFURT SYMBOL: CCG

March 23, 2017

Salazar intersects 14.43 metres (13.07m true) averaging 2.65 g/t gold, 10.58 
g/t silver, 1.32% copper, 6.63% zinc at its Curipamba Project

Hole extends mineralization of El Domo deposit

VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 23, 2017) - Salazar Resources 
Limited (TSX VENTURE:SRL) (FRANKFURT:CCG) ("Salazar" or the "Company") is 
pleased to report results from the first twelve holes (3,363 meters) of the 
Phase V diamond drill program in progress on the Company's 100-per-cent-owned 
(21,500 ha) Curipamba volcanogenic massive sulphide (VMS) project in Ecuador. 
These holes represent new exploratory drilling and were not included in the 
latest El Domo resource estimate which was released on January 16th, 2015. The 
twelve holes were drilled as part of the planned 40-hole (10,000 meters) drill 
program that is designed to further expand the El Domo volcanogenic massive 
sulphide ("VMS") deposit and explore its margins, as well as to test 
geophysical anomalies and surface showings (Figure 1). It is anticipated that 
the drill program will be complete by the third quarter of this year.

HIGHLIGHTS:

Hole CURI-218:

/T/

--  14.43 metres (13.07m true) averaging 2.65 g/t gold, 10.58 g/t silver,
1.32% copper, 6.63% zinc, including
--   3.58 metres averaging 9.68 g/t gold, 11.52 g/t silver, 0.46%
copper, 2.64% zinc, and
--   4.47 metres averaging 0.29 g/t gold, 15.05 g/t silver, 3.16%
copper, 19.25% zinc

/T/

Hole CURI-213:

/T/

--  4.14 metres (true width) averaging 1.009 g/t gold, 16.78 g/t silver,
0.67% copper, 0.95% lead and 4.77% zinc
--   29.37 metres (true width) averaging 0.58 g/t gold, 77.93 g/t silver,
0.17% copper, 0.17% lead, 0.89% zinc, including
--  10.55 meters averaging 0.385 g/t gold, 8.02 g/t silver, 0.44%
copper, 0.25% lead and 1.84% zinc, and
--  13.75 meters averaging 0.75 g/t gold, 149.7 g/t silver, 0.02%
copper, 0.15% lead and 0.32% zinc

/T/

Hole CURI-218, collared approximately 240 metres east of the El Domo deposit, 
was drilled westerly on section with hole CURI-176 (5.7 metres averaging 0.671 
g/t gold, 3.3 g/t silver, 0.61% copper, 0.01% zinc and 0.96% lead). CURI-218 
intersected 14.43 metres (13.07 metres true width) of massive and semi-massive 
pyrite-chalcopyrite-sphalerite grading 2.65 g/t gold, 10.58 g/t silver, 1.32% 
copper, 6.63% zinc beneath an andesite sill that occurs in this area (Table 1). 
The intersection in CURI-218 is located approximately 100 metres east of the 
intersection in CURI-176. It clearly demonstrates the extension of the El Domo 
mineralization to the east along with a significant increase in the thickness 
and grade of the mineralization. CURI-176 had previously marked the eastern 
limit of drilled mineralization in the El Domo deposit. Vertical hole CURI-155, 
drilled approximately 182 metres southeast of the collar of CURI-218, cut three 
mineralized zones with strong gold and silver values and anomalous zinc and 
copper values (see News Release of January 26, 2012) demonstrating the 
persistence of mineralization to the east. Further drilling is required to test 
this area.

Fredy Salazar, President and CEO, commented: "We are excited with the results 
from hole CURI-218 located to the east of the El Domo resource. The 
mineralization encountered is thicker and of better grade to the last hole 
drilled in the El Domo deposit on this section. The intersection indicates 
significant potential for additional discoveries in this prospective area 
approximately 800 metres in length, in a north-south direction, and between 350 
to 500 metres eastward of the deposit. Historic hole CURI-155 also indicates 
discovery potential in this area. We are currently drill testing this area with 
two drills. Also, this new finding paves the way and gets us closer to bringing 
this great project to a higher level."

Holes CURI-211, 213, 216 and 217 were drilled west of the El Domo deposit to 
test an area with massive sulphide float and exposures of hydrothermal breccia. 
CURI-213 and 216 were collared approximately 350 metres west of the deposit and 
approximately 100 metres west of historic holes CURI-30 and 32. CURI-213, 
drilled easterly on section with CURI-30, intersected two zones of 
mineralization (Table 1) in a section of hydrothermal breccias and gypsum 
stockworks in a dacitic unit similar to the one found below the El Domo VMS 
deposit:

/T/

--  4.14 meters (true width) averaging 1.01 g/t gold, 16.78 g/t silver,
0.67% copper, 0.95% lead and 4.77% zinc
--  29.37 metres (true width) averaging 0.5 g/t gold, 77.93 g/t silver,
0.17% copper, 0.17% copper, 0.89% zinc

/T/

The mineralization in CURI-213 may represent the down dip extension of the 
mineralization intersected in CURI-30 (From 19.75 meters to 29.50 meters: a 
total of 9.75 meters averaging 0.5 g/t gold, 32.3 g/t silver, 0.1% copper, 0.1% 
lead, 0.7% zinc). CURI-211, 216 and 217 did not intersect any mineralization.

Holes CURI-212, 214, 215, were drilled up to 500 metres south and southwest of 
the El Domo deposit. The holes targeted geophysical anomalies with low 
resistivity and moderate chargeability. CURI 212 and 214 were drilled in the 
area of historic holes CURI-15, 16, 17 and 18 which intersected significant 
gold and silver mineralization in a breccia zone/diatreme with clasts of 
polysulphides and barite in an argillic matrix (see News Release of March 12, 
2008). CURI-215 was drilled on section with, and 400 metres west of CURI-212 
which intersected 1.63 g/t gold over 2.05 metres (Table 1). The drill holes 
intersected weak to moderately anomalous mineralization in a dacitic unit that 
may represent the geophysical anomalies.

Holes CURI-207, 208, 209 and 210 were drilled up to 1.2 km southeast of the El 
Domo deposit to test targets identified by geological mapping which showed a 
lithological sequence similar to the one found in the El Domo deposit, as well 
as the presence of moderate geochemical mineralization and alteration. The 
drill holes intersected the expected geological sequence, however, no VMS 
mineralization was intersected.

Figure 1

To view the graphic associated with this release, please click on the following 
link: http://media3.marketwire.com/docs/Salazar%20Image.pdf

Table 1

SIGNIFICANT INTERSECTIONS

/T/

----------------------------------------------------------------------------
HOLE ID    FROM(m)  TO(m) WIDTH(m) Au (g/t) Ag (g/t)  Cu (%)  Pb (%)  Zn (%)
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located 1
CURI-207  km east from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-208  1.1 km east from El Domo resource
----------------------------------------------------------------------------
CURI-209  No samples taken, located 0.7 km east from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-210  0.5 km east from El Domo resource
----------------------------------------------------------------------------
CURI-211  No samples taken, located 0.4 km west from El Domo resource
----------------------------------------------------------------------------
CURI-212    283.95    286     2.05     1.63        -       -       -       -
----------------------------------------------------------------------------
CURI-213    105.34 109.48     4.14     1.01    16.78    0.67    0.95    4.77
----------------------------------------------------------------------------
133.65 163.02    29.37     0.59    77.93    0.17    0.17    0.89
----------------------------------------------------------------------------
Including   133.65  144.2    10.55     0.39     8.02    0.44    0.25    1.84
----------------------------------------------------------------------------
147.6 161.35    13.75     0.75    149.7    0.02    0.15    0.32
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-214  0.37 km south from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-215  0.43 km south west from El Domo
----------------------------------------------------------------------------
CURI-216  No samples taken, located 0.32 km west from El Domo resource
----------------------------------------------------------------------------
CURI-217    170.27  170.7     0.43        -      8.5    0.72       -    5.75
----------------------------------------------------------------------------
CURI-218    318.27  332.7    14.43     2.65    10.58    1.32       -    6.63
----------------------------------------------------------------------------
Including   318.27 321.85     3.58     9.68    11.52    0.46       -    2.64
----------------------------------------------------------------------------
328.23  332.7     4.47     0.29    15.05    3.16       -   19.25
----------------------------------------------------------------------------

/T/

Widths presented in Table 1 are downhole core lengths. Where possible, true 
width estimates are noted in the text.

A rigorous chain-of-custody and quality assurance/quality control program that 
included the insertion of certified standard control samples and blanks, and 
re-analysis of samples with high levels (overlimit) of gold, copper and zinc, 
was applied to the NQ-diameter, rock-sawn half-core samples. All samples were 
analyzed by Inspectorate Services Peru S.A.C. (Bureau Veritas), a certified ISO 
17025 and ISO 9001:2000 laboratory.

Table 2

/T/

----------------------------------------------------------------------------
HOLE ID             EAST       NORTH  ELEV (m)     AZIMUTH     DIP DEPTH (m)
----------------------------------------------------------------------------
CURI-207       696150.00  9854500.00    983.00 90 degrees     -70    206.75
----------------------------------------------------------------------------
CURI-208       696382.00  9854576.00    981.00 90 degrees     -70    292.29
----------------------------------------------------------------------------
CURI-209       696167.00  9855168.00   1030.00270 degrees     -60    317.50
----------------------------------------------------------------------------
CURI-210       695750.00  9854810.00    955.00270 degrees     -60    285.50
----------------------------------------------------------------------------
CURI-211       694500.00  9855000.00    896.00 90 degrees     -70    215.50
----------------------------------------------------------------------------
CURI-212       695000.00  9854600.00    928.00 90 degrees     -75    359.50
----------------------------------------------------------------------------
CURI-213       694570.00  9855100.00    860.00 90 degrees     -75    176.56
----------------------------------------------------------------------------
CURI-214       695080.00  9854500.00    919.00 90 degrees     -90    259.60
----------------------------------------------------------------------------
CURI-215       694600.00  9854600.00   1054.00 90 degrees     -75    299.40
----------------------------------------------------------------------------
CURI-216       694570.00  9855100.00    860.00270 degrees     -50    276.30
----------------------------------------------------------------------------
CURI-217       694600.00  9855000.00    860.00 90 degrees     -70    287.40
----------------------------------------------------------------------------
CURI-218       695575.00  9855200.00   1100.00270 degrees     -65    386.70
----------------------------------------------------------------------------
Total   3363.00
----------------------------------------------------------------------------

/T/

The scientific and technical information contained in this news release has 
been reviewed and approved by Kieran Downes, Ph.D., P.Geo. a Qualified Person 
as defined by National Instrument 43-101.

ON BEHALF OF THE BOARD OF SALAZAR RESOURCES LIMITED

Fredy Salazar, President & CEO

Salazar Resources Limited

Salazar Resources Ltd. is a publicly-listed (TSX VENTURE:SRL) mineral resource 
company engaged in the exploration and development of new highly prospective 
areas in Ecuador. Led by a senior Ecuadorian management team and most notably 
by its namesake Fredy Salazar, this team has been instrumental in other major 
discoveries throughout Ecuador, including Aurelian's Fruta Del Norte discovery, 
IAMGold's Quimsacocha Deposit, Mozo Deposit, Ex Newmont's Cangrejos Project and 
International Minerals Rio Blanco and Gaby Deposit. Being an Ecuadorian based 
company gives the Company a strategic advantage enabling the Company to 
complete exploration at a rapid pace. With an excellent property portfolio (4 
projects - 36,269 hectares), good geopolitical positioning and a number of 
strategic corporate and financial partnerships, Salazar has positioned itself 
to be a strategic player in Ecuador.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.
This press release contains "forward -looking information" within the meaning 
of applicable Canadian securities laws. All statements included herein, other 
than statements of historical fact, are forward-looking information and such 
information involves various risks and uncertainties. Forward-looking 
information herein includes, but is not limited to, statements that address 
activities, events or developments that the Company expects or anticipates will 
or may occur in the future, including such things as the execution of the Phase 
V drilling program. Such forward-looking information is based on a number of 
material factors and assumptions. Although the Company has attempted to 
identify important factors that could cause actual actions, events or results 
to differ materially from those described in forward-looking information, there 
may be other factors that cause actions, events or results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, and actual results and future events 
could differ materially from those anticipated in such information. A 
description of assumptions used to develop such forward-looking information and 
a description of risk factors that may cause actual results to differ 
materially from forward-looking information can be found in the Company's 
disclosure documents on the SEDAR website at www.sedar.com. Accordingly, 
readers should not place undue reliance on forward -looking information. The 
Company does not undertake to update any forward-looking information except in 
accordance with applicable securities laws

- 30 -

CONTACT INFO:

Salazar Resources Ltd.
ir@salazarresources.com
www.salazarresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=590031788


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Salazar Resources Limited

TSX VENTURE SYMBOL: SRL
FRANKFURT SYMBOL: CCG

March 23, 2017

Salazar intersects 14.43 metres (13.07m true) averaging 2.65 g/t gold, 10.58 
g/t silver, 1.32% copper, 6.63% zinc at its Curipamba Project

Hole extends mineralization of El Domo deposit

VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 23, 2017) - Salazar Resources 
Limited (TSX VENTURE:SRL) (FRANKFURT:CCG) ("Salazar" or the "Company") is 
pleased to report results from the first twelve holes (3,363 meters) of the 
Phase V diamond drill program in progress on the Company's 100-per-cent-owned 
(21,500 ha) Curipamba volcanogenic massive sulphide (VMS) project in Ecuador. 
These holes represent new exploratory drilling and were not included in the 
latest El Domo resource estimate which was released on January 16th, 2015. The 
twelve holes were drilled as part of the planned 40-hole (10,000 meters) drill 
program that is designed to further expand the El Domo volcanogenic massive 
sulphide ("VMS") deposit and explore its margins, as well as to test 
geophysical anomalies and surface showings (Figure 1). It is anticipated that 
the drill program will be complete by the third quarter of this year.

HIGHLIGHTS:

Hole CURI-218:

/T/

--  14.43 metres (13.07m true) averaging 2.65 g/t gold, 10.58 g/t silver,
1.32% copper, 6.63% zinc, including
--   3.58 metres averaging 9.68 g/t gold, 11.52 g/t silver, 0.46%
copper, 2.64% zinc, and
--   4.47 metres averaging 0.29 g/t gold, 15.05 g/t silver, 3.16%
copper, 19.25% zinc

/T/

Hole CURI-213:

/T/

--  4.14 metres (true width) averaging 1.009 g/t gold, 16.78 g/t silver,
0.67% copper, 0.95% lead and 4.77% zinc
--   29.37 metres (true width) averaging 0.58 g/t gold, 77.93 g/t silver,
0.17% copper, 0.17% lead, 0.89% zinc, including
--  10.55 meters averaging 0.385 g/t gold, 8.02 g/t silver, 0.44%
copper, 0.25% lead and 1.84% zinc, and
--  13.75 meters averaging 0.75 g/t gold, 149.7 g/t silver, 0.02%
copper, 0.15% lead and 0.32% zinc

/T/

Hole CURI-218, collared approximately 240 metres east of the El Domo deposit, 
was drilled westerly on section with hole CURI-176 (5.7 metres averaging 0.671 
g/t gold, 3.3 g/t silver, 0.61% copper, 0.01% zinc and 0.96% lead). CURI-218 
intersected 14.43 metres (13.07 metres true width) of massive and semi-massive 
pyrite-chalcopyrite-sphalerite grading 2.65 g/t gold, 10.58 g/t silver, 1.32% 
copper, 6.63% zinc beneath an andesite sill that occurs in this area (Table 1). 
The intersection in CURI-218 is located approximately 100 metres east of the 
intersection in CURI-176. It clearly demonstrates the extension of the El Domo 
mineralization to the east along with a significant increase in the thickness 
and grade of the mineralization. CURI-176 had previously marked the eastern 
limit of drilled mineralization in the El Domo deposit. Vertical hole CURI-155, 
drilled approximately 182 metres southeast of the collar of CURI-218, cut three 
mineralized zones with strong gold and silver values and anomalous zinc and 
copper values (see News Release of January 26, 2012) demonstrating the 
persistence of mineralization to the east. Further drilling is required to test 
this area.

Fredy Salazar, President and CEO, commented: "We are excited with the results 
from hole CURI-218 located to the east of the El Domo resource. The 
mineralization encountered is thicker and of better grade to the last hole 
drilled in the El Domo deposit on this section. The intersection indicates 
significant potential for additional discoveries in this prospective area 
approximately 800 metres in length, in a north-south direction, and between 350 
to 500 metres eastward of the deposit. Historic hole CURI-155 also indicates 
discovery potential in this area. We are currently drill testing this area with 
two drills. Also, this new finding paves the way and gets us closer to bringing 
this great project to a higher level."

Holes CURI-211, 213, 216 and 217 were drilled west of the El Domo deposit to 
test an area with massive sulphide float and exposures of hydrothermal breccia. 
CURI-213 and 216 were collared approximately 350 metres west of the deposit and 
approximately 100 metres west of historic holes CURI-30 and 32. CURI-213, 
drilled easterly on section with CURI-30, intersected two zones of 
mineralization (Table 1) in a section of hydrothermal breccias and gypsum 
stockworks in a dacitic unit similar to the one found below the El Domo VMS 
deposit:

/T/

--  4.14 meters (true width) averaging 1.01 g/t gold, 16.78 g/t silver,
0.67% copper, 0.95% lead and 4.77% zinc
--  29.37 metres (true width) averaging 0.5 g/t gold, 77.93 g/t silver,
0.17% copper, 0.17% copper, 0.89% zinc

/T/

The mineralization in CURI-213 may represent the down dip extension of the 
mineralization intersected in CURI-30 (From 19.75 meters to 29.50 meters: a 
total of 9.75 meters averaging 0.5 g/t gold, 32.3 g/t silver, 0.1% copper, 0.1% 
lead, 0.7% zinc). CURI-211, 216 and 217 did not intersect any mineralization.

Holes CURI-212, 214, 215, were drilled up to 500 metres south and southwest of 
the El Domo deposit. The holes targeted geophysical anomalies with low 
resistivity and moderate chargeability. CURI 212 and 214 were drilled in the 
area of historic holes CURI-15, 16, 17 and 18 which intersected significant 
gold and silver mineralization in a breccia zone/diatreme with clasts of 
polysulphides and barite in an argillic matrix (see News Release of March 12, 
2008). CURI-215 was drilled on section with, and 400 metres west of CURI-212 
which intersected 1.63 g/t gold over 2.05 metres (Table 1). The drill holes 
intersected weak to moderately anomalous mineralization in a dacitic unit that 
may represent the geophysical anomalies.

Holes CURI-207, 208, 209 and 210 were drilled up to 1.2 km southeast of the El 
Domo deposit to test targets identified by geological mapping which showed a 
lithological sequence similar to the one found in the El Domo deposit, as well 
as the presence of moderate geochemical mineralization and alteration. The 
drill holes intersected the expected geological sequence, however, no VMS 
mineralization was intersected.

Figure 1

To view the graphic associated with this release, please click on the following 
link: http://media3.marketwire.com/docs/Salazar%20Image.pdf

Table 1

SIGNIFICANT INTERSECTIONS

/T/

----------------------------------------------------------------------------
HOLE ID    FROM(m)  TO(m) WIDTH(m) Au (g/t) Ag (g/t)  Cu (%)  Pb (%)  Zn (%)
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located 1
CURI-207  km east from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-208  1.1 km east from El Domo resource
----------------------------------------------------------------------------
CURI-209  No samples taken, located 0.7 km east from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-210  0.5 km east from El Domo resource
----------------------------------------------------------------------------
CURI-211  No samples taken, located 0.4 km west from El Domo resource
----------------------------------------------------------------------------
CURI-212    283.95    286     2.05     1.63        -       -       -       -
----------------------------------------------------------------------------
CURI-213    105.34 109.48     4.14     1.01    16.78    0.67    0.95    4.77
----------------------------------------------------------------------------
133.65 163.02    29.37     0.59    77.93    0.17    0.17    0.89
----------------------------------------------------------------------------
Including   133.65  144.2    10.55     0.39     8.02    0.44    0.25    1.84
----------------------------------------------------------------------------
147.6 161.35    13.75     0.75    149.7    0.02    0.15    0.32
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-214  0.37 km south from El Domo resource
----------------------------------------------------------------------------
No significant mineralization encountered in this hole, located
CURI-215  0.43 km south west from El Domo
----------------------------------------------------------------------------
CURI-216  No samples taken, located 0.32 km west from El Domo resource
----------------------------------------------------------------------------
CURI-217    170.27  170.7     0.43        -      8.5    0.72       -    5.75
----------------------------------------------------------------------------
CURI-218    318.27  332.7    14.43     2.65    10.58    1.32       -    6.63
----------------------------------------------------------------------------
Including   318.27 321.85     3.58     9.68    11.52    0.46       -    2.64
----------------------------------------------------------------------------
328.23  332.7     4.47     0.29    15.05    3.16       -   19.25
----------------------------------------------------------------------------

/T/

Widths presented in Table 1 are downhole core lengths. Where possible, true 
width estimates are noted in the text.

A rigorous chain-of-custody and quality assurance/quality control program that 
included the insertion of certified standard control samples and blanks, and 
re-analysis of samples with high levels (overlimit) of gold, copper and zinc, 
was applied to the NQ-diameter, rock-sawn half-core samples. All samples were 
analyzed by Inspectorate Services Peru S.A.C. (Bureau Veritas), a certified ISO 
17025 and ISO 9001:2000 laboratory.

Table 2

/T/

----------------------------------------------------------------------------
HOLE ID             EAST       NORTH  ELEV (m)     AZIMUTH     DIP DEPTH (m)
----------------------------------------------------------------------------
CURI-207       696150.00  9854500.00    983.00 90 degrees     -70    206.75
----------------------------------------------------------------------------
CURI-208       696382.00  9854576.00    981.00 90 degrees     -70    292.29
----------------------------------------------------------------------------
CURI-209       696167.00  9855168.00   1030.00270 degrees     -60    317.50
----------------------------------------------------------------------------
CURI-210       695750.00  9854810.00    955.00270 degrees     -60    285.50
----------------------------------------------------------------------------
CURI-211       694500.00  9855000.00    896.00 90 degrees     -70    215.50
----------------------------------------------------------------------------
CURI-212       695000.00  9854600.00    928.00 90 degrees     -75    359.50
----------------------------------------------------------------------------
CURI-213       694570.00  9855100.00    860.00 90 degrees     -75    176.56
----------------------------------------------------------------------------
CURI-214       695080.00  9854500.00    919.00 90 degrees     -90    259.60
----------------------------------------------------------------------------
CURI-215       694600.00  9854600.00   1054.00 90 degrees     -75    299.40
----------------------------------------------------------------------------
CURI-216       694570.00  9855100.00    860.00270 degrees     -50    276.30
----------------------------------------------------------------------------
CURI-217       694600.00  9855000.00    860.00 90 degrees     -70    287.40
----------------------------------------------------------------------------
CURI-218       695575.00  9855200.00   1100.00270 degrees     -65    386.70
----------------------------------------------------------------------------
Total   3363.00
----------------------------------------------------------------------------

/T/

The scientific and technical information contained in this news release has 
been reviewed and approved by Kieran Downes, Ph.D., P.Geo. a Qualified Person 
as defined by National Instrument 43-101.

ON BEHALF OF THE BOARD OF SALAZAR RESOURCES LIMITED

Fredy Salazar, President & CEO

Salazar Resources Limited

Salazar Resources Ltd. is a publicly-listed (TSX VENTURE:SRL) mineral resource 
company engaged in the exploration and development of new highly prospective 
areas in Ecuador. Led by a senior Ecuadorian management team and most notably 
by its namesake Fredy Salazar, this team has been instrumental in other major 
discoveries throughout Ecuador, including Aurelian's Fruta Del Norte discovery, 
IAMGold's Quimsacocha Deposit, Mozo Deposit, Ex Newmont's Cangrejos Project and 
International Minerals Rio Blanco and Gaby Deposit. Being an Ecuadorian based 
company gives the Company a strategic advantage enabling the Company to 
complete exploration at a rapid pace. With an excellent property portfolio (4 
projects - 36,269 hectares), good geopolitical positioning and a number of 
strategic corporate and financial partnerships, Salazar has positioned itself 
to be a strategic player in Ecuador.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.
This press release contains "forward -looking information" within the meaning 
of applicable Canadian securities laws. All statements included herein, other 
than statements of historical fact, are forward-looking information and such 
information involves various risks and uncertainties. Forward-looking 
information herein includes, but is not limited to, statements that address 
activities, events or developments that the Company expects or anticipates will 
or may occur in the future, including such things as the execution of the Phase 
V drilling program. Such forward-looking information is based on a number of 
material factors and assumptions. Although the Company has attempted to 
identify important factors that could cause actual actions, events or results 
to differ materially from those described in forward-looking information, there 
may be other factors that cause actions, events or results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, and actual results and future events 
could differ materially from those anticipated in such information. A 
description of assumptions used to develop such forward-looking information and 
a description of risk factors that may cause actual results to differ 
materially from forward-looking information can be found in the Company's 
disclosure documents on the SEDAR website at www.sedar.com. Accordingly, 
readers should not place undue reliance on forward -looking information. The 
Company does not undertake to update any forward-looking information except in 
accordance with applicable securities laws

- 30 -

CONTACT INFO:

Salazar Resources Ltd.
ir@salazarresources.com
www.salazarresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=590031788