Source	MARKET NEWS
Date	03/23/2017
Time	09:56:55 AM

Company	 Alba Minerals Ltd.
Title	Phase I 
Drill Results from the Zeus Claim Block





    CDNX Symbol: AA











Press Release





NORAM VENTURES INC ("NRM-V")
ALBA MINERALS LTD ("AA.H-V")
- Phase I Drill Results from the Zeus Claim Block Continue to Deliver
- for Noram and Alba at Their Clayton Valley Lithium Project

- Weighted average lithium value in first three batches of drill
core samples exceeds the average lithium value of previously reported
surface samples by 72%

Noram Ventures Inc. ("Noram") and Alba Minerals Ltd. ("Alba") are
pleased to announce the third batch of drill core sample results from
the 46-hole Phase I drilling program that focused on the Zeus portion
of their Clayton Valley Lithium Project in Nevada (see Figure 1). The
Zeus claims are located within two kilometers (1.25 miles) of
Albemarle's Silver Peak Lithium Mine that has been in production since
1966 and is the only lithium-brine production operation in North
America.

The third group of 10 holes reported herein consisted of 132.4
meters (434 feet) of core drilling with an average hole depth of 13.2
meters (43.4 feet) and core sampling done primarily on 1.22 meter
(4-foot) intervals. Bradley C. Peek, MSc and Certified Professional
Geologist supervised the collection of the cores and samples; and
sample analysis was performed by ALS Labs (Reno, NV) on 111 samples
from the 10 holes using a 4-acid digestion and MS-ICP methods for 48
elements.

Table 1 lists each drill hole's location (NAD 83, Zone 11S),
elevation and depth - all in meters. All holes were vertical. All core
size was BQ.

//st
Table 1 - Drill Hole Location Information

Hole ID      UTM        UTM Approx.
Easting   Northing   Elev. Depth  Dip
CVZ-21  455961.7  4180720.2   1341   15.2  -90
CVZ-22  455926.0  4180650.8   1342   12.2  -90
CVZ-23  455837.3  4180785.9   1338   13.7  -90
CVZ-24  456031.3  4180594.5   1346   15.2  -90
CVZ-25  455780.8  4181171.1   1331   15.2  -90
CVZ-26  455479.0  4180533.1   1328   15.5  -90
CVZ-27  455504.0  4180452.5   1331    6.7  -90
CVZ-28  455814.5  4180544.1   1342   14.9  -90
CVZ-29  455129.8  4180984.9   1316   12.2  -90
CVZ-30  455421.0  4180593.0   1327   15.2  -90
//et

All but two of these drill holes are all located in an area of
close-spaced drilling measuring approximately 800 meters (2,600 feet)
by 520 meters (1,700 feet)(see Figure 2). Lithium values continue to be
very consistent across the close-spaced drilling area.

Table 2 lists the samples, their intervals, their weights and
their lithium analytical results. The core holes were vertical and the
sedimentary units that were tested are horizontal or dipping at less
than 5, so the intervals sampled are true widths.

//st
Hole ID Sample  Sample From   To From    To    Li
ID Wt. (kg) (ft) (ft)  (m)   (m) (ppm)
CVZ-21  289737    0.58    0    4  0.00  1.22 1630
CVZ-21  289738    0.92    4    8  1.22  2.44 1740
CVZ-21  289739    0.82    8   12  2.44  3.66 1930
CVZ-21  289740    0.70   12   16  3.66  4.88 1520
CVZ-21  289741    0.86   16   20  4.88  6.10 1580
CVZ-21  289742    0.86   20   24  6.10  7.32 1190
CVZ-21  289743    0.98   24   28  7.32  8.53 1120
CVZ-21  289744    0.76   28   32  8.53  9.75 1160
CVZ-21  289745    0.80   32   36  9.75 10.97  880
CVZ-21  289746    1.10   36   40 10.97 12.19  980
CVZ-21  289747    0.84   40   44 12.19 13.41 1170
CVZ-21  289748    0.84   44   48 13.41 14.63  970
CVZ-21  289749    0.30   48   50 14.63 15.24 1000

CVZ-22  289765    0.58    4    8  1.22  2.44 1080
CVZ-22  289766    0.84    8   12  2.44  3.66 1310
CVZ-22  289767    0.68   12   16  3.66  4.88 1380
CVZ-22  289768    0.68   16   20  4.88  6.10 1480
CVZ-22  289769    0.78   20   24  6.10  7.32 1640
CVZ-22  289770    0.60   24   28  7.32  8.53 1680
CVZ-22  289771    0.72   28   32  8.53  9.75 1340
CVZ-22  289772    0.68   32   36  9.75 10.97 1210
CVZ-22  289773    0.68   36   40 10.97 12.19 1070

CVZ-23  289725    0.36   0     4  0.00  1.22 1540
CVZ-23  289726    0.56   4     8  1.22  2.44  810
CVZ-23  289727    0.62   8    12  2.44  3.66 1030
CVZ-23  289728    0.58  12    16  3.66  4.88  940
CVZ-23  289729    0.52  16    20  4.88  6.10  950
CVZ-23  289730    0.54  20    24  6.10  7.32  990
CVZ-23  289731    0.52  24    28  7.32  8.53 1170
CVZ-23  289732    0.78  28    32  8.53  9.75 1300
CVZ-23  289733    0.74  32    36  9.75 10.97  930
CVZ-23  289734    0.62  36    40 10.97 12.19  970
CVZ-23  289735    0.74  40    45 12.19 13.72  850

CVZ-24  289751    0.42   0    4   0.00  1.22  680
CVZ-24  289752    1.00   4    8   1.22  2.44  900
CVZ-24  289753    0.94   8   12   2.44  3.66 1670
CVZ-24  289754    1.04  12   16   3.66  4.88 2340
CVZ-24  289755    0.84  16   20   4.88  6.10 1060
CVZ-24  289756    0.50  20   24   6.10  7.32  890
CVZ-24  289757    1.14  24   28   7.32  8.53  870
CVZ-24  289758    0.86  28   32   8.53  9.75 1010
CVZ-24  289760    0.94  32   36   9.75 10.97 1000
CVZ-24  289761    0.76  36   40  10.97 12.19 1550
CVZ-24  289762    0.74  40   44  12.19 13.41 1190
CVZ-24  289763    0.32  44   48  13.41 14.63 1330
CVZ-24  289764    0.28  48   50  14.63 15.24 1520

CVZ-25  289813    0.20   0    4   0.00  1.22  426
CVZ-25  289814    0.86   4    8   1.22  2.44  810
CVZ-25  289815    0.76   8   12   2.44  3.66  670
CVZ-25  289816    0.82  12   16   3.66  4.88  590
CVZ-25  289817    0.86  16   20   4.88  6.10  670
CVZ-25  289818    0.76  20   24   6.10  7.32  680
CVZ-25  289819    0.82  24   28   7.32  8.53  480
CVZ-25  289820    0.74  28   32   8.53  9.75  500
CVZ-25  289821    0.92  32   36   9.75 10.97  520
CVZ-25  289822    0.60  36   40  10.97 12.19  860
CVZ-25  289824    0.54  40   42  12.19 12.80  448

CVZ-26  289875    0.22   0    4   0.00  1.22 1520
CVZ-26  289876    0.62   4    8   1.22  2.44 1200
CVZ-26  289877    0.54   8   12   2.44  3.66 1260
CVZ-26  289878    0.62  12   16   3.66  4.88  960
CVZ-26  289879    0.50  16   20   4.88  6.10  880
CVZ-26  289880    0.66  20   24   6.10  7.32  920
CVZ-26  289881    0.48  24   28   7.32  8.53  740
CVZ-26  289882    0.74  28   32   8.53  9.75  730
CVZ-26  289883    0.80  32   36   9.75 10.97  980
CVZ-26  289884    0.86  36   40  10.97 12.19  800
CVZ-26  289885    0.80  40   44  12.19 13.41  860
CVZ-26  289886    0.58  44   48  13.41 14.63  960
CVZ-26  289887    0.64  48   51  14.63 15.54  750

CVZ-27  289889    0.28   0    4   0.00  1.22 1150
CVZ-27  289890    0.34   4    8   1.22  2.44 1380
CVZ-27  289891    0.34   8   12   2.44  3.66 1060
CVZ-27  289892    0.82  12   16   3.66  4.88 1350
CVZ-27  289893    0.62  16   20   4.88  6.10 1000
CVZ-27  289894    0.42  20 21.7   6.10  6.61  800

CVZ-28  289825    0.50   0    4   0.00  1.22 1270
CVZ-28  289826    0.62   4    8   1.22  2.44 1160
CVZ-28  289827    1.08   8   12   2.44  3.66 1400
CVZ-28  289828    1.02  12   16   3.66  4.88 1450
CVZ-28  289829    0.88  16   20   4.88  6.10 1680
CVZ-28  289830    0.90  20   24   6.10  7.32 1340
CVZ-28  289831    0.86  24   28   7.32  8.53 1270
CVZ-28  289832    0.86  28   32   8.53  9.75 1130
CVZ-28  289833    0.58  32   36   9.75 10.97  830
CVZ-28  289834    0.90  36   40  10.97 12.19 1050
CVZ-28  289835    0.66  40   44  12.19 13.41  930
CVZ-28  289836    0.86  44 48.8  13.41 14.87 1010

CVZ-29  289909    0.28   0    4   0.00  1.22  770
CVZ-29  289910    1.00   4    8   1.22  2.44 1010
CVZ-29  289911    1.06   8   12   2.44  3.66 1390
CVZ-29  289912    0.94  12   16   3.66  4.88 1670
CVZ-29  289913    0.94  16   20   4.88  6.10 1940
CVZ-29  289914    0.80  20   24   6.10  7.32 1320
CVZ-29  289915    0.88  24   28   7.32  8.53  900
CVZ-29  289916    1.00  28   32   8.53  9.75  880
CVZ-29  289917    0.94  32   36   9.75 10.97  880
CVZ-29  289918    0.70  36   40  10.97 12.19  870

CVZ-30  289799    0.36   0    4   0.00  1.22 1080
CVZ-30  289800    0.78   4    8   1.22  2.44  820
CVZ-30  289801    0.56   8   12   2.44  3.66  810
CVZ-30  289802    0.68  12   16   3.66  4.88  960
CVZ-30  289803    0.52  16   20   4.88  6.10  840
CVZ-30  289804    0.90  20   24   6.10  7.32  770
CVZ-30  289805    0.64  24   28   7.32  8.53  840
CVZ-30  289806    0.48  28   32   8.53  9.75  790
CVZ-30  289807    0.56  32   36   9.75 10.97  670
CVZ-30  289808    0.76  36   40  10.97 12.19  800
CVZ-30  289809    0.64  40   44  12.19 13.41  500
CVZ-30  289810    0.36  44   48  13.41 14.63  480
CVZ-30  289811    0.18  48   50  14.63 15.24  425
//et

Sample intervals were split by geologists at the drilling program
staging area. Half of the core was retained in the core boxes for
future review and/or sampling. The other half was securely sent to ALS
Laboratories in Reno, Nevada, USA for testing. Core recovery for these
third 10 core holes averaged 80.3%.

The lithium content of the 111 samples had an interval-weighted
average of 1,072.6 ppm with a minimum value of 425 ppm and a maximum
value of 2,340 ppm. The maximum value was over a 1.22m (4 ft)
intersection, while the minimum value was over a 0.61m (2 ft) interval.
The samples had a median value of 1000 ppm Li. Collectively, the
weighted average lithium value in first three batches of drill core
samples exceeds the average value of previously reported surface
samples by 72% when comparing the weighted average of the first 30
holes (1,066 ppm Li) to the average of the 77 surface samples (621 ppm
Li).

Laboratory standards with two different lithium ranges (1,237 ppm
and 783 ppm) were inserted into the sample stream, along with lithium
blanks and duplicate samples (10 QA/QC samples, in all, with these
samples). The standards and blanks were obtained from MEG Labs of Reno,
Nevada, USA. Duplicate samples were obtained by splitting the remaining
half of the split core (1/4 of the original core). All analyses of the
standards, blanks and duplicates were well within acceptable ranges.

"The lithium values continue to be consistent, both vertically and
horizontally, across all 30 holes we have reported to date," said Mark
Ireton President and CEO of Noram. These continued positive results are
supporting our near term goals, which includes on site bulk sampling
testing, and in-fill core drilling. Phase 2 drilling program would
encompass the Spartan claims, in addition to drilling along the outer
boundaries of the contiguous properties, to determine lithium content
property wide.

Analytical results from the remaining 16 drill holes of the Phase
1 drilling program are pending.

Noram is amassing one of the largest land packages in Nevada's
Clayton Valley. Its non-contiguous North and South Blocks now total 888
claims covering 17,738 acres and are positioned both north and south of
Albemarle's Silver Peak mine, North America's only lithium producer.

The technical information contained in this news release has been
reviewed and approved by Bradley C. Peek, MSc and Certified
Professional Geologist, who is a Qualified Person with respect to
Noram's Clayton Valley Lithium Project as defined under National
Instrument 43-101.

About Noram Ventures Inc.:

Noram Ventures Inc. (TSX-Venture: NRM / Frankfurt: N7R / OTCBB:
NRVTF) is a Canadian based junior exploration company, with a goal of
becoming a force in the Green Energy Revolution through the development
of lithium and graphite deposits and becoming a low-cost supplier for
the burgeoning lithium battery industry. The Company's primary business
focus since formation has been the exploration of mineral properties.
Current projects include lithium properties in the Clayton Valley of
Nevada and the Hector Lode in San Bernardino County, California; and
the Jumbo graphite property in southeastern British Columbia. Noram's
long term strategy is tobuild a multi-national lithium-graphite
dominant industrial minerals company to produce and sell lithium and
graphite into the markets of Europe, North America and Asia.

Please visit our web site for further information: www.noramventures.com.

ON BEHALF OF THE BOARD OF DIRECTORS

/s/ "Mark R. Ireton"
President & Director
Noram Ventures Inc.

This news release contains projections and forward-looking
information that involve various risks and uncertainties regarding
future events. Such forward-looking information can include without
limitation statements based on current expectations involving a number
of risks and uncertainties and are not guarantees of future performance
of the Company. The following are important factors that could cause
the Company's actual results to differ materially from those expressed
or implied by such forward looking statements; the uncertainty of
future profitability; and the uncertainty of access to additional
capital. These risks and uncertainties could cause actual results and
the Company's plans and objectives to differ materially from those
expressed in the forward-looking information. Actual results and future
events could differ materially from anticipated in such information.
These and all subsequent written and oral forward-looking information
are based on estimates and opinions of management on the dates they are
made and expressed qualified in their entirety by this notice. The
Company assumes no obligation to update forward-looking information
should circumstance or management's estimates or opinions change.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

To view this press release as a PDF file, click onto the following link:
public://news_release_pdf/NoramMar232017.pdf

Source: Noram Ventures Inc.
______________________________________
_______________________________________________
TSX Venture closing price for AA.H-V
Date: 2017/03/21
Closing Price: 0.15
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1708100035TS11708101371-09545920170323