Source	CANADA NEWSWIRE
Date	03/24/2017
Time	02:59:26 PM

Company	 Santacruz Silver Mining Ltd.
Title	Santacruz Silver Reports 2016 Annual Production Results and 2017 Update





    CDNX Symbol: SCZ











Press Release




" BC-Santacruz-ProdResults   03-24 2032
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Santacruz Silver Reports 2016 Annual Production Results and 2017 Update@

TSX.V: SCZFSE: 1SZ
VANCOUVER, March 24, 2017 /CNW/ - Santacruz Silver Mining Ltd.
(TSX.V:SCZ) (the "Company" or "Santacruz") reports its operating results from
the Rosario project in Charcas, San Luis Potosi, Mexico and the Veta Grande
project in Zacatecas, Mexico for the fourth quarter ("Q4") and year ended
December 31, 2016 and provides an update on the respective projects.
The Company produced a total of 970,332 silver equivalent ounces(1) in
fiscal 2016, including fourth quarter production of 242,048 silver equivalent
ounces(1) from its two operating projects. Production levels for the fourth
quarter of 2016 were impacted by ongoing development and optimization
activities at both the Rosario and Veta Grande projects which may allow for
increased production levels in 2017.
"We are excited to see the results of our efforts over these past months
coming to fruition with an anticipated production increase in fiscal 2017,"
stated Arturo Préstamo, Santacruz's President and CEO. "This expected increase
in production will be the result of significant development work completed at
the Veta Grande and Rosario projects in the fourth quarter of 2016, which has
set the stage for more robust 2017 operations. Although our focus on these
development activities had the effect of reducing our fourth quarter 2016
production total, I am pleased to advise that the Company is now well
positioned to steadily advance our production levels throughout the year."
Project Updates
Rosario project
At the Cinco Estrellas property, the Company has completed development
work on Levels 1, 2 and 3. Approximately 2855 tonnes of mineralized material
was mined and processed from the property in the fourth quarter of 2016 with
an estimated head grade of 3.3 g/t Au and 88 g/t Ag. To date in 2017
approximately 4950 tonnes of mineralized material has been mined and processed
from the property. The mineralized material mined in the fourth quarter and to
date in 2017 has been sourced from mine development workings. Importantly,
development of the first production stope has just been completed. The stope
is approximately 18 metres high, with vein widths ranging from 1.5 to 3.0
metres for approximately 150 metres. Chip samples collected from the top of
the stope range up to 6.0 g/t Au and 120 g/t Ag as compared to the bottom of
the stope that range up to 19 g/t Au and 220 g/t Ag. Management expects to
mine this stope at approximately 250 tpd.
In addition to the Cinco Estrellas property, the Company is evaluating
other nearby properties which could be integrated into the Rosario project in
order to leverage on Rosario´s milling capacity (approximately 600 tpd). The
Companys objective is to use the Rosario mill as a central processing facility
for numerous mining projects in the nearby area.
Veta Grande project
During the fourth quarter of 2016, significant mine development occurred
at the Veta Grande project,including approximately 1,400 metres of level
development and 480 metres of main access ramp development completed at the
Guadalupana mine, and approximately 350 metres of level development in
addition to 120 metres of main haulage ramp development completed at the
Garcia mine. Importantly, during the fourth quarter mineralized material from
previously mined stopes within the Veta Grande vein was identified and
accessed from old workings below Level 3 at the Garcia mine. This preparation
work took place at these areas and during the months of January and February
approximately 17,170 tonnes of material was extracted and processed from these
previously mined stopes with an estimated head grade of 166 g/t Ag, 1.67% Zn,
1.33% Pb and 0.42 g/t Au.
Mineralized material from the previously mined stopes at the Garcia mine
will be a primary source of millfeed to the Veta Grande milling facility in
2017, combined with mineralized material from other mine working faces
recently developed at the Garcia mine. In connection with this matter during
the first half of 2017 the Company plans to drive an access ramp for a
vertical depth of 120 metres from the current workings at the Veta Grande
vein, the largest of the vein systems contained within the Garcia mine.
In concert with the current optimized mine plan, the Company is deferring
the installation of the 1,250 tonne-per-day ball mill and 4,000 tonne-per-day
crushing circuit until the second half of 2017.
CONSOLIDATED OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4         2016 
Yr         2015 Yr
-----------------------------      -------         -------         
-------         -------

46,587          25,927         121,804          79,249

Material Processed (tonnes milled)
---------------------------------

242,048         268,319         970,332         832,284

Silver eqv. ounce production
----------------------------

100,199         143,937         486,136         471,893

Silver production (ounces)
-------------------------

251             103             569             336

Gold production (ounces)
-----------------------

348             254             991             780

Lead production (tonnes)
-----------------------

768             673           3,039           1,895

Zinc production (tonnes)
-----------------------

206             341             288             352

Average Head Grade (g/t Ag Eqv.)
--------------------------------

Note 1   2015 production includes only
nine months of the year, since during Q1
operations were suspended at the Rosario
project due to a tailings pipe
malfunction.    2015 silver equivalent
ounces produced have been calculated as
follows:


AgEqvOz(equal sign)(Au(x)Pau/31.1035)+(Ag(x)Pag/
31.1035)+(Pb(x)Ppb(x)22.05)+(Zn(x)Pzn(x)22.05)
---------------------------------------

(Pag)

Metal Prices: Ag $17.75, Au $1,250, Pb
$0.83, Zn $1.09


Note 2   2016 silver equivalent ounces
produced have been calculated as follows:


AgEqvOz(equal sign)(Au(x)Pau/31.1035)+(Ag(x)Pag/
31.1035)+(Pb(x)Ppb(x)22.05)+(Zn(x)Pzn(x)22.05)
---------------------------------------

(Pag)


Metal Prices: Ag $14.50, Au $1,100 Pb
$0.76, Zn $0.71

ROSARIO PROJECT OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4         2016 
Yr         2015 Yr
-----------------------------      -------         -------         
-------         -------

18,025          25,927          93,242          79,249

Material Processed (tonnes milled)
---------------------------------

135,529         268,319         863,873         832,284

Silver eqv. ounce production
----------------------------

70,356         143,937         456,293         471,893

Silver production (ounces)
-------------------------

126             178             163             194

Silver head grade (g/t)
-----------------------

96              97              94              96

Silver recovery (%)
------------------

136             103             454             336

Gold production (ounces)
-----------------------

116             254             759             780

Lead production (tonnes)
-----------------------

386             673           2,657           1,895

Zinc production (tonnes)
-----------------------

263             341             324             352

Average Head Grade (g/t Ag Eqv.)
--------------------------------

VETA GRANDE PROJECT OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4     2016 Yr         
2015 Yr
-----------------------------      -------         -------     -------         
-------

28,562           -          28,562           -

Material Processed (tonnes milled)
---------------------------------

106,519           -         106,519           -

Silver eqv. ounce production
----------------------------

29,843           -          29,843           -

Silver production (ounces)
-------------------------

Silver head grade (g/t)                         56           -              
56           -
-----------------------                        ---         ---             
---         ---

Silver recovery (%)                            58           -              
58           -
------------------                             ---         ---             
---         ---

115           -             115           -

Gold production (ounces)
-----------------------

232           -             232           -

Lead production (tonnes)
-----------------------

382           -             382           -

Zinc production (tonnes)
-----------------------

170           -             170           -

Average Head Grade (g/t Ag Eqv.)
--------------------------------

Management Change
The Company advises that it has appointed Dante Rodriguez as Interim
Chief Operating Officer, replacing Cesar Maldonado as COO. Mr. Maldonado has
agreed to remain as a consultant to the Company. The Company wishes to thank
Mr. Maldonado for his valuable contribution to the Company during his tenure
as COO.
Mr. Rodriguez has most recently held the position of Vice-President,
Exploration for the Company's wholly-owned subsidiary, Impulsora Minera
Santacruz, S.A. de C.V.
Sampling and Laboratory
The reported head grades have been estimated from assay results of
samples collected from stockpiles of mined mineralized material. The reported
stope grades are of assay results of underground chip samples collected across
the vein and at an average interval of three meters along the strike length of
the vein. Blanks, standards and duplicate control samples are not utilized in
the sampling procedure.
Samples collected from the Rosario and Veta Grande projects are assayed
at the Rosario and Veta Grande laboratories, respectively. Both laboratories
are owned and operated by Santacruz and the facilities are meant to serve the
mining operations at the projects. The Rosario and Veta Grande laboratories
are not independent of the Company and do not hold ISO certification. Samples
are prepared by drying, crushing, rifle splitting and pulverizing to <75
microns passing 200-mesh. Samples are analyzed by 3-acid digestion and Atomic
Absorption Spectrometry. Gold and silver are further analyzed by fire assay
with gravametric finish.
Qualified Persons
The technical information included in this statement has been reviewed
and approved by Van Phu Bui, P.Geo. of ARC Geoscience Group who is independent
of the Company and is a qualified person, pursuant to the meaning of such
terms in NI 43-101.
About Santacruz Silver Mining Ltd.
Santacruz is a Mexican focused silver company with two producing silver
projects (Rosario, including the Cinco Estrellas property, and the right to
operate the Veta Grande silver project and milling facility); and three
exploration properties including the Gavilanes property, Minillas property and
Zacatecas properties. The Company is managed by a technical team of
professionals with proven track records in developing, operating and
discovering silver mines in Mexico. Our corporate objective is to become a
mid-tier silver producer.
'signed'
Arturo Préstamo Elizondo,President, Chief Executive Officer and Director
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward looking information
Certain statements contained in this news release constitute
"forward-looking information" as such term is used in applicable Canadian
securities laws. Forward-looking information is based on plans, expectations
and estimates of management at the date the information is provided and is
subject to certain factors and assumptions. In making the forward-looking
statements included in this news release, the Company has applied several
material assumptions, that the Company's financial condition and development
plans do not change as a result of unforeseen events, that third party
mineralized material to be milled by the Company has properties consistent
with management's expectations, that the Company obtains all required
regulatory approvals, and that future metal prices and the demand and market
outlook for metals remains stable or improves. Forward-looking information is
subject to a variety of risks and uncertainties and other factors that could
cause plans, estimates and actual results to vary materially from those
projected in such forward-looking information. Factors that could cause the
forward-looking information in this news release to change or to be inaccurate
include, but are not limited to, the risk that any of the assumptions referred
to prove not to be valid or reliable, which could result in lower revenue,
higher cost, lower production levels, delays, and/or cessation in planned
work, that the Company's financial condition and development plans change,
delays in regulatory approval, risks associated with the interpretation of
data (including in respect of the third party ore), the geology, grade and
continuity of mineral deposits, the possibility that results will not 
beconsistent with the Company's expectations, as well as the other risks and
uncertainties applicable to mineral exploration and development activities and
to the Company as set forth in the Company's continuous disclosure filings
filed under the Company's profile at www.sedar.com. There can be no assurance
that any forward-looking information will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such statements. Accordingly, the reader should not place any undue reliance
on forward-looking information or statements. The Company undertakes no
obligation to update forward-looking information or statements, other than as
required by applicable law.
Rosario Mine
The decision to commence production at the Rosario Mine was not based on
a feasibility study of mineral reserves demonstrating economic and technical
viability, but rather on a more preliminary estimate of inferred mineral
resources. Accordingly, there is increased uncertainty and economic and
technical risks of failure associated with this production decision.
Production and economic variables may vary considerably, due to the absence of
a complete and detailed site analysis according to and in accordance with NI
43-101.
Veta Grande Project
The decision to commence production at Veta Grande Project was not based
on a feasibility study on mineral reserves demonstrating economic and
technical viability. Accordingly, there is increased uncertainty and economic
and technical risks of failure associated with this production decision.
Production and economic variables may vary considerably due to the absence of
a complete and detailed site analysis according to and in accordance with NI
43-101.
Cinco Estrellas Property
The decision to commence production at the Cinco Estrellas Property was
not based on a feasibility study on mineral reserves demonstrating economic
and technical viability. Accordingly, there is increased uncertainty and
economic and technical risks of failure associated with this production
decision. Production and economic variables may vary considerably due to the
absence of a complete and detailed site analysis according to and in
accordance with NI 43-101.
SOURCE SantaCruz Silver Mining Ltd.



To view the original version on PR Newswire, visit:
http://www.newswire.ca/en/releases/archive/March2017/24/c7863.html

-0-                  

" BC-Santacruz-ProdResults   03-24 2032
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Santacruz Silver Reports 2016 Annual Production Results and 2017 Update@

TSX.V: SCZFSE: 1SZ
VANCOUVER, March 24, 2017 /CNW/ - Santacruz Silver Mining Ltd.
(TSX.V:SCZ) (the "Company" or "Santacruz") reports its operating results from
the Rosario project in Charcas, San Luis Potosi, Mexico and the Veta Grande
project in Zacatecas, Mexico for the fourth quarter ("Q4") and year ended
December 31, 2016 and provides an update on the respective projects.
The Company produced a total of 970,332 silver equivalent ounces(1) in
fiscal 2016, including fourth quarter production of 242,048 silver equivalent
ounces(1) from its two operating projects. Production levels for the fourth
quarter of 2016 were impacted by ongoing development and optimization
activities at both the Rosario and Veta Grande projects which may allow for
increased production levels in 2017.
"We are excited to see the results of our efforts over these past months
coming to fruition with an anticipated production increase in fiscal 2017,"
stated Arturo Préstamo, Santacruz's President and CEO. "This expected increase
in production will be the result of significant development work completed at
the Veta Grande and Rosario projects in the fourth quarter of 2016, which has
set the stage for more robust 2017 operations. Although our focus on these
development activities had the effect of reducing our fourth quarter 2016
production total, I am pleased to advise that the Company is now well
positioned to steadily advance our production levels throughout the year."
Project Updates
Rosario project
At the Cinco Estrellas property, the Company has completed development
work on Levels 1, 2 and 3. Approximately 2855 tonnes of mineralized material
was mined and processed from the property in the fourth quarter of 2016 with
an estimated head grade of 3.3 g/t Au and 88 g/t Ag. To date in 2017
approximately 4950 tonnes of mineralized material has been mined and processed
from the property. The mineralized material mined in the fourth quarter and to
date in 2017 has been sourced from mine development workings. Importantly,
development of the first production stope has just been completed. The stope
is approximately 18 metres high, with vein widths ranging from 1.5 to 3.0
metres for approximately 150 metres. Chip samples collected from the top of
the stope range up to 6.0 g/t Au and 120 g/t Ag as compared to the bottom of
the stope that range up to 19 g/t Au and 220 g/t Ag. Management expects to
mine this stope at approximately 250 tpd.
In addition to the Cinco Estrellas property, the Company is evaluating
other nearby properties which could be integrated into the Rosario project in
order to leverage on Rosario´s milling capacity (approximately 600 tpd). The
Companys objective is to use the Rosario mill as a central processing facility
for numerous mining projects in the nearby area.
Veta Grande project
During the fourth quarter of 2016, significant mine development occurred
at the Veta Grande project,including approximately 1,400 metres of level
development and 480 metres of main access ramp development completed at the
Guadalupana mine, and approximately 350 metres of level development in
addition to 120 metres of main haulage ramp development completed at the
Garcia mine. Importantly, during the fourth quarter mineralized material from
previously mined stopes within the Veta Grande vein was identified and
accessed from old workings below Level 3 at the Garcia mine. This preparation
work took place at these areas and during the months of January and February
approximately 17,170 tonnes of material was extracted and processed from these
previously mined stopes with an estimated head grade of 166 g/t Ag, 1.67% Zn,
1.33% Pb and 0.42 g/t Au.
Mineralized material from the previously mined stopes at the Garcia mine
will be a primary source of millfeed to the Veta Grande milling facility in
2017, combined with mineralized material from other mine working faces
recently developed at the Garcia mine. In connection with this matter during
the first half of 2017 the Company plans to drive an access ramp for a
vertical depth of 120 metres from the current workings at the Veta Grande
vein, the largest of the vein systems contained within the Garcia mine.
In concert with the current optimized mine plan, the Company is deferring
the installation of the 1,250 tonne-per-day ball mill and 4,000 tonne-per-day
crushing circuit until the second half of 2017.
CONSOLIDATED OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4         2016 
Yr         2015 Yr
-----------------------------      -------         -------         
-------         -------

46,587          25,927         121,804          79,249

Material Processed (tonnes milled)
---------------------------------

242,048         268,319         970,332         832,284

Silver eqv. ounce production
----------------------------

100,199         143,937         486,136         471,893

Silver production (ounces)
-------------------------

251             103             569             336

Gold production (ounces)
-----------------------

348             254             991             780

Lead production (tonnes)
-----------------------

768             673           3,039           1,895

Zinc production (tonnes)
-----------------------

206             341             288             352

Average Head Grade (g/t Ag Eqv.)
--------------------------------

Note 1   2015 production includes only
nine months of the year, since during Q1
operations were suspended at the Rosario
project due to a tailings pipe
malfunction.    2015 silver equivalent
ounces produced have been calculated as
follows:


AgEqvOz(equal sign)(Au(x)Pau/31.1035)+(Ag(x)Pag/
31.1035)+(Pb(x)Ppb(x)22.05)+(Zn(x)Pzn(x)22.05)
---------------------------------------

(Pag)

Metal Prices: Ag $17.75, Au $1,250, Pb
$0.83, Zn $1.09


Note 2   2016 silver equivalent ounces
produced have been calculated as follows:


AgEqvOz(equal sign)(Au(x)Pau/31.1035)+(Ag(x)Pag/
31.1035)+(Pb(x)Ppb(x)22.05)+(Zn(x)Pzn(x)22.05)
---------------------------------------

(Pag)


Metal Prices: Ag $14.50, Au $1,100 Pb
$0.76, Zn $0.71

ROSARIO PROJECT OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4         2016 
Yr         2015 Yr
-----------------------------      -------         -------         
-------         -------

18,025          25,927          93,242          79,249

Material Processed (tonnes milled)
---------------------------------

135,529         268,319         863,873         832,284

Silver eqv. ounce production
----------------------------

70,356         143,937         456,293         471,893

Silver production (ounces)
-------------------------

126             178             163             194

Silver head grade (g/t)
-----------------------

96              97              94              96

Silver recovery (%)
------------------

136             103             454             336

Gold production (ounces)
-----------------------

116             254             759             780

Lead production (tonnes)
-----------------------

386             673           2,657           1,895

Zinc production (tonnes)
-----------------------

263             341             324             352

Average Head Grade (g/t Ag Eqv.)
--------------------------------

VETA GRANDE PROJECT OPERATIONAL RESULTS
Summary of Production Results      2016 Q4         2015 Q4     2016 Yr         
2015 Yr
-----------------------------      -------         -------     -------         
-------

28,562           -          28,562           -

Material Processed (tonnes milled)
---------------------------------

106,519           -         106,519           -

Silver eqv. ounce production
----------------------------

29,843           -          29,843           -

Silver production (ounces)
-------------------------

Silver head grade (g/t)                         56           -              
56           -
-----------------------                        ---         ---             
---         ---

Silver recovery (%)                            58           -              
58           -
------------------                             ---         ---             
---         ---

115           -             115           -

Gold production (ounces)
-----------------------

232           -             232           -

Lead production (tonnes)
-----------------------

382           -             382           -

Zinc production (tonnes)
-----------------------

170           -             170           -

Average Head Grade (g/t Ag Eqv.)
--------------------------------

Management Change
The Company advises that it has appointed Dante Rodriguez as Interim
Chief Operating Officer, replacing Cesar Maldonado as COO. Mr. Maldonado has
agreed to remain as a consultant to the Company. The Company wishes to thank
Mr. Maldonado for his valuable contribution to the Company during his tenure
as COO.
Mr. Rodriguez has most recently held the position of Vice-President,
Exploration for the Company's wholly-owned subsidiary, Impulsora Minera
Santacruz, S.A. de C.V.
Sampling and Laboratory
The reported head grades have been estimated from assay results of
samples collected from stockpiles of mined mineralized material. The reported
stope grades are of assay results of underground chip samples collected across
the vein and at an average interval of three meters along the strike length of
the vein. Blanks, standards and duplicate control samples are not utilized in
the sampling procedure.
Samples collected from the Rosario and Veta Grande projects are assayed
at the Rosario and Veta Grande laboratories, respectively. Both laboratories
are owned and operated by Santacruz and the facilities are meant to serve the
mining operations at the projects. The Rosario and Veta Grande laboratories
are not independent of the Company and do not hold ISO certification. Samples
are prepared by drying, crushing, rifle splitting and pulverizing to <75
microns passing 200-mesh. Samples are analyzed by 3-acid digestion and Atomic
Absorption Spectrometry. Gold and silver are further analyzed by fire assay
with gravametric finish.
Qualified Persons
The technical information included in this statement has been reviewed
and approved by Van Phu Bui, P.Geo. of ARC Geoscience Group who is independent
of the Company and is a qualified person, pursuant to the meaning of such
terms in NI 43-101.
About Santacruz Silver Mining Ltd.
Santacruz is a Mexican focused silver company with two producing silver
projects (Rosario, including the Cinco Estrellas property, and the right to
operate the Veta Grande silver project and milling facility); and three
exploration properties including the Gavilanes property, Minillas property and
Zacatecas properties. The Company is managed by a technical team of
professionals with proven track records in developing, operating and
discovering silver mines in Mexico. Our corporate objective is to become a
mid-tier silver producer.
'signed'
Arturo Préstamo Elizondo,President, Chief Executive Officer and Director
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward looking information
Certain statements contained in this news release constitute
"forward-looking information" as such term is used in applicable Canadian
securities laws. Forward-looking information is based on plans, expectations
and estimates of management at the date the information is provided and is
subject to certain factors and assumptions. In making the forward-looking
statements included in this news release, the Company has applied several
material assumptions, that the Company's financial condition and development
plans do not change as a result of unforeseen events, that third party
mineralized material to be milled by the Company has properties consistent
with management's expectations, that the Company obtains all required
regulatory approvals, and that future metal prices and the demand and market
outlook for metals remains stable or improves. Forward-looking information is
subject to a variety of risks and uncertainties and other factors that could
cause plans, estimates and actual results to vary materially from those
projected in such forward-looking information. Factors that could cause the
forward-looking information in this news release to change or to be inaccurate
include, but are not limited to, the risk that any of the assumptions referred
to prove not to be valid or reliable, which could result in lower revenue,
higher cost, lower production levels, delays, and/or cessation in planned
work, that the Company's financial condition and development plans change,
delays in regulatory approval, risks associated with the interpretation of
data (including in respect of the third party ore), the geology, grade and
continuity of mineral deposits, the possibility that results will not 
beconsistent with the Company's expectations, as well as the other risks and
uncertainties applicable to mineral exploration and development activities and
to the Company as set forth in the Company's continuous disclosure filings
filed under the Company's profile at www.sedar.com. There can be no assurance
that any forward-looking information will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such statements. Accordingly, the reader should not place any undue reliance
on forward-looking information or statements. The Company undertakes no
obligation to update forward-looking information or statements, other than as
required by applicable law.
Rosario Mine
The decision to commence production at the Rosario Mine was not based on
a feasibility study of mineral reserves demonstrating economic and technical
viability, but rather on a more preliminary estimate of inferred mineral
resources. Accordingly, there is increased uncertainty and economic and
technical risks of failure associated with this production decision.
Production and economic variables may vary considerably, due to the absence of
a complete and detailed site analysis according to and in accordance with NI
43-101.
Veta Grande Project
The decision to commence production at Veta Grande Project was not based
on a feasibility study on mineral reserves demonstrating economic and
technical viability. Accordingly, there is increased uncertainty and economic
and technical risks of failure associated with this production decision.
Production and economic variables may vary considerably due to the absence of
a complete and detailed site analysis according to and in accordance with NI
43-101.
Cinco Estrellas Property
The decision to commence production at the Cinco Estrellas Property was
not based on a feasibility study on mineral reserves demonstrating economic
and technical viability. Accordingly, there is increased uncertainty and
economic and technical risks of failure associated with this production
decision. Production and economic variables may vary considerably due to the
absence of a complete and detailed site analysis according to and in
accordance with NI 43-101.
SOURCE SantaCruz Silver Mining Ltd.



To view the original version on PR Newswire, visit:
http://www.newswire.ca/en/releases/archive/March2017/24/c7863.html

-0-                           03/24/2017
/For further information: Neil MacRae, Santacruz Silver Mining Ltd.,
Email: info(at)santacruzsilver.com, Telephone: (604) 569-1609/
/Web Site: www.santacruzsilver.com /
(SCZ.)

CO:  SantaCruz Silver Mining Ltd.
ST:  British Columbia
IN:  MNG
SU:  PER

-30-