Source	Marketwire
Date	03/27/2017
Time	06:30:52 AM

Company	 ANGEL GOLD CORP.
Title	Angel Gold Geophysical Survey Encounters Multiple Strong Chargeability 
Anomalies at Guayabales Prospect at the El Porvenir Project





    CDNX Symbol: ANG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Angel Gold Corp.

TSX VENTURE SYMBOL: ANG
OTCQX SYMBOL: ANGCF

March 27, 2017

Angel Gold Geophysical Survey Encounters Multiple Strong Chargeability 
Anomalies at Guayabales Prospect at the El Porvenir Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 27, 2017) - Angel Gold Corp. 
(TSX VENTURE:ANG)(OTCQX:ANGCF) ("Angel" or the "Company") is pleased to provide 
an update on recent progress on Angel's geophysical survey program at its 
Guayabales Prospect, the second of the three prospects surveyed at our El 
Porvenir project located in the Segovia Mining District of Antioquia, Colombia.

/T/

--  The Induced Polarization survey has been completed at Angel's Guayabales
Prospect over five lines at 200m spacing.
--  Preliminary results of the geophysical data obtained in the field
indicates several distinct high chargeability responses (notes (1) and
(2) below) as well as a separate broad zone of more moderate response
consistent with sulfide mineralization at depth.
--  Preparation of the final report with detailed interpretation is under
way.

/T/

"The Induced polarization data gathered at Guayabales is continuing to support 
and enhance our belief that our El Porvenir Project has the potential to host 
conductive sulfide bodies that may contain gold and silver mineralization. Two 
kilometers away in the district, high-grade vein-hosted mineralization is being 
mined at the Gran Colombia gold mine (Segovia project). We also have identified 
a type of mineralization previously undocumented in the Segovia Mining 
District: that of quartz-sericite breccia-hosted silver-gold mineralization 
that is intrusive related" says Stella Frias, President and CEO of Angel Gold 
Corp. "The chargeability geophysical anomalies identified at Guayabales, are 
coincident with surface silver-gold breccia hosted mineralization as well as to 
zoned multi-element soil responses, supporting our belief that these 
geophysical anomalies may represent the presence of blind or semi-blind bodies 
of sulfide mineralization. We have already determined from surface work that 
sulfide mineralization is related to silver and gold mineralization," added 
James Stephenson P.Geo, Vice-President of Exploration.

HIGH CHARGEABILTY ANOMALIES

/T/

--  Discrete high chargeability responses are believed to be associated with
individual sulfide-silica bodies such as that encountered in historic
drill hole RGBDDH049 which returned a down hole intersection of 9m at
89.9 g/t silver 0.76 g/t gold, and a small nearby surface exposure that
returned 190 g/t silver 1.57 g/t gold in a composite rock chip sample.
--  Interestingly this known silver-gold sulfide-silica breccia-hosted
mineralization yielded a significantly weaker and narrower chargeability
response than of the other discrete high chargeability anomalies; this
is strongly indicative that the significantly stronger and larger
chargeability highs are associated with larger and more sulfide-rich
bodies of sulfide-silica breccia fill. This potential is clearly
indicated in the two adjacent preliminary sections shown below in
Figures 1 and 2.

/T/

To view Figure 1, please follow this link: 
http://media3.marketwire.com/docs/d_000%20NE_GYBL_Pseudo_Figure%201.jpg

Figure 1: Section 0+00NE showing response over known sulfide-silica breccia 
hosted mineralization, outcropping at 0+ 00 SE (grid origin), showing a 
relatively modest anomaly of 15 to 20mV/V. Note the open anomaly on the 
right-hand end of the line which correlates with the strong anomaly in the 
right of Figure 2 below.

To view Figure 2, please follow this link: 
http://media3.marketwire.com/docs/c__200%20SW_GYBL_Pseudo_Figure%202.jpg

Figure 2: Provisional Section 2+00SW - (INCOMPLETE, with surveying of the right 
hand end of the line in progress at receipt of data of this incomplete 
section). The section shows a very low background of around 5mV/V, with 
anomalies in the right of section of over 20mV/V and the anomaly in the left of 
section to over 100mV/V. The left hand anomaly appears to correlate at depth 
with the shallower weaker mineralization encountered in Figure 1 above.

/T/

--  Strong chargeability responses were encountered on sections 6+00SW,
4+00SW, 2+00SW and 0+00NE
--  While the anomaly over the known mineralization extends to surface, the
strongest chargeability responses are all sub-surface, with some of
these deep anomalies continuing to surface as more weakly chargeable
responses, and others being completely blind. Significantly, where
multi-element soil geochemistry was interpreted as possibly reflecting
blind underlying mineralization, underlying high IP chargeability
responses were encountered.
--  Our interpretation of surface geochemical responses infers a more
silver-gold response to the soil geochemical anomalies in the left
(northwest) of the sections, but suggests a more gold-rich system
underlying the soil responses in the right (southeast) of the sections.
This can only be confirmed by drilling.

/T/

BROAD MODERATE CHARGEABILITY RESPONSE

/T/

--  Chargeability background progressively increases from5 mV/V and under in
sections 6+00SW and 4+00SW, to around 7 mV/V in 2+00SW, to 8 to 9 mV/V
in sections 0+00NE and 2+00NE suggesting some differing geology occurs
north of the surveyed area where different intrusive phases have been
identified.
--  A broad 600m wide zone (open to the left of section) of moderate
chargeability (10 to 15 mV/V)was encountered on the northernmost
surveyed line, section 2+00NE, possibly reflecting a disseminated
sulfide halo around a discrete body of more mafic diorite that was
identified a short distance to the north. Section 2+00NE is shown in
Figure 3 below.
--  An exposure of intense K-feldspar potassic alteration as well as more-
widespread sericite alteration had been previously noted in this poorly
exposed mafic diorite intrusive. The significance of the potassic
alteration at this time remains open to conjecture. Potassic alteration
is reported locally associated with vein mineralization in the Segovia
District, but no veins were observed anywhere near this exposure.

/T/

To view Figure 3, please follow this link: 
http://media3.marketwire.com/docs/e_200%20NE_GYBL_Pseudo_Figure%203.jpg

Figure 3: Provisional Section 2+00NE showing a broad zone of moderate 
chargeability (left half of section) possibly reflecting a disseminated sulfide 
halo around a mafic diorite body north of the section.

Conclusion

/T/

--  It is believed that these strong chargeability responses at Guayabales
could represent areas of intense silica-sulfide alteration that have the
potential to host sub-vertical, pipe-like to elongate, fissure-fill
bodies of silver-dominant (silver-gold) and gold-dominant (gold-silver)
mineralization.
--  Based on the geophysical anomalies the size potential for these bodies
could be as much as 100m in width rather than the average 1m of the
typical quartz vein hosted deposits in the Segovia Mining District.
--  The broad greater than 600m wide moderate chargeability response of the
northernmost line suggests disseminated sulfide mineralization that
could reflect a mineralized halo around a different intrusive phase
(mafic diorite as opposed to tonalite) and thus offer potential for more
disseminated styles of intrusive hosted mineralized targets.

/T/

NOTE(1): The accompanying "pseudosection" is a non-"inverted" presentation of 
results. The survey was carried out with a pole-dipole configuration 
progressing from left to right in the section, and by its very nature the 
method presents a leftwards slant to the results. No correction inversion 
algorithm has been applied to show the "true" position of the anomaly. The 
interpretation is done by matching the observed geology to the IP results. 
Mineralized bodies are inferred to be irregular but overall sub-vertical in 
orientation

NOTE(2): A chargeability response indicating the presence of sulfides reflects 
the location of the sulfide-bearing body below the base of oxidation, and not 
the oxidized surface portion of the body. Thus for a dipping sulfide zone the 
chargeability anomaly will displace away from the oxidized surface exposure.

Qualified Person

Mr. James G. Burns, P. Eng., a Qualified Person under National Instrument 
43-101 standards and a technical advisor to the Company has reviewed and 
approved the technical information contained in this news release.

About Angel Gold Corp.:

Angel is a Canada-based gold and silver exploration company focused on 
responsible development of mineral resources in Colombia, host to some of the 
world's largest gold deposits. Angel's flagship project the El Porvenir is 
located at less than 2 km from the Segovia project of Gran Colombia, the El 
Pino West Project is adjacent to the Gramalote project of B2Gold and Anglo Gold 
Ashanti JV and its Heliconia project is located north of the Titiribi District 
along the Cauca fault system.

Angel has been focused on acquiring and validating strategic mineral 
exploration opportunities in Colombia's best mining districts with the highest 
potential for new discoveries.

On Behalf of the Board of Directors of Angel Gold Corp

Blanca Stella Frias, Director, President and Chief Executive Officer

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this news release.

The TSX Venture Exchange has not reviewed the content of this News Release and 
therefore does not accept responsibility or liability for the adequacy or 
accuracy of the contents of this News Release. This news release contains 
certain "forward- looking statements" within the meaning of Section 21E of the 
United States Securities and Exchange Act of 1934, as amended. Except for 
statements of historical fact relating to the Company, certain information 
contained herein constitutes forward- looking statements. Forward-looking 
statements are based upon opinions and estimates of management at the date the 
statements are made, and are subject to a variety of risks and uncertainties 
and other factors which could cause actual results to differ materially from 
those projected in the forward looking statements. The reader is cautioned not 
to place undue reliance on forward-looking statements. The transaction 
described in this News Release is subject to a variety of conditions and risks 
which include but are not limited to: regulatory approval, shareholder 
approval, market conditions, legal due diligence for claim validity, financing, 
political risk, security risks at the property locations and other risks. As 
such, the reader is cautioned that there can be no guarantee that this 
transaction will complete as described in this News Release. We seek safe 
harbour.

- 30 -

CONTACT INFO:

For investor relations, please contact:
Stella Frias
+1 (360) 650 1440

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=590123178