Source	MARKET NEWS
Date	03/28/2017
Time	09:18:40 AM

Company	 Coronet Metals Inc.
Title	Joint 
Processing Agreement On White Caps Tailing





    CDNX Symbol: CRF











Press Release





IBERIAN MINERALS LTD ("IML-V")
CORONET METALS INC ("CRF-V")
- Joint Processing Agreement On White Caps Tailings Project

Iberian Minerals Ltd. (the "Company" or "Iberian") announced that
its 100% wholly owned subsidiary, Mineworx Technologies ("Mineworx")
has entered into a Binding Letter of Intent ("LOI") to form a Joint
Venture ("JV") with Coronet Metals Inc. ("Coronet") to process an
estimated 250,000 tonnes of gold bearing historic tails and mine dumps*
at Coronet's White Caps Gold Project near the town of Manhattan in
Northern Nye County, Nevada.

Under the terms of the agreement, Mineworx will apply its
exclusive license to utilize the EnviroLeach Technologies
patent-pending, non-cyanide leach formula. Under the terms of the
Agreement, Coronet will provide all necessary funding for the testing
and project development. With the commencement of commercial production
the Joint Venture shall be responsible for sharing all operational
costs and all profits will be shared on a 50/50 basis once Coronet has
fully recovered its investment in testing and development costs.
Mineworx's share of the JV will be reduced to 35% after a two year
period.

As per the February 2, 2017 news release by Coronet, detailed
mapping and systematic trenching of the tailings and dumps were
completed to provide approximately 300 lbs. of representative material
for testing. The samples were taken from four primary zones that
collectively makes up the gold-bearing tailings and mine dumps. The
four main zones are identified as; Bill Placer, White Caps Dumps, Pink
Tails and Brown Tails.

The first series of hydrometallurgical test results on the
gold-bearing tailings and dumps was performed by EnviroLeach
Technologies and Met-Solve Laboratories (Langley, B.C.) with ALS Global
(Vancouver) performing independent verification of the sample solutions
and solids. Highlights of the hydrometallurgical test work can be
summarized as follows:

//st

Head grades of 5.43 g/t on the Pink Tails

Head grades as high as 15.94 g/t on the White Caps Dumps (-35 mesh)

Recovery % as high as 70.74 % in 6 hour leach cycle and 87.24% in 24 hours
on the Brown Tails

Recovery % as high as 71.52 % in 24 hour leach cycle on the White Caps
Dumps (-35 mesh)

//et

Compared to hydrometallurgical test work performed at a lab in
Denver in 2012 on similar samples employing cyanide, the EnviroLeach
process shows significant improvement in recoveries using the
EnviroLeach solution vs. cyanide. The EnviroLeach residence time was 3
times shorter (24 hours vs. 72 hours) with 295% better recoveries on
the Pink Tails, 278% better on the Brown Tails, 170% better on the Bill
Placer and almost identical recoveries on the White Caps Dumps.

//st
Recovery (%)
Type of                              Leach              Bill White
Leach               Cyanide    Leach Dura- Pink Brown Placer  Caps
Solution  Grind PH Strength Enhancer tion Tails Tails   - 50  - 35
mesh  mesh
EnviroLeach  NO 6.1     N/A      N/A   24 55.25 87.24 73.04  71.52
hrs     %     %     %      %
Cyanide   75 um  11 2.0 g/l     200g   72 14.00 23.10 27.10  73.40
NaCN Pb(NO3)2  hrs     %     %     %      %
//et

Approximately 5kg of material from each zone was provided to
EnviroLeach for testing. Bottle roll tests were done on the samples at
certain particle sizes for the Bill Placer and White Caps Dumps samples
due to the variety of sizes in the samples. For the Bill Placer, two
different particle sizes of -50 mesh and +50 mesh were tested. The
White Caps Dumps were split into -35 mesh and +35 mesh sizes to
implement the test.

The first tests done on the samples were based on a 25% pulp
density and 6 hour leach residence time with intermediate samples taken
in the first and third hour. The initial tests were done on the Bill
Placer -50 mesh and +50 mesh. Recoveries were 75.16 % and 80.86%,
respectively. Residue grades and 24h solution grades were verified by
ALS and Met -Solve labs, respectively. Head grades (Calc. Head) are
achieved by the sum of residue grades and effective grades at the end
of the leach time (24th hour). Residues were assayed by ALS. Whitecaps
dump samples vary due to the variety of sizes in the samples.

Table 1 shows the test result in 24 hours where intermediate
samples were taken in 1st, 3rd and 6th hours.

//st
Time(hrs) Pink Brown Bill Placer White Caps   White Caps Dumps
Tails Tails   - 50 mesh      Dumps - 6 mesh + 35 mesh
- 35 mesh
1          1.19  5.79       2.61       5.23               0.20
3          2.37  8.30       2.76       9.31               0.35
6          2.54 11.58       3.19      11.21               0.47
24         3.00 13.26       3.63      11.40               0.54
Residue    2.43  1.94       1.34       4.54               5.55
Calc. Head 5.43 15.20       4.97      15.94               6.09

Table 1: Effective grades
of the samples in 24 hours
//et

Table 2 show the recovery rate of each sample during a 24 hours
leach time.

//st
Time(hrs) Pink Brown Bill Placer White Caps   White Caps Dumps
Tails Tails   - 50 mesh      Dumps - 6 mesh + 35 mesh
- 35 mesh
1       21.92%  35.37%    39.61%     17.59%              2.98%
3       43.65%  50.70%    41.88%     31.30%              5.21%
6       46.78%  70.74%    48.41%     37.69%              6.99%
24      55.25%  87.24%    73.04%     71.52%              8.87%

Table 2: Recovery rate
(%) in 24 hours
//et

Coronet and EnviroLeach Technologies Inc. subsequently proceeded
towards a second round of test work, adjusting the x-leach formula and
the results have either confirmed or improved upon the results from the
first phase of testing. Given these grades and recoveries, the two
companies decided to enter into a formal agreement to further
investigate the economic potential of processing of the material.

The JV will first build a small scale 50kg pilot plant to
determine recoverability and reusability of the formula, gold recovery
from solution, optimization and preliminary economics. Following a
successful small scale pilot plant test, a 1 tonne per day pilot plant
will be built to test 40 tonnes of material to confirm scalability,
recoveries and economics.

Mr. Fred Tejada, P.Geo, is a Qualified Person under the meaning of
Canadian National Instrument 43-101 and is responsible for the
scientific and technical disclosure in this news release.

Cautionary Notes Regarding the White Caps Production

The White Caps Mining Project has no established resource and is
without a known body of commercial ore. The decision to commence
production at the White Caps Mine and Coronet's plans for small scale
mining and milling operations of the historic tailings and mine dumps
were based on economic models prepared by Coronet in conjunction with
management's knowledge of the property and the prior limited recent
operating history of the White Caps Project. The production decision
and operating plan for the processing of the tailings and mine dumps
were not based on any preliminary economic assessment, a
pre-feasibility study or a feasibility study of mineral reserves
demonstrating economic and technical viability. Accordingly, there is
increased uncertainty and economic and technical risks of failure
associated with the production decision and operating plan, in
particular the risk that mineral quantities and/or grades will be lower
than expected, the risk that construction or operations will be more
difficult or more expensive than expected, the risk that the Company
will not be able to transport or sell the metal it produces on the
terms it expects, or at all, the risk that due to the absence of a
detailed economic and technical analysis according to and in accordance
with NI 43-101 the production and economic variables associated with
mineral extractions and sale may vary considerably. Readers are
cautioned that no reliable estimates of future production capability or
the economics of any extraction activity can be made.

* References to tonnages are historical estimates. The estimated
tonnage of 250,000 tonnes was provided by the two different mining
engineering companies in October 2011 that the Company engaged to
provide an estimate. The stockpile measurement is a technique to
measure the volume and weight of commodity stockpiles. It is a
scientific/ instrumental method, using Total Station equipment to
determine the volume of the stockpile quantity. A qualified person has
not done sufficient work to classify the historical estimate as current
mineral resources or mineral reserves nor does Coronet treat the
historical estimate as current mineral resources or mineral reserves.
The Company will have to conduct independent surveying, drilling,
sampling and assaying of the tailings and mine dumps to determine the
NI 43-101 tonnes and grades of the tailings and mine dumps. In
conjunction with that, the Company will have to continue with
independent metallurgical analysis to verify recoveries. This work will
form the basis to upgrade or verify the historical estimates as NI
43-101 mineral resources or mining reserves.

About Coronet Metals

Coronet Metals Inc. is engaged in the business of acquiring,
exploring and developing natural resource properties, with a focus on
precious mineral properties/projects which have the potential for both
near-term cash flow and significant exploration upside potential.
GCiCoronet's White Caps Gold Project is near the town of Manhattan in
Northern Nye County. The Project is well in line with its strategy of
acquiring precious metals mining projects which have the potential for
both near-term cash flow and exploration upside.

The Company has launched a fresh new web site so please visit
www.coronetmetals.com for more information on the project, the history
of the area and up to date information regarding its near-term plans,
execution and strategy.

About Iberian Minerals

Iberian Minerals is positioned for growth through partnerships
with advanced mining and e-Waste opportunities utilizing its
exclusively licensed cyanide-free precious metals extraction formula
and patent-pending portable extraction technologies. These three
innovations will increase and enhance business opportunities by
deploying cost-effective, environmentally friendly extractive
metallurgy solutions. This unique business model will provide
shareholders with consistent revenue growth while minimizing capital
costs and project risk.

For further information,go to www.iberianminerals.ca.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This press release contains certain statements which constitute
forward-looking statements or information ("forward-looking
statements"), including statements regarding Iberian's business. Such
forward-looking statements are subject to numerous risks and
uncertainties, some of which are beyond Iberian's control, including
the impact of general economic conditions, industry conditions,
volatility of commodity prices, currency fluctuations, environmental
risks, operational risks in exploration and development, competition
from other industry participants, the lack of availability of qualified
personnel or management, stock market volatility and the ability to
access sufficient capital from internal and external sources. Although
Iberian believes that the expectations in the forward-looking
statements are reasonable, they are based on factors and assumptions
concerning future events which may prove to be inaccurate. Those
factors and assumptions are based upon currently available information.
Such statements are subject to known and unknown risks, uncertainties
and other factors that could influence actual results or events and
cause actual results or events to differ materially from those stated,
anticipated or implied in the forward looking information. As such,
readers are cautioned not to place undue reliance on the forward
looking information, as no assurance can be provided as to future
results, levels of activity or achievements. The forward-looking
statements contained in this document are made as of the date of this
document and, except as required by applicable law, Iberian does not
undertake any obligation to publicly update or to revise any of the
included forward-looking statements, whether as a result of new
information, future events or otherwise. The forward-looking statements
contained in this document are expressly qualified by this cautionary
statement.

Contact Information:

Iberian Minerals Ltd.
Rick Gliege
V.P. Corporate Development
(250) 751-3661
rick@iberianminerals.ca
www.iberianminerals.ca

EnviroLeach Technologies Inc.
Duane Nelson
CEO
(604) 512-8118
duane@enviroleach.com
______________________________
_______________________________________________
TSX Venture closing price for CRF-V
Date: 2017/03/27
Closing Price: 0.18
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1708600041TS11708601480-09173220170328