Source	CANADA NEWSWIRE
Date	03/30/2017
Time	05:46:39 AM

Company	 Hannan Metals Ltd.
Title	Hannan Mineralogical Analysis for the Kilbricken Project, Ireland





    CDNX Symbol: HAN











Press Release




" BC-HANAnalysisKilbrick   03-30 1057
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Hannan Mineralogical Analysis for the Kilbricken Project, Ireland@

VANCOUVER, March 30, 2017 /CNW/ - Hannan Metals Limited ("Hannan" or the
"Company") (TSX.V: HAN) announces the results of a gap analysis on
mineralogical investigations on the Kilbricken project, Ireland by Dr. Kurt
Forrester of Arn Perspective Ltd.
Key points:
<<

--  Based on the available information it is likely a conventional lead-zinc
flotation circuit at Kilbricken would be able to achieve saleable
mineral concentrates;

--  It is anticipated that there should be no penalties due to the presence
of deleterious elements (arsenic, manganese, cadmium, selenium), subject
to confirmation from the assessment of bulk element deportment during
lead-zinc flotation;

--  A primary grind of between 100µm to 150µm is anticipated to achieve
satisfactory liberation and there are no red flags with the modal
mineralogical analysis with respect to mineral processing and
beneficiation;

--  Based on the information available, it is anticipated that Kilbricken
should be able to achieve high recoveries of both zinc and lead
concentrates. Results from limited grade recovery analysis indicated the
following recoveries probable using a conventional flowsheet:

o Targeting a sphalerite grade of 85% in the zinc concentrate would
result in recoveries in excess of 85%;

o Targeting a galena grade of 70% in the lead concentrate would result
in recoveries in excess of 75%;

--  Recommendations include conducting metallurgical test work across the
deposit as part of an ongoing exploration and development program. To
this end, Hannan plans to start drilling at Kilbricken during April
2017. The first two drill holes will collect metallurgical samples for
locked cycle flotation testwork.
>>
Mr Hudson, CEO and Chairman states, "In general, Irish style zinc-lead
deposits are typically attractive because of their simple mineralogy and
polymetallic nature. It is most encouraging that this also appears to be the
case at Kilbricken with these results suggesting a conventional lead-zinc
flotation circuit at Kilbricken would be able to achieve saleable mineral
concentrates, with no penalties likely due to the presence of deleterious
metals. Our metallurgical studies will continue, with drilling to start in
April, to focus on gaining fresh metallurgical samples."
The findings were based on a gap analysis performed by Dr. Kurt Forrester
of Arn Persepective Ltd, based on a report by SGS Mineral Services, Lakefield
Facility, dated September 2010 and titled: "An Investigation by High
Definition Mineralogy into the mineralogical characteristics of Fourteen Rock
Samples from A Carbonate Hosted Base Metal Deposit, Ireland, prepared for
Lundin Mining Exploration". The study examined fourteen mineralized samples
from Kilbricken and was carried out with X-ray diffraction (XRD), QEMSCAN(TM),
electron microprobe and chemical analysis. The purpose of the mineralogical
appraisal test program was to determine the overall mineral assemblage and
textural characteristics in each sample, and the liberation characteristics.
Material employed in these analyses were taken from zones across a number of
mineralogical domains identified in 2010 during historical exploration
undertaken by Lundin Mining Exploration Limited and there is no guarantee that
the samples analyzed will form part of any future resource area.
About Hannan Metals Limited (TSX.V:HAN)
Hannan Metals Limited has 100% ownership of the County Clare Zn-Pb-Ag-Cu
project in Ireland, which consists of 9 prospecting licences for 32,223
hectares. The Kilbricken project, a new high-grade Zn-Pb-Ag-Cu discovery is
the Company's flagship project. Better intersections, to date, include DH 46:
20.5m (at) 7.5% Zn, 9.9% Pb, 0.07% Cu, 74.6g/t Ag, DH06: 21.3m (at) 11% Zn, 
4.8% Pb,
0.06% Cu, 94.4g/t Ag. The project is drilled over more than 1.5 kilometres
and, importantly, holds large upside with a 40-kilometre trend to test, which
includes the Milltown prospect (incl. DH19: 13.3m at 5.8% Pb and 10.5% Zn).
The true thickness of the mineralized intervals quoted is interpreted to be
approximately 95% of the sampled thickness.
Zinc remains in tight supply amidst rising demand and stagnant supply.
Ireland is a leading global jurisdiction for zinc mining and exploration. It
has been stated that Irish base metal ore field is ranked first in the world
in terms of zinc discovered per square kilometre, and second in the world with
respect to lead. In 2015, Ireland was the world's 10th largest zinc producing
nation with 230,000 tonnes produced.
Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in Europe.
Additionally, the team holds extensive zinc experience, gained from the
world's largest integrated zinc producer of the time, Pasminco Ltd.
Dr. Kurt Forrester, Chartered Chemical Engineer (CEng MIChemE) and
Chartered Professional Metallurgist (MAusIMM CP(Metallurgy), is a Qualified
Person as defined in National Instrument 43-101 and has reviewed and approved
the technical disclosure contained in this news release.
On behalf of the Board,
"Michael Hudson"___________ Michael Hudson, CEO & Chairman
Forward Looking Statements
Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact, certain
information contained herein constitutes forward-looking statements, which
include the Company's expectations regarding future performance based on
current results, expected cash costs based on the Company's current internal
expectations, estimates, projections, assumptions and beliefs, which may prove
to be incorrect. These statements are not guarantees of future performance and
undue reliance should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which may cause
the Company's actual performance and financial results in future periods to
differ materially from any projects of future performance or results expressed
or implied by such forward-looking statement. These risks and uncertainties
include, but are not limited to: timing of commencement of planned drill
programs; anticipated mineral recoveries, liabilities inherent in mine
development and production, geological risks, the financial markets generally,
and the ability of the Company to raise additional capital to fund future
operations. There can be no assurance that forward-looking statements will
prove to be accurate, and actual results and future events could differ
materially from those anticipated in such statements. The Company undertakes
no obligation to update forward-looking statements if circumstances or
management's estimates or opinions should change except as required by
applicable securities laws. The reader is cautioned not to place undue
reliance on forward-looking statements.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
SOURCE Hannan Metals Ltd.



To view the original version on PR Newswire, visit:
http://www.newswire.ca/en/releases/archive/March2017/30/c7438.html

-0-                           03/30/2017
/For further information: www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7; Mariana Bermudez, Corporate Secretary, +1 (604)
685 9316, info(at)hannanmetals.com/
(HAN.)

CO:  Hannan Metals Ltd.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-