Source	MARKET NEWS
Date	03/30/2017
Time	07:18:46 AM

Company	 Hannan Metals Ltd.
Title	Mineralogical 
Analysis for the Kilbricken Projec





    CDNX Symbol: HAN











Press Release





HANNAN METALS LTD ("HAN-V")
- Mineralogical Analysis for the Kilbricken Project, Ireland

Hannan Metals Limited ("Hannan" or the "Company") announces the
results of a gap analysis on mineralogical investigations on the
Kilbricken project, Ireland by Dr. Kurt Forrester of Arn Perspective
Ltd.

Key points:

//st

Based on the available information it is likely a conventional
lead-zinc flotation circuit at Kilbricken would be able to achieve saleable
mineral concentrates;



It is anticipated that there should be no penalties due to the
presence of deleterious elements (arsenic, manganese, cadmium, selenium),
subject to confirmation from the assessment of bulk element deportment
during lead-zinc flotation;



A primary grind of between 100m to 150m is anticipated to achieve
satisfactory liberation and there are no red flags with the modal
mineralogical analysis with respect to mineral processing and
beneficiation;



Based on the information available, it is anticipated that
Kilbricken should be able to achieve high recoveries of both zinc and lead
concentrates. Results from limited grade recovery analysis indicated the
following recoveries probable using a conventional flowsheet:

Targeting a sphalerite grade of 85% in the zinc concentrate would
result in recoveries in excess of 85%;

Targeting a galena grade of 70% in the lead concentrate would result
in recoveries in excess of 75%;



Recommendations include conducting metallurgical test work across
the deposit as part of an ongoing exploration and development program. To
this end, Hannan plans to start drilling at Kilbricken during April 2017.
The first two drill holes will collect metallurgical samples for locked
cycle flotation testwork.

//et

Mr Hudson, CEO and Chairman states, "In general, Irish style
zinc-lead deposits are typically attractive because of their simple
mineralogy and polymetallic nature. It is most encouraging that this
also appears to be the case at Kilbricken with these results suggesting
a conventional lead-zinc flotation circuit at Kilbricken would be able
to achieve saleable mineral concentrates, with no penalties likely due
to the presence of deleterious metals. Our metallurgical studies will
continue, with drilling to start in April, to focus on gaining fresh
metallurgical samples."

The findings were based on a gap analysis performed by Dr. Kurt
Forrester of Arn Persepective Ltd, based on a report by SGS Mineral
Services, Lakefield Facility, dated September 2010 and titled: "An
Investigation by High Definition Mineralogy into the mineralogical
characteristics of Fourteen Rock Samples from A Carbonate Hosted Base
Metal Deposit, Ireland, prepared for Lundin Mining Exploration". The
study examined fourteen mineralized samples from Kilbricken and was
carried out with X-ray diffraction (XRD), QEMSCAN(TM), electron
microprobe and chemical analysis. The purpose of the mineralogical
appraisal test program was to determine the overall mineral assemblage
and textural characteristics in each sample, and the liberation
characteristics. Material employed in these analyses were taken from
zones across a number of mineralogical domains identified in 2010
during historical exploration undertaken by Lundin Mining Exploration
Limited and there is no guarantee that the samples analyzed will form
part of any future resource area.

About Hannan Metals Limited (TSX.V:HAN)

Hannan Metals Limited has 100% ownership of the County Clare
Zn-Pb-Ag-Cu project in Ireland, which consists of 9 prospecting
licences for 32,223 hectares. The Kilbricken project, a new high-grade
Zn-Pb-Ag-Cu discovery is the Company's flagship project. Better
intersections, to date, include DH 46: 20.5m @ 7.5% Zn, 9.9% Pb, 0.07%
Cu, 74.6g/t Ag, DH06: 21.3m @ 11% Zn, 4.8% Pb, 0.06% Cu, 94.4g/t Ag.
The project is drilled over more than 1.5 kilometres and, importantly,
holds large upside with a 40-kilometre trend to test, which includes
the Milltown prospect (incl. DH19: 13.3m at 5.8% Pb and 10.5% Zn). The
true thickness of the mineralized intervals quoted is interpreted to be
approximately 95% of the sampled thickness.

Zinc remains in tight supply amidst rising demand and stagnant
supply. Ireland is a leading global jurisdiction for zinc mining and
exploration. It has been stated that Irish base metal ore field is
ranked first in the world in terms of zinc discovered per square
kilometre, and second in the world with respect to lead. In 2015,
Ireland was the world's 10th largest zinc producing nation with 230,000
tonnes produced.

Over the last decade, the team behind Hannan has forged a long and
successful record of financing and discovering mineral projects in
Europe. Additionally, the team holds extensive zinc experience, gained
from the world's largest integrated zinc producer of the time, Pasminco
Ltd.

Dr. Kurt Forrester, Chartered Chemical Engineer (CEng MIChemE) and
Chartered Professional Metallurgist (MAusIMM CP(Metallurgy), is a
Qualified Person as defined in National Instrument 43-101 and has
reviewed and approved the technical disclosure contained in this news
release.

On behalf of the Board,

"Michael Hudson"
Michael Hudson, CEO & Chairman

Forward Looking Statements

Certain information set forth in this news release contains
"forward-looking statements", and "forward- looking information" under
applicable securities laws. Except for statements of historical fact,
certain information contained herein constitutes forward-looking
statements, which include the Company's expectations regarding future
performance based on current results, expected cash costs based on the
Company's current internal expectations, estimates, projections,
assumptions and beliefs, which may prove to be incorrect. These
statements are not guarantees of future performance and undue reliance
should not be placed on them. Such forward-looking statements
necessarily involve known and unknown risks and uncertainties, which
may cause the Company's actual performance and financial results in
future periods to differ materially from any projects of future
performance or results expressed or implied by such forward-looking
statement. These risks and uncertainties include, but are not limited
to: timing of commencement of planned drill programs; anticipated
mineral recoveries, liabilities inherent in mine development and
production, geological risks, the financial markets generally, and the
ability of the Company to raise additional capital to fund future
operations. There can be no assurance that forward-looking statements
will prove to be accurate, and actual results and future events could
differ materially from those anticipated in such statements. The
Company undertakes no obligation to update forward-looking statements
if circumstances or management's estimates or opinions should change
except as required by applicable securities laws. The reader is
cautioned not to place undue reliance on forward-looking statements.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

SOURCE Hannan Metals Ltd.

For further information:  www.hannanmetals.com, 1305 - 1090 West Georgia
St., Vancouver, BC, V6E 3V7; Mariana Bermudez, Corporate Secretary, +1
(604) 685 9316, info@hannanmetals.com
______________________________
_______________________________________________
TSX Venture closing price for HAN-V
Date: 2017/03/29
Closing Price: 0.49
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1708800031TS11708801001-07171520170330