Source	MARKET NEWS
Date	03/29/2017
Time	07:27:40 AM

Company	 Alba Minerals Ltd.
Title	Final 
Results from Phase I Drilling at Their Lit





    CDNX Symbol: AA











Press Release




[200/News Release]AA.HVALBA MINERALS LTDMAR 29 2017  07:26 AMFinal 
Results from Phase I Drilling at Their Lithium Project inClayton Valley, 
Nevada; Phase I results will be included in initialNI 43 101 Resource Estimate 
in progress --->@NEWS RELEASE
NORAM VENTURES INC ("NRM-V")
ALBA MINERALS LTD ("AA.H-V")
- Final Results from Phase I Drilling at Their Lithium Project in
- Clayton Valley, Nevada; Phase I results will be included in
- initial NI 43-101 Resource Estimate in progress

Noram Ventures Inc. ("Noram") and Alba Minerals Ltd. ("Alba") are
pleased to announce the last batch of drill core sample results from
the 46-hole Phase I drilling program that focused on the Zeus portion
of their Clayton Valley Lithium Project in Nevada (see Figure 1). The
Zeus claims are located within two kilometers (1.25 miles) of
Albemarle's Silver Peak Lithium Mine that has been in production since
1966 and is the only lithium-brine production operation in North
America.

The last group of 16 holes reported herein consisted of 228.1
meters (748 feet) of core drilling with an average hole depth of 14.3
meters (46.8 feet) and core sampling done primarily on 1.22 meter
(4-foot) intervals. Bradley C. Peek, MSc and Certified Professional
Geologist supervised the collection of the cores and samples; and
sample analysis was performed by ALS Labs (Reno, NV) on 191 samples
from the 16 holes using a 4-acid digestion and MS-ICP methods for 48
elements.

Table 1 lists each drill hole's location (NAD 83, Zone 11S),
elevation and depth - all in meters. All holes were vertical. All core
size was BQ. Figure 2 is an overview of all of the Phase 1 drill holes.


Table 1 - Drill Hole Location Information

//st
Hole ID     UTM       UTM Approx. Depth Dip
Easting  Northing   Elev.
CVH-01 452876.5 4175657.0   1378   14.3 -90
CVX-01 457245.5 4182107.8   1377    8.2 -90
CVZ-31 455373.0 4180734.2   1324   15.2 -90
CVZ-32 455454.6 4180613.8   1326   15.2 -90
CVZ-33 456205.5 4180418.8   1354   28.0 -90
CVZ-34 455103.5 4181446.1   1306   14.0 -90
CVZ-35 454998.5 4181166.9   1310   15.2 -90
CVZ-36 455782.3 4181387.1   1324   13.4 -90
CVZ-37 456086.2 4181416.3   1334   15.2 -90
CVZ-38 455673.6 4181224.7   1322   13.4 -90
CVZ-39 455802.1 4181266.9   1331   15.2 -90
CVZ-40 455878.0 4181578.2   1325   14.6 -90
CVZ-41 455821.1 4181672.6   1322   12.2 -90
CVZ-42 455858.8 4181319.8   1329   15.2 -90
CVZ-43 455706.6 4181821.3   1315    9.4 -90
CVZ-44 455718.3 4181366.6   1329   13.7 -90
//et

Only three of these latest drill holes are located in the
redefined area of close-spaced drilling measuring approximately 970
meters (3,180 feet) by 830 meters (2,720 feet)(shown as rectangle in
Figure 3). Lithium values continue to be very consistent across the
close-spaced drilling area, but values were shown to decrease to the
north of the close-spaced drilling area. Since the northern area was
only tested with shallow drilling, it may still hold promise with
further testing. The areas to the east, west and south of the
close-spaced drilling remain open and untested, as well as other large
areas on the remainder of the claim holdings covering 17,738 acres
(7,178 hectares).

Two holes were drilled in outlying areas as preliminary tests and
showed very encouraging results. These were holes CVX-01 near the Zeus
Extension claims, approximately 1.5 kilometers (0.93 miles) northeast
of the main grouping of Zeus holes; and CVH-01 on the Hades claim,
approximately 5 kilomenters (3.1 miles) southwest of the main grouping,
near the previously reported borehole. CVX-01, had a weighted average
of 807 ppm Li for the entire hole. Outwash gravel in the top 4.6 meters
(15 feet) of CVH-01 prevented any core recovery, but the lower 9.8 (32
feet) of the hole had a weighted average of 1,023 ppm Li, somewhat
higher than the 933 ppm average of 3 samples from the borehole's spoil
pile.

A National Instument 43-101 resource estimate based on the
analytical results from the Phase 1 drilling program is being prepared
and will be announced upon completion.

Table 2 lists the samples, their intervals, their weights and
their lithium analytical results. The core holes were vertical and the
sedimentary units that were tested are horizontal or dipping at less
than 5, so the intervals sampled are true widths.

//st
Hole ID Sample Sample From   To  From     To    Li
ID Wt.(kg) (ft) (ft)   (m)    (m) (ppm)
CVH-01  293379   0.64   15   20  4.57   6.10   920
CVH-01  293380   0.36   20   24  6.10   7.32  1090
CVH-01  293381   0.5    24   28  7.32   8.53   990
CVH-01  293382   0.28   28   32  8.53   9.75  1140
CVH-01  293383   0.42   32   36  9.75  10.97  1290
CVH-01  293384   0.68   36   40 10.97  12.19   970
CVH-01  293385   0.24   40   44 12.19  13.41   980
CVH-01  293386   0.32   44   47 13.41  14.33   770
CVX-01  320253   0.06    0    4  0.00   1.22   450
CVX-01  320254   0.36    4    8  1.22   2.44   930
CVX-01  320255   0.66    8   12  2.44   3.66   820
CVX-01  320256   0.68   12   16  3.66   4.88   780
CVX-01  320257   0.72   16   20  4.88   6.10   800
CVX-01  320258   1.08   20   24  6.10   7.32  1220
CVX-01  320259   0.62   24   27  7.32   8.23   600

CVZ-31  293368   0.32    0    4  0.00   1.22   860
CVZ-31  293369   0.66    4    8  1.22   2.44   820
CVZ-31  293370      1    8   12  2.44   3.66   810
CVZ-31  293371   0.68   12   16  3.66   4.88  1160
CVZ-31  293372   0.34   16   20  4.88   6.10   970
CVZ-31  293373   0.72   20   24  6.10   7.32   790
CVZ-31  293374   0.42   42    8  7.32   8.53  1040
CVZ-31  293375   0.58   28   32  8.53   9.75  1180
CVZ-31  293376   0.72   32   36  9.75  10.97   830
CVZ-31  293377   0.44   36   38 10.97  11.58   960

CVZ-32  289896   0.1     0    8  0.00   2.44   730
CVZ-32  289897   0.7     8   12  2.44   3.66   750
CVZ-32  289898   0.66   12   16  3.66   4.88  1010
CVZ-32  289899   0.72   16   20  4.88   6.10   730
CVZ-32  289900   0.88   20   24  6.10   7.32   730
CVZ-32  289901   0.86   24   28  7.32   8.53   940
CVZ-32  289902   0.82   28   32  8.53   9.75   750
CVZ-32  289903   0.8    32   36  9.75  10.97   660
CVZ-32  289904   0.66   36   40 10.97  12.19  1050
CVZ-32  289906   0.28   40   44 12.19  13.41   650
CVZ-32  289907   0.62   44   48 13.41  14.63   510
CVZ-32  289908   0.18   48   50 14.63  15.24   293

CVZ-33  289851   0.54    0    4  0.00   1.22  1120
CVZ-33  289852   0.56    4    8  1.22   2.44   910
CVZ-33  289853   0.76    8   12  2.44   3.66   690
CVZ-33  289854   0.88   12   16  3.66   4.88  1020
CVZ-33  289855   0.78   16   20  4.88   6.10   580
CVZ-33  289856   0.66   20   24  6.10   7.32   750
CVZ-33  289857   0.66   24   28  7.32   8.53   760
CVZ-33  289858   0.72   28   32  8.53   9.75   640
CVZ-33  289859    0.9   32   36  9.75  10.97   710
CVZ-33  289860   0.42   36   40 10.97  12.19  1000
CVZ-33  289862   0.64   40   44 12.19  13.41   880
CVZ-33  289863   0.86   44   48 13.41  14.63   610
CVZ-33  289864   0.96   48   52 14.63  15.85   550
CVZ-33  289865   0.88   52   56 15.85  17.07   630
CVZ-33  289866   0.8    56   60 17.07  18.29  1080
CVZ-33  289867   0.78   60   64 18.29  19.51  1060
CVZ-33  289868   0.62   64   68 19.51  20.73   910
CVZ-33  289869   0.92   68   72 20.73  21.95   900
CVZ-33  289870   0.9    72   762 1.95  23.16  1090
CVZ-33  289871   0.94   76   80 23.16  24.38   920
CVZ-33  289872   0.98   80   84 24.38  25.60   850
CVZ-33  289873   0.8    84   88 25.60  26.82  1130
CVZ-33  289874   0.66   88   92 26.82  28.04  2380

CVZ-34  289838   0.38    0    4  0.00   1.22   670
CVZ-34  289839   0.2     4    8  1.22   2.44   770
CVZ-34  289840   0.68    8   12  2.44   3.66   750
CVZ-34  289841   0.86   12   16  3.66   4.88   620
CVZ-34  289842   0.9    16   20  4.88   6.10   950
CVZ-34  289843   0.62   20   24  6.10   7.32   730
CVZ-34  289844   0.64   24   28  7.32   8.53   690
CVZ-34  289845   0.58   28   32  8.53   9.75   640
CVZ-34  289846   0.64   32   36  9.75  10.97   417
CVZ-34  289847   0.4    36   40 10.97  12.19   385
CVZ-34  289848   0.58   40   44 12.19  13.41   355
CVZ-34  289849   0.38   44   46 13.41  14.02   316

CVZ-35  289945   0.22    0    4  0.00   1.22   580
CVZ-35  289946   0.76    4    8  1.22   2.44   690
CVZ-35  289947   0.6     8   12  2.44   3.66   510
CVZ-35  289948   0.8    12   16  3.66   4.88   530
CVZ-35  289949   0.7    16   20  4.88   6.10   760
CVZ-35  289950   0.66   20   24  6.10   7.32   750
CVZ-35  289951   0.74   24   28  7.32   8.53   550
CVZ-35  289952   0.94   28   32  8.53   9.75   690
CVZ-35  289953   0.48   32   36  9.75  10.97   740
CVZ-35  289955   0.82   36   40 10.97  12.19   950
CVZ-35  289956   0.56   40   44 12.19  13.41   770
CVZ-35  289957   0.8    44   50 13.41  15.24   810
CVZ-35  289958   0.3  46.5 47.8 14.17  14.57  1030

CVZ-36  320275   0.2     0    4  0.00   1.22 185.5
CVZ-36  320276   0.52    4    8  1.22   2.44   382
CVZ-36  320277   0.86    8   12  2.44   3.66   440
CVZ-36  320278   0.64   12   16  3.66   4.88   361
CVZ-36  320279   0.54   16   20  4.88   6.10   400
CVZ-36  320280   0.66   20   24  6.10   7.32   440
CVZ-36  320281   0.76   24   28  7.32   8.53   378
CVZ-36  320282   0.64   28   32  8.53   9.75   460
CVZ-36  320283   0.52   32   36  9.75  10.97   273
CVZ-36  320284   0.76   36   40 10.97  12.19   331
CVZ-36  320285   0.9    40   44 12.19  13.41   600

CVZ-37  289959   0.44    0    4  0.00   1.22   510
CVZ-37  289960   0.68    4    8  1.22   2.44   600
CVZ-37  289961   0.72    8   12  2.44   3.66   570
CVZ-37  289962   0.74   12   16  3.66   4.88   438
CVZ-37  289963   0.58   16   20  4.88   6.10   860
CVZ-37  289964   0.72   20   24  6.10   7.32   530
CVZ-37  289965   0.68   24   28  7.32   8.53   490
CVZ-37  289966   0.7    28   32  8.53   9.75   630
CVZ-37  289967   0.44   32   36  9.75  10.97   550
CVZ-37  289968   0.3    36   40 10.97  12.19   396
CVZ-37  289969   0.84   40   44 12.19  13.41   860
CVZ-37  289970   0.86   44   48 13.41  14.63   820
CVZ-37  289971   0.46   48   50 14.63  15.24   720

CVZ-38  289920   0.16    0    4  0.00   1.22   421
CVZ-38  289921   0.56    4    8  1.22   2.44   404
CVZ-38  289922   0.38    8   12  2.44   3.66   470
CVZ-38  289923   0.86   12   16  3.66   4.88   412
CVZ-38  289924   0.68   16   20  4.88   6.10   421
CVZ-38  289925   0.66   20   24  6.10   7.32   421
CVZ-38  289926   0.5    24   28  7.32   8.53   385
CVZ-38  289927   0.52   28   32  8.53   9.75   460
CVZ-38  289928   0.5    32   36  9.75  10.97   368
CVZ-38  289929   0.84   36   40 10.97  12.19   352
CVZ-38  289930   0.68   40   44 12.19  13.41   368

CVZ-39  320287   0.22    0    4  0.00   1.22   560
CVZ-39  320288   0.66    4    8  1.22   2.44   600
CVZ-39  320289   0.32    8   12  2.44   3.66   460
CVZ-39  320290   0.72   12   16  3.66   4.88   431
CVZ-39  320291   0.88   16   20  4.88   6.10   830
CVZ-39  320292   0.78   20   24  6.10   7.32   850
CVZ-39  320293   0.72   24   28  7.32   8.53   570
CVZ-39  320294   0.76   28   32  8.53   9.75   860
CVZ-39  320295   0.92   32   36  9.75  10.97   830
CVZ-39  320296   0.78   36   40 10.97  12.19   630
CVZ-39  320297   0.78   40   44 12.19  13.41   470
CVZ-39  320298   0.78   44   48 13.41  14.63   421
CVZ-39  320299   0.44   48   50 14.63  15.24   520

CVZ-40  289932   0.24    0    4  0.00   1.22 186.5
CVZ-40  289933   0.44    4    8  1.22   2.44   335
CVZ-40  289934   0.46    8   12  2.44   3.66   296
CVZ-40  289935   0.7    12   16  3.66   4.88   325
CVZ-40  289936   0.62   16   20  4.88   6.10   326
CVZ-40  289937   0.42   20   24  6.10   7.32   404
CVZ-40  289938   0.52   24   28  7.32   8.53   560
CVZ-40  289939   0.32   28   32  8.53   9.75   350
CVZ-40  289940   0.54   32   36  9.75  10.97   334
CVZ-40  289941   0.7    36   40 10.97  12.19   404
CVZ-40  289942   0.48   40   44 12.19  13.41   368
CVZ-40  289943   0.46   44   48 13.41  14.63   308

CVZ-41  289982   0.22    0    4  0.00   1.22 199.5
CVZ-41  289983   0.26    4    8  1.22   2.44   259
CVZ-41  289984   0.42    8   12  2.44   3.66   344
CVZ-41  289985   0.12   12   16  3.66   4.88   201
CVZ-41  289986   0.68   16   20  4.88   6.10   295
CVZ-41  289987   0.72   20   24  6.10   7.32   335
CVZ-41  289988   0.74   24   28  7.32   8.53   381
CVZ-41  289989   0.7    28   32  8.53   9.75   397
CVZ-41  289990   0.82   32   36  9.75  10.97   350
CVZ-41  289991   0.82   36   40 10.97  12.19   338
CVZ-41  289992   0.68   40   44 12.19  13.41   333
CVZ-41  289993   0.54   44   48 13.41  14.63   330
CVZ-41  289994   0.6    48   50 14.63  15.24   407

CVZ-42  320261   0.16    0    4  0.00   1.22   460
CVZ-42  320262   0.56    4    8  1.22   2.44   309
CVZ-42  320263   0.38    8   12  2.44   3.66   315
CVZ-42  320264   0.68   12   16  3.66   4.88   710
CVZ-42  320265   0.66   16   20  4.88   6.10   490
CVZ-42  320266   0.84   20   24  6.10   7.32   740
CVZ-42  320267   0.76   24   28  7.32   8.53   610
CVZ-42  320268   0.76   28   32  8.53   9.75   410
CVZ-42  320269   0.74   32   36  9.75  10.97   630
CVZ-42  320270   0.5    36   40 10.97  12.19   530
CVZ-42  320271   0.86   40   44 12.19  13.41   470
CVZ-42  320272   0.8    44   48 13.41  14.63   450
CVZ-42  320273   0.3    48   50 14.63  15.24   510

CVZ-43  289973   0.2     0    4  0.00   1.22   195
CVZ-43  289974   0.38    4    8  1.22   2.44   185
CVZ-43  289975   0.32    8   12  2.44   3.66   217
CVZ-43  289976   0.38   12   16  3.66   4.88 189.5
CVZ-43  289977   0.44   16   20  4.88   6.10   211
CVZ-43  289978   0.28   20   24  6.10   7.32 162.5
CVZ-43  289979   0.2    24   28  7.32   8.53   250
CVZ-43  289980   0.46   28   31  8.53   9.45   245

CVZ-44  289996   0.48    0    4  0.00   1.22   480
CVZ-44  289997   0.56    4    8  1.22   2.44   540
CVZ-44  289998   0.84    8  13.3 2.44   4.05   590
CVZ-44  289999   0.32 13.3  15.7 4.05   4.79   176
CVZ-44  290000   0.46 15.7   18  4.79   5.49   373
CVZ-44  293360   0.72   18   22  5.49   6.71   500
CVZ-44  293361   0.6    22   26  6.71   7.92   460
CVZ-44  293362   0.7    26   30  7.92   9.14   480
CVZ-44  293363   0.7    30   34  9.14  10.36   480
CVZ-44  293364   0.6    34   38 10.36  11.58   460
CVZ-44  293365   0.58   38   42 11.58  12.80   431
CVZ-44  293366   0.38   42   45 12.80  13.72   434
//et

Sample intervals were split by geologists at the drilling program
staging area. Half of the core was retained in the core boxes for
future review and/or sampling. The other half was securely sent to ALS
Laboratories in Reno, Nevada, USA for testing. Core recovery for these
last 16 core holes averaged 74.1%.

The lithium content of the 191 samples from the last 16 holes had
an interval-weighted average of 613.9 ppm with a minimum value of 163
ppm and a maximum value of 2,380 ppm. The minimum and maximum values
were collected over 1.22m (4 ft) intersections. The samples had a
median value of 560 ppm Li. Collectively, the weighted average lithium
value in this last batch of drill core samples approximated the average
value of previously reported surface samples (621 ppm Li).
Laboratory standards with two different lithium ranges (1,237 ppm
and 783 ppm) were inserted into the sample stream, along with lithium
blanks and duplicate samples (13 QA/QC samples, in all, with these
samples). The standards and blanks were obtained from MEG Labs of Reno,
Nevada, USA. Duplicate samples were obtained by splitting the remaining
half of the split core (1/4 of the original core). All analyses of the
standards, blanks and duplicates were well within acceptable ranges.

"We are extremely pleased with the results from our Phase 1
drilling program and expect to have our initial lithium resource
estimate completed shorty," said Mark Ireton President and CEO of
Noram. "The Phase 1 results will also be instrumental in planning our
Phase 2 drilling program that will encompass the Spartan and Hades
claims and enable us to determine the lithium potential of our entire
South Block property."

Noram is amassing one of the largest land packages in Nevada's
Clayton Valley. Its non-contiguous North and South Blocks now total 888
claims covering 17,738 acres and are positioned both north and south of
Albemarle's Silver Peak mine, North America's only lithium producer.

The technical information contained in this news release has been
reviewed and approved by Bradley C. Peek, MSc and Certified
Professional Geologist, who is a Qualified Person with respect to
Noram's Clayton Valley Lithium Project as defined under National
Instrument 43-101.

About Noram Ventures Inc.:

Noram Ventures Inc. (TSX-Venture: NRM / Frankfurt: N7R / OTCBB:
NRVTF) is a Canadian based junior exploration company, with a goal of
becoming a force in the Green Energy Revolution through the development
of lithium and graphite deposits and becoming a low-cost supplier for
the burgeoning lithium battery industry. The Company's primary business
focus since formation has been the exploration of mineral properties.
Current projects include lithium properties in the Clayton Valley of
Nevada and the Hector Lode in San Bernardino County, California; and
the Jumbo graphite property in southeastern British Columbia. Noram's
long term strategy is tobuild a multi-national lithium-graphite
dominant industrial minerals company to produce and sell lithium and
graphite into the markets of Europe, North America and Asia.

Please visit our web site for further information:
www.noramventures.com.

ON BEHALF OF THE BOARD OF DIRECTORS

/s/ "Mark R. Ireton"

President & Director
Noram Ventures Inc.

This news release contains projections and forward-looking
information that involve various risks and uncertainties regarding
future events. Such forward-looking information can include without
limitation statements based on current expectations involving a number
of risks and uncertainties and are not guarantees of future performance
of the Company. The following are important factors that could cause
the Company's actual results to differ materially from those expressed
or implied by such forward looking statements; the uncertainty of
future profitability; and the uncertainty of access to additional
capital. These risks and uncertainties could cause actual results and
the Company's plans and objectives to differ materially from those
expressed in the forward-looking information. Actual results and future
events could differ materially from anticipated in such information.
These and all subsequent written and oral forward-looking information
are based on estimates and opinions of management on the dates they are
made and expressed qualified in their entirety by this notice. The
Company assumes no obligation to update forward-looking information
should circumstance or management's estimates or opinions change.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

To view this press release as a PDF file, click onto the following link:
public://news_release_pdf/Noram03292017.pdf

Source: Noram Ventures Inc.
______________________________________
_______________________________________________
TSX Venture closing price for AA.H-V
Date: 2017/03/21
Closing Price: 0.15
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1708700017TS11708701090-07264820170329