Source	MARKET NEWS
Date	03/29/2017
Time	08:03:39 AM

Company	 Corex Gold Corporation
Title	Santana Heap 
Leach Gold Project; 2017 Constructi





    CDNX Symbol: CGE











Press Release





COREX GOLD CORP ("CGE-V")
- Santana Heap-Leach Gold Project; 2017 Construction Update

Corex Gold Corp. ("Corex" or the "Company") is continuing
construction and mining activities at its 100%-owned Santana heap-leach
gold project in Sonora, Mexico.

Jaw crushing and loading started on Nicho Norte zone in late
November 2016. A total of 11,210 tonnes of material was crushed in
November and December and loaded onto the 1st leach pad. An additional
11,989 tonnes were loaded in January bringing the total to 23,199
tonnes. The pad loading was completed on January 26, 2017. The heap was
contoured and the surface broken up in preparation for leaching.

Construction continued on the bulk test process plant and the
completion of the distribution system plumbing with several application
methods of leach fluid tested. Application of charged leachant to
establish alkaline pH has begun with metal leaching to commence later
this month.

A second leach pad will allow a separate batch of finer crushed
material to be tested to determine the leach and cost characterization
of much finer crushing. The results from the two bulk leach pads will
be utilized by the Company to verify metallurgical viability of heap
leaching and to optimize the most efficient operating methods and
equipment.

Construction of the 2nd leach pad, which connects to the first
leach pad, is in progress. The 2nd leach pad is about 4,500 square
meters. The earthwork or moving of material is substantially complete.
The HDPE liners have been ordered and should be installed in early
March 2017. This will provide a total leach pad of about 9,000 square
meters.

(For recent photos of the Santana heap-leach gold project click
here).

"This is an exciting time for shareholders, as we commence our
bulk mining and process testing on our Santana Gold Project," said
Craig Schneider, Corex's President and CEO.

The Company is not basing its production effort on a feasibility
study with demonstrated mineral reserves and estimated economic and
technical viability. As a result, the Company acknowledges and accepts
the higher risk of failure with uncertainty of unverified economic and
technical outcome. Corex believes the past experience and prudent track
record of Chester Millar developing this type of mine helps ameliorate
possible technical risk.

Mel Herdrick P. Geo., is the acting Qualified Person as defined by
National Instrument 43-101. He has reviewed and approved the
preparation of the technical information in this release. He is a
shareholder of the company.

The reader should be cautioned the Company has neither completed
economic nor technical feasibility studies or metallurgical studies
confirming the projected production capacity at Santana and there is no
certainty the Company's plans will be economically viable.

About Corex Gold Corp.

Corex Gold Corp. is a Canadian resource company focused on
achieving near-term economic gold production from its 100% owned
flagship property, Santana Project, Sonora State, Mexico.

Cautionary Statement:
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. The foregoing information may contain forward-looking
statements relating to the future performance of Corex Gold Corp.
Forward-looking statements, specifically those concerned with future
performance are subject to certain risks and uncertainties, and actual
results may differ materially. These risks and uncertainties are
detailed from time to time in Corex Gold Corp.'s filings with the
appropriate securities commissions.

Contact Information:

Corex Gold Corp.
Craig Schneider
President & CEO
604.683.2505
604.683.2506 (FAX)
info@corexgold.com
www.corexgold.com
______________________________
_______________________________________________
TSX Venture closing price for CGE-V
Date: 2017/03/28
Closing Price: 0.13
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1708700023TS11708701175-08014420170329