Source	MARKET NEWS
Date	03/28/2018
Time	10:10:02 AM

Company	 Rizal Resources Corporation
Title	T'Boli 
Gold Mine Exploration Update





    CDNX Symbol: RZL











Press Release




[200/News Release]RZLVRIZAL RESOURCES CORPMAR 28 2018  10:06 AMT'Boli 
Gold Mine Exploration Update --->@NEWS RELEASE
RIZAL RESOURCES CORP ("RZL-V")
- T'Boli Gold Mine Exploration Update

Rizal Resources Corporation ("Rizal" or the "Company") announces
that it has filed a technical report in the form prescribed by Canadian
National Instrument 43-101 titled NI 43-101 Technical Report, T'Boli
Gold-Silver Project, South Cotabato, Mindanao, Philippines. The report
was prepared by Steven Olsen B.Sc.(Hons), M.Sc., MAIG, of Victoria,
Australia. This news release provides summary information from the
technical report as well as updates on the Company's exploration
activities at the T'Boli Gold-Silver Project ("T'Boli" or "the
Project").

The Company is currently conducting exploration activities at
T'Boli for the purpose of defining the geological controls and the
continuity of the gold mineralization that exists at the Project. This
work has focused on the exploration of two defined vein systems known
as the north veins and south veins, via a series of exploration
development tunnel's. Work completed to date has now been interpreted
and collated to identify a number of high grade mineralized zones from
the exploration development. Based on this review, over 457m of high
grade gold mineralization has now been defined (see Table 1), including
the following highlights:

- South Vein FW2 - 22m long with average thickness (true width) of
0.51m and gold grade of 57.7g/t

- South Vein FW1 - 18m long with average thickness (true width) of
0.47m and gold grade of 29.7g/t

- South Vein V3 - 32m long with average thickness (true width) of
0.68m and gold grade of 23.8g/t

- South Vein V4 - 50m long with average thickness (true width) of
1.2m and gold grade of 21g/t

- North Vein V1 - 53m long with average thickness (true width) of
1.3m and gold grade of 18.8g/t

To date the exploration development has centered on the north
veins, which is the first structure that can be accessed from the
underground development. The north veins have limited drilling
information with most of the technical information at this location
derived from the exploration development.

The Company has also commenced trial mining activities in parts of
the north veins. The results from the trial mining activities are still
at a preliminary stage with results from the reconciliation of this
work anticipated in the second half of 2018.

In contrast to the north veins, the south veins have received very
limited exploration development. However, the bulk of the more
significant prior drilling information exists on the south veins. In
addition, the south veins are interpreted to exist in a more favourable
geological location for the formation of high-grade gold mineralization
in comparison with the north veins.

The Company plans to access and commence exploration drives on the
south veins in the second quarter of 2018. The exploration development
on the south veins is planned to come in close proximity to some of the
more significant drill intercepts recorded in the T'Boli database
including drill hole TG038 which returned a intersection of 8m (true
width) @ 14.2g/t gold (uncut).

Note that the T'Boli Project does not have a current Mineral
Resource estimate or Mineral Reserves and that in the absence of a
feasibility study of Mineral Reserves demonstrating economic and
technical viability is associated with an increased risk of failure of
the mining operations due to increased uncertainty of results. Mining
and processing activity at the T'Boli Project is ongoing on a
small-scale basis associated with the Company's underground exploration
activities and this should not be construed as Rizal having made a
commercial production decision.

Background Information

The exploration development drives that exist at T'Boli, both
historically and more recently under the current management, are within
a small portion of a larger complex of mineralized structures that lie
between two major North-West trending faults called the Kematau fault
and the Desawo fault (Figure 1).

Figure 1: Plan representing the location of the T'Boli Mine Site
and north and south vein structures relative to the broader regional
potential that exists throughout the area between the Kematau fault and
the Desawo fault. The location of grab samples from small scale miners
workings and their results are also shown. Note: Grab samples are
selective and an indication of the presence of mineralization only and
should not be taken to represent the average grade of potential Mineral
Resources.

The focus of the exploration activities by Rizal over a number of
stages has been to define gold mineralization situated within two broad
vein systems known at the north veins and the south veins (Figure 2)
located near the TMC Mine Site, highlighted in Figure 1. There are also
extensive small-scale mine workings throughout the broader region at
T'Boli, as note in Figure 1, and those workings that may be suitable
for future exploration work but have not received any significant
attention in recent years.

Earlier drilling campaigns, which make up the current drill hole
database, have identified multiple high-grade gold intersections
underneath an extensive set of surface mine workings close to the TMC
Mine Site. The drilling results are very encouraging in terms of
indicating the presence of a large gold system, however the complexity
and large number of gold bearing structures make the interpretation and
continuity of the gold mineralization difficult to confirm with
confidence without first exploring them further with underground
development.

It is for this reason, and also due to the ability to easily
access the shallow gold bearing structures, that the exploration plan
for the Project at numerous stages has been to define the gold
mineralization via a series of underground tunnels ("exploration
development").

To further validate the gold mineralization defined from the
exploration development and to assist with the Company's cash flow,
processing of the material from the exploration development has been
undertaken at its current small-scale processing facility which exists
6.4km from the TMC Mine site at T'Boli.

The aim of the current work program is to confirm the distribution
and continuity of the gold mineralization over the two major vein sets
that have been defined at T'Boli leading to a new Mineral Resource
estimate in the second half of 2018.

Local Geology and Mineralized Structures

The gold mineralization at T'Boli is contained within a number of
complex vein and breccia zones or structures which vary considerably in
their gold content and are often closely associated with low grade gold
in the surrounding host rock.

There are broad structural "Domains" which are known as the north
veins, hosted in a Dacitic rock, and the south veins, which straddle a
Dacite/Volcaniclastic boundary, but are predominantly hosted within a
Volcaniclastic rock (Figure 2).

Figure 2: Plan projection of the mapped veins and structures from
the exploration development at the 550mRL level. The two separate vein
systems are highlighted with the referenced location of the vertical
long sections for both the north veins (A-A) and south veins (B-B) as
shown in figures 3 and 4 respectively.

Each domain has a set of structures/narrow veins which are
predominantly striking in an east-west orientation and are dipping
steeply to south, at between 60 degrees and 90 degrees. In some
locations a complex series of veins have developed over an area
covering a total of 30m in width. Not all of the vein structures
contain high grade gold mineralization, and progress continues to be
made with regard to understanding the controls on the higher-grade
sections of the veins and structures that exist at T'Boli.

When the mineralized structures come close together, there is
often low-grade mineralization lying in the altered host rock between
the structures. When this has been observed in the exploration
development the size of the development has often increased in an
attempt to capture all of the gold mineralization where possible.

The current level of geological information gathered to date is
greater in the north veins, as this location is easier to access and
has been developed and explored over a much greater strike length than
the south veins.

In contrast to the location of the exploration development, the
drilling information has focused on testing the south veins, which
exist in an interpreted more favourable host rock for the formation of
gold mineralization. There are very few drill intersections that exist
over the broader potential area on the north veins outside of the
existing exploration development.

Exploration Development Results

At the north veins, the mineralization occurs as multiple zones
over a 300m strike length. Development has also occurred in the
hangingwall and footwall to the main structure, particularly where the
sampling has indicated that high grade gold exists in these other
structures. In total, there has been over 700m of development around
the 550mRL level over multiple stages to define 210m of high grade
mineralization, which exists within a 300m strike length corridor
(Figure 3). In addition, development has commenced at the 525mRL level
and also the 515mRL level with the development focused vertically
beneath the higher-grade mineralization defined on the 550mRL level.

Figure 3: Vertical Long Section (view looking to the North)
representation of the main structure developed in the north veins. The
information obtained from the exploration development has been collated
into geological domains that represent the higher-grade portions of the
uncovered mineralized structures. The results from each domain are
represented on this long section in their respective position
highlighting the total strike length, average thickness (in meters) and
weighted average (uncut) gold grade (g/t).

At the 515mRL level, the exploration development has accessed a
position where two structures exist close together. Based on an
interpretation that this larger mineralized position extends up to the
550mRL level, the decision was made to commence trial bulk mining
methods. This trial mining is still at an early stage of assessment
with mining and reconciliation work ongoing.

It is still considered that many of the narrow, mineralized
structures will be mined using narrow vein mining techniques. However,
a more modern assessment of this approach remains to be tested. To this
end, the Company has identified 3 locations on the north vein that will
soon be available for trial narrow vein mining. Some further
exploration development is required on the 525mRL level on the north
vein to complete the access for 2 of these trial mining locations.

For the south veins the mineralization appears to exist in
sections over a strike length of at least 350m, with the high-grade
zones interpreted at this stage to cumulatively total a strike length
of approximately 200m. The development on the south veins is not as
extensive as the exploration development on the north veins, however,
there has been some smaller sections accessed over multiple stages,
with multiple access points. At this stage, the drilling information
indicates that high grade gold mineralization still exists to the east
beyond the current extent of the level development.

Exploration development is planned to access the south veins close
to the defined position of the prior drill hole, TG038 which has a
reported drill intersection of 8m (true width) at an average grade of
14.2g/t.

Figure 4: Vertical Long Section (View looking to the North)
representation of the main structure developed in the south veins. All
prior drill hole intersections that exist within 150m depth of the of
the previous development have been projected onto this longsection,
with the interval length adjusted for their estimated true width. The
information obtained from the exploration development has been collated
into geological domains that represent the higher-grade portions of the
uncovered mineralized structures. The results from each domain are
represented on this long section in their respective position
highlighting the total strike length, average thickness (in meters) and
weighted average (uncut) gold grade (in grams per ton).

Planned Development

Table 1 is a summary of the high-grade mineralized zones that have
been defined to date from the exploration development activity at the
T'Boli Project.

//st

Location
Defined high-grade Structures ~550m RL
Strike    Average    Average
Length    Width      Grade
(m)       (m)        (g/t gold)
North Vein    53        1.3        18.8
North HW1     110       0.36       17.5
North Vein    18        1.18       7.1
North Bulk    100       5          Results Pending
South Vein    32        1.3        14.5
South Vein    22        0.46       18.8
South FW1     18        0.47       29.7
South FW2     22        0.51       57.7
South Vein    32        0.68       23.8
South Vein - Planned
Est. 50+
TOTAL
457

//et

Table 1: Summary of defined higher-grade mineralized zones that
are considered potential locations for future mining and to aid the
focus of the level development at the levels underneath the 550mRL. All
reported average widths are true widths and all average grades are
un-cut. The dominant interpreted structure at both the north veins and
south veins is reported as North Vein and South Vein respectively.
Veins/Mineralized Structures that exists immediately South of the more
dominant Vein at each location are defined as a Hangingwall ("HW")
vein. Veins/Mineralized Structures that exist immediately to the North
of the more dominant vein at each location are defined as a Footwall
("FW") vein.

Future Work Program

The Company has made substantial progress over the past 12 months
since it first commenced exploration development into the mineralized
structures at T'Boli. The goals for this ongoing work program are to
develop, explore and define the controls on the gold mineralization
across the north veins and south veins. The results from this work will
be analyzed with the objective of preparing a new Mineral Resource
estimate by the end of 2018.

The Company will provide regular updates on the results of its
exploration activities, with particular attention paid to the results
identified from the south veins, which is considered be located in a
more favourable location for the development of high grade gold
mineralization.

All of the information gathered as part of the Company's
exploration activities at the TMC Mine Site and associated processingof the 
material derived from these activities will enable the Company
to gather valuable information for any future proposed production
activities.

Quality Control

Channel sampling undertaken within the exploration development
drives are consistently taken on a horizontal line as rock chip samples
between 1m to 1.5m above the floor of the development which is
approximately perpendicular to the dominant dip of the mineralized
structures. The dominant geological domains and mineralized structures
dip to the South at between 60 and 90 degrees. Sample intervals vary
from between 0.2m and 1.0m in width with the sample boundaries obeying
the observed geological contacts.

Drill cores from the prior drilling programs were HQ, NQ and BQ in
size. For drill core that was HQ or NQ size, selected sampling
intervals were sub-sampled using different techniques depending on the
nature of the drill core. Competent drill core was cut longitudinally
in half with a core saw; Clay dominant or soft core was divided into
two halves using a spatula; Broken core or rubble was physically
separated into 2 separate and equal halves. For drill core that was BQ
in size, the whole sample interval was taken for analysis. Sample
intervals taken were predominantly at 1m or less, with sample interval
boundaries selected to ensure that the sampling interval did not cross
over a defined geological contact.

Of particular note with regard to the quality control of the prior
drill core samples is that for many of the sampling locations the core
recovery was reported to be poor. Based on the observations of the
mineralized structures from the underground development this is
interpreted to be a result of some clay rich sections that occur in
close proximity to the mineralized structures. The underground channel
sampling has also identified that the clay rich locations often contain
significant gold mineralization. The above observations indicate that
the core loss recorded in the prior drilling is due to the poor capture
of the mineralized clay rich material surrounding parts of the larger
structures at T'Boli. The loss of mineralized material may result in an
underestimation of the gold content within some of the reported
drilling intercepts.

Prior drilling samples were analysed by Interteck, which is an
independent external laboratory, with the processing laboratory
situated in Manila, Philipppines.

Sampling preparation and analysis for the channel samples are
undertaken at the Company's internal laboratory situated at T'Boli.

For both the prior drilling and the current channel samples from
the exploration development, the Company has maintained quality control
systems which includes the insertion of blanks, standards and pulp
duplicates. The control samples from the prior drilling information
have been reviewed for any possible lab bias. The review has concluded
that there are no material biases or inaccuracies in the assay
database, with additional check data required to confirm an observation
that there may be a slight bias of results on the low side resulting in
a slight understatement in the reported gold assay information.

Qualified Persons

Steven Olsen, member of AIG, has reviewed the exploration data and
prepared the scientific and technical information regarding exploration
results contained within this news release. Steven Olsen, an
Independent Consultant, is a "Qualified Person" as such term is defined
in National Instrument 43-101 and he has verified and approved the
contents of this news release.

About Rizal

Rizal is an exploration Company with a focus on its flagship
T'Boli Gold Project situated in the Philippines. The Company is using
underground development to explore and define the extensive gold
mineralization that exists at T'Boli. The Company's current objectives
are to complete exploration work with a view to establishing a current
mineral resource estimate, while generating short term cash flow from
small scale production at its existing processing plant.

Peter Main
President and CEO
pmain@rizalresources.com

For further information please visit our website at www.rizalresources.com,
Email us at info@rizalresources.com,
Phone: 778-370-1372 Fax: 604-608-5442

Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1808600039TS11808601878-10063620180328