Source	MARKET NEWS
Date	04/02/2018
Time	08:19:48 AM

Company	 Nicola Mining Inc.
Title	Drills 100.6 
Metres of 1.33% Copper and Reports





    CDNX Symbol: NIM











Press Release





NICOLA MINING INC ("NIM-V;HUSIF-0")
- Drills 100.6 Metres of 1.33% Copper and Reports on the Winter
- Drilling Program at the New Craigmont Project, British Columbia

Nicola Mining Inc. (the "Company" or "Nicola") is pleased to
provide the results of their latest drill hole, as well as a summary of
results on its 2017-2018 Winter Drilling Program (the "Program"). The
Program focused on extending and defining boundaries on the Craigmont
West Zone, previously referred to as the Embayment Zone at the
Company's 100%-owned New Craigmont Project, British Columbia. The name
was changed from "Embayment" to "Craigmont West" to denote the westward
extension of the mineralized skarn zone mined in the historic Craigmont
open pit and underground mine.

The program was designed to target the full width and western
extent of a segment of copper-iron-skarn mineralization believed to be
the continuation of the mineralized zone extending west from the
historic Craigmont Mine. The initial drilling results at Embayment were
reported in news releases dated February 28, 2018, January 12, 2018 and
December 21, 2017. Nicola has since received all results from the
remaining drilling to date.

Hole NC-2018-03 Highlights

//st

* Hole NC-2018-03 intersected the following:
* 100.6 metres at 1.33% Cu including:
* 40.2m at 2.52% Cu
* And 15.0m grading 5.18% Cu

//et

The results have improved the geological understanding of the area
and continue to establish the width and continuity of the Craigmont
West Zone.

Previous Craigmont West Zone Exploration Highlights include:

//st

* *71.4 metres at 0.6% Cu from hole NC-2018-01 (Released Feb. 28, 2018)
including:
* 16m at 1.4% Cu

* *32 metres at 0.3% Cu from NC-2017-01 (Released Dec. 21, 2017)
including:
* 10m at 0.6% Cu

* *85.6 metres at 1.1% Cu from DDH-THU-002 (Released Sept. 7, 2016)
including:
* 13.8m at 2.71% Cu

//et

* indicates results released previously

Peter Espig, CEO commented, "Results from the initial stages of
drilling at Craigmont West have been very encouraging and more drilling
is clearly necessary for advancing the project toward establishing a
resource and exploring west along strike and at depth.  This drilling
has intersected grades and widths comparable to mineralized zones mined
at the historical Craigmont Mine."  Frank Hogel, Chairman commented,
"It is becoming increasingly clear that this is a very special project
and we look forward to providing an explanation on the ongoing
exploration program in a subsequent news release."

Exploration Summary

From September 2017 to February 2018, a total of 8 diamond drill
holes were drilled at Craigmont West, totaling 4436.13 metres (Figure
1). The drill holes were planned as a follow-up to the drilling program
Nicola executed in 2016 which intercepted 85.92 metres of 1.11% Cu in
hole DDH-THU-002. Although the intersection in DDH-THU-002 was
significant in grade and width, the mineralized zone in this hole was
cut-off by the Embayment fault and the true-width potential of the zone
could not be evaluated. The objectives of the 2017-2018 exploration
program were to:

//st

* Successfully intersect and define the full width of the
mineralized skarn zone, particularly between historic holes
S-100 and DDH-THU-002;
* Test the continuity of the zone to the west and at depth; and
* Gain further understanding of the lithologic sequence and its
control on mineralization.

//et

Out of the 8 holes drilled, 6 successfully intersected skarn
mineralization within an approximately 200-metre long segment of the
Craigmont West zone (Table 1), and the final hole NC-2018-03
intersected the entire width of the zone from 292.7 to 393.3 metres
downhole.

The Embayment Fault cuts mineralization where it was exposed in
underground development and displaced the mineralized zone on the west
side of the fault to the north by approximately 300 metres. While the
underground mine was active, underground development was extended to
within 150 metres of the Craigmont West Zone before low copper prices
forced the mine to close in 1988 and exploration ceased.  Exploration
of the Craigmont West Zone, which remains open along strike and at
depth has been the focus of the drilling programs executed by the
Company in 2016 and 2017-2018.

Integration of the recent drilling results with historical data is
on-going by Nicola's geological team.  Once complete, a follow-up drill
program will be designed to expand the mineralization zone encountered
in the current drill program and test other targets identified within
the Craigmont West Zone.

Table 1. Assay Results for Craigmont West Drilling (reported
widths are based on a vertically dipping zone; however, data is
insufficient at this time to reliably determine the orientation of the
mineralized zone).

** Assumes the Craigmont West zone is vertical

To view an enhanced version of Table 1. Assay Results for Craigmont West
Drilling, please visit:
[http://orders.newsfilecorp.com/files/4873/33798_a1522675806187_91.jpg]

Figure 1. Location map of Nicola's Craigmont West drilling.

To view an enhanced version of Figure 1. Location map of Nicola's Craigmont
West drilling, please visit:
[http://orders.newsfilecorp.com/files/4873/33798_a1522675806421_65.jpg]

The Craigmont Skarn Zone: East, Central and West

Since beginning drilling in 2016, Nicola has successfully traced
the Craigmont Skarn Zone for approximately 1km west and 2km east of the
Craigmont Pit (Figure 2). It is now believed that this east-west
corridor is one continuous mineralized system. Therefore, Nicola has
decided to change the naming convention to Craigmont East, Central and
West. The Company believes the revised names are more appropriate for
identifying segments along the continuous skarn alteration and
mineralization zone rather than referring to seemingly isolated
entities. Craigmont West extends from NC-2017-04 east to the Embayment
Fault. Within Craigmont West lies the former "Embayment Zone".
Craigmont Central is defined to the west by the Embayment fault and to
the east by the eastern extent of the Craigmont waste dumps. It
encompasses the historic open pit and the majority of historic
underground mine workings. Craigmont East extends eastward from the
limit of the Waste Dumps to the Eric showing.

Figure 2. Location and geology of the New Craigmont Property
identifying Craigmont East, Central and West.

To view an enhanced version of Figure 2. Location and geology of the New
Craigmont Property, please visit:
[http://orders.newsfilecorp.com/files/4873/33798_a1522675806609_43.jpg]

Scientific and Technical Information

All information of a scientific or technical nature contained in
this document, including sampling, analytical and test data has been
reviewed and approved by Kevin Wells, P. Geo., a consulting Geologist
to the Company. Mr. Wells is a Qualified Person as defined by National
Instrument 43-101 -- Standards of Disclosure for Mineral Projects.

Sample Preparation, Analysis and Quality Assurance/Quality Control


Nicola Mining applies a thorough quality assurance/quality control
program at the New Craigmont Project compliant with industry best
practices. A qualified geoscientist has logged and sampled all core and
samples have been delimited according to lithologic, alteration and
mineralization characteristics. This includes systematic insertion of
blank, duplicate, and certified reference materials into the sample
batches by Nicola's geological staff. Core is then halved, where the
sample is placed in a labelled sample bag with sample tag and the other
half of the core is retained on site as a physical record. Samples are
placed in sealed bags and transported to Actlabs (ISO 17025 Certified)
in Kamloops, British Columbia for analysis, following a Chain of
Custody. Samples are crushed up to 80% passing 2mm, rifle split (250 g)
and pulverized to 95% passing 105 m. Samples are analyzed using Fire
Assay (1A2) and Aqua Regia-ICP-OES 38-element (1E3) packages. All
samples greater than 10,000 ppm Copper are tested using over-limit mass
spectrometry methods (8-AR). All results included in this release have
passed the QA/QC procedures as described above and have been reviewed
by Kevin Wells, P.Geo. There are no known factors that could materially
affect the reliability of data collected and verified. No quality
assurance/quality control issues have been identified to date.

About Nicola Mining

Nicola Mining Inc. is a junior mining company listed on the TSX
Venture Exchange and is in the process of recommencing mill feed
processing operations at its 100% owned state-of-the-art mill and
tailings facility, located near Merritt, British Columbia. It has
already signed four mill profit share agreements with high grade gold
producers. The fully-permitted mill can process both gold and silver
mill feed via gravity and flotation processes. The Company also owns
100% of Treasure Mountain, its high-grade silver property, and an
active gravel pit that is located adjacent to its milling operations.

On behalf of the Board of Directors

"Peter Espig"
Peter Espig
CEO & Director

For additional information

Contact: Peter Espig
Phone: (778) 385-1213
Email: info@nicolamining.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 604-647-0142    NICOLA MINING INC
FAX: 604-647-0143
E-mail: ir@nicolamining.com
Website: http://www.nicolamining.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809100028TS11809101188-08171220180402