Source	Marketwire
Date	05/08/2014
Time	06:00:20 AM

Company	 NEWMARKET GOLD INC.
Title	Newmarket Completes Diamond Drillling Program at the Point Leamington 
Gold-Rich Massive Sulphide Deposit, Newfoundland





    CDNX Symbol: NGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Newmarket Gold Inc.

TSX VENTURE SYMBOL: NGN

May 8, 2014

Newmarket Completes Diamond Drillling Program at the Point Leamington Gold-Rich 
Massive Sulphide Deposit, Newfoundland


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 8, 2014) - Newmarket Gold Inc. 
(the "Company" or "Newmarket") (TSX VENTURE:NGN) announces that it has 
completed drilling, sampling and assaying of diamond drill core samples from 
its 100% owned Point Leamington gold-zinc-silver-copper-lead massive sulphide 
deposit located in north-central Newfoundland, Canada (the "Project"). The 
drill samples will be used to create a composite for metallurgical testing.

Highlights

/T/

--  Drilling intersected up to 40 metres of massive sulphide mineralization
and returned a number of intercepts including 13.38 metres grading 2.5
g/t Au, 2.44% Zn and 0.90% Cu (PL14-079) and 10.57 metres grading 1.0
g/t Au, 4.60% Zn and 0.39% Cu (PL14-078)

/T/

A total of 259 metres in two diamond drill holes (PL14-078 - 116 metres and 
PL14-079 - 143 metres) were completed. Each drill hole intersected an average 
of approximately 40 metres of massive sulphides.

Results for massive sulphide intervals from the 2014 Point Leamington drill 
program include;

/T/

----------------------------------------------------------------------------
DDH                 from      to      m  Au g/t  Ag g/t   Cu %   Pb %   Zn %
----------------------------------------------------------------------------
----------------------------------------------------------------------------
PL14-078           45.97   48.21   2.24   0.386    19.8   0.36   0.04   3.00
PL14-078           50.71   67.30  16.59   0.601    19.0   0.36   0.11   2.56
PL14-078           76.04   86.61  10.57   1.023    26.5   0.39   0.10   4.60
PL14-078           95.00  105.37  10.37   0.374     7.4   1.89   0.01   0.19
PL14-078          112.00  116.00   4.00   0.499    15.0   1.69   0.01   0.73
PL14-079           49.90   59.23   9.33   0.479    20.7   0.32   0.19   3.23
PL14-079           67.16   76.67   9.51   0.357    15.0   0.73   0.01   2.32
PL14-079           80.80   87.11   6.31   0.998     9.4   0.35   0.01   0.74
PL14-079           92.58  102.00   9.42   1.025    16.0   1.41   0.07   1.25
PL14-079          107.96  121.34  13.38   2.519    16.2   0.90   0.07   2.44
PL14-079          125.00  132.00   7.00   0.634    10.4   0.01   0.07   0.13
----------------------------------------------------------------------------

1.  Length weighted averages of uncut assays and analyses.
2.  Analyses completed at ACME Analytical, Vancouver, B.C.
3.  Results passed QA/QC including the insertion of blanks and standards and
sample duplicates.

/T/

A total of 154 samples (excluding QA/QC samples) were collected and shipped to 
ACME Labs (A Bureau Veritas Group Company) of Vancouver, B.C., an ISO Certified 
Facility, for analyses. Samples were analyzed for gold by fire assay and a 
further 24 elements including copper, lead, silver and zinc by aqua regia 
digestion and ICP-ES analysis.

A composite sample is being prepared which approximates the average grade of 
the existing resource. Metallurgical testwork will be completed by the 
Metallurgical Division of Inspectorate Exploration and Mining Services of 
Richmond, British Columbia.

The metallurgical testwork will consist of a series of metallurgical scoping 
tests designed to study the potential for copper, zinc and precious metal 
recovery by flotation. Previous work since 1972 had focused on recovering only 
one product at a time, depending on the samples tested. The current work will 
study the recovery of all potentially economic minerals using a sequential 
flotation circuit in which a series of concentrates are recovered in sequential 
stages. An alternative bulk flotation method will also be tested.

The technical content in this news release was reviewed and approved by Gregory 
Smith, P.Geo, a technical consultant for the Company who is the Qualified 
Person as defined by NI 43-101.

About Newmarket Gold Inc.

Newmarket Gold Inc. is a Canadian gold company focused on creating shareholder 
value through the acquisition of quality gold production opportunities and 
outstanding development stage assets in mining friendly, politically stable 
jurisdictions world-wide. The Company was founded by an experienced group of 
dealmakers, mine developers, financiers and capital markets professionals and 
is focused on a disciplined approach to asset acquisition and growth.

ON BEHALF OF THE BOARD

Douglas Forster, M.Sc., P.Geo., President and CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Newmarket Gold Inc.
Douglas Forster
President & CEO
604-559-8040
dforster@newmarketgoldinc.com
www.newmarketgoldinc.com

INDUSTRY: Computers and Software - Software, Media and Entertainment - 
Information Services
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=480793102