Source	MARKET NEWS
Date	05/14/2014
Time	06:32:08 AM

Company	 Great Bear Resources Ltd.
Title	New 
Sediment Hosted Oxide Gold, Copper and Polym





    CDNX Symbol: GBR











Press Release	





GREAT BEAR RESOURCES LTD. ("GBR-V")
- New Sediment-Hosted Oxide Gold, Copper and Polymetallic Targets
- Identified at Perdito Project

Great Bear Resources Ltd. ("Great Bear", or the "Company") is
pleased to announce that it has identified multiple sediment-hosted
oxide gold, copper and polymetallic targets at its Perdito project,
Inyo County, California, where the Company has an option to earn a 100%
interest.

The Company further reports that it has received favorable
feedback from the Bureau of Land Management (BLM) regarding its Phase 1
drill permit. The Company will not be required to complete either
archaeological or faunal surveys but is required to complete a
botanical survey of the proposed drill sites, which is now underway.
The company expects to receive its drill permit after review of the
survey findings by the BLM.

While the Company's main focus remains the oxide gold system
previously drilled by Newmont Mining Corp. (NYSE: NEM, "Newmont") and
BHP Ltd. (NYSE: BHP) on the eastern half of its main claim block, the
Company is also investigating the 20 square km area that comprises the
western half of the claim block, previously the focus of exploration by
Asamera Minerals Inc. ("Asamera"). Findings from recent field work in
this western area by GBR include:

-Discovery of new sediment-hosted oxide gold targets and
confirmation of previously drilled targets. Highlights include channel
sampling of 10.7 m (35 ft) of 1.73 g/t (0.05 oz/st) Au.

-Identification of porphyry style veining, alteration and related
copper-silver+/-gold mineralization. Highlights include composite grab
samples returning up to 15.29% Cu and 106 g/t (3.10 oz/st) Ag.

-Polymetallic mineralization including
silver-lead+/-gold+/-zinc+/-copper in a peripheral halo to the porphyry
style veining and alteration. Highlights include composite grab samples
returning 0.51 g/t (0.05 oz/st) Au, 805 g/t (23.48 oz/st) Ag, 0.39% Cu
and 2.60% Pb.

Work carried out from December 2013 to April 2014 on the western
half of the main claim block included collection of 100 channel and
grab samples, and mapping and interpretive work by two internationally
recognized porphyry experts. Highlights are provided in Table 1.

//st



---------------------------------------------------------------------------
|SAMPLE|Au   |Au     |Ag    |Ag     |Cu   |Pb   |Zn  |TYPE      |HOST
|      |(g/t)|(oz/st)|(g/t) |(oz/st)|(%)  |(%)  |(%) |          |
|--------------------------------------------------------------------------
|SV-3  |0.16 |0.005  |3.90  |0.11   |0.03 |0.01 |0.01|5' Channel|Limestone
|--------------------------------------------------------------------------
|SV-56 |0.01 |0.000  |1.83  |0.05   |2.93 |0.00 |0.00|3' Channel|Limestone
|--------------------------------------------------------------------------
|SV-58 |0.74 |0.021  |15.00 |0.44   |0.31 |0.03 |0.02|Float     |-
|
|--------------------------------------------------------------------------
|SV-65 |0.00 |0.000  |26.18 |0.76   |0.03 |4.54 |0.01|Comp. Grab|Qz Vein
|--------------------------------------------------------------------------
|SV-68 |1.73 |0.050  |2.18  |0.06   |0.01 |0.02 |0.03|35'       |Siltstone
|      |     |       |      |       |     |     |    |Channel   |
|--------------------------------------------------------------------------
|SV-72 |2.84 |0.083  |0.21  |0.01   |0.00 |0.00 |0.01|15'       |Sandstone
|      |     |       |      |       |     |     |    |Channel   |
|--------------------------------------------------------------------------
|SV-75 |0.05 |0.001  |5.04  |0.15   |7.36 |0.00 |0.02|6' Channel|Porphyry
|--------------------------------------------------------------------------
|SV-76 |0.03 |0.001  |69.26 |2.02   |1.10 |0.01 |0.02|Comp. Grab|Qz Vein
|--------------------------------------------------------------------------
|SV-77 |0.05 |0.002  |1.84  |0.05   |0.15 |0.00 |0.00|4' Channel|Porphyry
|--------------------------------------------------------------------------
|SV-78 |0.03 |0.001  |67.49 |1.97   |2.18 |0.00 |0.01|Comp. Grab|Limestone
|--------------------------------------------------------------------------
|SV-83 |0.21 |0.006  |32.66 |0.95   |3.02 |0.03 |0.04|Comp. Grab|Limestone
|--------------------------------------------------------------------------
|SV-84 |0.51 |0.015  |805.00|23.48  |0.39 |2.60 |0.10|Comp. Grab|Qz Vein
|--------------------------------------------------------------------------
|SV-85 |0.13 |0.004  |0.42  |0.01   |0.01 |0.00 |0.01|30'       |Siltstone
|      |     |       |      |       |     |     |    |Channel   |
|--------------------------------------------------------------------------
|SV-100|0.02 |0.001  |107.00|3.12   |0.02 |4.44 |1.25|Comp. Grab|Bx'd
|      |     |       |      |       |     |     |    |          |Diorite
|--------------------------------------------------------------------------
|SV-109|0.02 |0.000  |314.00|9.16   |0.04 |9.01 |4.55|4' Channel|Bx'd
|      |     |       |      |       |     |     |    |          |Diorite
|--------------------------------------------------------------------------
|SV-110|0.01 |0.000  |304.00|8.87   |0.08 |13.05|4.15|3' Channel|Bx'd
|      |     |       |      |       |     |     |    |          |Limestone
|--------------------------------------------------------------------------
|SV-111|0.02 |0.001  |773.00|22.55  |0.02 |27.61|1.56|Comp. Grab|Bx'd
|      |     |       |      |       |     |     |    |          |Limestone
|--------------------------------------------------------------------------
|SV-118|0.00 |0.000  |952.00|27.77  |0.04 |29.09|1.95|Comp. Grab|Bx'd
|      |     |       |      |       |     |     |    |          |Diorite
|--------------------------------------------------------------------------
|SV-145|1.98 |0.058  |0.39  |0.01   |0.00 |0.00 |0.01|5' Channel|Siltstone
|--------------------------------------------------------------------------
|SV-148|6.13 |0.179  |2.58  |0.08   |0.00 |0.02 |0.07|3' Channel|Limestone
|--------------------------------------------------------------------------
|SV-149|1.35 |0.039  |0.75  |0.02   |0.00 |0.01 |0.03|6' Channel|Diorite
|--------------------------------------------------------------------------
|SV-153|0.05 |0.001  |27.57 |0.80   |0.47 |0.01 |0.01|4' Channel|Limestone
|--------------------------------------------------------------------------
|SV-154|0.22 |0.006  |247.40|7.22   |14.74|0.13 |0.21|Comp. Grab|Limestone
|--------------------------------------------------------------------------
|SV-155|0.13 |0.004  |62.74 |1.83   |1.62 |0.05 |0.07|4' Channel|Limestone
|--------------------------------------------------------------------------
|SV-156|0.05 |0.001  |106.40|3.10   |15.29|0.06 |0.09|Comp. Grab|Limestone
|--------------------------------------------------------------------------
|SV-157|1.90 |0.056  |144.80|4.22   |0.83 |0.03 |0.10|15'       |Limestone
|      |     |       |      |       |     |     |    |Channel   |
|--------------------------------------------------------------------------
|SV-159|0.06 |0.002  |25.58 |0.75   |2.15 |0.04 |0.05|4' Channel|Siltstone
|--------------------------------------------------------------------------
|AW004 |0.02 |0.001  |8.04  |0.23   |0.01 |0.10 |0.07|Comp. Grab|Limestone
---------------------------------------------------------------------------

//et

Table  @ 1: Highlights of sampling results from across the western
half of the main claim block. "Bx'd" refers to hydrothermal
brecciation. Channel samples in ft.

About 25% of the mapped area consists of various porphyritic to
equigranular dikes, sills and stocks of presumed Jurassic to Cretaceous
age, showing various styles of alteration and mineralization. The large
number of intrusive bodies distinguishes the area from the Newmont and
BHP area to the east, where mineralization is exclusively sediment
hosted.

The Company is currently working with its consultants to
reinterpret the zoned mineralization patterns that have been discovered
across an approximately 2.5 km by 6.5 km (16 sq km) area, and will
report results work when available. Preliminary review suggests the
patterns are broadly consistent with the upper levels of at least one
porphyry and/or skarn target at modest depth.

A summary of historic work was provided in Great Bear's news
release of April 18, 2013. More than 100 drill holes were completed on
the western half of the main claim block by Asamera in the 1980's,
however original data is sparse and in many cases only highlighted
values in historic reports are available. In most cases the reported
intervals include high cutoff values of about 1 g/t gold, and lack
multi-element analysis including copper and silver. Nonetheless, gold
mineralization has been drill confirmed in three areas across five
kilometers of strike. Highlighted results of that drilling are
presented in Table 2.

//st

----------------------------------------------
|Drill   |From|To  |Width|Width|Gold   |Gold |
|Hole    |(ft)|(ft)|(ft) |(m)  |(oz/st)|(g/t)|
|--------------------------------------------|
|SR-09   |250 |270 |20   |6.1  |0.152  |5.21 |
|--------------------------------------------|
|SR-15   |150 |165 |15   |4.6  |0.167  |5.73 |
|--------------------------------------------|
|SR87 C-3|258 |280 |22   |6.7  |0.253  |8.67 |
|--------------------------------------------|
|DG-1    |31  |76  |45   |13.7 |0.025  |0.86 |
|--------------------------------------------|
|DG-5    |46.5|57.3|10.8 |3.3  |0.051  |1.75 |
|--------------------------------------------|
|SC-3    |0   |64  |64   |19.5 |0.025  |0.86 |
|--------------------------------------------|
|SC-8    |25  |30  |5    |1.5  |0.253  |8.67 |
----------------------------------------------

//et

Table  @ 2: Highlighted historic drill results from the western
half of the Company's main claim block as reported in historic Asamera
reports

Mr. Chris Taylor, M.Sc. P.Geo, is the Qualified Person as defined
by National Instrument 43-101 responsible for the accuracy of this news
release.

For further information please contact Mr. Chris Taylor at
604-681-0037.

"Chris Taylor"

Chris Taylor, President and CEO

Inquiries:

Tel: 604-681-0037

Fax: 604-681-0094

info@greatbearresources.ca

www.greatbearresources.ca

About Great Bear

Great Bear is a well-funded Canadian precious metals exploration
company working in leading jurisdictions of Canada and the United
States. A 100% interest can be obtained in the Perdito oxide gold
project, California, and a 70% interest can be obtained in the BA
silver-rich VMS project, Eskay Creek District, northern British
Columbia.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy o this release.



This new release may contain forward-looking statements. These
statements are based on current expectations and assumptions that are
subject to risks and uncertainties. Actual results could differ
materially because of factors discussed in the management discussion
and analysis section of our interim and most recent annual financial
statement or other reports and filings with the TSX Venture Exchange
and applicable Canadian securities regulations. We do not assume any
obligation to update any forward-looking statements.

We seek safe harbor




__________________________________________________
_______________________________________________
TSX Venture closing price for GBR-V
Date: 2014/05/08
Closing Price: 0.09
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1413300018TS11413301139-06311020140514