Source	MARKET NEWS
Date	05/14/2014
Time	01:19:27 PM

Company	 Tosca Mining Corp.
Title	Completes 
Initial Drilling on Carol Copper Proje





    CDNX Symbol: TSQ











Press Release	





TOSCA MINING CORP ("TSQ-V;TSMNF-0")
- Completes Initial Drilling on Carol Copper Project

Tosca Mining Corp. announces that it has completed an initial
drill program on its Carol Copper project located in southern Sonora
State, Mexico.  The program consisted of six HQ size angled drill holes
(-50 degree to -60 degrees) totaling 577 metres, that was designed to
investigate the continuity and potential extent of skarn mineralization
encountered in trenches and outcrop (see news release January 27,
2014).
The six holes focused on the Balde Sur area and tested the
shallowly dipping metasedimentary sequence over a distance of
approximately one kilometre.  All holes encountered interbedded zones
of moderately to intensely altered skarn, quartzite and
dolomite/limestone, often highly fractured and brecciated.
Samples will be submitted to Inspectorate Labs in Hermosillo and
will be analyzed for a multi element ICP package that includes copper,
zinc and silver as well as gold by fire assay. Results will be released
when available.
About the Carol Copper Project
The Carol Copper project covers over 750 hectares and is located
in southern Sonora State, Mexico. It is approximately five km northeast
of the producing Piedras Verdes copper mine, Mexico's third largest.
Operated by Cobre del Mayo SA de CV, the mine produces over 70 million
pounds of copper annually at a cash cost of $1.62 per pound (Cobre del
Mayo presentation, October, 2013).  At Carol, polymetallic
(copper-silver-zinc-gold) skarn mineralization has been outlined in two
mineralized zones: one measuring 1,100 meters by 400 meters and the
second 700 meters by 180 meters.
Tosca has the right to acquire a 100 percent interest in the Carol
project under an option agreement further described in its Oc. 14,
2013, news release.
Ian Foreman, P.Geo., president of Alta Vista Ventures and
independent to Tosca, is the Qualified Person, as defined by NI 43-101,
for the Carol Project and is responsible for the technical information
in this news release.



On behalf of the Board of Directors,

Ron Shenton

President & CEO

Tosca Mining Corp.



Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.



Statements in this press release, other than purely historical information,
including statements relating to the Company's future plans and objectives
or expected results, may include forward-looking statements.
Forward-looking statements are based on numerous assumptions and are
subject to all of the risks and uncertainties inherent in resource
exploration and development. As a result, actual results may vary
materially from those described in the forward-looking statements.
______________________
_______________________________________________
TSX Venture closing price for TSQ-V
Date: 2014/05/13
Closing Price: 0.05
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1413300051TS11413302710-13172020140514