Source	MARKET NEWS
Date	05/22/2014
Time	07:08:12 AM

Company	 CB Gold Inc.
Title	Average Combined 
Gravity Flotation Gold And Silv





    CDNX Symbol: CBJ











Press Release	





CB GOLD INC ("CBJ-V")
- Average Combined Gravity Flotation Gold And Silver Recoveries
- Of 88.6% And 81.4%, Respectively From Additional Metallurgical
- Results For Its Vetas Gold Project

CB Gold Inc. ("CB Gold"or the "Company") is very pleased to report
additional positive results from its second run of metallurgical
testwork on material from the Company's Vetas Gold project. The results
confirm the excellent recovery for gold and silver. The 40 Vetas ore
samples tested responded well to the gravity-flotation process,
achieving combined average recoveries of 88.6% Au and 81.4% Ag, with a
large portion of the samples reporting Au recoveries in the high 90%
range and up to 99.8%.

A laboratory testing program was conducted on forty (40) drill
core samples collected by CB Gold from their Vetas Gold project to
determine their amenability to gold and silver recovery via centrifugal
gravity concentration followed by sulphide flotation processes. The
samples were selected from various areas and drill holes so as to be as
representative of the deposit as possible. The tests were conducted
using the optimized process conditions from the 2013 test work program.


The results from the 2014 testing indicate:

//st

Combined gravity / flotation concentrate recoveries of up to 99.8%;

Recoveries of up to 91.4%+ for traditional gravity gold recovery;

Strong recoveries occurred at relatively coarse grind sizes of
P(sub)80(/sub) 100 microns;

The Vetas samples were not found to be sensitive to grind size with
respect to metal recoveries;

Sulphur concentration was found to be proportional to overall metal
recovery;

//et

For further information the reader is directed to CB Gold's
website at www.cbgoldinc.com where the metallurgical testing reports
entitled "Project Report For Metallurgical Testing on Samples From the
CB Gold Inc Vetas Gold Project, August 7th, 2013" and "Metallurgical
Testing On 40 Drill Core Samples From the Vetas Gold Project, May 16th,
2014" can be found.
Fabio Capponi, CEO, commented, "We are very pleased with
the additional test results which not only confirms the strong
recoveries for gold and silver throughout the deposit but even more the
processing options, including the possibility to produce a high-grade
concentrate for direct smelting. The Company will advance with
additional metallurgical testwork as may be required by the different
processing options".

Gravity-Flotation Test Methodology

The gravity-flotation tests were carried out to evaluate the
variability between each of the Vetas samples' response to this method
of recovering gold and silver. The grind size target used for these
tests was P80 100 m, which was determined in the previous test program
to be optimal. A grind time of 20 minutes was used for each sample to
provide data on the variability of ore hardness between the samples.

For each test, a 2 kg ground sample was pulped to 20% solids and
fed through a 3" laboratory Knelson concentrator. The concentrate from
the first pass was cleaned by panning, and the pan tails were combined
with the first-pass tails and run through the Knelson for a second
pass. The pan concentrates from both passes were assayed for Au and Ag.


Rougher-cleaner flotation tests were conducted on the combined
second-pass Knelson tails and second pan tails to recover precious
metals that are associated with the sulphide minerals. Each test
consisted of four (4) rougher stages followed by two stages of
cleaning. All tests were run at pH ~8 and used Potassium Amyl Xanthate
(PAX) and Aeropromoter 208 as collectors, along with frother methyl
isobutyl carbinol (MIBC).

Gold recovery data is provided in the following table:

//st



Gold
Grade, g/t Au                     Gold Recovery, %           Recovery
----------------------------------------  ---------------------------------

Flotation                          Flotation

-----------------------            -----------------------
P80   Sulphur
Test                                      Size  Grade,   Meas.   Gravity
No       Drill Hole     From(m)  To(m)   (mm)     %     Head     Conc.
-----   --------------   -------  ------  ----  -------  -----  --------
GF1      RM-DDH12-119      98.20  100.25    79     1.08   0.55     175.5
GF2      RM-DDH12-119     123.12  125.39    99     1.76  18.41    1024.5
GF3      RM-DDH12-119     160.11  164.00    73     2.01   4.75    2293.9
GF4      RM-DDH11-046     124.48  127.00    67     2.54   0.90      84.2
GF5      RM-DDH12-110     222.67  226.48    84     2.74   3.51     222.9
------   ---------------  -------  ------  ----  -------  -----  --------
GF6      RM-DDH12-113     101.75  103.04    68     0.62   0.50     223.8
GF7      RM-DDH12-113     438.10  441.06   103     1.26   1.23     103.0
GF8      RM-DDH12-117     318.20  321.08   113     3.05   0.48      20.6
GF9      SI-DDH12-116      61.68   64.11    80     4.65   2.14     137.4
GF10     ED-DDH11-028      80.00   81.88   111     3.30   1.29     215.2
------   ---------------  -------  ------  ----  -------  -----  --------
GF11     ED-DDH11-028     362.00  363.70   116     3.53   1.52      36.6
GF12     ED-DDH11-032     419.85  421.85    86     3.82   2.04     108.7
GF13     AR-DDH11-039     164.73  166.15    81     4.17   2.87      60.2
GF14     AR-DDH11-041      54.50   56.85    88     4.35   1.71      17.3
GF15     LD-DDH11-051     124.41  127.73   140     5.17   4.59     129.6
------   ---------------  -------  ------  ----  -------  -----  --------
GF16     LD-DDH11-054     162.10  164.00   165     6.14   4.21     176.9
GF17     RM-DDH13-161     139.79  143.60    91     3.20   4.43    1665.2
GF18     RM-DDH13-159     159.27  161.54    95     1.84   1.42     532.5
GF19     RM-DDH13-158     257.50  259.50    83     2.01   1.97     107.3
GF20     RM-DDH13-156      75.40   78.19    61     0.57   2.36     731.5
------   ---------------  -------  ------  ----  -------  -----  --------
GF21     RM-DDH13-156     269.30  272.70    86     0.98   1.77   13342.8
GF22     RM-DDH13-154     155.00  158.01    83     3.32   2.45      48.8
GF23     RM-DDH13-152      83.47   86.31    90     0.48   0.70      25.8
GF24     RM-DDH13-152     143.90  147.90    83     3.63   1.62     529.6
GF25     RM-DDH12-143     105.30  107.00    78     0.57   2.37      55.5
------   ---------------  -------  ------  ----  -------  -----  --------
GF26     RM-DDH12-141      96.80   99.15    76     1.83   3.05    2113.1
GF27     RM-DDH12-139     163.35  165.16    75     1.55   1.32    1249.8
GF28     RM-DDH12-137     209.70  211.73    79     1.13   0.08    1046.7
GF29     RM-DDH12-135      71.25   73.64    49     0.38   2.32    3011.5
GF30     LD-DDH12-133      53.96   57.30   125     3.82   1.33      72.9
------   ---------------  -------  ------  ----  -------  -----  --------
GF31     RM-DDH12-130      74.15   77.15    44     0.35   1.21     666.6
GF32     SI-DDH12-127      85.69   87.78   143     2.66   3.63     449.4
GF33     RM-DDH12-126      99.65  102.10    72     1.50   8.42     109.3
GF34     SI-DDH12-086      78.50   81.45   159     4.51   2.37     102.3
GF35     SI-DDH12-086     122.36  124.15    94     5.94   4.62     588.0
------   ---------------  -------  ------  ----  -------  -----  --------
GF36     SI-DDH12-114      89.02   91.55   204     2.15   3.82      41.0
GF37     RM-DDH12-088      82.42   84.66    94     0.82  30.68   27333.6
GF38     SI-DDH12-105     134.70  139.70    96     1.93   1.55     170.6
GF39     ED-DDH12-106A    321.43  324.80   119     3.01   5.16    1810.1
GF40     RM-DDH12-113     241.60  243.92    95     2.40   1.22     593.8
------   ---------------  -------  ------  ----  -------  -----  --------
//et

The test results indicate average combined gravity-flotation gold
and silver recoveries of 88.6% and 81.4%, respectively. Gravity gold
recovery among the 40 samples tested averaged 27.3%, but varied greatly
between 1.5% and 91.4% and produced an average concentrate grade of
1,535.7 g/t. It was found that in general the samples that reported the
highest gravity gold recoveries were also the most weathered (contained
less sulphur).
Similarly, the samples which contained the highest sulphur content
also reported the highest flotation recoveries. There was no clear
correlation between metal head grades and gravity or overall
recoveries; however the samples with the highest head grades did report
consistently high overall recoveries.

The results of the 2014 metallurgical testing program were very
positive and are in line with expected results based on the 2013
preliminary testwork.

About CB Gold Inc.:

CB Gold is a mineral exploration company headquartered in
Vancouver, British Columbia. CB Gold, through its wholly-owned
subsidiary, Leyhat Colombia Sucursal, is actively pursuing the
exploration and development of mineral properties in the Republic of
Colombia. The Vetas Gold Project consists of a number of previously
operating mines and exploration concessions.

For more information on CB Gold please visit our web site at
www.cbgoldinc.com or contact +1 (604) 630-5870, or info@cbgoldinc.com.

Neither the TSX Venture Exchange nor its Regulation
Services Provider (as that term is defined in the policies of the TSX
Venture Exchange) accepts responsibility for the adequacy or accuracy
of this news release.

The securities of CB Gold described herein have not been
and will not be registered under the United States Securities Act of
1933, as amended (the "U.S. Securities Act")          or any state
securities laws and may not be offered or sold within the United States
or to U.S. Persons unless registered under the U.S. Securities Act and
applicable state securities laws or an exemption from such registration
is available.

Some of the statements contained in this release are
forward-looking statements, such as estimates and statements that
describe the Company's future plans, objectives or goals, including
words to the effect that the Company or management expects a stated
condition or result to occur. Since forward-looking statements address
future events and conditions, by their very nature, they involve
inherent risks and uncertainties. Actual results in each case could
differ materially from those currently anticipated in such statements.

TSX Venture closing price for CBJ-V
Date: 2014/05/21
Closing Price: 0.12

TEL:  +1 (604) 630-5870 CB Gold Inc.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1414100036TS11414101519-07054020140522