Source	MARKET NEWS
Date	05/22/2014
Time	07:32:36 AM

Company	 Codrington Resource Corporation
Title	Mercury 
Free Gold Test Production to Begin at Gr





    CDNX Symbol: CA











Press Release	





CODRINGTON RESOURCE CORP ("CA-V")
- Mercury Free Gold Test Production to Begin at Groete
- Gold Copper Project

The Company is providing an update on activities at the Groete
Gold Copper Project, Guyana, South America. The project is comprised of
three Mining Permits, which allow the exploitation of the project in
compliance with the Mining Act of 1989 ( Guyana ). The project has a 50
year history of past alluvial production, with many historical pits
over a two mile zone. Over the past six months, management has focused
attention on designing and developing a small scale gold recovery
operation on site. The zone of interest was identified during a 52 hole
Geoprobe deep soil sample program during 2012. The gold zone measures
approximately 150 meters north south and 250 meters east west, with
significant mineralization beginning at surface. Select results within
the zone include hole DH3 which returned 2.65 grams per tonne (gpt) (
4.77 grams gold per cubic yard ) Au over its entire 8.75 meter length,
hole R1H5ST4 averaged 1.24 gpt Au( 2.23 grams gold per cubic yard )
over its entire 9 meter length, R3H6ST2 which averaged 0.912 gpt Au (
1.63 grams gold per cubic yard ) over its entire 10 meter length, and
R1H5 which averaged 0.89 gpt Au ( 1.6 grams gold per cubic yard ) over
its entire 9 meter length( All assay work was completed in 2012 by
Lorings Labs of Georgetown Guyana ). These select holes represent
higher values within the identified zone, and demonstrate the
variability of grade within the zone. The objective will be to recover
an average grade of 0.5 grams gold per cubic yard processed. The target
production rate is 500 cubic yards per day, within a 25 day working
month.
Mercury has long been associated with the concentration of gold in
Guyana. Its widespread use has become an environmental issue in the
country, and around the world where artisanal mining is common
practice. The United States as of 2008 restricted the use of mercury by
enacting the Mercury Export Ban. Other countries have followed this
practice, but mercury is still used on a wide scale in Guyana.
Codrington Resource Corporation will be testing an extraction system
designed to concentrate the free gold without the use of mercury, nor
any other toxic chemical. The test plan of the operation will involve
the transportation of 1,000 gallons per minute of water via an eight
inch pipeline, over a 2,000 foot distance, to a gold zone identified by
prior Geoprobe drilling. Engineering work for the water transportation
was completed by Jones Engineers Inc., of Bellingham Washington. The
zone of interest is measured at 200 meters by 150 meters of surface
gold mineralization.
At the gold zone, a slurry will be created from the water flow and
pumped to a recovery site via a large gravel pumping system
manufactured locally to company specifications. Gold concentration will
be completed utilizing a Global Mining Solutions GMS 2DST Gravity
Shaker Table that can process up to 4 tons per hour of -200 sand size
material. Global Mining Solutions is a leader in gravity extraction
solutions for the mining industry, with more information available at
www.globablminingsolutions.com. The Company has all production
equipment on site including two CL320 excavators and a D6 bulldozer for
this operation. Some equipment is undergoing rehabilitation in advance
of service, and the shaker table will be located on site when the hose
has cleared and is ready for shipment. The operation is expected to
begin a test phase in June.
Codrington Resource Corporation is the 100% owner of the Groete
Gold Copper Project, located in Guyana, S.A. The project is very well
located for development, and contains a National Instrument 43-101
compliant in-pit Inferred Resource of 1.59 million ounces at 0.66 grams
per tonne gold equivalent (AuEq) including 0.49 g/t Au and 0.12% copper
(Cu) contained in 74.8 million tonnes. A global sensitivity to the
in-pit resource estimate (inside plus outside of pit) was calculated to
be 2.0M AuEq ounces at 0.64 g/t AuEq including 0.47 g/t Au and 0.11% Cu
contained in 97.4 M tonnes . All work was completed in 2013 by P and E
Mining Consultants Inc. of Ontario, Canada. A company press release of
January 24, 2013 contains all relevant details and values used in the
calculation of this resource. Recent metallurgical evaluation completed
by SGS Laboratories Canada Inc. on samples from the Groete Gold Copper
project returned 82.4 % recovery for gold and 96.6% recovery for copper
in floatation tests.( readers are referred to the applicable press
releases ).
During the test period, any technical issues will be addressed,
and the work flow will be standardized. Upon completion of a successful
test period, management intends to establish a profitable small scale
gold operation at the Groete Gold Copper Project, so that the Company
can become self- sustaining during the current down cycle in gold
exploration financing. The permits allow the production of up to 1,000
cubic yards per day of material per claim.
To avoid further dilution, the Company will not proceed with the
previously announced private placement, but await results from the
surface test operation before considering further financing options.
Development costs have been financed by loans to the Company from key
management. The Company intends to file its first quarter on May 28th,
with further details provided within the Management Discussion and
Analysis.
Contents of this press release have been reviewed by Dr.
A.D.Drummond, P.Eng., a director of the company and a qualified person
as defined under NI 43-101.

On Behalf of the Board of Directors of Codrington Resource Corporation,
Adrian F.C.Hobkirk
President and Chief Executive Officer
US Exploration Office: 2450 Newmarket St, Ste 101-221 Bellingham, WA, USA
98226
ahobkirk@resourceexploration.com
direct: 714-316-3272

The TSX Venture Exchange has not reviewed the content of this News Release
and therefore does not accept responsibility or liability for the adequacy
or accuracy of the contents of this News Release. This news release
contains certain "forward- looking statements" within the meaning of
Section 21E of the United States Securities and Exchange Act of 1934, as
amended. Except for statements of historical fact relating to the Company,
certain information contained herein constitutes forward- looking
statements. Forward-looking statements are based upon opinions and
estimates of management at the date the statements are made, and are
subject to a variety of risks and uncertainties and other factors which
could cause actual results to differ materially from those projected in the
forward looking statements. The reader is cautioned not to place undue
reliance on forward-looking statements. The test phase for gold production
described in this News Release is subject to a variety of conditions and
risks which include but are not limited to: regulatory approval, equipment
failure, supply and logistic delays, legal due diligence for claim
validity, financing, political risk, security risks at the property
location and other risks not presently identified. As such, the reader is
cautioned that there can be no guarantee that the test phase at the Groete
Gold Copper Project will complete as described in this News Release. We



















TSX Venture closing price for CA-V
Date: 2014/05/16
Closing Price: 0.08

TEL:  714-316-3272  Adrian F.C.Hobkirk, President and CEO
ahobkirk@resourceexploration.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1414100048TS11414101630-07300320140522