Source	MARKET NEWS
Date	05/26/2014
Time	05:36:08 AM

Company	 Bayswater Uranium Corporation
Title	Receives 
New Preliminary Feasibility Study For R





    CDNX Symbol: BYU











Press Release	





BAYSWATER URANIUM CORP ("BYU-V;BYSWF-0")
- Receives New Preliminary Feasibility Study
- For Reno Creek Project

Bayswater Uranium Corporation is pleased to report the receipt of
a new independent Preliminary Feasibility Study (PFS) for the Reno
Creek ISR Uranium Project located in the Powder River Basin of Wyoming
(Project). The new PFS was prepared for AUC LLC (AUC), the operator of
the project, by TREC, Inc. and Tetra Tech and incorporated Measured and
Indicated resources of 21.87 million pounds uranium "(U3O8)"estimated
by Behre Dolbear in AUC's November 30, 2012 technical report.  The new
PFS evaluates the technical and economic feasibility of the Project,
based on reserves estimated by Tetra Tech. Using the current scientific
and engineering information available, the results of the PFS
demonstrate both the technical and economic feasibility of the Project.

Key Highlights of the Preliminary Feasibility Study:
* Measured and Indicated Resources of 21.87 million pounds U3O8 at
0.30 %-ft GT cutoff
* 20.12 million pounds of Probable Reserves as U3O8
* Recoverable Uranium of 14.94 million pounds U3O8
* Production Designed for 1.5 million pounds U3O8 per year
* Initial Capital Cost: US$78.4 million
* Cash Operating Costs: US$18.84 per pound U3O8
* Total Project Costs (pre-tax):  US$33.87 per pound U3O8
* Life of Mine After-Tax Earnings (undiscounted): US$359.8 million

* NPV8% of US$150 million (after-tax), IRR 32.2% (after tax),
Payback 3.2 Years

Project Overview
The Reno Creek Project includes approximately 21,000 acres located
in the Powder River Basin of northeastern Wyoming, USA, a
well-established, ISR uranium mining district. Uranium ISR projects in
or near the Powder River Basin include Uranium One's operating Willow
Creek facility, Cameco Corporation's operating Smith Ranch-Highland
facilities, Cameco's operating North Butte satellite facility, Uranerz
Energy Corporation's operating Nichols Ranch/Hank satellite facility,
and Uranium One's Moore Ranch Project which is permitted but not yet
under construction.  Uranium One's Allemand Ross and Ludeman projects
are in the permitting process (Figure 1).

Figure 1: Reno Creek Project Location Map

The Reno Creek Project defines five Resource Units (Figure 2). The
North and Southwest Reno Creek Units will be operated as a single unit
(the Reno Creek Resource Unit). The proposed Central Processing Plant
(CPP) is to be located within the Reno Creek Resource Unit near the
intersection of State Highway 287 and the Clarkelen Rd.   The Moore and
Bing Resource Units contain roll-front uranium mineralization in the
same and contiguous stratigraphic horizons as the Reno Creek Resource
Unit.  The Pine Tree Resource Unit contains mineralization in the same
stratigraphic horizons as the Reno Creek Unit plus a slightly higher
stratigraphic unit.  Estimated resources for the Pine Tree Unit were
not included in the reserves estimate for the Reno Creek Project
provided for in the PFS.

Figure 2: Reno Creek Project Resource Units

An NI 43-101 compliant mineral resource estimate was prepared for
the Reno Creek Project in November, 2012, by Behre Dolbear as shown in
Table 1 and the results were used in the development of this PFS.

//st
Table 1:  Measured and Indicated Resources for Reno Creek at 0.30 %-ft
GT Cutoff

RESOURCE            Pounds U3O8 at a GT)=0.30 %-ft (millions)
CLASS                          Resource Unit
North    SW
Reno     Reno                       Pine
Creek    Creek    Moore    Bing     Tree     Total
Measured      2.96     3.32     1.56     0.21     0.32      8.37
Indicated     5.13     3.55     2.97     0.72     1.13     13.50
Measured +
Indicated    8.09     6.87     4.53     0.93     1.45     21.87
//et

The Technical Report estimated current in place "measured and
indicated" resources of 20.9 million tons at an average grade of 0.052%
U3O8 containing 21.87 million pounds of uranium.  In addition, the
report estimated an "Inferred" resource of 1.6 million tons at an
average grade of 0.050% U3O8, containing 1.6 million pounds of uranium.

As part of the PFS, Tetra Tech estimated a total of 20.1 million
pounds of probable reserves, after excluding the Pine Tree Project
area, resources above water table, and resources lying outside of
proposed Production Units, as shown in Table 2, below. No proven
reserves are reported.

//st

Table 2: Estimated Probable In-Situ Reserves for Reno Creek

RESERVES1,2     Contained Pounds U3O8 at a GT1)=0.30%-ft Cutoff
(millions)
Probable Reserves
CLASS                          Resource Unit
North    SW
Reno     Reno                       Pine
Creek    Creek    Moore    Bing     Tree     Total
Probable      7.99     6.81     4.41     0.91     0.00     20.12



1.     GT = Grade x Thickness in %-feet
2.     Resources adjusted to exclude the Pine Tree Project, uranium below
water table, and outside of proposed Production Units.
//et

Tetra Tech estimated that 14.94 million pounds of uranium (as
U3O8) can be recovered at the Reno Creek Project, as a result of the
application of a recovery factor of 74.25% (Sweep efficiency of 75% x
Solution Recovery in the plant of 99%) to the probable reserves. The
Reno Creek, Moore, Pine Tree, and Bing resource units all contain
additional prospective areas along and adjacent to the strike of
recognized roll fronts. The PFS recommends additional drilling in these
areas to increase defined resources and reserves.
Project Development Plans
The Reno Creek Project consists of the proposed development of a
commercial uranium in-situ recovery (ISR) and processing operation.
Development of the Project will be by conventional ISR processes to
recover uranium from the host sandstone to produce uranium as a U3O8
yellowcake product.  The yellowcake will be packaged in 55 gallon drums
and further processed at a licensed conversion facility. The Project is
designed to produce up to 1.5 million pounds per year of uranium as
U3O8 from 16 production units and a Central Processing Plant (CPP) over
the 12 years of production.
The CPP will include ion exchange, elution, precipitation,
yellowcake drying and packaging operations.  Groundwater restoration
and reclamation/decommissioning operations are also part of the
integrated development and closure plan in the PFS.  The CPP is
designed to allow the acceptance of lixiviant or resin from other
nearby sources.  The CPP will be located in the southwestern part of
the Reno Creek Project on land owned by AUC.        The first
production units will be developed in the Reno Creek Resource Unit,
which is currently being permitted; development of the Moore, Pine
Tree, and Bing Resource Units will follow. All of the production units
will be connected to the CPP via pipelines.  No satellite recovery
units are contemplated.
Summary of Project Economics
The PFS concludes the proposed Reno Creek Project is technically
and economically feasible selling 14.94 million pounds of U3O8 at an
average price of US$65 per pound. The Net Present Value (NPV) for the
Project, using a discount rate of 8%, is estimated to be approximately
US$150 million after-tax, and the Internal Rate of Return (IRR) is
estimated to be 32.2% after-tax.  Payback is projected to occur in the
first quarter of the third year of production with net after-tax
earnings (undiscounted) of US$359.8 million over the life of the mine.
Total initial project capital costs are estimated at US$78.4
million including the CPP (US$44 million), the first production unit
(US$19.3 million) which consists of six wellfield/header houses and
approximately 480 production wells and 40 monitor wells, and indirect
costs of US$15.1 million. Cash operating costs, including production,
groundwater restoration, site decommissioning, reclamation,
administrative costs, royalties and production taxes are estimated at
US$18.84 per pound U3O8. Total project costs, including cash operating
costs, subsequent wellfield development/installation costs plus initial
and subsequent capital, are estimated at US$33.87 per pound U3O8. A
uranium price projection of US$65 per pound for long term contracts is
based on a wide variety of industry sources. A summary of key project
economics are shown in Table 3.

//st
Table 3: Summary of Key Project Economics
Item                         Total (US$m)     US$/pound U3O8 Recovered
Revenue                         971.2            65.00
Cash Operating Costs (LOM)
Initial Project Capital Costs   281.5            18.84
78.4

Total Project Costs (LOM)         506            33.87
Net Cash Flow Undiscounted
(After-Tax)                      360            24.09
NPV8% (After-Tax)                 150
IRR (After-Tax)                 32.2%
//et

The PFS titled "Reno Creek Preliminary Feasibility Study Wyoming,
USA" was prepared by TREC and Tetra Tech; they are responsible for the
PFS, and have reviewed and approved the content of this release. The
PFS will be available on the Company's profile on SEDAR
(www.sedar.com).
Permits Update
AUC is well into the permitting and licensing process.  The Permit
to Mine from the Wyoming Department of Environmental Quality is nearing
its public comment period.  The Nuclear Regulatory Commission is in the
process of preparing a Draft Supplemental Environmental Impact
Statement (EIS) and a draft Safety Evaluation Report, and has indicated
that it intends to issue the draft reports later in 2014 towards
issuance of a Source Materials License.  The National Historic
Preservation Act Section 106 Tribal consultation is in process.
BYU Tax Statement
The Company provides the following additional information
concerning the impact of taxes upon the Company in relation to the
Project.  Section 22.3 of the PFS provides a discussion of the impact
of Wyoming state and local taxes, other fees, and US Federal income
taxes on AUC, but as the report was prepared for AUC, the PFS does not
provide further analysis on the impact of taxes on BYU as a
shareholder. It is anticipated that distributions by AUC of its
after-tax income to its shareholders as dividends will be pro rata in
accordance with their respective ownership interests therein, of which
the Company currently owns an 11.09% interest. The Company is expected
to receive such distribution on a tax free basis.
Project Ownership
Bayswater currently holds an approximate 11.09% indirect interest
in the Reno Creek Uranium Project ("Project").  The balance, 88.91%, is
held by Pacific Road Resources Funds ("PRRF"). The Project is operated
by AUC, and indirect wholly owned subsidiary of Reno Creek Holdings
Inc. (RCHI). PRRF has the right to convert its investment in RCHI into
common shares of Bayswater at any time up to six months following the
later of completion of a feasibility study or receipt of all requisite
mining permits, but in any event not later than April 7, 2015, provided
certain conditions are met. In the event ofconversion, PRRF's
investment in RCHI would be converted into common shares of Bayswater
pursuant to prescribed formulas as previously described in the
Company's news release dated March 3, 2010. In the event of any such
conversion Bayswater would own a 100% effective interest in the Reno
Creek property.
Qualified Person
Dr. Rex Bryan, Mr. Alva Kuestermeyer and Dr. David Richers of
Tetra Tech and Mr. Douglass Graves of TREC, Qualified Persons under NI
43-101, have reviewed the contents of this news release.
About Bayswater Uranium Corporation
Bayswater Uranium Corporation is a uranium exploration and
development company.  Bayswater's focus is the Reno Creek ISR uranium
development project in Wyoming in which the Company currently owns
approximately a 11% interest.  Shares of the Company are listed on the
TSX Venture Exchange under the symbol "BYU".             For further
information see the Company's profile on SEDAR (www.sedar.com).
About Pacific Road Resources Funds and Pacific Road Capital
Management Pty Limited
The Pacific Road Resources Funds are private equity funds
investing in the global mining industry. They provide expansion and
buyout capital for mining projects, mining related infrastructure and
mining services businesses located throughout resource-rich regions of
the world. The Pacific Road Resources Funds are managed and advised by
Pacific Road Capital Management Pty Ltd ("PRCM"). The PRCM team,
located in Sydney, Australia, San Francisco, USA, and Vancouver,
Canada, is comprised of experienced mining investment professionals
that have extensive knowledge and experience in the mining and
infrastructure sectors, including considerable operating, project
development, transactional and investment banking experience. For
further information on the Pacific Road Resources Funds and PRCM,
please go to their website at www.pacroad.com.au.

On behalf of the Board of:

BAYSWATER URANIUM CORPORATION

Victor Tanaka
President



Statements in this news release other than purely historical information,
including statements relating to the Company's future plans and objectives
or expected results, constitute forward-looking statements, including
statements with respect to the future price of uranium, the estimation of
mineral resources, production and recovery, the realization of mineral
resources, the timing and amount of future production, expected costs (both
capital and operating), the success of exploration, development and mining
activities and permitting timelines.  Forward-looking statements are based
on numerous assumptions and are subject to all of the risks and
uncertainties inherent in the Company's business, including risks inherent
in mineral exploration, development and mining.  There can be no assurance
that such forward-looking statements will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such statements.  Accordingly, readers should not place undue reliance on
such statements. The Company does not undertake to update any
forward-looking statements that are incorporated by reference herein,
except in accordance with applicable securities laws. Neither the TSX
Venture Exchange nor its Regulation Services Provider (as that term is
defined in the policies of the TSX Venture Exchange) accepts responsibility



















































TSX Venture closing price for BYU-V
Date: 2014/05/23
Closing Price: 0.07
TEL:  (604) 687-2153  John Gomez, Corporate Development
www.bayswateruranium.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1414500010TS11414500285-05342220140526