Source	MARKET NEWS
Date	05/06/2015
Time	06:32:26 AM

Company	 San Marco Resources Inc.
Title	Expands 
Three And Identifies Two New Targets At





    CDNX Symbol: SMN











Press Release	





SAN MARCO RESOURCES INC ("SMN-V;SMREF-0")
- Expands Three And Identifies Two New Targets At Cuatro De Mayo

San Marco Resources Inc. ("San Marco" or "the Company") announces
its recent field exploration program at the 100% owned Cuatro de Mayo
Project in Sonora, Mexico resulted in the expansion of three
previously-identified targets (Chunibas, Valle and Oregano) and the
identification of two new targets (Tabacote and Chinos).

San Marco's geologists spent approximately 3 weeks during March
mapping, rock- and soil- sampling, and conducting reconnaissance
exploration at a number of sites in the Cuatro de Mayo project
(described below). Follow-up field work is currently underway.

Summary of the March 2015 Field Program:

Chunibas Target;

Chunibas is a vein target hosted in intrusive rocks that intrude
tuff agglomerate. There are several sub-vertical main veins on the
property and numerous high-grade iron-oxide shear zones that have been
mined by local miners.

Limited historical RC drilling has been conducted at Chunibas,
which indicated the presence of mineralization in the intrusive host
rock. Modest open cut mining of the oxide zones of some of the veins
occurred several years ago.

//st

Five gold-bearing veins (two of which are newly discovered) identified over
a mineralized corridor that is approximately 800m long and 700m wide.

Soil sampling completed south of the known vein traces indicates gold
enrichment may extend further to the south.

Veins are generally 1-2m wide, and rock chip and channel samples of the
veins collected by the Company and previous property owners typically assay
between 3 and 18 g/t gold. Highlights include:

//st

16.7 g/t gold from the Santa Rosa vein

15.5 g/t gold from the Santa Fe vein

18.4 g/t gold from the Argentina vein

6.6 g/t gold from the newly discovered Gusima-1 vein, and

7.6 g/t gold from the newly discovered Western vein.

//et

Importantly, a continuous rock chip sample of the Santa Fe vein hanging
wall rock returned 3.8 g/t gold over 10 meters.

//et

Follow-up work will include additional rock sampling of the Gusima
and Western veins, soil sampling south of the main target area to trace
potential extensions of the vein system, and vein wall rock sampling
where outcrop exists.

Oregano Target

Oregano is a low sulphidation high level vein target. There was no
previous mining or drilling on this property.

//st

Three low sulphidation veins (two of which are newly discovered) were
identified over an area approximately 3km long and 450m wide.

Typical low sulphidation textures such as bladed quartz after calcite,
crustiform, banded, quartz and coxcomb textures were observed.

Elevated mercury and antimony indicate that the upper level of veins are
exposed at surface.

//et

Follow-up work will include mapping and additional sampling of the
known veins, and soil sampling across extensions of the newly
discovered two veins.

Valle Target;

Valle is a stack of shallow dipping sub-parallel shear zones and
dikes hosted in tuff agglomerate. There was no previous mining or
drilling on this property.

//st

New geochemical data led to reinterpretation of the previous geological
model.

New model suggests that the Valle Target consists of multiple sub-parallel
mineralized shear zones that are currently traced for over 500m and that
the mineralized zone is at least 300m wide.

Mineralization appears to be fine gold hosted in 100% oxidized rocks.

Mineralized zone dips at around 30 degrees and it is a drill-ready target.

//et

Follow-up work will include soil sampling with a focus on extending
the presently known zone along its strike and identifying additional
sub-parallel mineralizes shears.

Tabacote Target

Tabacote is a high sulphidation (high level) system that has no
history of previous mining or drilling.

//st

It is a newly discovered target approximately 500m x 500m (open in all
directions) consisting of mineralization that is indicative of the upper
levels of a high sulphidation epithermal system.

Anomalous silver, lead, antimony and tellurium is hosted in highly
siliceous, vuggy silica altered and oxidized dacite and dacitic tuff.

Follow-up field work will include mapping, rock and soil sampling of the
anomalous target area as well as collecting samples for petrography and
PIMA alteration studies.

//et

Chinos Target

Chinos is a high sulphidation system that has no history of
previous mining or drilling.

//st

It is a newly discovered, potential high sulfidation epithermal target
traced along strike for approximately 200m (open in all directions).
Anomalous gold is hosted in vuggy silica dacite tuffs at the contact with
overlying rhyolites.

//et

Follow-up work will include additional sampling, mapping, and PIMA
testing of the target area

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company
with a portfolio of three promising properties in mining-friendly
Mexico, including the Cuatro de Mayo Project in Sonora State and the
recently acquired El Chunibas area concession. The Company maintains a
strategic project generation program focused on high-calibre,
low-opportunity cost projects in the Cuatro de Mayo District. San Marco
has a committed management team with extensive experience in Mexico and
a proven track record of building shareholder value.

National Instrument 43-101 Disclosure

The technical information contained in this document has been
verified, and this news release has been approved, by San Marco's CEO,
Robert D. Willis, P.Eng., a "Qualified Person" as defined in National
Instrument 43-101, Standards of Disclosure for Mineral Projects of the
Canadian Securities Administrators.

The samples discussed in this document were prepared for assay at
ALS Chemex Lab in Mexico and assayed at their facility in Vancouver,
BC. A 30 gram split is analyzed for gold, using the Au-AA23 method.
Sample results greater than 10 ppm are re-assayed, using AA23 fire
assay and gravimetric finish. For silver, copper, lead and zinc, a
multi-element, four acid digestion (ME -- ICP 61) method is used. For
initial assays of silver ) 100 ppm, copper, lead and zinc ) 10,000 ppm
(over limits), the OG62 method is used for re-analysis. San Marco's
sample collection, integrity, and quality control and assurance
procedures are in line with industry best practices and comply with
National Instrument 43-101 requirements.

Forward-Looking Information

Information set forth in this document includes forward-looking
statements, such as: the nature of additional work that may be
undertaken on the Cuatro de Mayo project; the potential size of the
mineralized targets identified to date; and the potential mineral
deposit type of the Cuatro de Mayo targets currently identified. While
these statements reflect management's current plans, projections and
intents, by their nature, forward-looking statements are subject to
numerous risks and uncertainties, some of which are beyond the control
of San Marco Resources Inc. Readers are cautioned that the assumptions
used in the preparation of such information, although considered
reasonable at the time of preparation, may prove to be imprecise and,
as such, undue reliance should not be placed on these forward-looking
statements. San Marco's actual results, programs, activities and
financial position could differ materially from those expressed in or
implied by these forward-looking statements.

Neither the TSX Venture Exchange nor the Investment Industry
Regulatory Organization of Canada accepts responsibility for the
adequacy or accuracy of this release.

Robert Willis
CEO
Phone: 604-568-5951
Cell: 604-813-2606
rwillis@sanmarcocorp.com

Barbara Henderson
Investor Relations Officer and Corporate Secretary
Phone: 604-568-5951
Cell: 604-789-7689
bhenderson@sanmarcocorp.com
______________________________________
_______________________________________________
TSX Venture closing price for SMN-V
Date: 2015/04/28
Closing Price: 0.06
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1512500015TS11512501108-06315320150506