Source	CANADA NEWSWIRE
Date	05/14/2015
Time	05:06:33 AM

Company	 Rathdowney Resources Ltd.
Title	Rathdowney files Technical Report for Project Olza PEA





    CDNX Symbol: RTH











Press Release	




" BC-Rathdowney-PEA   05-14 1398
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Rathdowney files Technical Report for Project Olza PEA@

VANCOUVER, May 14, 2015 /CNW/ - Rathdowney Resources Ltd. ("Rathdowney"
or the "Company") (TSXV: RTH) announces that it has filed on SEDAR the NI
43-101 Technical Report for the Preliminary Economic Assessment ("PEA") of
Olza zinc-lead project ("Project Olza") located in southwestern Poland.
The development scenario recommended in the PEA is a conventional
underground mine and processing facility at a rate of 6,000 tonnes per day or
2.16 million tonnes per year. Standard flotation treatment will produce
marketable low iron zinc and lead concentrates that would be shipped by
existing rail facilities to smelters.
Key results of the Project Olza PEA1, presented in US dollars, include:
<<

--  After tax Internal Rate of Return of 30% with a payback of 2.4 years.
The Net Present Value after taxes is $170 million at an 8% discount
rate.
--  Initial capital is $227 million, sustaining capital is $51 million and
total operating cost is $69.88/tonne milled (including on-site and
off-site costs).
--  Life of mine production yielding 1,338 million tonnes of payable zinc
and 449 million tonnes of payable lead.
--  Excellent potential to increase mineral resources and extend project
life.
>>
The final technical report recommends advancing to the feasibility level
in a phased approach, using the PEA as a basis for the refining and optimizing
the project. In parallel, the Company would move the project forward through
the Polish permitting and development process.
The PEA is preliminary in nature and includes Inferred Mineral Resources
that are considered too speculative geologically to have the economic
considerations applied to them that would enable them to be categorized as
Mineral Reserves. There is no certainty that the PEA will be realized.
Rathdowney Chairman David Copeland said
"We are pleased with the strong results of the PEA, highlighted here and
described in our April 20, 2015 news release. Additional details can be
obtained from the technical report, which is now available on Rathdowney's
website www.rathdowneyresources.com as well as under the Company's profile on
SEDAR at www.sedar.com.
Additionally, further to our announcement on May 5, 2015, I want to take
this opportunity to thank our former CFO Paul Mann for his important
contributions to the Company over the past five years."
The Company would also like to confirm that its Annual General Meeting
will be held on June 8, 2015 at 11 am in the boardroom at Rathdowney's head
office at Suite 1500, 1040 West Georgia Street, Vancouver, BC.
About Rathdowney and Project Olza
Rathdowney Resources Ltd. is focused on advancing Project Olza through
permitting and into production.
Project Olza is located in the Upper Silesian Mining District of
southwestern Poland, a world-class region of Mississippi Valley-type deposits
with well-developed mining infrastructure. Easily accessible by road, the Olza
project site is a one-hour drive from Krakow, a major city with full services,
including an international airport. The deposits at Olza are 25 km from the
ZGH zinc smelter at Boleslaw. A railway line runs through the Olza
project-area, linking it to the local facilities and also to other smelters
through ports on the Baltic Sea.
Rathdowney's Phase I confirmatory drilling program built on the extensive
drill database assembled by Polish State Survey to delimit 24.4 million tonnes
of inferred mineral resources, grading 7.02% combined zinc and lead2, with
excellent potential for expansion. These mineral resources provide the
foundation for its current Phase II program of engineering, environmental
baseline and other technical studies necessary for mine planning and
permitting.
_____________________________________________
(1)Assumptions for the PEA incorporate median zinc and lead metal
price forecasts of over 30 independent banks and investment dealers,
and include $1.10/lb in Year 1 and 2 and $1.00/lb in the remaining
life of mine (LOM) for zinc; and $1.09/lb in Year 1, $1.00/lb in Year
2 and $0.95/lb in the remaining LOM for lead.
2 Estimated at a 2.0% zinc cutoff; individual grades are 5.53% zinc
and 1.49% lead. Mineral resources that are not mineral reserves do
not have demonstrated economic viability.

David Copeland, PEng., Chairman of Rathdowney and a qualified person as
defined under NI43-101, has reviewed the technical information in this
release.
On behalf of the Board of DirectorsDavid CopelandChairman
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Forward Looking Information and other Cautionary Factors
All information contained in this press release relating to the contents
of the Preliminary Economic Assessment, including but not limited to
statements of the Project Olza's potential are "forward looking statements".
The PEA was prepared to broadly quantify the project's capital and operating
cost parameters and to provide guidance on the type and scale of future
project engineering and development work that will be needed to ultimately
define the project's likelihood of feasibility and optimal production rate.
The PEA uses Inferred Mineral Resources which are considered too speculative
geologically to be categorized as mineral reserves and to have economic
considerations applied to them. There can be no assurance that the operating
and financial projections contained in the PEA will be realized.
The following are the principal risk factors and uncertainties which, in
management's opinion, are likely to most directly affect the conclusions of
the PEA and the ultimate feasibility of the project. The PEA is based on the
inferred resources. Additional process tests and other engineering and
geological work will be required to determine indicated or measured mineral
resources at Project Olza and if an economically exploitable reserve can be
established. Final feasibility work has not been done to confirm the
underground design, mining methods, and processing methods assumed in the
Preliminary Economic Assessment. Final feasibility could determine that the
assumed underground design, mining methods, and processing methods are not
correct. Construction and operation of the mine and processing facilities
depends on securing environmental and other permits on a timely basis. No
permits have been applied for and there can be no assurance that required
permits can be secured or secured on a timely basis. Data is incomplete and
cost estimates have been developed in part based on the expertise of the
individuals participating in the preparation of the PEA and on costs at
projects believed to be comparable, and not based on firm price quotes. Costs,
including design, procurement, construction, and on-going operating costs and
metal recoveries could be materially different from those contained in the
Preliminary Economic Assessment. There can be no assurance that mining can be
conducted at the rates and grades assumed in the Preliminary Economic
Assessment. Energy risks include the potential for significant increases in
the cost of fuel and electricity. The PEA assumes specified, long-term prices
levels for zinc and lead. Prices for these commodities are historically
volatile, and Rathdowney has no control of or influence on those prices, all
of which are determined in international markets. There can be no assurance
that the prices of these commodities will continue at current levels or that
they will not decline below the prices assumed in the Preliminary Economic
Assessment. Prices for zinc and lead have been below the price ranges assumed
in PEA at times during the past ten years, and for extended periods of time.
The project will require major financing, probably a combination of debt and
equity financing. Interest rates are at historically low levels. There can be
no assurance that debt and/or equity financing will be available on acceptable
terms. A significant increase in costs of capital could materially and
adversely affect the value and feasibility of constructing the project. Other
general risks include continuity of mineralization, those ordinary to large
construction projects including the general uncertainties inherent in
engineering and construction cost, the need to comply with generally
increasing environmental obligations, and accommodation of local and community
concerns, potential environmental issues or liabilities associated with
exploration, development and mining activities, exploitation and exploration
successes, delays due to third party opposition, and changes in government
policies regarding mining and natural resource exploration and exploitation.
The Company is also subject to the specific risks inherent in the mining
business, as well as general economic and business conditions. For more
information on the Company, Investors should review the Company's filings that
are available at www.sedar.com.
SOURCE Rathdowney Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/May2015/14/c5240.html

-0-                           05/14/2015
/For further information: For further information on Rathdowney and
Project Olza, please visit www.rathdowneyresources.com or contact: Roger
Blair, Investor Relations, Tel: 778-373-6725, Toll free (NA): 1-800-667-2114/
/Web Site: www.rathdowneyresources.com /
(RTH.)

CO:  Rathdowney Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-