Source	Marketwire
Date	05/26/2015
Time	11:03:51 AM

Company	 BRUNSWICK RESOURCES INC.
Title	Brunswick Resources: Update for the Chester Property





    CDNX Symbol: BRU











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Brunswick Resources Inc.

TSX VENTURE SYMBOL: BRU

May 26, 2015

Brunswick Resources: Update for the Chester Property


ROUYN-NORANDA, CANADA--(Marketwired - May 26, 2015) - Brunswick Resources Inc. 
(the "Corporation" or "Brunswick") (TSX VENTURE:BRU) is pleased to announce the 
review of the previously completed exploration program on the western part of 
the Chester property, located in north-central New Brunswick, Canada. The 
claims are located about 55 km west northwest of Miramichi City or 35 km from 
Sunny Corner and 72 km southwest of Bathurst. It is located in the southern 
edges of the main Bathurst Mining Camp as shown in the attached map of Bathurst 
Mining Camp.

An extensive ground exploration program was conducted on the western part of 
the Chester Property, concentrating mainly on the west side of the Clearwater 
Stream in an area that has not been explored since the late 1950's. The purpose 
was to explore the possibility of finding additional near surface mineralized 
zones similar to the known Chester Copper and VMS zones. It was already 
confirmed by a previous operator (First Narrows 2004 and historical drilling 
1967-68) that the main zone copper stringer deposit exists for 500 to 700 
metres west of the calculated resource.

In July and August 2014, Brunswick Resources Inc. completed a total of 1,103 
metres of diamond drilling in 10 short holes on the western part of the Chester 
property (Chester West claims) as shown on the attached drill hole location 
plan. The objective of the program was to test soil geochemical anomalies 
discovered and outlined in a detailed soil sampling program completed by Explor 
Resources Inc. in 2013 (Press Release dated December 2, 2013). It was also to 
check the underlying geology for structure and lithologies because the 
stratigraphy is relatively flat-lying in this area of the Camp. The flat nature 
of the stratigraphy and the sparcity of outcrops makes it difficult to 
interpret what is going on as little as 30 cm beneath the surface of an 
outcrop, particularly the thickness and lithologies of stratigraphic units.

Drill holes CHS 14-01 to CHS 14-04 were drilled to check the source of a large 
and dominant lead in soil anomaly from the 2013 soil sampling program. There is 
also a weaker zinc and copper anomaly in the same trend. All 4 of these holes 
intersected lead and zinc mineralization although it is fracture fillings in 
felsics rocks. The holes were all terminated in the 104 to 131 metres range and 
intersected a series of felsic volcanic interlayered with sediments.

Drill hole CHS 14-01 intersected a 13.35 metres section of felsic rocks with 
scattered lead and zinc sulphide mineralized unit near the surface. This 
correlates to a similar unit found nearby in outcrop on the access road. It 
went into a series of felsic and sedimentary rocks until it intersected a fault 
at 91.4 to 93.9 metres, after which it went back into a feldspar unit again 
which appears to be the Clearwater Stream Formation. Both units are altered but 
only the top units reported lead and zinc mineralization. This hole confirmed 
the suspected and interpreted fault and it also confirmed the presence of base 
metal mineralization in that unit. (The Clearwater Stream Formation is the host 
stratigraphic unit for the layer containing the Chester Copper Stringer zone 
and the Chester VMS deposit, located approximately 2 kilometres to the east).

Drill hole CHS 14-02 was drilled 50 metres behind and to the south of drill 
hole CHS 14-01. It also collared in sediments and then went into a layer of 
felsics. It intersected a 16.35 metres thick felsic unit just below the 
sediments. This unit is also feldspar phyric and chlorite and sericite altered 
and contains scattered and disseminated sulphides including lead, zinc and 
copper sulphides. Although grades appear low, it was sampled in its entirety. 
This unit is correlative with the similar unit in the first hole and shows the 
continuity of alteration and mineralization in this horizon, which appear to be 
the Clearwater Stream Formation. It also suggests that the horizon may be 
thickening to the south since, at only 50 m away, it is 3 metres thicker in the 
second hole. Both have similar characteristics of alteration and 
mineralization. The resultant dip is 15 degrees southward.

Drill holes CHS 14-03 and CHS 14-04 were drilled about 50 metres further south 
and 100 metres east of the first two holes. They, too, intersected layers of 
sediments and felsics with varying amounts of sulphides, mainly pyrrhotite and 
pyrite with some chalcopyrite, galena and sphalerite (copper, lead and zinc) 
mineralization. These holes were set back further from the target and were 
drilled shorter and appear to have been drilled a bit too short. It is 
recommended that they be deepened to at least 200 m each, if not deeper. This 
is the first drilling in this area and the subsurface geology is just being 
discovered. The geological model is the Chester VMS and copper stringer zones 
about 1.5 to 2 km to the east. The details as the strike and dip of the western 
limits of the zone are still not yet defined and the western limits appear to 
be different in dip than the eastern limits.

Drill holes CHS 14-05 to CHS 14-10 were located in the northern section of the 
property and were drilled to test a widespread copper in soil anomaly 
discovered in 2013. Drill hole CHS 14-05 was drilled to test an electromagnetic 
target just off of the soil anomaly and under it. From 54.7 m to 72.25 metres, 
it intersected scattered chalcopyrite mineralization with pyrrhotite and pyrite 
mineralization in felsic rocks of varying degrees of alteration from talcy to 
chloritic. The pyrrhotite ranged from short massive layers with disseminated 
chalcopyrite but overall about 6 to 8% with lesser amounts of chalcopyrite. The 
soil anomaly is coincident with the area where the mineralized horizon projects 
to surface.

Drill hole CHS 14-06 was drilled to test the same copper anomaly as Drill hole 
CHS 14-05 but by drilling a vertical hole directly into the anomaly. The source 
of the copper anomaly was discovered in leached and weathered bedrock 
consisting of altered felsics that is the same horizon that was intersected in 
Drill hole CHS 14-05 but 250 metres to the northeast. Drill hole CHS 14-07 was 
drill vertically about 200 metres south of Drill hole CHS 14-06. From 9.5 
metres to 36.8 metres, it intersected altered felsics (probable Clearwater 
Stream Formation) with scattered and disseminated chalcopyrite, pyrite and 
pyrrhotite. From 29.75 metres to 30.9 metres, a zone of massive to semi-massive 
pyrrhotite was intersected that contained disseminated chalcopyrite. The host 
rock is the Clearwater Stream Formation.

Drill holes CHS 14-08, CHS 14-09 and CHS 14-10 were drilled to test other parts 
of the soil anomaly. They met with limited success since leaching of the 
anomalous horizon has removed most of the copper out of the near surface 
bedrock. It should be noted that the anomalous bedrock is flat lying and 
shallow. Drill hole CHS 14-08 intersected sediments and some felsics and 
terminated in an unidentified calcareous basaltic-looking rock. Drill hole CHS 
14-09 was drilled vertically to a depth of 137 metres, stopping in a series of 
rhyolites, basalts and feldspar porphyritic material, suspected to be a western 
extension of the Sevogle River Formation overlying the Clearwater Stream 
Formation.

In summary, the drilling program of 2014 shows indications of potential 
widespread mineralization in an area of the property where had not previously 
been aggressively pursued and drilled for almost 50 years.

The last 6 drill holes have shown that an AEM anomaly that has been picked up 
on several airborne surveys since 1996 has an in-situ bedrock source and is due 
to a layer of massive sulphides containing disseminated copper mineralization. 
The down dip plunge extension of this zone should now be pursued as a valid 
exploration target since it has all the right rock types and age dates for this 
part of the Bathurst Mining Camp as determined by using the Chester VMS and 
copper stringers zones as a model.

The first 4 drill holes have extended the productive Chester horizon not only 
to the west by a kilometer or so beyond any historic drilling but also that it 
may actually extend up dip to surface in an area where it was not previously 
known. Additional drilling is required.

Christian Dupont, P. Eng., is the qualified person responsible of the 
information contained in this press release.

Brunswick Resources Inc. is a publicly listed company trading on the TSX 
Venture Exchange (BRU).

This press release was prepared by Brunswick Resources Inc. Neither the TSX 
Venture Exchange Inc nor its Regulation Services Provider (as that term is 
defined in the Policies of the TSX Venture Exchange) has reviewed or accepts 
responsibility for the adequacy or accuracy of this release.

About Brunswick Resources Inc.

Brunswick Resources Inc. is a Canadian-based natural resources company with 
mineral holdings in Ontario and New Brunswick. Brunswick is currently focused 
on exploration in the Bathurst Mining Camp. The Bathurst Mining camp is where 
47 VMS (volcanic massive sulfide) deposits have been found to date, including 
the Brunswick No. 12 and the Brunswick No. 6 Mines where more than 130,000,000 
tonnes of Base metal ore has been produced to date. Brunswick Resources 
Flagship project is the Chester Copper and VMS Project located in the Bathurst 
Mining camp. The Chester mineral resource (Explor Resources Press Release dated 
April 10, 2014) includes the following:

MINERAL RESOURCE ESTIMATE - CHESTER DEPOSIT (MARCH 7, 2014)

/T/


----------------------------------------------------------------------------
Cut-off                    Cu        Zn        Ag
Class                        (Cu%)     Ktonnes       (%)       (%)     (g/t)
----------------------------------------------------------------------------
In-Pit
----------------------------------------------------------------------------
Measured                       0.5         101      1.87      0.14       6.7
----------------------------------------------------------------------------
Indicated                     0.5       1,296      1.34      0.06       3.3
----------------------------------------------------------------------------
Measured and Indicated         0.5       1,397      1.38      0.06       3.5
----------------------------------------------------------------------------
Inferred                      0.5       2,060      1.25       n/a       n/a
----------------------------------------------------------------------------
Below Pit
----------------------------------------------------------------------------
Inferred                      2.0          29      2.33       n/a       n/a
----------------------------------------------------------------------------
Combined
----------------------------------------------------------------------------
Measured                       0.5         101      1.87      0.14       6.7
----------------------------------------------------------------------------
Indicated                     0.5       1,299      1.34      0.06       3.3
----------------------------------------------------------------------------
Measured and Indicated         0.5       1,400      1.38      0.06       3.5
----------------------------------------------------------------------------
Inferred                 Variable       2,089      1.26       n/a       n/a
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Note: Inferred resources are based primarily on older drilling results which do 
not have sufficient zinc and silver analyses to generate resource grades for 
these elements.

Robert Sim, P.Geo, an independent consultant, served as the Qualified Person 
responsible for preparing the Technical Report, as defined in National 
Instrument 43-101, Standards of Disclosure for Mineral Projects (NI 43-101), in 
compliance with Form 43-101F1 (the Technical Report). Mr. Sim is a Geologist 
with more than 30 years of experience primarily in base and precious metals 
exploration, operations, resource modeling, and feasibility-level evaluations. 
Mr. Sim has worked on similar volcanogenic massive sulphide (VMS) deposits, 
including the Winston Lake deposit in Ontario and the Cayeli deposit in Turkey. 
Mr. Sim received assistance from Geo-statistician Bruce Davis, Ph.D., FAusIMM, 
of BD Resource Consulting, Inc.

This document may contain forward-looking statements relating to Brunswick's 
operations or to the environment in which it operates. Such statements are 
based on operations, estimates, forecasts and projections. They are not 
guarantees of future performance and involve risks and uncertainties that are 
difficult to predict and may be beyond Brunswick's control. A number of 
important factors could cause actual outcomes and results to differ materially 
from those expressed in forward-looking statements, including those set forth 
in other public filling. In addition, such statements relate to the date on 
which they are made. Consequently, undue reliance should not placed on such 
forward-looking statements. Brunswick disclaims any intention or obligation to 
update or revise any forward-looking statements, whether as a result of new 
information, future events or otherwise, save and except as may be required by 
applicable securities laws.

To view the maps associated with this release, please click on the following 
link : http://media3.marketwire.com/docs/1009066e.pdf

- 30 -

CONTACT INFO:

Christian Dupont, President and CEO
(888) 764-5195
(819) 797-0596
Fax: (819) 797-6050
www.brunswickresources.com
brunswick@tlb.sympatico.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=529881659