Source	Marketwire
Date	05/28/2015
Time	05:00:25 AM

Company	 SOURCE EXPLORATION CORP.
Title	Source Reports New Discovery With Multiple Mineralized Intercepts 
Including 5.74 g/t Gold Equivalent Over 17.0 Metres





    CDNX Symbol: SOP











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Source Exploration Corp.

TSX VENTURE SYMBOL: SOP

May 28, 2015

Source Reports New Discovery With Multiple Mineralized Intercepts Including 
5.74 g/t Gold Equivalent Over 17.0 Metres

High-grade Intercepts include 35.02 g/t Au Eq over 1.0 Metre

THUNDER BAY, ONTARIO--(Marketwired - May 28, 2015) - Source Exploration Corp. 
(the "Company" or "Source") (TSX VENTURE:SOP)(FRANKFURT:4QW) is pleased to 
announce that recent drilling at the Nopaltepec target of its Las Minas 
property has resulted in the discovery of a new highly mineralized zone. 
Discovery hole LM-15-NP-01 intersected multiple mineralized intercepts of gold, 
silver and copper from near the collar to a depth of 203.0 metres. The 
intercepts include 5.74 g/t Au Eq over 17.0 metres, including  5.0 metres 
grading 13.70 g/t Au Eq, containing a 1.0 metre interval grading 35.02 g/t Au 
Eq.  Additional and separate mineralized intercepts included 1.33 g/t Au Eq 
over 10.3 metres, 2.21 g/t Au Eq over 8.0 metres, 0.55 g/t Au Eq over 44.0 
metres and 1.20 g/t Au Eq over 4.0 metres. The hole ended in mineralization.

The new zone occurs approximately 100-150 metres above the downward projection 
of the recently drilled El Dorado /Juan Bran zone - see press releases dated 
May 7 & 26, 2015. The grades and type of mineralization are similar to the high 
-grade mineralization at the Santa Cruz target, located approximately 250 
metres to the east.

Composite Assays are included in Table 1 below.

Table 1 Composite Assay Results for Nopaltepec & Santa Cruz Drilling

/T/


----------------------------------------------------------------------------
Nopaltepec Drilling Results
----------------------------------------------------------------------------
Inter-
From    To   cept    Au    Ag    Cu  Au Eq
Hole No (Az/Dip)      (m)   (m)    (m) (g/t) (g/t)     %  (g/t) Comments
----------------------------------------------------------------------------
LM-15-NP- 01 (35/-   18.5  28.7   10.3  1.03  1.18  0.17   1.33 Breccia
45)
----------------------------------------------------------------------------
and                  83.0  91.0    8.0  1.01  8.93  0.62   2.21 Endo-skarn
----------------------------------------------------------------------------
and                 108.7 125.7   17.0  2.84  9.50  1.61   5.74
----------------------------------------------------------------------------
including           112.6 113.6    1.0  8.77  69.7  14.7  35.02 Endo-skarn
----------------------------------------------------------------------------
within              110.6 115.6    5.0  4.86  27.9  4.89  13.70 Endo-skarn
and breccia
----------------------------------------------------------------------------
and                 153.0 191.0   44.0  0.29  0.28  0.15   0.55 Breccia with
native
copper
----------------------------------------------------------------------------
and                 199.0 203.0    4.0  0.98  1.40  0.12   1.20 Ended in
mineralizati
on
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-15-NP-02 (64/-    24.6  32.0    7.4  0.61  5.44  0.42   1.42
60)
----------------------------------------------------------------------------
22.5  33.0   10.5  0.54  4.73  0.35   1.22
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-15-NP -03 (320/-  16.4  24.4    8.0  0.37  0.15  0.03   0.42
45)
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
Santa Cruz Drilling Results
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-15-SC-11(60/-45) 145.0 149.0    4.0  0.87  4.60  0.35   1.54 Deepening
----------------------------------------------------------------------------
within              141.0 149.0    8.0  0.63  2.69  0.20   1.02
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-15-SC-18 (85/-    13.0  14.0    1.0  3.24 14.90  1.44   5.94
46)
----------------------------------------------------------------------------
within               13.0  18.0    5.0  0.71  3.28  0.44   1.51
----------------------------------------------------------------------------

----------------------------------------------------------------------------

/T/

David Baker, Chairman, commented: "We are very excited about the discovery of 
high-grade mineralization over significant intervals at Nopaltepec. The 
numerous intercepts and their close proximity to the high-grade Santa Cruz zone 
lead Source's management team to believe that the two zones are part of the 
same mineralizing system, with considerable opportunity to define a mineral 
resource."

For a drill plan showing the hole locations, please click here: 
http://media3.marketwire.com/docs/9421a.pdf

For a cross section of Nopaltepec holes LM-15-NP -01, 02, & 03, please click 
here: http://media3.marketwire.com/docs/9421b.pdf

Nopaltepec Drilling

Discovery hole LM-15-NP-01 was drilled to explore for mineralization in an area 
located across a small canyon from the high -grade Santa Cruz zone. The hole 
intersected multiple mineralized intercepts from near the collar to a depth of 
191.0 metres. A high-grade intercept grading 5.74 g/t Au Eq over 17.0 metres 
was intersected from 108.7 metres to 125.7 metres. Higher up in the hole, 1.33 
g/t Au Eq over 10.3 metres was intersected from 18.5 to 28.7 metres, as well as 
an additional 8.0 metre intercept grading 2.21 g/t Au Eq from 83.0 to 91.0 
metres. Deeper in the hole, a long intercept measuring 44.0 metres grading 0.55 
g/t Au Eq was intersected from 153.0 to 191.0 metres. The hole ended in 
mineralization, with the bottom 4.0 metres grading 1.20 g/t Au Eq.

Holes LM-15-NP- 02 and 03 were drilled as step -out holes to the south. They 
were not extended to depth due to a concentration of post mineralization dykes 
in this part of the zone. Hole LM-15-NP- 02 intersected 1.42 g/t Au Eq over 7.4 
metres, contained within 10.5 metres grading 1.22 g/t Au Eq. Hole LM-NP-03  
returned 0.42 g/t Au Eq over 8.0 metres near the collar of the hole.

Santa Cruz Drilling

Hole LM-15-SC- 11 (deepening of LM-14-SC-11 - see press release dated August 6, 
2014) intersected 4.0 metres grading 1.54 g/t Au Eq, within 8.0 metres assaying 
1.02 g/t Au Eq, confirming the downward projection of the Santa Cruz 1-3 zone.

Hole LM-15-SC-18 was drilled to verify evidence of a NE-SW (orthogonal) 
orientation of the structure hosting the high-grade mineralization intersected 
in holes LM-14-SC-07 and 08 (see press release dated August 6, 2014). The hole 
intersected 1.0 metre grading 5.94 g/t Au Eq contained within 5.0 metres 
grading 1.51 g/t Au Eq.

All reported intervals referred to in this news release are core lengths and 
additional information is required to determine true widths. Assays are uncut, 
length - weighted average values.

(1) Gold equivalent (Au Eq) calculations use metal prices of US $1,200/oz. for 
gold, US $19.00/oz. for silver and US $3.00/lb. for copper. No adjustments have 
been made for potential relative differences in metal recoveries. Au Eq g/t 
equals Au g/t + (Ag g/t x 0.016) + (Cu% x1.71)

Samples containing free metallic gold were assayed by SGS Mineral Services at 
Durango, Mexico, an accredited and independent laboratory, using the FAS30K-Au 
metallic screen fire assay method.

About Las Minas

The Las Minas Project hosts near-surface gold - silver and copper skarn 
mineralization and high-grade gold - silver epithermal vein deposits. The 
project is comprised of six mineral concessions covering approximately 1,616 
hectares (3,995 acres), with several small scale, past-producing mines and a 
number of untested targets.

The district is host to one of the largest under explored gold - silver copper 
skarn systems known in Mexico, and has a production history that extends back 
to the Aztec era. The Las Minas granodiorite intrusive measures approximately 
10 kilometres in diameter and underlies the Las Minas concessions. The 
mineralization controls and association with magnetite appear to be similar to 
the Guerrero Gold belt, which is the site of the Los Filos and Morelos gold 
deposits.

Las Minas is an early-stage exploration project and does not contain any 
mineral resource estimates as defined by National Instrument 43-101 Standards 
of Disclosure for Mineral Projects ("NI 43-101"). The potential quantities and 
grades disclosed herein are conceptual in nature, and there has been 
insufficient exploration to define a mineral resource for the targets discussed 
herein. It is uncertain if further exploration will result in these targets 
being delineated as a mineral resource.

Quality Assurance/Quality Control

The technical information in this news release has been reviewed and approved 
by Sonny Bernales, P. Geo., a registered Professional Geoscientist in the 
Province of British Columbia and a qualified person as defined by NI 43-101. 
Mr. Bernales is responsible for logistics and supervision of all exploration 
activity conducted by Source on the property.

The Company has implemented and adheres to a strict Quality Assurance/Quality 
Control program which includes inserting mineralized standards and blanks into 
the sample stream, about 1 for every 10 samples. The standards and blanks were 
obtained from CDN Resource Laboratories Ltd. of Langley, BC, Canada. Each 
sample bag is properly sealed and kept in a secured, restricted storage place 
prior to shipping to the lab. Samples are shipped directly by Source or 
picked-up by the lab vehicle with chain of custody/sample submittal signed and 
dated. The Company sends it samples to SGS Mineral Services (ISO/IEC 17025) at 
Durango, Mexico, an accredited and independent laboratory. Check samples are 
also sent to ALS-Chemex Laboratories in North Vancouver, Canada.

About Source Exploration

Source Exploration is a Canadian based mineral exploration company committed to 
building long-term value through ongoing discoveries and strategic acquisitions 
of prospective precious metals deposits in Mexico. Source is exploring the Las 
Minas Project, which is located in the core of the Las Minas district in the 
Veracruz State, Mexico. The district is host to one of the largest under 
explored skarn systems known in Mexico and has a strong production history that 
dates back to the Aztec era.

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION: This news release 
includes certain information that may constitute "forward-looking information" 
under applicable Canadian securities legislation. Forward-looking information 
includes, but is not limited to, statements about the magnitude or quality of 
mineral deposits, anticipated advancement of mineral properties or programs, 
future operations, results of exploration, prospects, commodity and precious 
metals prices, future work programs, anticipated financial and operational 
results, capital expenditures and objectives and the completion and timing of 
mineral resource estimates. Forward-looking information is necessarily based 
upon a number of estimates and assumptions that, while considered reasonable, 
are subject to known and unknown risks, uncertainties, and other factors, which 
may cause the actual results and future events to differ materially from those 
expressed or implied by such forward-looking information, including the risks 
identified in the Company's disclosure documents available at www.sedar.com. 
There can be no assurance that such information will prove to be accurate, as 
actual results and future events could differ materially from those anticipated 
in such information. Accordingly, readers should not place undue reliance on 
forward-looking information. All forward-looking information contained in this 
press release is given as of the date hereof and is based on the opinions and 
estimates of management and information available to management as at the date 
hereof. The Company disclaims any intention or obligation to update or revise 
any forward-looking information, whether as a result of new information, future 
events or otherwise, except as required by law.

- 30 -

CONTACT INFO:

Source Exploration Corp.
David Baker
Executive Chairman
604-817-4211 or 604-970-8052

or

Source Exploration Corp.
Brian Robertson
President & CEO
807-474-4270 or 807-251-1816
Fax: 807-474-4272

or

Source Exploration Corp.
Camille Turner
Investors Relations
604-669-7840 or 604-970-8052
info@sourceexploration.com
www.sourceexploration.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=530220797