Source	Marketwire
Date	05/19/2016
Time	02:01:01 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Drills 8.00 m @ 3.21 g/t Au and 1.85 m @ 15.08 g/t Au at 
Hebert-Brent Zone, Yellowknife City Gold





    CDNX Symbol: TXR











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
OTC PINK SYMBOL: TRXXF

May 19, 2016

TerraX Drills 8.00 m @ 3.21 g/t Au and 1.85 m @ 15.08 g/t Au at Hebert-Brent 
Zone, Yellowknife City Gold


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 19, 2016) - TerraX Minerals 
Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has received assay 
results from a 19 hole drill program totalling 784 meters at the Hebert-Brent 
Zone on the Yellowknife City Gold Project ("YCG"), immediately north of 
Yellowknife in the Northwest Territories. All holes were very shallow (average 
41 meters depth) testing interpreted shallow dip, plunge, and strike extensions 
of the mineralized zones exposed on surface.

The Hebert-Brent Zone was originally discovered in the summer of 2015 and was 
channel sampled along exposed zones of mineralization (11.0 m @ 7.55 g/t Au, 
news release August 11, 2015), and was subsequently tested with 6 drill holes 
(10.26 m @ 3.61 g/t Au, news release November 18, 2015). The zone has 
particular interest to TerraX as it demonstrates that the YCG has sulphide 
replacement style mineralization with little or no quartz veining, a deposit 
type that can produce large deposits.

The drilling reported here tested several potential extensions to the surface 
mineralization. Six holes (TCG16-34, 040, 043, 044, 052 and 053) totalling 242 
meters tested mineralization along strike and to the south of the surface 
mineralization. All these holes hit sulphide replacement gold zones over a 
strike length of 125 m. Highlights include:

/T/

--  8.00 m @ 3.21 g/t Au, including 3.00 m @ 7.09 g/t Au in hole TCG16-052
--  1.85 m @ 15.08 g/t Au in hole TCG16-040
--  7.10 m @ 3.61 g/t Au, including 1.04 m @ 12.75 g/t Au in hole TCG16-034

/T/

Based on this drilling, we believe that the main Hebert-Brent zone and the 
Hebert-Brent South Zone have potential along a projected southerly dip. Due to 
the limited meterage budgeted for this program and time constraints, drilling 
was terminated before the southern dip potential of both zones could be tested.

Of the remaining holes, eight holes (TCG16-35 to 038, 041, 049, 050, and 051) 
totalling 315 meters tested an interpreted northerly dipping quartz feldspar 
dyke (QFP) that hosts some of the mineralization exposed on surface. None of 
these holes intersected significant gold mineralization. Three holes (TCG16-54 
to 056) totalling 151 meters tested a projected strike extension of the 
Hebert-Brent zone to the east, and a sulphide chert horizon beneath the 
projected zone. Drill hole TCG16-055 hit Hebert-Brent style mineralization 
(0.85 m @ 4.61 g/t Au). Two holes (TCG16-39 and 042) totalling 76 meters tested 
the northerly dipping QFP dyke associated with the surface exposure of the 
Hebert-Brent South Zone. Neither hole hit significant mineralization.

The Hebert-Brent deposit type remains a high priority target for TerraX as 
larger zones of similar alteration and mineralization have been located to the 
north, east, and south of Hebert-Brent. Using the knowledge gained from the 
Hebert-Brent Zone these new zones will be comprehensively mapped and sampled 
during the 2016 field season beginning in June.

A map showing the location of drill holes on the Hebert-Brent target area is 
available on our web site under "2016 Field Exploration".

Drill holes were drilled close to normal to the interpreted strike and dip of 
the zones. Current interpretations for dip, based on the surface trenching and 
the drill holes, indicate that the true width of the drill holes reported here 
are approximately 75-100% of drill intersection width.

The winter 2016 drilling was completed on March 30, 2016 with 7,310 meters 
drilled of which 3,825 meters have been reported to date. Logging and cutting 
of the core has been completed and results of the remaining zones that were 
tested, encompassing 3,485 meters of drilling on multiple zones, will be 
interpreted and released in the coming weeks.

TerraX collected 526 samples for assay from the drilling reported here. Results 
ranged from below detection to 26.30 g/t Au. Drill hole collar locations were 
surveyed to sub-meter accuracy. Down hole surveying (Easy Shot) was completed 
on all holes. TerraX inserts certified standards and blanks into the sample 
stream as a check on laboratory QC. Drill core samples are cut by diamond saw 
at TerraX's core facilities in Yellowknife. A halved core sample is left in the 
core box. The other half core is sampled and transported by TerraX personnel in 
securely sealed bags to ALS Chemex's (ALS) preparation laboratory in 
Yellowknife. After sample preparation, samples are shipped to ALS's Vancouver 
facility for gold and ICP analysis. Gold assays of greater than 3 g/t are 
re-assayed on a 30 gm split by fire assay with a gravimetric finish. ALS is a 
certified and accredited laboratory service. ALS routinely inserts certified 
gold standards, blanks and pulp duplicates, and results of all QC samples are 
reported.

/T/


---------------------------------------------------------------------------
From          To
Drill Hole Dip  Azimuth     UTM Location                    (m)         (m)
----------------------
Easting   Northing
---------------------------------------------------------------------------
Hebert-Brent Main Zone
---------------------------------------------------------------------------
TCG16-034  -80       30     636796    6942503              1.90        9.00
------------------------------
incl.        1.90        2.94
---------------------------------------------------------------------------
TCG16-040  -60       30     636834    6942469              1.50        3.35
---------------------------------------------------------------------------
TCG16-043  -60      290     636816    6942499              9.09       19.30
---------------------------------------------------------------------------
TCG16-044  -85      290     636816    6942499              8.61       19.62
---------------------------------------------------------------------------
TCG16-052  -45      135     636817    6942499             16.00       24.00
------------------------------
incl.       20.00       23.00
---------------------------------------------------------------------------
TCG16-053  -45      160     636847    6942478              6.40       17.05
---------------------------------------------------------------------------

---------------------------------------------------------------------------


---------------------------------------------------------------------
Interval          Au
Drill Hole Dip  Azimuth     UTM Location              (m)         g/t
----------------------
Easting   Northing
---------------------------------------------------------------------
Hebert-Brent Main Zone
---------------------------------------------------------------------
TCG16-034  -80       30     636796    6942503        7.10        3.61
------------------------
1.04       12.75
---------------------------------------------------------------------
TCG16-040  -60       30     636834    6942469        1.85       15.08
---------------------------------------------------------------------
TCG16-043  -60      290     636816    6942499       11.30        1.19
---------------------------------------------------------------------
TCG16-044  -85      290     636816    6942499       11.01        1.01
---------------------------------------------------------------------
TCG16-052  -45      135     636817    6942499        8.00        3.21
------------------------
3.00        7.09
---------------------------------------------------------------------
TCG16-053  -45      160     636847    6942478       10.65        0.75
---------------------------------------------------------------------

---------------------------------------------------------------------

/T/

The technical information contained in this news release has been approved by 
Joseph Campbell, the President of TerraX, who is a Qualified Person as defined 
in "National Instrument 43-101, Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold ("YCG") encompasses 118 sq km of contiguous land 
immediately north and south of the City of Yellowknife in the Northwest 
Territories. Through a series of acquisitions, TerraX now controls one of the 
six major high-grade gold camps in Canada. Being within 15 km of the City of 
Yellowknife, the YCG is close to vital infrastructure, including 
transportation, service providers, hydro-electric power and skilled 
tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering 23 km of 
strike length on the southern and northern extensions of the shear system that 
hosted the high-grade Con and Giant gold mines. The project area contains 
multiple shears that are the recognized hosts for gold deposits in the 
Yellowknife gold district, with innumerable gold showings and recent high grade 
drill results that serve to indicate the project's potential as a world-class 
gold district.

For more information on the YCG project, please visit our web site at 
www.terraxminerals.com.

On behalf of the Board of Directors

Joe Campbell
President and CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408
Toll Free: 1-866-460-0408
info@paradox-pr.ca
www.terraxminerals.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=567049559