Source	MARKET NEWS
Date	05/19/2016
Time	05:04:11 AM

Company	 Terrax Minerals Inc.
Title	Drills 8.00 
M @ 3.21 G/t Au And 1.85 M @ 15.08 G





    CDNX Symbol: TXR











Press Release





TERRAX MINERALS INC ("TXR-V;TRXXF-0")
- Drills 8.00 M @ 3.21 G/t Au And 1.85 M @ 15.08 G/t Au At
- Hebert-Brent Zone, Yellowknife City Gold

TerraX Minerals Inc. has received assay results from a 19 hole
drill program totalling 784 meters at the Hebert-Brent Zone on the
Yellowknife City Gold Project ("YCG"), immediately north of Yellowknife
in the Northwest Territories. All holes were very shallow (average 41
meters depth) testing interpreted shallow dip, plunge, and strike
extensions of the mineralized zones exposed on surface.

The Hebert-Brent Zone was originally discovered in the summer of
2015 and was channel sampled along exposed zones of mineralization
(11.0 m @ 7.55 g/t Au, news release August 11, 2015), and was
subsequently tested with 6 drill holes (10.26 m @ 3.61 g/t Au, news
release November 18, 2015). The zone has particular interest to TerraX
as it demonstrates that the YCG has sulphide replacement style
mineralization with little or no quartz veining, a deposit type that
can produce large deposits.

The drilling reported here tested several potential extensions to
the surface mineralization. Six holes (TCG16-34, 040, 043, 044, 052 and
053) totalling 242 meters tested mineralization along strike and to the
south of the surface mineralization. All these holes hit sulphide
replacement gold zones over a strike length of 125 m. Highlights
include:

//st

8.00 m @ 3.21 g/t Au, including 3.00 m @ 7.09 g/t Au in hole TCG16-052

1.85 m @ 15.08 g/t Au in hole TCG16-040

7.10 m @ 3.61 g/t Au, including 1.04 m @ 12.75 g/t Au in hole TCG16-034

//et

Based on this drilling, we believe that the main Hebert-Brent zone
and the Hebert-Brent South Zone have potential along a projected
southerly dip. Due to the limited meterage budgeted for this program
and time constraints, drilling was terminated before the southern dip
potential of both zones could be tested.

Of the remaining holes, eight holes (TCG16-35 to 038, 041, 049,
050, and 051) totalling 315 meters tested an interpreted northerly
dipping quartz feldspar dyke (QFP) that hosts some of the
mineralization exposed on surface. None of these holes intersected
significant gold mineralization. Three holes (TCG16-54 to 056)
totalling 151 meters tested a projected strike extension of the
Hebert-Brent zone to the east, and a sulphide chert horizon beneath the
projected zone. Drill hole TCG16-055 hit Hebert-Brent style
mineralization (0.85 m @ 4.61 g/t Au). Two holes (TCG16-39 and 042)
totalling 76 meters tested the northerly dipping QFP dyke associated
with the surface exposure of the Hebert-Brent South Zone. Neither hole
hit significant mineralization.

The Hebert-Brent deposit type remains a high priority target for
TerraX as larger zones of similar alteration and mineralization have
been located to the north, east, and south of Hebert-Brent. Using the
knowledge gained from the Hebert-Brent Zone these new zones will be
comprehensively mapped and sampled during the 2016 field season
beginning in June.

A map showing the location of drill holes on the Hebert-Brent
target area is available on our web site under "2016 Field
Exploration".

Drill holes were drilled close to normal to the interpreted strike
and dip of the zones. Current interpretations for dip, based on the
surface trenching and the drill holes, indicate that the true width of
the drill holes reported here are approximately 75-100% of drill
intersection width.

The winter 2016 drilling was completed on March 30, 2016 with
7,310 meters drilled of which 3,825 meters have been reported to date.
Logging and cutting of the core has been completed and results of the
remaining zones that were tested, encompassing 3,485 meters of drilling
on multiple zones, will be interpreted and released in the coming
weeks.

TerraX collected 526 samples for assay from the drilling reported
here. Results ranged from below detection to 26.30 g/t Au. Drill hole
collar locations were surveyed to sub-meter accuracy. Down hole
surveying (Easy Shot) was completed on all holes. TerraX inserts
certified standards and blanks into the sample stream as a check on
laboratory QC. Drill core samples are cut by diamond saw at TerraX's
core facilities in Yellowknife. A halved core sample is left in the
core box. The other half core is sampled and transported by TerraX
personnel in securely sealed bags to ALS Chemex's (ALS) preparation
laboratory in Yellowknife. After sample preparation, samples are
shipped to ALS's Vancouver facility for gold and ICP analysis. Gold
assays of )3 g/t are re-assayed on a 30 gm split by fire assay with a
gravimetric finish. ALS is a certified and accredited laboratory
service. ALS routinely inserts certified gold standards, blanks and
pulp duplicates, and results of all QC samples are reported.

//st

---------------------------------------------------------------------------
From          To
Drill Hole Dip  Azimuth     UTM Location                    (m)         (m)
----------------------
Easting   Northing
---------------------------------------------------------------------------
Hebert-Brent Main Zone
---------------------------------------------------------------------------
TCG16-034  -80       30     636796    6942503              1.90        9.00
------------------------------
incl.        1.90        2.94
---------------------------------------------------------------------------
TCG16-040  -60       30     636834    6942469              1.50        3.35
---------------------------------------------------------------------------
TCG16-043  -60      290     636816    6942499              9.09       19.30
---------------------------------------------------------------------------
TCG16-044  -85      290     636816    6942499              8.61       19.62
---------------------------------------------------------------------------
TCG16-052  -45      135     636817    6942499             16.00       24.00
------------------------------
incl.       20.00       23.00
---------------------------------------------------------------------------
TCG16-053  -45      160     636847    6942478              6.40       17.05
---------------------------------------------------------------------------

---------------------------------------------------------------------------



---------------------------------------------------------------------
Interval          Au
Drill Hole Dip  Azimuth     UTM Location              (m)         g/t
----------------------
Easting   Northing
---------------------------------------------------------------------
Hebert-Brent Main Zone
---------------------------------------------------------------------
TCG16-034  -80       30     636796    6942503        7.10        3.61
------------------------
1.04       12.75
---------------------------------------------------------------------
TCG16-040  -60       30     636834    6942469        1.85       15.08
---------------------------------------------------------------------
TCG16-043  -60      290     636816    6942499       11.30        1.19
---------------------------------------------------------------------
TCG16-044  -85      290     636816    6942499       11.01        1.01
---------------------------------------------------------------------
TCG16-052  -45      135     636817    6942499        8.00        3.21
------------------------
3.00        7.09
---------------------------------------------------------------------
TCG16-053  -45      160     636847    6942478       10.65        0.75
---------------------------------------------------------------------

---------------------------------------------------------------------
//et

The technical information contained in this news release has been
approved by Joseph Campbell, the President of TerraX, who is a
Qualified Person as defined in "National Instrument 43-101, Standards
of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold ("YCG") encompasses 118 sq km of
contiguous land immediately north and south of the City of Yellowknife
in the Northwest Territories. Through a series of acquisitions, TerraX
now controls one of the six major high-grade gold camps in Canada.
Being within 15 km of the City of Yellowknife, the YCG is close to
vital infrastructure, including transportation, service providers,
hydro-electric power and skilled tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering
23 km of strike length on the southern and northern extensions of the
shear system that hosted the high-grade Con and Giant gold mines. The
project area contains multiple shears that are the recognized hosts for
gold deposits in the Yellowknife gold district, with innumerable gold
showings and recent high grade drill results that serve to indicate the
project's potential as a world-class gold district.

For more information on the YCG project, please visit our web site
at www.terraxminerals.com.

On behalf of the Board of Directors

Joe Campbell
President and CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.




























TSX Venture closing price for TXR-V
Date: 2016/05/18
Closing Price: 0.35

TEL: 514-341-0408
Toll Free: 1-866-460-0408
E-mail:   info@paradox-pr.ca
Internet: www.terraxminerals.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1613900002TS11613900443-05015120160519