Source	MARKET NEWS
Date	05/19/2016
Time	08:30:40 AM

Company	 Engold Mines Ltd.
Title	Gold 
Equivalent Values for 2008 2015 Aurizon Sou





    CDNX Symbol: EGM











Press Release





ENGOLD MINES LTD. ("EGM-V")
- Gold Equivalent Values for 2008-2015 Aurizon South Gold
- Drill Results

David H. Brett, President & CEO, EnGold Mines Ltd., ("EnGold,"
www.engold.ca, formerly GWR Resources Inc. GWQ) reports results of 25
drill holes completed between 2008 and 2015 from its 100% owned Aurizon
South Gold Project calculated in equivalent gold values to incorporate
the significant copper and silver grades into a single gold grade,
which has resulted in a considerable increase in the expressed gold
grades. For example, AZS08-07 includes a previously published intercept
of 14 metres grading 10.36 gpt gold, 1.46% copper & 7.2 gpt silver,
which when published as a gold equivalent returns 14 metres grading
12.17 gpt gold, a 14.8% increase in the value attributed to the gold
grade.
A full table of the revised results and the formula for
calculating the gold equivalent values is provided below. The Aurizon
South Gold Project is located within Engold's 18,275 hectare (45,158
acres) Lac La Hache Property in BC's Cariboo region.
"Incorporating Aurizon South's considerable copper and silver
values into our published gold grades makes assessing the significance
of our drill results a lot easier," said EnGold President & CEO David
Brett. "I believe Aurizon South has the potential to develop into a
high grade, low cost gold producer, with the copper and silver values
having significant impact."
EnGold VP of Exploration Robert Shives, P.Geo., states:
"Drilling at Aurizon South shows high gold (plus copper and
silver) grades occur within a near-vertical structure measuring 300m
along strike (open), across potentially mineable true widths ranging
from 3 to )10 m, to depths of more than 600 m (open). High grades of
gold, copper and silver are common, hosted mainly by hydrothermal
breccia, related fractures, quartz veins and silicified zones.
Although multi-gram gold values are of primary interest at Aurizon
South, considerable additional value is provided by accompanying copper
(grades up to several percent) and silver (grades exceeding 20 grams
per tonne) as indicated in the tables below, expressed as equivalent
gold values. In addition, drill plan maps are available on the
corporate website."

Selected core assays 2008 - 2012, Aurizon South Prospect

http://www.newsfilecorp.com/release/20686/EnGold-Reports-Gold-Equivalent-Va
lues-for-20082015-Aurizon-South-Gold-Drill-Results



Notes
True thickness of the mineralized zone at Aurizon South is
variable: assays are reported over drill core intervals.
* Gold equivalent grade includes copper and silver values.
Metallurgical recoveries are assumed to be 100%.
* Au Eq = Au g/t + (Cu grade x ((Cu price per pound/Au price per
ounce) x 0.06857 pounds per ounce x 10000 g per %)) + Ag grade x (Ag
price per ounce/Au price per ounce)).
10-day average metal price on May 12, 2016 in $Canadian: Gold $C
1634/ounce, Copper $C 2.79/lb, Silver $C 22.31/ounce
USD to CAD exchange rate: 1$US = 1.28$CA (May 12, 2016)
1 metric tonne = 2204.62 pounds1 pound = 14.48 troy ounces1 troy
ounce = 31.103 grams
Quality Control/Quality Assurance Program
EnGold Mines Ltd follows procedures which ensure sample security,
chain of custody and Quality Assurance/Quality Control (QA/QC) for all
drilling and geochemical sampling, conforming to best current industry
practices as defined by the Canadian Institute for Mining, Metallurgy
and Petroleum (CIM) standards, and required for TSX-listed companies as
defined by National Instrument 43-101.
All drill core was logged, photographed and cut in half with a
diamond saw. Half core samples were bagged, sealed and sent securely to
ALS Canada Ltd in Kamloops for preparation. Analyses were completed by
ALS Minerals in Vancouver for Au (30 gram split fire assay, atomic
absorption finish, gravimetric finish), Cu (ore grade, aqua regia), Ag
(ore grade, aqua regia) and 35 additional elements by 4 acid digestion
of a 0.25 g sample followed by an inductively coupled plasma - atomic
absorption spectroscopy finish. As part of our comprehensive QA/QC
program, one standard, and one in-line replicate were inserted into the
sample stream in each group of 20 samples, as well as one or more field
blanks in each analytical batch.
Robert B.K. Shives, P.Geo., a Qualified Person as defined under
National Instrument 43-101, has reviewed and approved the technical
content of this release.
Engold Mines Ltd.
Per/
David Brett, President & CEO
For further information, please contact: David Brett, Telephone:
604-682-2421
This news release may contain "forward-looking statements".
Readers are cautioned that any such statements are not guarantees of
future performance and that actual development or results may vary
materially from those in these "forward looking statements."
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

To view a printable version of the press release, please visit:

http://orders.newsfilecorp.com/files/2268/20686_27590_aurizonupdatefinal.pd
f




______________________________________
_______________________________________________
TSX Venture closing price for EGM-V
Date: 2016/05/16
Closing Price: 0.06
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1613900033TS11613901413-08292620160519