Source	MARKET NEWS
Date	05/16/2016
Time	09:56:37 AM

Company	 Amex Exploration Inc.
Title	2016 
Winter Drilling Program Completed At Amex's





    CDNX Symbol: AMX











Press Release





AMEX EXPLORATION INC ("AMX-V")
AGNICO EAGLE MINES LTD ("AEM-T")
- 2016 Winter Drilling Program Completed At Amex's Perron Property

Amex Exploration Inc. has been informed by Agnico Eagle Mines Ltd
"Agnico Eagle" that it has completed its winter exploration program on
Amex 100% owned Perron Property as planned and announced in January
2016 (see PR2016-01-25). The Perron project is located approximately 8
km northwest of the village of Normetal, and approximately 110
kilometers North of the town of Rouyn-Noranda in the Abitibi region of
Quebec.

Agnico Eagle's winter drilling program consisted of 9 drill holes
totalling 4,643 meters of drilling with combined down hole pulse EM
geophysic on two defined target areas.

The first and main target area was located in the vicinity of the
latest follow-up drilling of the new mineralisation intersected in
previous phase of drilling on the Normetal Mine Horizon (NMH) that
returned values of 0.17% Cu, 1.62% Zn, 6.28 g/t Ag and 0.22g/t Au over
2.1 meters in hole 163-15-023 (see PR-2015-12-16).

Eight drill holes were drilled to test the extension of the
stratabound mineralized horizon laterally and at variable depth
covering an area of about 6 km of strike length along the NMH.
Polymetallic intervals, from previous drilling in holes 015, 022 and
023, show a continuous panel concordant to the stratigraphy that makes
the target zone very predictable. In these holes, the mineralization
lies within the same intermediate lapilli-tuff unit (with the garnet
porphyroblasts and the pervasive chlorite alteration) that is similar
to the old Normetal Mine (11 MT @ 2.15% Cu, 5.12% Zn, 0.55 g/t Au and
45.25 g/t Ag).

The second target area is located at about 700 meters to the south
of the first target area in a different stratigraphic unit where a
single drill hole was executed to test the Perron gold rich
polymetallic mineralization located near the favourable V1-V2 contact.
This drill hole tested at depth the mineralized intersect of hole
163-15-21 that returned 9.45 g/t Au, 2.60 g/t Ag, 300 ppm Cu and 1100
ppm Zn over 0.8 meters within a broader silicified and sericitized
altered zone that returned 1.70 g/t Au, 0.58 g/t Ag, 87 ppm Cu and 557
ppm Zn over 5.5m (see PR2015-06-16).

A total of 1,368 samples were taken and sent to ALS -Chemex
Laboratories in Val d'Or and Amex have been informed by Agnico Eagle
that all of the results should be received at the latest by early June
2016. When available, these results will be announced by Amex promptly.


Amex Exploration Inc. is a junior mining exploration company
listed on the TSX Venture Exchange whose primary objective is to
develop and bring into production viable gold and base metal deposits.

Jacques Marchand, P.Eng., who is a Qualified Persons as defined by
Canadian NI 43-101, have approved the technical information reported in
this news release.

Forward-looking statements:

Except for statements of historical facts, all statements in this
news release regarding, without limitation, new project acquisitions,
future plans and objectives are forward-looking statements which
involve risks and uncertainties. There can be no assurance that such
statements will prove to be accurate; Actual results and future events
could differ materially from those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for AMX-V
Date: 2016/05/12
Closing Price: 0.06

TEL: (514) 866-8209  Jacques Trottier, PhD
President and Chief Executive Officer
Amex Exploration Inc.
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1613600041TS11613602397-09542020160516