Source	Marketwire
Date	05/24/2016
Time	02:30:24 AM

Company	 AQM COPPER INC.
Title	AQM Copper Releases Positive Results From Preliminary Feasibility Study of 
the Zafranal Copper Project in Peru





    CDNX Symbol: AQM











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: AQM Copper Inc.

TSX VENTURE, BVL SYMBOL: AQM

May 24, 2016

AQM Copper Releases Positive Results From Preliminary Feasibility Study of the 
Zafranal Copper Project in Peru


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 24, 2016) - AQM Copper Inc. 
(TSX VENTURE:AQM)(BVL:AQM) ("AQM" or the "Company") is pleased to announce the 
completion of a positive, independent Preliminary Feasibility Study ("PFS") of 
the Company's Zafranal Project ("Project") located in the southern Peru 
porphyry copper belt.

The Zafranal Copper Project is owned by Compania Minera Zafranal S.A.C. 
("CMZ"), a joint venture company that is beneficially owned by AQM, Teck 
Resources Limited, and Mitsubishi Materials Corporation. AQM, through Minera 
AQM Copper Peru S.A.C. ("MAQM"), has been the operator of the Project since 
2009.

The Zafranal PFS was independently prepared by Ausenco Peru S.A.C., 
("Ausenco"), Amec Foster Wheeler PLC ("AmecFW") and NCL Ingenieria y 
Construccion SpA ("NCL"), with the support from other specialist consultants. 
The PFS report reflects the design of an open pit mine, conventional flotation 
concentrator processing facility and associated infrastructure.

PFS Highlights:

/T/

--  The reported mineral reserve totals 401 million tonnes ("Mt") grading
0.40 % total copper ("Cu") and 0.07 g/t gold ("Au"), and the mine-
concentrator as designed is expected to produce 3.1 billion pounds of
copper and 484,000 ounces of gold over the 19-year life of the
operation.
--  Initial capital cost is US$ 1.16 billion and the base case after-tax
valuation yields an expected net cash flow of US$ 1.6 billion with a net
present value ("NPV") of US$ 496 million at an 8 % discount rate.
--  After-tax internal rate of return ("IRR") is 15.9 % and the Project has
a 5.1-year payback period from the start of operations.
--  Production averages 120,000 tonnes per annum ("tpa") of copper in
concentrate over the first 5-year period and 75,000 tpa over the life of
the operations.
--  A total of 4.4 million dry metric tons ("dmt") of concentrate will be
produced over a 19-year period with an average grade of 32.5 % copper
and 3.4 grams per tonne gold.
--  No deleterious elements in any significant concentration were found in
the copper concentrate produced from the flotation testwork, and all the
impurity elements were found to be below smelter penalty limits.
--  A brackish-water aquifer located within 35 kilometres ("km") of the
proposed process plant site has the potential to satisfy the project's
process water requirements. Testwork has indicated this water is
suitable for concentrator processing,
--  Thickened tailings disposal will be in a natural basin approximately 1
km downhill from the plant site.

/T/

Bruce Turner, President and Chief Executive Officer of AQM states, "We are 
extremely pleased with the results of the PFS as it provides a solid basis for 
advancing the Project. The PFS reflects the combined experience and efforts of 
the partners and our consultants in delivering an excellent result. Our 
engagement with the regional and local authorities and representatives of the 
local communities has generated a constructive space for continued dialogue and 
we are optimistic that all the stakeholders will benefit from the continued 
development of the Zafranal Project. AQM currently has CDN$ 2 million in the 
bank in Canada, and an additional US$ 10 million in its subsidiary MAQM in Peru 
to contribute towards its share of the cost of the next level of study for the 
Project. We are currently in discussions with our partners as to the next steps 
to advance the Project."

The PFS was commissioned to further define the development plan for the 
Zafranal deposit based on the findings from earlier studies but incorporating 
the following modifications:

/T/

--  An additional 17,671 metres ("m") of diamond drilling and 9,931 m of
reverse circulation ("RC") drilling, including 5,534 m in-fill drilling
of Zafranal Main Zone, 4,965 m of metallurgical drilling, 2,267 m of
geotechnical drilling, 8,388 m of hydrogeological drilling and 6,447 m
of condemnation drilling
--  Revised geological and resource models, and development of a
geometallurgical model
--  Variable concentrator throughput based on mineral zone (competence,
hardness and rock quality)
--  Variable recovery and concentrate grade based on geometallurgical
domains
--  Identification and investigation of a brackish groundwater resource
within 35 km of the process plant site that is unlikely to be of value
for other than industrial uses and could potentially be a water supply
for the Project.

/T/

PFS Results Summary:

Economic Analysis

Long-term forecasted copper and gold prices of US$ 3.00 /lb and US$ 1200 /oz, 
respectively, were used to estimate Mineral reserves and the base case 
valuation. The basis of the economic analysis contained in the PFS was signed 
off by Ausenco and contains production parameters, capital costs, operating 
costs, pre-tax and post-tax financial projections. The Project is projected to 
yield the following financial results:

Summary of Financial Results (1)

/T/

----------------------------------------------------------------------------
DESCRIPTION                                      PRE-TAX (2)    POST-TAX (3)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital Cost (US$ million)                     1,157           1,157
----------------------------------------------------------------------------
Net Cash Flow (US$ million)                            2,711           1,649
----------------------------------------------------------------------------
Net Present Value at 5 % discount rate (US$
million)                                              1,536             813
----------------------------------------------------------------------------
Net Present Value at 8 % discount rate (US$
million)                                              1,084             496
----------------------------------------------------------------------------
Net Present Value at 10 % discount rate (US$
million)                                                849             333
----------------------------------------------------------------------------
Payback (years) (4)                                      2.6             5.1
----------------------------------------------------------------------------
Internal Rate of Return (%)                             23.8            15.9
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
1.  Valuation based on 100% Project and 100% Equity. The Zafranal Project is
owned through CMZ, a 50/50 corporate joint venture between Teck
Resources Limited and the Company's operating subsidiary, Minera AQM
Copper Peru S.A.C. ("MAQM"). MAQM is owned 60% by the Company and 40% by
Mitsubishi Materials Corporation. As such, the Company has a 30%
beneficial ownership interest in the Zafranal Project.
2.  Based on pre-tax economic cash flows.
3.  Based on after-tax economic cash flows, reflecting mining royalty,
special mining tax, corporate income tax (26%) and workers' profit
sharing. A 9.3% dividend withholding tax is not included but it would be
applied to any repatriation of profits. The calculation of taxes in the
valuation was reviewed by Peruvian tax specialists from the law firm of
Zuzunaga, Assereto & Zegarra Abogados, Lima Peru.
4.  From the start of mill operations.

/T/

Key Operating Parameters

/T/

----------------------------------------------------------------------------
DESCRIPTION                                                UNITS         LOM
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine Production
----------------------------------------------------------------------------
Flotation Ore                                                 kt     400,569
----------------------------------------------------------------------------
Waste                                                         kt     583,684
----------------------------------------------------------------------------
Stripping Ratio (incl. Leach Stockpile)                                 1.46
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Ore Processing
----------------------------------------------------------------------------
Flotation Ore                                                 kt     400,569
----------------------------------------------------------------------------
Copper Head Grade - Average                                    %        0.40
----------------------------------------------------------------------------
Gold Head Grade - Average                                    g/t        0.07
----------------------------------------------------------------------------
Copper Recovery - Average                                      %        88.1
----------------------------------------------------------------------------
Gold Recovery - Average                                        %        54.3
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Metal Production
----------------------------------------------------------------------------
Copper - Recovered                                    million lb       3,123
----------------------------------------------------------------------------
Copper - Annual Average                               million lb         164
----------------------------------------------------------------------------
Gold - Recovered                                             koz         484
----------------------------------------------------------------------------
Gold - Annual Average                                        koz          25
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Initial Capital Cost

The initial capital cost, including contingency, for the Project is estimated 
at US$ 1,157 million with an expected accuracy range of +/-25 %. The PFS 
envisages that a mining contractor will operate the open pit for the pre-mine 
period and until Year 3 of production. Year 4 will be a transition year with 
the contractor winding down and the CMZ operation of the open pit ramping up 
and continuing until the end of mine life. A summary of initial capital 
expenditures follows:

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine                                                             $       142
----------------------------------------------------------------------------
Concentrator                                                     $       430
----------------------------------------------------------------------------
On-Site Infrastructure                                           $        33
----------------------------------------------------------------------------
Off-Site Infrastructure                                          $        98
----------------------------------------------------------------------------
Total Direct Capital                                             $       703
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Project Preliminaries                                            $       103
----------------------------------------------------------------------------
Indirect Costs                                                   $       132
----------------------------------------------------------------------------
Owners Costs                                                     $        68
----------------------------------------------------------------------------
Total Indirect Capital                                           $       303
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Contingency (15%)                                                $       151
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Initial Capital Cost                                       $     1,157
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Sustaining Capital Cost

The significant sustaining capital in the Mine reflects the purchase of mine 
equipment fleet in Year 3 and 4 of production as CMZ takes over operation of 
the mine.

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine                                                             $       213
----------------------------------------------------------------------------
Concentrator                                                     $        15
----------------------------------------------------------------------------
On-Site Infrastructure                                           $         1
----------------------------------------------------------------------------
Total Sustaining Capital                                         $       229
----------------------------------------------------------------------------
----------------------------------------------------------------------------Cont
ingency (15%)                                                $        34
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Sustaining Capital Cost                                    $       263
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Total Project Capital Cost

The total Project capital cost is shown in the following table for the LOM:

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital Cost                                             $     1,157
----------------------------------------------------------------------------
Sustaining Capital Cost                                          $       263
----------------------------------------------------------------------------
Project Closure Cost                                             $       136
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Capital Cost                                               $     1,556
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Each element of the estimate is developed initially as a base cost only. A 
growth allowance has then been allocated to each element of the cost to reflect 
the level of definition in pricing and design maturity relating to that 
element. A growth allowance of US$ 95 million, which is expected to be 
expended, has been included in the initial capital cost, and represents 11.2 % 
of Total Direct Cost.

The estimated contingency was then assessed as 15 % of total initial capital 
cost and 15 % of total sustaining capital cost to arrive at a project estimate 
within the required 50 % confidence interval ("P50"). The estimated project 
closure cost was deemed to already include sufficient contingency. The value of 
the base estimate, the growth allowance, the contingency and the project 
closure cost represent the total project estimate. Risk events that may or may 
not affect the capital cost estimate are covered in the positive range of 
sensitivity analyses.

Operating Cost

Average mine site production cost is estimated to be $ 1.29 /lb copper produced 
from plant feed material processed, including mining, re-handling, milling, and 
flotation as shown below:

/T/

----------------------------------------------------------------------------
COST ITEM                         UNIT          UNIT COST
(US$)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Contractor Mining (Y1 to Y4)                      $ /tonne mined        1.93
----------------------------------------------------------------------------
Owner Mining (Y4 to Y19)                          $ /tonne mined        1.76
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Production Mining (Y1 to Y19)                        $ /t milled        4.25
----------------------------------------------------------------------------
Milling                                              $ /t milled        4.59
----------------------------------------------------------------------------
G&A                                                  $ /t milled        1.22
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mine Site Operations                           $ /t milled       10.05
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mine Site Operations                     $ /lb Cu Produced        1.29
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
The estimated costs exclude the two-year pre-stripping period. Rounding of
numbers may result in apparent summation differences.

/T/

Average C1 operating costs for the 19-year production period total $ 1.59 per 
payable pound of copper net of transport losses and smelter deductions. A 
breakdown of these costs is shown in the following table, along with estimates 
for C2 and C3 costs as per Wood Mackenzie definitions.

/T/

----------------------------------------------------------------------------
COST ITEM                AVERAGE      YEAR 1 TO    YEAR 6 TO
FOR 19 YEARS    YEAR 5       YEAR 10
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Onsite Costs (Mine, Mill and G&A)            1.33         0.95         1.35
----------------------------------------------------------------------------
Concentrate Road Transportation              0.06         0.06         0.06
----------------------------------------------------------------------------
Port Charges, Ocean Freight &
Insurance                                   0.14         0.13         0.14
----------------------------------------------------------------------------
TC/RC's and Marketing                        0.24         0.23         0.24
----------------------------------------------------------------------------
Less By-Product Credits                     (0.17)       (0.15)       (0.17)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C1 Costs                               1.59         1.21         1.62
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Depreciation & Amortization                  0.49         0.57         0.33
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C2 Costs                               2.07         1.78         1.96
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Royalties                                    0.07         0.09         0.06
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C3 Costs                               2.14         1.87         2.02
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
Unit Costs based on payable pounds of copper and rounding of numbers may
result in apparent summation differences.

/T/

Financial Sensitivities

In addition to the base case after-tax evaluation of economic cash flows using 
a copper price of $3.00 /lb, initial capital cost of US$ 1,157 million and a 
discount rate of 8 %; different copper prices and other variables at the base 
case copper price were tested to determine financial sensitivities of the 
Project as shown in the following tables:

/T/

Copper Prices (US$/lb)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Copper Price Sensitivity                   2.00   2.50   3.00   3.50   4.00
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Undiscounted Cash Flows       Pre-Tax      (311) 1,204  2,711  4,236  5,753
----------------------------------------------
US$M                          After-Tax    (478)   648  1,649  2,623  3,574
----------------------------------------------------------------------------
After-Tax NPV US$M at         5%           (515)   180    813  1,426  2,029
----------------------------------------------
Discount Rates                8%           (547)    (5)   496    978  1,454
----------------------------------------------
10%          (567)  (101)   333    749  1,162
----------------------------------------------------------------------------
Internal Rate of Return       IRR %         0.0%   7.9%  15.9%  22.1%  27.6%
----------------------------------------------------------------------------
----------------------------------------------------------------------------


-----------------------------------
Changes To Base Case NPV8% (US$M)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inputs /Changes to Inputs       Base Case   -25%   -10%     0%    10%    25%
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital (US$M real)         1,157   745    595    496    394    241
----------------------------------------------------------------------------
Total Op. Costs (US$/t milled)
(1)                                10.05   788    613    496    374    188
----------------------------------------------------------------------------
Head Grade - Feed (Cu %)            0.401  (155)   239    496    745  1,118
----------------------------------------------------------------------------
Head Grade - Feed (Au g/t)          0.069   455    479    496    510    534
----------------------------------------------------------------------------

Notes:
1.  Excludes in-land freight costs

/T/

Location

The Zafranal Project is located in southern Peru about 166 km by road (90 km 
straight-line distance) northwest of the city of Arequipa, 80 km from tidewater 
and approximately 216 km by road from the Port of Matarani.

The regional climate is arid with scarce precipitation, and average 
temperatures range between 7 degrees C in winter and 24 degrees C in summer. 
Elevation ranges between 1,400 and 2,900 m above sea level ("masl") in the 
Project area.

Geology

Zafranal is a classic example of an Andean style porphyry copper-gold deposit. 
Mineralization is hosted in Jurassic volcano-sedimentary rocks and in a diorite 
intrusive suite of late Cretaceous age. The emplacement of mineralized 
porphyries is structurally controlled and occurs near or at the intersection of 
a series of northwest trending strike-slip faults belonging to the Incapuquio 
fault system, and regional east-west trending structures. Primary 
mineralization occurs as chalcopyrite both as disseminations and in quartz 
stockworks. A near surface well-developed sub-horizontal chalcocite rich 
supergene enrichment blanket has developed over a 2.5 km strike length, with 
thicknesses of up to 180 m.

Mining

Conventional open pit operation with mine life of approximately 19 years 
(excluding two years of pre-stripping) with an average waste to ore strip ratio 
of 1.36: 1, for the production period. The mine plan developed for the Zafranal 
Project is designed for a variable feed to a concentrator in the range of 
55,000 to 64,000 tonnes per day depending on mineral type, with a peak total 
material movement of 75 million tonnes per year. The mine is scheduled to work 
seven days per week or 365 days per year.

The mine design proposes two contiguous pits with a combined strike length of 
3,500 m, maximum width of 1,000 m, and maximum depth of 456 m. Pre-production 
stripping of 45 Mt will be required prior to the start-up of the concentrator. 
Peak daily movement of 205,000 t of material occurs in production Year 1.

A total of 18 Mt of waste from the mine will be used to construct facility 
platforms and roadways, and the remaining 548 Mt of waste will be deposited in 
valley dumps using relatively short haulage cycles. The mine will utilize three 
of these types of dumps, two above and one below the planned open pits. The 
northeast dump will receive 12.8 million tonnes. The north waste dump will 
receive 151 Mt and the central waste dump, below the main open pit will receive 
384 Mt. A 17.6 Mt oxide and mixed mineral stockpile will be created on top of 
the north section of the central waste dump with a crest elevation of 2,580 
masl. There are no plans to construct a process plant to process this material 
at this time and the material in this stockpile is considered as waste. A 38.7 
Mt low-grade sulfide stockpile will be created to the west of the open pit. 
This material will be reclaimed at the end of the mine life and processed 
through the concentrator.

Milling



NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: AQM Copper Inc.

TSX VENTURE, BVL SYMBOL: AQM

May 24, 2016

AQM Copper Releases Positive Results From Preliminary Feasibility Study of the 
Zafranal Copper Project in Peru


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 24, 2016) - AQM Copper Inc. 
(TSX VENTURE:AQM)(BVL:AQM) ("AQM" or the "Company") is pleased to announce the 
completion of a positive, independent Preliminary Feasibility Study ("PFS") of 
the Company's Zafranal Project ("Project") located in the southern Peru 
porphyry copper belt.

The Zafranal Copper Project is owned by Compania Minera Zafranal S.A.C. 
("CMZ"), a joint venture company that is beneficially owned by AQM, Teck 
Resources Limited, and Mitsubishi Materials Corporation. AQM, through Minera 
AQM Copper Peru S.A.C. ("MAQM"), has been the operator of the Project since 
2009.

The Zafranal PFS was independently prepared by Ausenco Peru S.A.C., 
("Ausenco"), Amec Foster Wheeler PLC ("AmecFW") and NCL Ingenieria y 
Construccion SpA ("NCL"), with the support from other specialist consultants. 
The PFS report reflects the design of an open pit mine, conventional flotation 
concentrator processing facility and associated infrastructure.

PFS Highlights:

/T/

--  The reported mineral reserve totals 401 million tonnes ("Mt") grading
0.40 % total copper ("Cu") and 0.07 g/t gold ("Au"), and the mine-
concentrator as designed is expected to produce 3.1 billion pounds of
copper and 484,000 ounces of gold over the 19-year life of the
operation.
--  Initial capital cost is US$ 1.16 billion and the base case after-tax
valuation yields an expected net cash flow of US$ 1.6 billion with a net
present value ("NPV") of US$ 496 million at an 8 % discount rate.
--  After-tax internal rate of return ("IRR") is 15.9 % and the Project has
a 5.1-year payback period from the start of operations.
--  Production averages 120,000 tonnes per annum ("tpa") of copper in
concentrate over the first 5-year period and 75,000 tpa over the life of
the operations.
--  A total of 4.4 million dry metric tons ("dmt") of concentrate will be
produced over a 19-year period with an average grade of 32.5 % copper
and 3.4 grams per tonne gold.
--  No deleterious elements in any significant concentration were found in
the copper concentrate produced from the flotation testwork, and all the
impurity elements were found to be below smelter penalty limits.
--  A brackish-water aquifer located within 35 kilometres ("km") of the
proposed process plant site has the potential to satisfy the project's
process water requirements. Testwork has indicated this water is
suitable for concentrator processing,
--  Thickened tailings disposal will be in a natural basin approximately 1
km downhill from the plant site.

/T/

Bruce Turner, President and Chief Executive Officer of AQM states, "We are 
extremely pleased with the results of the PFS as it provides a solid basis for 
advancing the Project. The PFS reflects the combined experience and efforts of 
the partners and our consultants in delivering an excellent result. Our 
engagement with the regional and local authorities and representatives of the 
local communities has generated a constructive space for continued dialogue and 
we are optimistic that all the stakeholders will benefit from the continued 
development of the Zafranal Project. AQM currently has CDN$ 2 million in the 
bank in Canada, and an additional US$ 10 million in its subsidiary MAQM in Peru 
to contribute towards its share of the cost of the next level of study for the 
Project. We are currently in discussions with our partners as to the next steps 
to advance the Project."

The PFS was commissioned to further define the development plan for the 
Zafranal deposit based on the findings from earlier studies but incorporating 
the following modifications:

/T/

--  An additional 17,671 metres ("m") of diamond drilling and 9,931 m of
reverse circulation ("RC") drilling, including 5,534 m in-fill drilling
of Zafranal Main Zone, 4,965 m of metallurgical drilling, 2,267 m of
geotechnical drilling, 8,388 m of hydrogeological drilling and 6,447 m
of condemnation drilling
--  Revised geological and resource models, and development of a
geometallurgical model
--  Variable concentrator throughput based on mineral zone (competence,
hardness and rock quality)
--  Variable recovery and concentrate grade based on geometallurgical
domains
--  Identification and investigation of a brackish groundwater resource
within 35 km of the process plant site that is unlikely to be of value
for other than industrial uses and could potentially be a water supply
for the Project.

/T/

PFS Results Summary:

Economic Analysis

Long-term forecasted copper and gold prices of US$ 3.00 /lb and US$ 1200 /oz, 
respectively, were used to estimate Mineral reserves and the base case 
valuation. The basis of the economic analysis contained in the PFS was signed 
off by Ausenco and contains production parameters, capital costs, operating 
costs, pre-tax and post-tax financial projections. The Project is projected to 
yield the following financial results:

Summary of Financial Results (1)

/T/

----------------------------------------------------------------------------
DESCRIPTION                                      PRE-TAX (2)    POST-TAX (3)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital Cost (US$ million)                     1,157           1,157
----------------------------------------------------------------------------
Net Cash Flow (US$ million)                            2,711           1,649
----------------------------------------------------------------------------
Net Present Value at 5 % discount rate (US$
million)                                              1,536             813
----------------------------------------------------------------------------
Net Present Value at 8 % discount rate (US$
million)                                              1,084             496
----------------------------------------------------------------------------
Net Present Value at 10 % discount rate (US$
million)                                                849             333
----------------------------------------------------------------------------
Payback (years) (4)                                      2.6             5.1
----------------------------------------------------------------------------
Internal Rate of Return (%)                             23.8            15.9
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
1.  Valuation based on 100% Project and 100% Equity. The Zafranal Project is
owned through CMZ, a 50/50 corporate joint venture between Teck
Resources Limited and the Company's operating subsidiary, Minera AQM
Copper Peru S.A.C. ("MAQM"). MAQM is owned 60% by the Company and 40% by
Mitsubishi Materials Corporation. As such, the Company has a 30%
beneficial ownership interest in the Zafranal Project.
2.  Based on pre-tax economic cash flows.
3.  Based on after-tax economic cash flows, reflecting mining royalty,
special mining tax, corporate income tax (26%) and workers' profit
sharing. A 9.3% dividend withholding tax is not included but it would be
applied to any repatriation of profits. The calculation of taxes in the
valuation was reviewed by Peruvian tax specialists from the law firm of
Zuzunaga, Assereto & Zegarra Abogados, Lima Peru.
4.  From the start of mill operations.

/T/

Key Operating Parameters

/T/

----------------------------------------------------------------------------
DESCRIPTION                                                UNITS         LOM
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine Production
----------------------------------------------------------------------------
Flotation Ore                                                 kt     400,569
----------------------------------------------------------------------------
Waste                                                         kt     583,684
----------------------------------------------------------------------------
Stripping Ratio (incl. Leach Stockpile)                                 1.46
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Ore Processing
----------------------------------------------------------------------------
Flotation Ore                                                 kt     400,569
----------------------------------------------------------------------------
Copper Head Grade - Average                                    %        0.40
----------------------------------------------------------------------------
Gold Head Grade - Average                                    g/t        0.07
----------------------------------------------------------------------------
Copper Recovery - Average                                      %        88.1
----------------------------------------------------------------------------
Gold Recovery - Average                                        %        54.3
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Metal Production
----------------------------------------------------------------------------
Copper - Recovered                                    million lb       3,123
----------------------------------------------------------------------------
Copper - Annual Average                               million lb         164
----------------------------------------------------------------------------
Gold - Recovered                                             koz         484
----------------------------------------------------------------------------
Gold - Annual Average                                        koz          25
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Initial Capital Cost

The initial capital cost, including contingency, for the Project is estimated 
at US$ 1,157 million with an expected accuracy range of +/-25 %. The PFS 
envisages that a mining contractor will operate the open pit for the pre-mine 
period and until Year 3 of production. Year 4 will be a transition year with 
the contractor winding down and the CMZ operation of the open pit ramping up 
and continuing until the end of mine life. A summary of initial capital 
expenditures follows:

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine                                                             $       142
----------------------------------------------------------------------------
Concentrator                                                     $       430
----------------------------------------------------------------------------
On-Site Infrastructure                                           $        33
----------------------------------------------------------------------------
Off-Site Infrastructure                                          $        98
----------------------------------------------------------------------------
Total Direct Capital                                             $       703
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Project Preliminaries                                            $       103
----------------------------------------------------------------------------
Indirect Costs                                                   $       132
----------------------------------------------------------------------------
Owners Costs                                                     $        68
----------------------------------------------------------------------------
Total Indirect Capital                                           $       303
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Contingency (15%)                                                $       151
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Initial Capital Cost                                       $     1,157
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Sustaining Capital Cost

The significant sustaining capital in the Mine reflects the purchase of mine 
equipment fleet in Year 3 and 4 of production as CMZ takes over operation of 
the mine.

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mine                                                             $       213
----------------------------------------------------------------------------
Concentrator                                                     $        15
----------------------------------------------------------------------------
On-Site Infrastructure                                           $         1
----------------------------------------------------------------------------
Total Sustaining Capital                                         $       229
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Contingency (15%)                                                $        34
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Sustaining Capital Cost                                    $       263
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Total Project Capital Cost

The total Project capital cost is shown in the following table for the LOM:

/T/

----------------------------------------------------------------------------
Description                                                      $US Million
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital Cost                                             $     1,157
----------------------------------------------------------------------------
Sustaining Capital Cost                                          $       263
----------------------------------------------------------------------------
Project Closure Cost                                             $       136
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Capital Cost                                               $     1,556
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

Each element of the estimate is developed initially as a base cost only. A 
growth allowance has then been allocated to each element of the cost to reflect 
the level of definition in pricing and design maturity relating to that 
element. A growth allowance of US$ 95 million, which is expected to be 
expended, has been included in the initial capital cost, and represents 11.2 % 
of Total Direct Cost.

The estimated contingency was then assessed as 15 % of total initial capital 
cost and 15 % of total sustaining capital cost to arrive at a project estimate 
within the required 50 % confidence interval ("P50"). The estimated project 
closure cost was deemed to already include sufficient contingency. The value of 
the base estimate, the growth allowance, the contingency and the project 
closure cost represent the total project estimate. Risk events that may or may 
not affect the capital cost estimate are covered in the positive range of 
sensitivity analyses.

Operating Cost

Average mine site production cost is estimated to be $ 1.29 /lb copper produced 
from plant feed material processed, including mining, re-handling, milling, and 
flotation as shown below:

/T/

----------------------------------------------------------------------------
COST ITEM                         UNIT          UNIT COST
(US$)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Contractor Mining (Y1 to Y4)                      $ /tonne mined        1.93
----------------------------------------------------------------------------
Owner Mining (Y4 to Y19)                          $ /tonne mined        1.76
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Production Mining (Y1 to Y19)                        $ /t milled        4.25
----------------------------------------------------------------------------
Milling                                              $ /t milled        4.59
----------------------------------------------------------------------------
G&A                                                  $ /t milled        1.22
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mine Site Operations                           $ /t milled       10.05
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mine Site Operations                     $ /lb Cu Produced        1.29
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
The estimated costs exclude the two-year pre-stripping period. Rounding of
numbers may result in apparent summation differences.

/T/

Average C1 operating costs for the 19-year production period total $ 1.59 per 
payable pound of copper net of transport losses and smelter deductions. A 
breakdown of these costs is shown in the following table, along with estimates 
for C2 and C3 costs as per Wood Mackenzie definitions.

/T/

----------------------------------------------------------------------------
COST ITEM                AVERAGE      YEAR 1 TO    YEAR 6 TO
FOR 19 YEARS    YEAR 5       YEAR 10
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Onsite Costs (Mine, Mill and G&A)            1.33         0.95         1.35
----------------------------------------------------------------------------
Concentrate Road Transportation              0.06         0.06         0.06
----------------------------------------------------------------------------
Port Charges, Ocean Freight &
Insurance                                   0.14         0.13         0.14
----------------------------------------------------------------------------
TC/RC's and Marketing                        0.24         0.23         0.24
----------------------------------------------------------------------------
Less By-Product Credits                     (0.17)       (0.15)       (0.17)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C1 Costs                               1.59         1.21         1.62
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Depreciation & Amortization                  0.49         0.57         0.33
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C2 Costs                               2.07         1.78         1.96
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Royalties                                    0.07         0.09         0.06
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total C3 Costs                               2.14         1.87         2.02
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
Unit Costs based on payable pounds of copper and rounding of numbers may
result in apparent summation differences.

/T/

Financial Sensitivities

In addition to the base case after-tax evaluation of economic cash flows using 
a copper price of $3.00 /lb, initial capital cost of US$ 1,157 million and a 
discount rate of 8 %; different copper prices and other variables at the base 
case copper price were tested to determine financial sensitivities of the 
Project as shown in the following tables:

/T/

Copper Prices (US$/lb)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Copper Price Sensitivity                   2.00   2.50   3.00   3.50   4.00
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Undiscounted Cash Flows       Pre-Tax      (311) 1,204  2,711  4,236  5,753
----------------------------------------------
US$M                          After-Tax    (478)   648  1,649  2,623  3,574
----------------------------------------------------------------------------
After-Tax NPV US$M at         5%           (515)   180    813  1,426  2,029
----------------------------------------------
Discount Rates                8%           (547)    (5)   496    978  1,454
----------------------------------------------
10%          (567)  (101)   333    749  1,162
----------------------------------------------------------------------------
Internal Rate of Return       IRR %         0.0%   7.9%  15.9%  22.1%  27.6%
----------------------------------------------------------------------------
----------------------------------------------------------------------------


-----------------------------------
Changes To Base Case NPV8% (US$M)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inputs /Changes to Inputs       Base Case   -25%   -10%     0%    10%    25%
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Initial Capital (US$M real)         1,157   745    595    496    394    241
----------------------------------------------------------------------------
Total Op. Costs (US$/t milled)
(1)                                10.05   788    613    496    374    188
----------------------------------------------------------------------------
Head Grade - Feed (Cu %)            0.401  (155)   239    496    745  1,118
----------------------------------------------------------------------------
Head Grade - Feed (Au g/t)          0.069   455    479    496    510    534
----------------------------------------------------------------------------

Notes:
1.  Excludes in-land freight costs

/T/

Location

The Zafranal Project is located in southern Peru about 166 km by road (90 km 
straight-line distance) northwest of the city of Arequipa, 80 km from tidewater 
and approximately 216 km by road from the Port of Matarani.

The regional climate is arid with scarce precipitation, and average 
temperatures range between 7 degrees C in winter and 24 degrees C in summer. 
Elevation ranges between 1,400 and 2,900 m above sea level ("masl") in the 
Project area.

Geology

Zafranal is a classic example of an Andean style porphyry copper-gold deposit. 
Mineralization is hosted in Jurassic volcano-sedimentary rocks and in a diorite 
intrusive suite of late Cretaceous age. The emplacement of mineralized 
porphyries is structurally controlled and occurs near or at the intersection of 
a series of northwest trending strike-slip faults belonging to the Incapuquio 
fault system, and regional east-west trending structures. Primary 
mineralization occurs as chalcopyrite both as disseminations and in quartz 
stockworks. A near surface well-developed sub-horizontal chalcocite rich 
supergene enrichment blanket has developed over a 2.5 km strike length, with 
thicknesses of up to 180 m.

Mining

Conventional open pit operation with mine life of approximately 19 years 
(excluding two years of pre-stripping) with an average waste to ore strip ratio 
of 1.36: 1, for the production period. The mine plan developed for the Zafranal 
Project is designed for a variable feed to a concentrator in the range of 
55,000 to 64,000 tonnes per day depending on mineral type, with a peak total 
material movement of 75 million tonnes per year. The mine is scheduled to work 
seven days per week or 365 days per year.

The mine design proposes two contiguous pits with a combined strike length of 
3,500 m, maximum width of 1,000 m, and maximum depth of 456 m. Pre-production 
stripping of 45 Mt will be required prior to the start-up of the concentrator. 
Peak daily movement of 205,000 t of material occurs in production Year 1.

A total of 18 Mt of waste from the mine will be used to construct facility 
platforms and roadways, and the remaining 548 Mt of waste will be deposited in 
valley dumps using relatively short haulage cycles. The mine will utilize three 
of these types of dumps, two above and one below the planned open pits. The 
northeast dump will receive 12.8 million tonnes. The north waste dump will 
receive 151 Mt and the central waste dump, below the main open pit will receive 
384 Mt. A 17.6 Mt oxide and mixed mineral stockpile will be created on top of 
the north section of the central waste dump with a crest elevation of 2,580 
masl. There are no plans to construct a process plant to process this material 
at this time and the material in this stockpile is considered as waste. A 38.7 
Mt low-grade sulfide stockpile will be created to the west of the open pit. 
This material will be reclaimed at the end of the mine life and processed 
through the concentrator.

Milling

The primary crusher will be located adjacent to the mine on the opposite 
hillside of the valley immediately south of the Main Zone open pit at a base 
elevation of 2,494 masl. Due to the steep topography between the primary 
crusher and the rest of the concentrator, the conveyor that transfers the 
crushed ore to the crushed ore stockpile, which feeds the grinding circuit, 
passes through a 3,600 m long tunnel.
The rest of the concentrator will be terraced down a ridge with the major 
facilities including: the crushed ore stockpile and reclaim, grinding and 
pebble crushing; flotation, regrind, reagents, and concentrate thickening; 
filtration; concentrate load-out and tailings discharge and water utilities. 
The concentrator support buildings, general and administration buildings and 
accommodation camp are located further downhill from the concentrator on the 
same ridge. The areas are compact but adequate for the facilities.

The tailings management facility ("TMF") will be located 1 km southeast of the 
concentrator and has been sized to provide sufficient capacity to store 
approximately 396 million tonnes of tailings based on the mine and concentrator 
production schedules. Due to the favourable topography in the TMF area which 
provides a natural basin for the impoundment, only one embankment will be 
initially required in the southwest of the impoundment with a small embankment 
required later in the northwest. Sand cycloned from the tailings will be used 
to raise tailings embankments in ongoing operations. During the design of the 
TMF to its current status a number of trade-off studies were developed 
involving alternative disposal sites, disposal methods, embankment construction 
methods and alternative construction materials.

A comprehensive metallurgical testwork program was performed by C.H. Plenge 
Laboratories in Lima, Peru and supervised by Transmin Metallurgical 
Consultants. The testwork was completed on representative samples of the 
proposed concentrator feed appropriately representative for the PFS. The 
results of the comminution and flotation programs were combined with results 
from previous programs for a comprehensive geometallurgical analysis. The 
proposed flotation feed is amenable to typical copper flotation using 
conventional concentrator processing technology.

A variable throughput design has been established for the concentrator, 
dependent on the proportions of feed from each mineral zone ("minzone") domain, 
based on geometallurgical analysis of the results of comminution testwork and 
rock quality data, as follows:

/T/

----------------------------------------------------------------------------
MINZONE DOMAIN                                          PROJECTED THROUGHPUT
----------------------------------------------------------------------------
t/d
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Hypogene                                                              57,400
----------------------------------------------------------------------------
Supergene                                                             65,300
----------------------------------------------------------------------------
Mixed                                                                 72,500
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
During the first year of concentrator operation throughput has been ramped
up in staged intervals reaching 55,000 t/d after 11 months of operation, and
this throughput rate was also maintained for the full second year of
operation. Variable throughput commences at the beginning of the third year
of concentrator operation and continued until the end of operations.

/T/

Variable concentrate grades and recoveries have been assigned to the 
concentrator feed based on geometallurgical analysis of flotation testwork 
results as follows:

/T/

----------------------------------------------------------------------------
MINZONE DOMAIN          GEOMETALLURGICAL           RECOVERY %    CONCENTRATE
----------------------------------------------------------------------------
CHARATERISTICS             COPPER  GOLD   GRADE % CU
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Hypogene                Low secondary copper         90.5    56           28
----------------------------------------------------------------------------
Supergene               Low acid soluble copper        89    52           37
----------------------------------------------------------------------------
Medium acid soluble
Supergene                copper                        84    55           34
----------------------------------------------------------------------------
Supergene/Mixed         High acid soluble copper       77    52           32
----------------------------------------------------------------------------
Oxide                   Low S/Fe ratio                  -     -            -
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

A total of 4.4 million dmt of concentrate will be produced over the life of the 
Project. No deleterious elements in any significant concentration were found in 
the copper concentrate produced from the testwork, and all the impurity 
elements were found to be below smelter penalty limits.

Site Access:

CMZ has secured all legal rights for the Project's mineral concessions, and 
these rights have been recorded at the Public Registry.

CMZ holds the right of surface access to Project's mining concessions to carry 
out mineral exploration through a renewable lease agreement entered into with, 
Autodema, the regional governmental agency that manages the Majes Siguas 
irrigation project. The lease agreement term was last renewed on 11 September 
2015 and is in force until 27 October 2017. This annual renewable agreement 
allows for continued exploration activities within the Zafranal Project and 
may, under certain conditions, be modified to allow for future development of 
the Zafranal Project.

CMZ is aware of an ongoing title dispute between Autodema and local landowners, 
and although CMZ is not involved in the legal dispute, it maintains open 
dialogue with both parties. As a result of these discussions, CMZ has entered 
into an option to purchase agreement to acquire the land needed for development 
of the Project from the local landowners who are disputing title with Autodema 
to ensure that it will have access to surface rights required for the Zafranal 
Project regardless of the final outcome of the litigation process.

The main access to the site for personnel and supplies will be via 34 km of an 
existing and partially paved road from Pedregal de Majes on the Pan American 
Highway, then from there to the plant site via 9 km of new gravel topped road. 
A refurbished 26 km gravel topped access road will also be constructed from 
Anexo de Pedregal to the plant site for transporting personnel, supplies and 
copper concentrate. Concentrate will be truck transported 216 km, initially 
from the plant site to Anexo de Pedregal then via existing road to the coast 
and from there, southeast to the Port of Matarani, using the newly constructed 
highway along the coast.

Industrial Water Supply

An estimated 410 liters per second ("L/s") of make-up water is required for 
operations. Field investigations have identified several potential sources of 
brackish water, unsuitable for human and animal consumption or irrigation of 
crops, one of which could become a water supply for the Project. One of these 
is a brackish groundwater resource located 35 km from the process plant site 
where the groundwater quality is poor but potentially suitable for industrial 
use at the Zafranal Project. Groundwater extraction from this or any other 
aquifer will require the approval of the water authorities and the acceptance 
of the local authorities and community residents. Metallurgical testwork using 
this brackish water has produced positive results.

Power Supply

The power delivery and site power distribution systems are based on total 
installed equipment rated at 99 MW with a peak demand of 91 MW. Power supply 
for production is scheduled to be available from the New Socabaya Substation 
that is located close to the city of Arequipa. This will require the 
installation of an approximately 96 km long transmission line to a proposed 220 
kV substation that will be located adjacent to the concentrator.

Social and Environment

CMZ has an ongoing extensive stakeholder relations program implemented in an 
effort to ensure that the Company fully engages with the local communities and 
regional authorities, informs on project activities, addresses concerns and 
reduces or mitigates the potential impacts of the Project. A working table 
forum was established in 2015 with representatives from the local communities.

Environmental and social baseline studies for the Project have been conducted 
to compile a third modification of the Semi-Detailed Environmental Impact 
Assessment (EIAsd) in order to obtain environmental certifications and permits 
for the ongoing exploration and study programs of the Project. The application 
is currently under review by the relevant authorities.

Formal baseline studies for the Project are being carried out with the 
completion of the Environmental Impact Assessment (EIA) currently scheduled for 
December 2017.

Mineral Resource Estimate

Geological logging and assay results from 295 core holes totalling 95,619 m and 
88 RC holes totalling 27,041 m were used as the basis for preparation of three 
dimensional (3D) wireframe models of geological structures, lithology, 
alteration, and mineral zonation envelopes.

CMZ prepared the new mineral resource estimate using the revised geological 
model of the Zafranal Main and Victoria Zones. The mineral resource was 
subsequently reviewed and audited by Amec Foster Wheeler ("AmecFW"). The 
resource estimate included in the PFS pertains to the Main Zone and Victoria 
deposits only, as other known mineralized areas in the Project area were not 
deemed to be economically attractive at this time. AmecFW reviewed the resource 
model that had been provided by CMZ and considered that it was suitable for use 
in resource estimation.

An external review of the analytical QA/QC program completed by Julio Bruna, 
MAusIMM CP (Geology) and Qualified Person under National Instrument 43-101, of 
Politax S.A. Santiago, Chile, concluded that the sample preparation, analysis 
and security program provided an acceptable level of confidence in the assay 
results and that they can be used for resource estimation and mine planning 
studies.

Mineral resources were estimated using long-term forecasted copper and gold 
prices of US$ 3.50 /lb and US$ 1,400 /oz, respectively.

A summary of the mineral resource for the PFS at a 0.15 % total copper cut-off 
grade appears in the following table:

Mineral Resource Estimate for the Zafranal Deposit based on a 0.15% Total 
Copper Cut-off

Effective Date 14 December 2015, Peter Oshust, PGeo

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Tonnage        Grade         Contained Metal
Classification          (Mt)   Cu (%)  Au (g/t)  Cu (Mlb)  Au (Moz)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Measured
----------------------------------------------------------------------------
Mixed                                -       -         -         -         -
Supergene                         83.3    0.58      0.07     1,056      0.20
Hypogene                         120.5    0.28      0.07       744      0.28
----------------------------------------------------------------------------
Total Measured                   203.8    0.40      0.07     1,801      0.47
----------------------------------------------------------------------------

Indicated
----------------------------------------------------------------------------
Mixed                             23.5    0.28      0.12       146      0.09
Supergene                        100.3    0.53      0.07     1,176      0.21
Hypogene                         139.7    0.26      0.06       804      0.28
----------------------------------------------------------------------------
Total Indicated                  263.5    0.37      0.07     2,126      0.58
----------------------------------------------------------------------------

Measured and Indicated
----------------------------------------------------------------------------
Mixed                             23.5    0.28      0.12       146      0.09
Supergene                        183.6    0.55      0.07     2,234      0.40
Hypogene                         260.2    0.27      0.07     1,543      0.56
----------------------------------------------------------------------------
Total Measured and Indicated     467.3    0.38      0.07     3,925      1.05
----------------------------------------------------------------------------

Inferred
----------------------------------------------------------------------------
Mixed                              7.8    0.22      0.09        37      0.02
Supergene                          8.7    0.30      0.04        57      0.01
Hypogene                           4.9    0.18      0.03        20      0.00
----------------------------------------------------------------------------
Total Inferred                    21.4    0.24      0.06       114      0.04
----------------------------------------------------------------------------
----------------------------------------------------------------------------

Notes:
1.  Mineral resources are reported inclusive of those mineral resources that
have been converted to mineral reserves. Mineral resources are reported on a 
100% basis.
2.  Mineral resources are reported within a constraining pit shell developed
using Whittle(TM) software. Assumptions include metal prices of US$3.50
/lb for Cu and $1,400 /oz for Au; process recoveries of 86% for Cu and
50% for Au in supergene, 86% recoveries for Cu and 50% recoveries for Au
in mixed, and 89% for Cu and 50% for Au in hypogene, US$1.58 /t of
mining at 2,534 m plus $0.01 /bench downward and $0.03 /bench upward.
US$5.45 /tonne for processing, and US$0.38 /tonne for G&A.
3.  Assumptions include 100% mining recovery.
4.  An external dilution factor was not considered during this resource
estimation. Internal dilution within a 15 m x 15 m x 12 m SMU was
considered.
5.  The 1.0% Royalty was not considered during the preparation of the
constraining pit.
6.  Quantities and grades in the mineral resource estimate are rounded to an
appropriate number of significant figures to reflect that they are
approximations.

/T/

Rounding as required by reporting guidelines may result in apparent summation 
differences between tonnes, grade and contained metal content. The reader 
should be aware that mineral resources that are not mineral reserves so do not 
have demonstrated economic viability.

Mineral Reserve Estimate

NCL Ingenieria y Construccion SpA ("NCL") prepared the mine design and mineral 
reserve estimate by evaluating the measured and indicated mineral resource and 
sequencing the mining development based on the scheduling the mine pushbacks 
according to their net processed value. A summary of the mineral reserve for 
the PFS at a 0.15 % total copper cut-off grade appears in the following table:

Mineral Reserve Estimate for Zafranal Deposit

/T/

----------------------------------------------------------------------------
Reserve           Ore                Ore Grade         Contained Metal
------------------------------------------------------------------
Category       Type        Mt      % Cu     g/t Au     Mlbs Cu     koz Au
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Proven Mineral Reserves
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mixed               0.4     0.48       0.11           4          1
----------------------------------------------------------------------------
Supergene            97     0.61       0.08       1,308        233
----------------------------------------------------------------------------
Hypogene            105     0.28       0.07         660        249
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Proven Mineral
Reserves                     202     0.44       0.07       1,972        483
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Probable Mineral Reserves
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mixed                 2      0.4       0.11          16          6
----------------------------------------------------------------------------
Supergene            78      0.5       0.06         861        156
----------------------------------------------------------------------------
Hypogene            118     0.27       0.06         694        246
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Probable Mineral
Reserves                     198     0.36       0.06       1,571        408
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mineral Reserves (proven and probable)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Mixed                 2     0.41       0.11          20          8
----------------------------------------------------------------------------
Supergene           175     0.56       0.07       2,169        389
----------------------------------------------------------------------------
Hypogene            224     0.27       0.07       1,354        495
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total Mineral Reserves
(proven and probable)        401      0.4       0.07       3,543        891
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Notes to accompany mineral reserves table

Notes:
1.  The Qualified Person for the estimate is Carlos Guzman, RM CMC and
FAusIMM, an NCL employee. Mineral Reserves have an effective date of 31
March 2016. Mineral reserves are reported on a 100% basis.
2.  Mineral Reserves are reported as constrained within measured and
Indicated pit designs, and supported by a mine plan featuring variable
cut-off. The pit designs and mine plan were optimized using the
following economic and technical parameters: metal prices of US$3.0 /lb
Cu and US$1,200 /oz; recovery to concentrate assumptions according to
geometallurgical domains for Cu and Au; copper concentrate treatment
charges of US$90 /dmt, US$0.09 /lb of Cu refining charges and US$4.0 /oz
of Au refining charges; concentrate charges of US$12 /wmt for marketing,
US$37.55 /wmt for road transport, US$20 /wmt for port and insurance,
US$65 /wmt for shipping and 0.3% for transport losses; average
payability of 96.9% for Cu and 90% for Au; average mining cost of
US$1.86 /t, process costs of US$4.47 /t for mixed and supergene
materials and US$4.75 /t for hypogene, and G&A US$1.25 /t processed;
average pit slope angles that range from 36 degrees to 41 degrees; a
1% royalty rate assumption, and an assumption of 100% mining recovery.
3.  Rounding as required by reporting guidelines may result in apparent
summation differences between tonnes, grade and contained metal content.
4.  Tonnage and grade measurements are in metric units. Reported copper
grades are total copper grades. Contained gold ounces are reported as
troy ounces.

/T/

Qualified Persons for this Press Release

The NI 43-101 Technical Report has been prepared by an integrated engineering 
team led by Ausenco in Lima, Peru. The Technical Report will be filed on SEDAR 
within 45 days of the Press Release date.

The geological information for this press release was approved by Alvaro 
Fernandez-Baca, P.Geo, a consulting geologist and a Qualified Person under NI 
43 - 101.

The analytical QA/QC program for drill samples was reviewed and approved by 
Julio Bruna Novillo, MAusIMM CP (Geology), of Politax S.A. and a Qualified 
Person under NI 43 -101.

The mineral resource estimate was prepared by CMZ then reviewed and approved by 
Peter Oshust, P. Geo., of Amec Foster Wheeler plc and a Qualified Person under 
NI 43 -101.

The mine design and mineral reserves estimate were prepared under the 
supervision of Carlos Guzman, RM CMC and FAusIMM, an employee of NCL Ingenieria 
y Construccion SpA, and a Qualified Person under NI 43 - 101

The metallurgical and process information contained in this release was 
approved by Greg Lane, FAusIMM, of Ausenco Services Pty Ltd and a Qualified 
Person under NI 43 -101.

The full list of other Qualified Persons and their responsibilities for 
geotechnical, hydrogeological, hydrological, environmental and other 
contributions to the Preliminary Feasibility Study (PFS) will be provided in 
the Technical Report.

The scientific and technical information contained in this news release has 
been reviewed, summarized from the PFS and approved by Bruce L Turner, P.Eng., 
CEO of AQM Copper Inc., and a Qualified Person under NI 43-101.

On Behalf of the Board

AQM COPPER INC.

Bruce L. Turner, President and Chief Executive Officer

About AQM Copper

AQM Copper Inc. is a Canadian mineral exploration company exploring and 
developing copper deposits in South America. Through its Peruvian subsidiary, 
Minera AQM Copper Peru S.A.C. (MAQM), the Company is developing the Zafranal 
Copper-Gold Porphyry Project located in Southern Peru. MAQM is the operator of 
a 50/50 Joint Venture with Teck Resources Limited through a sole purpose 
Peruvian company, Compania Minera Zafranal. MAQM is owned 60 % by AQM Copper 
Inc. and 40 % by Mitsubishi Materials Corporation.

The Company's management and directors have extensive experience working for 
the world's largest mining copper producers and investment banking backgrounds. 
Please refer to the Company's website at www.aqmcopper.com, for further 
information regarding the Company and the Zafranal Project.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION

Except for statements of historical fact relating to AQM Copper Inc., certain 
information contained herein constitutes "forward-looking statements". 
Forward-looking statements include statements that are predictive in nature, 
depend upon or refer to future events or conditions, or include words such as 
"expects", "anticipates", "plans", "believes", "considers", "intends", 
"targets", or negative versions thereof and other similar expressions, or 
future or conditional verbs such as "may", "will", "should", "would" and 
"could". We provide forward-looking statements for the purpose of conveying 
information about our current expectations and plans relating to the future and 
readers are cautioned that such statements may not be appropriate for other 
purposes. By its nature, this information is subject to inherent risks and 
uncertainties that may be general or specific and which give rise to the 
possibility that expectations, forecasts, predictions, projections or 
conclusions will not prove to be accurate, that assumptions may not be correct 
and that objectives, strategic goals and priorities will not be achieved. These 
risks and uncertainties include but are not limited to those identified and 
reported in AQM Copper Inc's public filings, which may be accessed at 
www.sedar.com. Other than as specifically required by law, we undertake no 
obligation to update any forward-looking statement to reflect events or 
circumstances after the date on which such statement is made, or to reflect the 
occurrence of unanticipated events, whether as a result of new information, 
future events, results or otherwise.

- 30 -

CONTACT INFO:

To speak with an Investor Relations representative,
please contact:
Spyros P. Karellas
Pinnacle Capital Markets LTD.
(416) 433-5696 or (416) 800-8921
spyros@pinnaclecapitalmarkets.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=567216839