Source	Marketwire
Date	05/24/2016
Time	05:02:08 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Results from 2016 Exploration Drilling at the Paris 
Target Area, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

May 24, 2016

Scorpio Gold Reports Results from 2016 Exploration Drilling at the Paris Target 
Area, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 24, 2016) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports results 
from the 2016 exploration drilling program on the Paris target at its 70% owned 
Mineral Ridge project, located in Nevada.

The Paris target is a previously undrilled area located NNW of the Solberry 
deposit. It was targeted as one of several possible northwest strike extensions 
of the Drinkwater mineralization based on rock chip sampling and limited 
historic underground workings. Significant faulting to the northwest of 
Drinkwater has offset and obscured the Drinkwater trend. First-pass drilling in 
2016 intersected mineralization in 19 of 24 RC holes collared over a 150 x 450 
meter area. Based on a review of the geology and assay results, Paris is not 
considered a continuation of the Drinkwater trend. No further drilling is 
currently planned in the Paris target area.

A drill hole location map is available at: DH Plan

Table 1. Paris Target Area - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole            Azm  Dip   From   To Width  From     To  Width   Gold   Gold
No.             (deg)(deg) (ft) (ft)  (ft)   (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR161953-954    0    -90                No Significant Results
----------------------------------------------------------------------------
MR161955        0    -90    120  125     5 36.58  38.10   1.52  0.017   0.58
----------------------------------------------------------------------------
MR161959        0    -90                No Significant Results
----------------------------------------------------------------------------
MR161960        0    -90    130  140    10 39.62  42.67   3.05  0.013   0.43
----------------------------------------------------------------------------
MR161961        0    -90    210  215     5 64.01  65.53   1.52  0.071   2.43
----------------------------------------------------------------------------
MR161962        0    -90    270  275     5 82.30  83.82   1.52  0.047   1.61
----------------------------------------------------------------------------
MR161963        0    -90    250  265    15 76.20  80.77   4.57  0.060   2.05
----------------------------------------------------------------------------
MR161964        0    -90    150  155     5 45.72  47.24   1.52  0.019   0.65
----------------------------------------------------------------------------
230  235     5 70.10  71.63   1.52  0.018   0.62
----------------------------------------------------------------------------
MR161965        0    -90     60   65     5 18.29  19.81   1.52  0.015   0.51
----------------------------------------------------------------------------
MR161966        0    -90     20   30    10  6.10   9.14   3.05  0.052   1.78
----------------------------------------------------------------------------
180  185     5 54.86  56.39   1.52  0.016   0.55
----------------------------------------------------------------------------
MR161967        0    -90    135  145    10 41.15  44.20   3.05  0.011   0.38
----------------------------------------------------------------------------
MR161968        0    -90    105  110     5 32.00  33.53   1.52  0.017   0.58
----------------------------------------------------------------------------
MR161970        090  -45    110  115     5 33.53  35.05   1.52  0.010   0.34
----------------------------------------------------------------------------
MR161971        091  -47    105  110     5 32.00  33.53   1.52  0.017   0.58
----------------------------------------------------------------------------
185  190     5 56.39  57.91   1.52  0.016   0.55
----------------------------------------------------------------------------
MR161972        092  -46                No Significant Results
----------------------------------------------------------------------------
MR161973,975    0    -90                No Significant Results
----------------------------------------------------------------------------
MR161974        0    -90     85   90     5 25.91  27.43   1.52  0.031   1.06
----------------------------------------------------------------------------
MR161976        0    -90    455  460     5138.68 140.21   1.52  0.189   6.48
----------------------------------------------------------------------------
MR161978        0    -90    190  195     5 57.91  59.44   1.52  0.023   0.79
----------------------------------------------------------------------------
450  455     5137.16 138.68   1.52  0.052   1.78
----------------------------------------------------------------------------
MR161979        0    -90    380  385     5115.82 117.35   1.52  0.061   2.09
----------------------------------------------------------------------------
MR161980        0    -90    295  310    15 89.92  94.49   4.57  0.032   1.11
----------------------------------------------------------------------------
325  330     5 99.06 100.58   1.52  0.024   0.82
----------------------------------------------------------------------------
MR161981        0    -90    400  415    15121.92 126.49   4.57  0.039   1.35
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Scorpio Gold 
utilizes the analytical services of ALS Minerals (Reno, Nevada), an ISO/IEC 
17025:2005 (CAN-P-4E, CAN-P-1579) accredited testing laboratory, and Bureau 
Veritas (Reno, Nevada), an ISO 9001 certified testing laboratory. External 
check assays to verify lab accuracy are routinely completed. Further details 
are presented in the Company's quality assurance and quality control program 
for the Mineral Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Elevon, LLC (30%). Mineral Ridge is a conventional open pit mining and heap 
leach operation. The Mineral Ridge property is host to multiple gold-bearing 
structures, veins and lenses at exploration, development and production stages. 
Scorpio Gold also holds a 100% interest in the advanced exploration-stage 
Goldwedge property in Manhattan, Nevada, with a fully permitted underground 
mine and 400 ton per day mill facility. The Goldwedge mill facility has been 
placed on a care and maintenance basis and can be restarted immediately when 
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a Qualified Person 
as defined by National Instrument 43-101 and has reviewed and approved the 
content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=567214751