Source	MARKET NEWS
Date	05/24/2016
Time	06:01:21 AM

Company	 Scorpio Gold Corporation
Title	Results From 
2016 Exploration Drilling At The Pa





    CDNX Symbol: SGN











Press Release





SCORPIO GOLD CORP ("SGN-V;SRCRF-0")
- Results From 2016 Exploration Drilling At The Paris Target Area,
- Mineral Ridge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") reports
results from the 2016 exploration drilling program on the Paris target
at its 70% owned Mineral Ridge project, located in Nevada.

The Paris target is a previously undrilled area located NNW of the
Solberry deposit. It was targeted as one of several possible northwest
strike extensions of the Drinkwater mineralization based on rock chip
sampling and limited historic underground workings. Significant
faulting to the northwest of Drinkwater has offset and obscured the
Drinkwater trend. First-pass drilling in 2016 intersected
mineralization in 19 of 24 RC holes collared over a 150 x 450 meter
area. Based on a review of the geology and assay results, Paris is not
considered a continuation of the Drinkwater trend. No further drilling
is currently planned in the Paris target area.

A drill hole location map is available at: DH Plan

Table 1. Paris Target Area - Significant Drill Results

//st
Hole       Azm   Dip From   To Width   From     To Width  Gold  Gold
No.      (deg) (deg) (ft) (ft)  (ft)    (m)    (m)   (m) (OPT) (g/t)
MR161953-954 0   -90                          No Significant Results
MR161955     0   -90  120  125     5  36.58  38.10  1.52 0.017  0.58
MR161959     0   -90                          No Significant Results
MR161960     0   -90  130  140    10  39.62  42.67  3.05 0.013  0.43
MR161961     0   -90  210  215     5  64.01  65.53  1.52 0.071  2.43
MR161962     0   -90  270  275     5  82.30  83.82  1.52 0.047  1.61
MR161963     0   -90  250  265    15  76.20  80.77  4.57 0.060  2.05
MR161964     0   -90  150  155     5  45.72  47.24  1.52 0.019  0.65
230  235     5  70.10  71.63  1.52 0.018  0.62
MR161965     0   -90   60   65     5  18.29  19.81  1.52 0.015  0.51
MR161966     0   -90   20   30    10   6.10   9.14  3.05 0.052  1.78
180  185     5  54.86  56.39  1.52 0.016  0.55
MR161967     0   -90  135  145    10  41.15  44.20  3.05 0.011  0.38
MR161968     0   -90  105  110     5  32.00  33.53  1.52 0.017  0.58
MR161970   090   -45  110  115     5  33.53  35.05  1.52 0.010  0.34
MR161971   091   -47  105  110     5  32.00  33.53  1.52 0.017  0.58
185  190     5  56.39  57.91  1.52 0.016  0.55
MR161972   092   -46                          No Significant Results
MR161973,975 0   -90                          No Significant Results
MR161974     0   -90   85   90     5  25.91  27.43  1.52 0.031  1.06
MR161976     0   -90  455  460     5 138.68 140.21  1.52 0.189  6.48
MR161978     0   -90  190  195     5  57.91  59.44  1.52 0.023  0.79
450  455     5 137.16 138.68  1.52 0.052  1.78
MR161979     0   -90  380  385     5 115.82 117.35  1.52 0.061  2.09
MR161980     0   -90  295  310    15  89.92  94.49  4.57 0.032  1.11
325  330     5  99.06 100.58  1.52 0.024  0.82
MR161981     0   -90  400  415    15 121.92 126.49  4.57 0.039  1.35
//et

All holes presented in Table 1 were completed by reverse
circulation (RC) drilling. True width is estimated at 80-100% of
downhole width. Scorpio Gold utilizes the analytical services of ALS
Minerals (Reno, Nevada), an ISO/IEC 17025:2005 (CAN-P-4E,CAN-P-1579)
accredited testing laboratory, and Bureau Veritas (Reno, Nevada), an
ISO 9001 certified testing laboratory. External check assays to verify
lab accuracy are routinely completed. Further details are presented in
the Company's quality assurance and quality control program for the
Mineral Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge
gold mining operation located in Esmeralda County, Nevada with joint
venture partner Elevon, LLC (30%). Mineral Ridge is a conventional open
pit mining and heap leach operation. The Mineral Ridge property is host
to multiple gold-bearing structures, veins and lenses at exploration,
development and production stages. Scorpio Gold also holds a 100%
interest in the advanced exploration-stage Goldwedge property in
Manhattan, Nevada, with a fully permitted underground mine and 400 ton
per day mill facility. The Goldwedge mill facility has been placed on a
care and maintenance basis and can be restarted immediately when
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a
Qualified Person as defined by National Instrument 43-101 and has
reviewed and approved the content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for SGN-V
Date: 2016/05/20
Closing Price: 0.09

TEL: (819) 825-7618       Peter J. Hawley
phawley@scorpiogold.com   President & CEO
www.scorpiogold.com       SCORPIO GOLD CORPORATION
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1614400013TS11614400790-05591920160524