Source	MARKET NEWS
Date	05/24/2016
Time	05:47:12 AM

Company	 Victoria Gold Corp.
Title	Confirms 
High Grade Mineralization Between The O





    CDNX Symbol: VIT











Press Release





VICTORIA GOLD CORP ("VIT-V;VITFF-0")
- Confirms High Grade Mineralization Between The Olive And
- Shamrock Zones Including 26.5m At 2.1 G/t Gold

Victoria Gold Corp. "Victoria" or the "Company" is pleased to
announce the 3rd set of results from the 2016 Olive-Shamrock diamond
drilling program. The results from the latest assays received confirm
the continuation of gold mineralization between Olive and Shamrock and
validate the exploration model currently testing the near surface, high
grade material in the Olive-Shamrock Shear Zone.

"The Olive-Shamrock Zone is shaping up nicely and while still early
in the drill program, the continuity of mineralization at grades above
1.0 g/t bodes well for the economics of the zone." said John McConnell,
President and CEO. "When one steps back from the task at hand and looks
at the coverage of this growing zone, it is an impressive size."

2016 Olive-Shamrock Zone Assay Results

The assay results for the recent 10 holes received included step out
drilling along strike from Olive Main towards the Shamrock Zone, and are
summarized in the table below:

//st
Hole ID          Location From      (m) To (m) Length      (m) Gold (g/t)
DG16-662C        Olive NE          19.1   41.5            22.4      1.0
including                          32.0   36.9             4.9      4.2
&                                  86.7  140.2            53.5      0.4
including                          93.3  103.4            10.1      1.1

DG16-663C Olive Extension          83.0  111.4            28.4      1.0
including                          83.0   92.1             9.1      2.6
&                                 124.4  161.5            37.2      1.5
including                         136.8  153.9            17.1      2.7

DG16-664C      Olive Main          38.1   68.7            30.6      0.5
including                          59.0   68.7             9.7      1.0
&                                  99.5  123.4            23.9      0.6
including                         106.7  121.9            15.2      0.7

DG16-665C Olive Extension          88.4  111.3            22.9      1.5
including                          94.5   99.1             4.6      4.3
&                                 121.9  143.4            21.5      0.4
including                         132.6  138.7             6.1      0.8

DG16-666C Olive Extension          29.6   30.8             1.2      7.5
&                                  72.0  100.3            28.3      0.4

DG16-667C      Olive Main          91.1  155.5            64.3      0.7
Including                          97.5  103.6             6.1      1.5
Including                         132.8  141.7             8.9      1.5
&                                 198.1  199.6             1.5      7.8

DG16-668C        Olive NE          40.3   53.7            13.4      1.5
including                          40.3   46.9             6.6      3.0

DG16-669C        Olive NE           1.5   55.9            54.4      1.3
including                          16.6   32.0            15.4      2.0

DG16-670C        Olive NE          33.5   70.1            36.6      0.4
including                          57.5   70.1            12.6      0.8

DG16-671C      Connection           1.7   68.2            66.5      1.1
including                          10.9   37.5            26.5      2.1

//et

Note:     Reported intersections are drilled intersections, but are
estimated at approximately two-thirds of true width of the mineralized
zone.

The strike length of the Olive Shear Zone tested with the 2016 drilling
program is at least 750 metres while the strike length of the Shamrock
Zone, the subject of current drilling efforts, is approximately 250 metres.
The entire length of the Olive-Shamrock zone being tested this season is
therefore estimated to be at least 1 kilometre. The Olive-Shamrock zone
remains open along strike to the Northeast, at depth and to the North where
a number of geophysical and geochemical soils anomalies have yet to be
fully tested.

An updated plan map and drill sections relating to the assay results
presented above, as well as a summary table of the 2016 Olive drilling
results, will be made available on the Company's website
www.vitgoldcorp.com.

Analytical Method

All exploration drill core from the Olive-Shamrock 2016 program was
analyzed at SGS Canada Inc. of Burnaby, B.C. utilizing the GE-ICP40B,
34-element analytical package with FAA5515 50-gram Fire Assay with
Gravimetric finish for gold on all samples. All core samples were split
on-site at Victoria's Eagle camp and shipped to SGS Canada Inc.'s mobile
sample preparation laboratory that has been set-up on-site, at the Eagle
Gold Project. There, samples were sorted and crushed to appropriate
particle size (coarse crush) and representatively split to a smaller size
(250 grams) for shipment to SGS Canada Inc.'s Burnaby analytical laboratory
facilities. A comprehensive system of standards, blanks and field
duplicates has been implemented for the 2016 Olive-Shamrock drilling
program and is monitored as chemical assay data become available.

2016 Olive-Shamrock Exploration Program

The Olive-Shamrock Zone is a near-surface mineralized target situated
approximately 2 kilometers from the fully-permitted Eagle Gold project and
has the potential to enhance Eagle Project economics by virtue of
additional higher-grade ore; increased flexibility in mine planning and
lowering capital intensity from shared infrastructure.

The $3.6 million Olive-Shamrock definition and exploration program began in
March 2016. The program will consist of diamond drilling, surface trenching
and geophysical surveys over the Olive-Shamrock zone with a focus on the
previously undrilled areas linking Olive and Shamrock mineralization. The
exploration program will concentrate on expanding the strike length of
confirmed near-surface, high-grade gold mineralization within the
Olive-Shamrock shear zone trend and target the previously un-tested, 300
metre separation zone between the Olive and Shamrock mineralization. The
program is designed to result in the maiden Resource Estimate for the
Olive-Shamrock Zone.

About Olive-Shamrock

The Olive-Shamrock target lies 2 kilometers from the proposed
infrastructure at the Eagle Gold Project, along the Potato Hills Trend,
importantly, drilling and surface trench results to date indicate the
existence of near-surface, high-grade potential feed into Eagle operations.
(see New Releases dated May 20, June 24, July 28, August 13, and Nov 4,
2014). Metallurgical testing completed in 2015 (see New Releases dated
February 24, and August 7, 2015) has indicated that the high-grade
Olive-Shamrock Zone is amenable to Eagle Project heap leach recovery at the
same crush size as Eagle Project feed.

Olive-Shamrock is defined by a broad gold/arsenic in-soils geochemical
anomaly and lies on the intrusive-sediment contact of the Potato Hills
Trend (as does the Eagle Deposit) and is punctuated by several historically
exploited high-grade sulphide veins. The Olive area was mined on a small
scale from shallow shafts and adits in the early 1900's and via placer
mining in creeks draining the area. The Olive vein system is located near
the top of Olive Gulch and consists of gold-bearing
quartz-scorodite-arsenopyrite vein material centralized in a shear zone
structure. More detail and a current summary of all Olive-Shamrock Zone
exploration can be found on the Company's website.

About the Dublin Gulch Project

Victoria Gold's 100%-owned Dublin Gulch gold property is situated in the
central Yukon Territory, Canada, approximately 375 kilometers north of the
capital city of Whitehorse, and approximately 85 kilometers from the town
of Mayo. The Property is accessible by road year-round, and is located
within Yukon Energy's electrical grid. The Company has constructed and
maintains a 100 person all-season camp at the project site.

The Property covers an area of approximately 555 square kilometers, and is
the site of the Company's Eagle Gold Deposit. The Eagle Gold Deposit is
expected to be Yukon's next operating gold mine and includes Probable
Reserves of 2.3 million ounces of gold from 92 million tonnes of ore with a
grade of 0.78 grams of gold per tonne, as outlined in a National Instrument
43-101 feasibility study. The NI 43-101 Mineral Resource has been estimated
to host 222 million tonnes averaging 0.68 grams of gold per tonne,
containing 4.9 million ounces of gold in the "Indicated" category,
inclusive of Probable Reserves, and a further 78 million tonnes averaging
0.60 grams of gold per tonne, containing 1.5 million ounces of gold in the
"Inferred" category.

Qualified Person

The technical content of this news release has been reviewed and approved
by Paul D. Gray, P.Geo., as the Qualified Person.

Cautionary Language and Forward-Looking Statements

Neither the TSX Venture Exchange, nor its Regulation Services Provider
accepts responsibility for the adequacy or accuracy of this release. This
press release includes certain statements that may be deemed
"forward-looking statements". All statements in this discussion, other than
statements of historical facts, that address future exploration drilling,
exploration activities, anticipated metal production, internal rate of
return, estimated ore grades, commencement of production estimates and
projected exploration and capital expenditures (including costs and other
estimates upon which such projections are based) and events or developments
that the Company expects, are forward looking statements. Although the
Company believes the expectations expressed in such forward looking
statements are based on reasonable assumptions, such statements are not
guarantees of future performance and actual results or developments may
differ materially from those in forward-looking statements. Factors that
could cause actual results to differ materially from those in
forward-looking statements include metal prices, exploration successes,
continued availability of capital and financing, and general economic,
market or business conditions. Accordingly, readers should not place undue
reliance on forward-looking statements.




John McConnell
President & CEO



















TSX Venture closing price for VIT-V
Date: 2016/05/20
Closing Price: 0.47

TEL: 416-866-8800
FAX: 416-866-8801
Internet: www.vitgoldcorp.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1614400007TS11614400736-05453720160524