Source	MARKET NEWS
Date	05/25/2016
Time	06:13:17 AM

Company	 Tinka Resources Limited
Title	Increases 
Inferred Mineral Resources At Ayawilca





    CDNX Symbol: TK











Press Release





TINKA RESOURCES LTD ("TK-V;TKRFF-0")
- Increases Inferred Mineral Resources At Ayawilca; Zinc
- Resource Now 18.8 Million Tonnes At 8.2% Zinc Eq, Initial Tin
- Resource 5.4 Million Tonnes At 0.89% Tin Eq

Tinka Resources Limited ("Tinka" or the "Company") is pleased to
announce a resource update for its 100%-owned Ayawilca zinc - indium -
silver - lead sulphide deposit in Peru, which now consists of 18.8
million tonnes grading 8.2% zinc equivalent (ZnEq)at a cut-off grade of
5% ZnEq. In addition, Tinka announces its first tin - copper - silver
resource consisting of 5.4 million tonnes grading 0.89% tin equivalent
(SnEq)at a cut-off grade of 0.45% SnEq. The Tin Zone resources lies
spatially beneath the Zinc Zone and do not overlap. Both of the Mineral
Resources are in accordance with the NI 43-101 Inferred Mineral
Resource category at a cut-off grade equivalent to approximately
US$60/t, as estimated by Roscoe Postle Associates Inc. (RPA) of
Toronto, Canada.

Dr. Graham Carman, Tinka's President and CEO, stated: "The Mineral
Resource update of the Zinc Zone represents a significant increase in
tonnage and grade from the previous resource estimate (February 23,
2015) as a result of our successful resource step-out drill campaign
especially at Central Ayawilca, during the latter part of 2015. In
addition, we are very pleased to report a tin-copper-silver Mineral
Resource estimate for the first time. The updated Zinc and first Tin
resources remain open for expansion in most directions, and will be
tested through an extensive drill program later in 2016, subject to
obtaining final approvals."

"Market fundamentals for both zinc and tin are strong due to mine
closures and diminishing mine grades. Tinka is well placed to take
advantage of a supply shortfall in base metals as the mining cycle
continues, and as Tinka continues to prove the potential of a
significant zinc/tin deposit at Ayawilca."

Table 1 - Ayawilca Deposit Inferred Mineral Resources - Zinc Zone

//st
ZnEq% Cut-off Tonnage (Mt) ZnEq% Grade Zinc % Lead % Indium g/t Silver g/t
3                     22.3         7.5    5.5    0.2         67         13
4                     20.9         7.8    5.6    0.2         70         14
5                     18.8         8.2    5.9    0.2         74         15
6                     13.1         9.4    6.6    0.2         93         16
7                      9.5        10.4    7.2    0.2        110         17

//et

Notes: 1. Base case highlighted.

Table 2 - Ayawilca Deposit Inferred Mineral Resources - Tin Zone

//st
SnEq% Cut-off   Tonnage (Mt)  SnEq% Grade  Tin %  Copper %  Silver g/t
0.25                     5.7         0.87   0.73      0.30          18
0.35                     5.6         0.87   0.74      0.31          18
0.45                     5.4         0.89   0.76      0.31          18
0.55                     3.8         1.06   0.91      0.36          18
0.65                     3.2         1.15   1.00      0.36          18

//et

Notes: 1. Base case highlighted. 2. See Table 4 for notes.

Detail of Mineral Resource Estimates

RPA updated the Ayawilca Mineral Resource estimate using the drill
results available to May 15, 2016 . The resources now include tin
(Sn)-copper (Cu) mineralization ("Tin Zone") located below the zinc
(Zn) -indium (In)-silver (Ag) -lead (Pb) mineralization ("Zinc Zone") -
seeFigure 1. The two types of mineralization are distinct, and were
treated separately using different cut-off values equivalent to an
approximate US$60/t cut-off, on the basis of a possible underground
mining scenario.

The Zinc Zone Mineral Resources are hosted by Triassic Pucara
Group limestone approximately 200 metres thick beneath a sandstone unit
that hosts the Colquipucro silver oxide deposit located 1.5 km to the
north. The Zinc Zone deposit is made up of multiple, gently dipping
lenses or 'mantos' within three structural zones (West, Central and
East) located above the Paleozoic basement. The bulk of the
polymetallic mineralization in central Peru is located in a similar
geological environment. Inferred Mineral Resources within the Zinc
Zone, reported at a 5% zinc equivalent (ZnEq) cut-off, are estimated to
total 18.8 million tonnes at average grades of 5.9% Zn, 74 g/t In, 15
g/t Ag, and 0.2% Pb. The increase in average grade as compared to the
February 2015 estimate is due to the use of current lower metal prices.
The 5.5 Mt of additional resources since February 2015 are due to
mineralization found during the 2015 drilling campaign.

CIM definitions were followed for Mineral Resources.

Mineral Resources are reported above a cut-off grade of 5% ZnEq or
approximately US$60 per tonne NSR value (i.e., the same cut-off as was used
for the February 2015 resource estimate).

The ZnEq grade was based on estimated metallurgical recoveries, assumed
metal prices and smelter terms, which include payable factors, treatment
charges, penalties, and refining charges. Metal price assumptions were:
US$1.00/lb Zn, US$500/kg In, US$20/oz Ag, and US$1.00/lb Pb. Metal recovery
assumptions were: 90% Zn, 75% In, 50% Ag, and 75% Pb. The NSR value for
each block was calculated using the following NSR factors: US$11.88 per %
Zn, US$4.16 per % Pb, US$0.30 per gram In, and US$0.28 per gram Ag.

The zinc equivalent (ZnEq.%) value was calculated using the following
formula: ZnEq.(%) =
[Zn(%)*US$11.88+Pb(%)*US$4.16+In(g/t)*US$0.30+Ag(g/t)*US$0.28]/ US$11.88

Numbers may not add due to rounding.

//et

The Tin Zone Mineral Resources are commonly hosted as disseminated
cassiterite and chalcopyrite in massive to semi-massive pyrrhotite
lenses at the contact between the Pucara Group and underlying phyllite
of the Devonian Excelsior Group, and can also occur as quartz sulphide
stockwork veinlets hosted by the phyllite. Inferred Mineral Resources
within the Tin Zone, reported at a 0.45% tin equivalent (SnEq) cut-off,
are estimated to total 5.4 million tonnes at average grades of 0.89%
Sn, 0.3% Cu and 18 g/t Ag.

Table 4 - Tin Zone Inferred Mineral Resources at Ayawilca as of
May 25, 2016

//st
Tonnage (Mt)  Sn Eq.  Sn (%)  Cu (%)  Ag (g/t)  Sn  Cu   Ag
(%)   (Mlb)   (Mlb)     (Moz)
Tin Zones            5.4    0.89    0.76    0.31        18  90  37  3.1

//et

Notes:

//st

CIM definitions were followed for Mineral Resources.

Mineral Resources are reported above a cut-off grade of 0.45% SnEq or
approximately US$60 per tonne NSR value.

The SnEq grade was based on estimated metallurgical recoveries, assumed
metal prices and smelter terms, which include payable factors, treatment
charges, penalties, and refining charges. Metal price assumptions were:
US$9/lb Sn, US$3/lb Cu, and US$20/oz Ag. Metal recovery assumptions were:
85% Sn, 75% Cu, and 50% Ag. The NSR value for each block was calculated
using the following NSR factors: US$130.36 per % Sn, US$41.26 per % Cu, and
US$0.28 per gram Ag.

The tin equivalent (Sn Eq.%) value was calculated using the following
formula: Sn Eq.(%) = [Sn(%)*US$130.36+Cu(%)*US$41.26+Ag(g/t)*US$0.28]/
US$130.36

Numbers may not add due to rounding.

//et

The Ayawilca drill database includes 27,248 m in 74 diamond drill
holes. A set of cross-sections and level plans were interpreted to
construct three-dimensional wireframe models at approximate cut-offs of
5% ZnEq for the zinc zones and 0.45% SnEq for the tin zones. Prior to
compositing to two metre lengths, high Zn, Sn, In, and Ag values were
cut to 25%, 4%, 500 g/t, and 100 g/t, respectively. Block model grades
within the wireframe models were interpolated by inverse distance
cubed. Despite lead grades being low it is assumed that lead and silver
will be recovered in a lead concentrate. Density was estimated to be
3.6 t/m3 for the Zinc Zones and 3.9 t/m3 for the Tin Zones. All Mineral
Resources were assigned to the Inferred category due to the widely
spaced drilling. No Mineral Reserves have yet been estimated at
Ayawilca.

The Mineral Resource estimate for the Colquipucro silver oxide
deposit (Indicated Mineral Resource of 7.4 Mt at a grade of 60 g/t Ag
for 14.3 Moz Ag and Inferred Mineral Resource of 8.5 Mt at a grade of
48 g/t Ag for 13.2 Moz Ag, using US$15/t cut-off and a metal price of
$24/oz Ag) remains unchanged from the February 26, 2015 news release.

Qualified Person - Mineral Resources: The Mineral Resources
disclosed in this press release have been estimated by Mr. David Ross,
P.Geo., an employee of RPA and independent of Tinka. By virtue of his
education and relevant experience, Mr. Ross is a "Qualified Person" for
the purpose of National Instrument 43-101. The Mineral Resources have
been classified in accordance with CIM Definition Standards for Mineral
Resources and Mineral Reserves (May, 2014). Mr. Ross, P.Geo. has read
and approved the contents of this press release as it pertains to the
disclosed Mineral Resource estimates.

A National Instrument 43-101 Technical Report will be filed on
SEDAR within 45 days.

About Tinka Resources Limited

Tinka is an exploration and development company with projects in
Peru. Tinka's focus is on its 100%-owned Ayawilca Project in the highly
mineralized zinc-lead-silver belt of central Peru, 200 kilometres north
of Lima and 40 kilometres from Peru's largest historic zinc mine at
Cerro de Pasco. Ayawilca has Inferred Mineral Resources of 18.8 Mt at
8.2% Zinc Eq, and 5.4 Mt at 0.89% Tin Eq (this release), open for
expansion. The Colquipucro silver oxide project located 2km to the
north (Indicated Mineral Resource of 7.4 Mt at 60g/t Ag for 14.3 Moz Ag
and Inferred Mineral Resource of 8.5 Mt at 48g/t Ag for 13.2 Moz Ag;
Feb' 26, 2015) is a near-surface, sandstone-hosted, silver oxide
deposit.

On behalf of the Board,

"Graham Carman"

Dr. Graham Carman, President & CEO

Forward Looking Statements: Certain information in this news
release contains forward-looking statements and forward-looking
information within the meaning of applicable securities laws
(collectively "forward-looking statements"). All statements, other than
statements of historical fact are forward-looking statements.
Forward-looking statements are based on the beliefs and expectations of
Tinka as well as assumptions made by and information currently
available to Tinka's management. Such statements reflect the current
risks, uncertainties and assumptions related to certain factors
including, without limitations, the successful completion of future
drill programs, the interpretation and actual results from the drill
programs, the Company's expectations regarding mineral resource
calculations, capital and other costs varying significantly from
estimates, production rates varying from estimates, changes in world
metal markets, changes in equity markets, uncertainties relating to the
availability and costs of financing needed in the future, equipment
failure, unexpected geological conditions, imprecision in resource
estimates or metal recoveries, success of future development
initiatives, competition, operating performance, environmental and
safety risks, delays in obtaining or failure to obtain necessary
permits and approvals from local authorities, community relations, and
other development and operating risks. Should any one or more of these
risks or uncertainties materialize, or should any underlying
assumptions prove incorrect, actual results may vary materially from
those described herein. Although Tinka believes that assumptions
inherent in the forward-looking statements are reasonable,
forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to
the inherent uncertainty therein. Except as may be required by
applicable securities laws, Tinka disclaims any intent or obligation to
update any forward-looking statement.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

To view the map associated with this press release, please click
on the following link:
http://www.marketwire.com/library/20160525-tinka1.jpg

Investor Information:
Mariana Bermudez
1.604.699.0202
info@tinkaresources.com
(604) 683-1585 (FAX)
www.tinkaresources.com
______________________________________
_______________________________________________
TSX Venture closing price for TK-V
Date: 2016/05/24
Closing Price: 0.23
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1614500017TS11614500961-06114020160525