Source	Marketwire
Date	05/25/2016
Time	07:01:16 AM

Company	 KHALKOS EXPLORATION INC.
Title	Khalkos Obtained up to 20 g/t Au on its Malartic Property (Revillard Part)





    CDNX Symbol: KAS











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Khalkos Exploration Inc.

TSX VENTURE SYMBOL: KAS

May 25, 2016

Khalkos Obtained up to 20 g/t Au on its Malartic Property (Revillard Part)


MONTREAL, QUEBEC--(Marketwired - May 25, 2016) - KHALKOS EXPLORATION. 
("Khalkos") (TSX VENTURE:KAS) - Management of Khalkos is pleased to announce 
results of surface sampling undertaken on its new Malartic property, Revillard 
part (see press release May 11, 2016). The due diligence done by Khalkos on the 
main stripping zone and its surrounding area indicated that the principal 
showing (100 m in length and 30 m in width) remains open to the west with a 
selected sample that yielded 13 g/t Au. No channel sampling was done on this 
zone. Note that in 2006, Britannica Resources undertook 334 channel samples 
(0,5 m length each) for a total of 125 metres. Khalkos yielded a 20 g/t Au in a 
selected sample, approaching the highest value obtained in channel sampling 
that was 29 g/t Au (see press release of Britannica Resources July 19, 2006). 
Two other random samples on the trench yielded abnormal values between 0,18 and 
0,26 g/t Au. Note that the northern part of the trench yielded more than 14 g/t 
Au and no follow-up was done by previous manager. It is thus obvious that the 
principal showing remains open and other stripping is required. In addition, 
Khalkos' team discovered, at more than 200 metres west of the main stripping 
zone, an ancient trench containing quartz vein blocks mineralized in pyrite, 
chalcopyrite, covellite, galena and native gold. Two samples were collected and 
yielded 11,5 g/t and 1,6 g/t Au. No stripping or recent drilling took place in 
this zone. Khalkos plans to undertake shortly surface fieldworks on the main 
stripping zone and its possible extension.

The Malartic property (part JAG, part Malartic Lakeshore, part Revillard) is 
constituted of 82 mining claims covering more than 10 km of favorable 
auriferous structure in the Malartic mining camp, 30 km north-west of the 
Val-d'Or city. The property is located in the heart of Cadillac deformation 
zone and at the proximity of important gold producers, at only 2 km of Lapa 
mine (Agnico Eagle "AEM"), 11 km of Canadian Malartic mine (Yamana - AEM) and 
20 km of Laronde mine (AEM), on the same geological contact where the gold 
mines Doyon-Bousquet, Laronde as well as Westwood are located.

Samples from the Malartic property were assayed by ALS Chemex laboratory in 
Val-d'Or, Quebec. Following the fire assay, samples yielded greater than 10 g/t 
were re-assayed by the gravimetric method. Samples were prepared following 
standard procedures of the laboratory.

This press release was prepared by Robert Gagnon, President of Khalkos, 
Qualified Person pursuant to National Instrument 43-101.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

A map is available at the following address: 
http://file.marketwire.com/release/1056294.jpg

- 30 -

CONTACT INFO:

Robert Gagnon
President
(819) 825-2303
rgagnon@khalkos.com

or

Christian Guilbaud
Corporate Development
(514) 813-7862
Fax: (514) 510-7964
cguilbaud@videotron.ca
www.khalkos.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=567481820