Source	MARKET NEWS
Date	05/31/2016
Time	07:18:13 AM

Company	 ATAC Resources Ltd.
Title	Positive 
Results Of An Updated Pea At The High g





    CDNX Symbol: ATC











Press Release




[200/News Release]ATCVATAC RESOURCES LTDMAY 31 2016  07:16 AMPositive 
Results Of An Updated Pea At The High grade Tiger GoldDeposit, Rackla Gold 
Project, Yukon --->@NEWS RELEASE
ATAC RESOURCES LTD ("ATC-V;ATADF-0")
- Positive Results Of An Updated Pea At The High-grade
- Tiger Gold Deposit, Rackla Gold Project, Yukon

ATAC Resources Ltd. is pleased to announce the completion of an
updated Preliminary Economic Assessment ("PEA") for the Tiger Deposit,
located at the western side of the Company's 100% owned Rackla Gold
Project, Yukon.

The 2016 PEA has incorporated results of geotechnical and infill
drilling conducted in 2015 and metallurgical studies completed in early
2016. Key changes to the 2014 PEA consist of the inclusion of both
oxide and sulphide resources and the adoption of a simplified
year-round agitated tank carbon-in-pulp ("CIP") leaching process. The
2014 PEA (see ATAC news release dated July 23, 2014) only investigated
the extraction of oxide resources by means of a seasonal hybrid
heap-leach and agitated tank carbon-in-leach ("CIL") process.

2016 PEA Highlights:

Highlights from the 2016 PEA, with the base case gold price of
US$1,250/oz and an exchange rate of CA$1.00 equal to US$0.78 are as
follows. Unless specified otherwise, all values are shown in Canadian
dollars.

//st

NPV(sub)(5%)(/sub) of $106.6 million and an IRR of 34.8% before tax,
and an NPV(sub)(5%)(/sub) of $75.7 million and an IRR of 28.2% after tax,
with an all-in sustaining cost of US$864/oz;

Compared to the 2014 PEA, the 2016 PEA extends the mine life by 2
years, more than doubles the pre-tax NPV(sub)(5%)(/sub) and increases the
pre-tax IRR by 4.8%;

Approximately 302,307 ounces of gold produced at an average undiluted
grade of 3.81 g/t gold;

Total project life increases to approximately 9 years, including 1 year
of construction and pre-stripping followed by 6 years of owner-operated
open-pit mining and 2 years of reclamation; and,

Pre-production capital cost of $109.4 million and life-of-mine ("LOM")
sustaining capital costs totaling $8.3 million.

//et

"We are very pleased to have doubled the pre-tax NPV to over $100
million and to have been able to improve on every other 2014 PEA
metric. The future development of the Tiger Deposit would bring
critical infrastructure, including tote road access, to the Rackla Gold
Project. Exploration will begin shortly at the newly discovered 10 km2
Airstrip gold anomaly and elsewhere within the Rau Trend with the
objective of identifying additional nearby resources. ATAC will
continue to explore opportunities to advance or monetize the Tiger
Deposit through sole development or joint venture," states Graham
Downs, President and CEO of ATAC. "ATAC remains committed to further
advancing the entire Rackla Gold Project, including the Carlin-type
targets within the Nadaleen Trend. Drilling is scheduled to begin soon
at the Orion discovery, where one of the last holes of 2015
(ARB-15-026) intersected 3.79 g/t gold over 47.24 m."

Tetra Tech WEI Inc. ("Tetra Tech") (mining, processing,
infrastructure, financial analysis) was contracted to complete the PEA
in cooperation with Blue Coast Metallurgy Ltd. (metallurgy), Knight
Piesold Ltd. (tailings), Resource Strategies (environmental and
permitting), Giroux Consultants Ltd. (mineral resource) and Archer,
Cathro & Associates (1981) Limited (geology, mineralization and
exploration).

//st
Table I: Comparison of Key Results & Parameters
2014 PEA             2016
PEA*
Gold Price (US$/oz)                               $1250              $1250
Exchange Rate (US$/CA$)                            0.92               0.78

Pre-tax NPV(5%) (millions)                        $52.2             $106.6
Pre-tax IRR                                       30.0%              34.8%
Post-tax NPV(5%) (millions)                      $33.67             $75.71
Post-tax IRR                                      21.5%              28.2%

Recovered Gold                               221,558 oz            302,307oz
Average Gold Grade                             3.72 g/t              3.81g/t
Average Oxide Recovery                            89.8%             90.3%
Average Sulphide Recovery                            0%             57.7%

Pre-production Capital (millions)                 $92.3            $109.4
Sustaining Capital (millions)                     $26.5              $8.3

Payback (pre-tax)                             2.2 years            1.85years
Payback (post-tax)                            2.6 years            1.93years
Pre-production Period                            1 year                1year
Mine Life                                       4 years             6.2years
Closure Period                                  2 years               2years
Project Life                                    7 years             9.2years

Process                           Hybrid CIL/Heap Leach                  CIP
Production Rate                               3,300 tpd            1,500 tpd
Operational Period                 Seasonal (158 days) Year-round (365 days)
Strip Ratio                                       5.6:1                4.9:1
Access Method                               Winter Road            Tote Road

//et

* The 2016 PEA does not consider silver resources.

Key Improvements over the 2014 PEA:

The 2016 PEA envisions a conventional year-round operation and has
improved upon all aspects of the 2014 PEA. Key improvements include:

//st

Increased the pre-tax NPV(sub)(5%)(/sub) by $54.4M;

36% increase in total recovered ounces;

Project life extended by 2 years;

Pre-tax payback period reduced to 1.85 years;

Tote road access: supports year-round operations and simplifies
project logistics;

100% CIP process: simplified and conventional process allows for
year-round operations and reduces LOM sustaining capital costs;
Relocated and consolidated project infrastructure: reduced overall
environmental footprint and haulage costs; and,

Year-round operations: alleviates logistical and staffing challenges
associated with seasonal access and operations.

//et

Economic Results and Sensitivities

The following tables demonstrate the sensitivity of the Tiger
Deposit pre-tax economics to changes to the price of gold and exchange
rates. The base case, highlighted in the tables below, assumes US$1,250
per ounce of gold at an exchange rate of CA$1.00 equals US$0.78.

//st
Table II: Summary of Gold Price Sensitivity (0.78 US$/CA$)
Gold Price (US$/oz)                     $1,200  $1,250  $1,300
Pre-tax Cumulative Net Cash Flow ($M)   $130.1  $149.4  $168.7
Pre-tax NPV(5%) ($M)                     $90.8  $106.6  $122.3
Pre-tax IRR                              30.8%   34.8%   38.8%

//et

//st
Table III: Summary of Exchange Rate Sensitivity (US$1,250/oz Au)
Exchange Rate (US$/CA$)               0.76 US$/CA$ 0.78 US$/CA$ 0.80 US$/CA$
Pre-tax Cumulative Net Cash Flow ($M)       $162.0       $149.4     $137.4
Pre-tax NPV(5%) ($M)                        $116.9       $106.6      $96.8
Pre-tax IRR                                  37.4%        34.8%      32.3%

//et

Mining and Processing

The Tiger Project has been modeled as an owner-operator,
conventional truck-and-shovel open-pit mining operation with a
conventional CIP gold recovery process. Year-round operations would be
supported via a 68 km tote road, which connects the project to the
Yukon highway system, near Keno City.

Mineralized material will be loaded into 40 tonne articulated
trucks and delivered to the process plant, located 1 km southwest of
the pit. High-grade mineralized material will be sent directly to the
primary crusher, while low-grade stockpile material will be stored
close to the primary crusher. Waste material from the pit will be
stored in two waste dumps, located at the northwest and southwest sides
of the pit. A total of 3.2 Mt of the Mineral Resource and 15.6 Mt of
waste rock will be produced from the pit during the 7 years of mining
operations and pre-stripping. The LOM average gold grade of mined oxide
and sulphide resources is 4.06 g/t and 2.99 g/t, respectively. The LOM
stripping ratio (defined as waste material mined divided by Mineral
Resources mined) is 4.9.

Due to the soft nature of the mineralization and host rock, a
single stage of crushing will be performed by a MMD sizer. Crushed
material will be ground to 80% passing 75 microns using a
semi-autogenous grinding mill and a ball mill in series before cyanide
leaching in a conventional CIP circuit. The leach tailings will be
detoxified and stored in a lined facility within the Tiger Valley. Gold
will be refined into dore bars on site through a standard Adsorption,
Desorption and Recovery treatment. Based on the results of
metallurgical testwork and the mining schedule, projected LOM average
recoveries are 90.3% for oxide mineralization and 57.7% for sulphide
mineralization.

The processing plant will operate year-round at a rate of 1,500
tonnes per calendar day, and will achieve full throughput in Year 2.
Peak annual production will be approximately 86,555 oz of gold in Year
2, with a LOM average annual production of approximately 50,000 oz
gold, excluding the final year which will operate for a reduced period.


Capital and Operating Costs

Total LOM capital costs are $117.7 million, with $109.4 million in
pre-production costs and $8.3 million in sustaining capital. To
minimize initial capital costs, the PEA has assumed that modular
equipment would be used where possible and that some equipment and
facilities will be leased.

The following tables summarize the project capital and operating
costs.

//st
Table IV: Pre-Production & Sustaining Capital Costs
Area                         Pre-Production ($M)* Sustaining ($M)* LOM ($M)*
Site Infrastructure                           $8.1                -   $8.1
Tote Road                                    $11.0                -  $11.0
Open Pit Mining**                            $13.2            $0.03  $13.2
Materials Crushing & Handling                 $2.0                -   $2.0
Process Plant                                $29.7                -  $29.7
Tailings & Water Management                   $7.9             $6.1  $14.0
Project Indirects                            $19.8                -  $19.8
Owner's Costs                                 $1.2                -   $1.2
Contingencies***                             $16.5             $2.2  $18.7
Total                                       $109.4             $8.3 $117.7

//et

* Totals may not add exactly due to rounding.

** Includes capitalized pre-production mining costs. Major mining
equipment is leased.

*** Contingencies were factored on an area-by-area basis depending
on the detail level of each estimate.

//st
Table V: Operating Costs
Description                                 LOM Average
Mining Cost ($/t mined)*                          $4.31
Processing Cost ($/t processed)                  $26.98
G&A ($/t processed)                              $12.38
Surface Services ($/t processed)                  $3.80
Equipment Leasing ($/t processed)                 $1.68

//et

*Not including capitalized pre-production mining costs

Opportunities to Enhance Value

ATAC is very pleased with the increased value of the Tiger Deposit
shown in this updated PEA relative to the initial 2014 PEA and believes
that opportunities exist to further enhance the economics of the
project. Some key opportunities include:

//st

Significant potential exists to increase the resource base and life
expectancy of the project with the exploration of more than 15 early-stage
satellite oxide gold targets and geochemical anomalies;

Additional geotechnical studies may permit steeper pit slopes, which
would further reduce the strip ratio and could potentially allow additional
known resources to be accessed;

Additional diamond drilling within the sulphide zone would convert
inferred resources to the indicated category and could potentially lead to
the inclusion of additional known sulphide resources; and,

Additional diamond drilling targeting high-grade oxide structures
(including 162.0 g/t gold over 2.90 m in Rau-09-019) could better define
high-grade domains for inclusion in future resource estimates.

//et

Environmental and Community Engagement

Since 2008, ATAC has completed comprehensive water, heritage,
wildlife and fisheries studies. ATAC will continue environmental
baseline work and ongoing studies as it advances the Tiger Deposit and
other targets throughout the Rackla Gold Project.

Community and First Nation engagement began in 2008, and an
Exploration Cooperation Agreement with the First Nation of Na Cho Nyak
Dun ("NNDFN") was signed in 2010. This Exploration Cooperation
Agreement with the NNDFN provides a framework within which exploration
activities and environmental regulatory process on ATAC's Rackla Gold
Project have been and will continue to be carried out. The Rackla Gold
Project lies exclusively within the Traditional Territory of the NNDFN.


Metallurgy

Metallurgical testwork has been previously conducted in several
phases on both the oxide and sulphide material, including work by G&T
Metallurgical, SGS Canada, and Kappes, Cassiday & Associates in support
of the 2014 PEA. Additional variability cyanide leach testwork was
conducted on the Tiger Deposit by Blue Coast Research Ltd. in 2016 for
the updated PEA. Bottle roll testing was conducted on eight oxide and
eight sulphide composites, and master composites samples. Samples were
selected to evaluate potential variability in grade and mineralization
throughout the deposit. Oxide recoveries from 24-hr bottle roll tests
ranged from 77% to 98%. Sulphide recoveries from 24-hour bottle roll
tests ranged from 13% to 88%.

Mineral Resources

The Mineral Resource estimate used in the updated PEA was
completed by Gary Giroux, P.Eng., M.A.Sc. (Giroux Consultants Ltd.)
using 6,222 assays taken from 150 diamond drill holes, totalling 26,844
m. The effective date of this Mineral Resource estimate is October 28,
2015. A three dimensional solid model was constructed to constrain
oxide and sulphide mineralization.

Gold distribution, within the mineralized solids, was examined
using a lognormal cumulative frequency plot to determine appropriate
capping levels. Three metre composites were formed, honouring solid
boundaries, using the capped assay data. Ordinary Kriging was used to
interpolate gold and silver values into a 5x5x5 m block model.

Mineral Resources are reported at a 0.5 g/t cut-off in oxides and
1.0 g/t cut-off in sulphides are reported in the table below. Thesecut-off 
grades were selected based on comparison to other analogous
deposits.

//st
Table VI: Combined Oxides & Sulphide Resource

//et

The primary difference between this Mineral Resource and the
Mineral Resource used in the 2014 PEA is an increase in measured
resources within the oxide domain. There is little difference in the
total tonnes and contained ounces of gold between the two mineral
resources.

Tiger Tote Road

Access to the Rau Trend and Tiger Gold Deposit, 55 km northeast of
Keno City, would be by means of a tote road, which ATAC intends to
permit and construct to support advanced exploration activities. The
proposed tote road would branch off the Hanson Lake Road west of Keno
City and is envisioned as a gated, single-lane (5 m wide) and
radio-controlled road suitable for vehicles that support advanced
exploration at the Tiger Deposit and throughout the Rau Trend. The
total length of the tote road would be approximately 68 km and would
consist of 51 km of new road and upgrading of 17 km of pre-existing
winter road.

For the purposes of this PEA, the full cost of the tote road is
included in the pre-production capital costs.

ATAC has been active in preparing for permitting the tote road to
the Rackla Gold Project. Discussions regarding access and development
of the Tiger Deposit with the NNDFN, local communities and other
interested parties has been ongoing for more than seven years. Recent
meetings in March and April 2016 included several town meetings in Mayo
and Keno City to discuss the proposed tote road. Details of this
consultation can be found on ATAC's website. NNDFN and community
consultation is ongoing.

About ATAC

ATAC is a Yukon-based exploration company focused on developing
Canada's only Carlin-type gold district at its 100% owned 1,700 km2
Rackla Gold Project. Recent work on the project has resulted in
drilling of multiple high-grade Carlin-type gold zones and the
identification of numerous early-stage gold exploration targets. The
Rackla Gold Project has no underlying royalties or third-party
interests. ATAC is well financed with approximately $19 million in its
treasury.

Qualified Persons

The reader should be cautioned that the PEA is preliminary in
nature. It includes Inferred Mineral Resources that are considered too
speculative geologically to have the economic considerations applied to
them that would enable them to be categorized as mineral reserves.
There is no certainty that the results of the PEA will be realized.

A Technical Report supporting the PEA in accordance with National
Instrument 43-101 will be filed on SEDAR (www.sedar.com) and ATAC's
website (www.atacresources.com) within 45 days. Further details
regarding the 2011 Mineral Resource and the 2014 PEA can be found in
the Technical Reports dated November 15, 2011, and September 4, 2014,
which are both filed on SEDAR and ATAC's website.

The PEA was prepared under the direction of Tetra Tech WEI Inc., in
cooperation with other industry consultants, all of whom are Qualified
Persons (QPs) under terms of NI 43-101 and have reviewed the technical
content of this press release and approved its dissemination. QPs
contributing to the PEA are listed in the following table.

//st
Table VII: QPs contributing to the PEA
Qualified Person, Designation                                       Company
Sabry Abdel Hafez, Ph.D., P.Eng.                        Tetra Tech WEI Inc.
Hassan Ghaffari, P.Eng., M.A.Sc.                        Tetra Tech WEI Inc.
John Huang, Ph.D., P.Eng.                               Tetra Tech WEI Inc.
Chris Martin, C.Eng.                             Blue Coast Metallurgy Ltd.
Gary Giroux, P.Eng., M.A.Sc.                        Giroux Consultants Ltd.
Bruno Borntraeger, P.Eng.                               Knight Piesold Ltd.
Rob McIntyre, R.E.T.                                    Resource Strategies
Matthew Dumala, P.Eng.           Archer, Cathro & Associates (1981) Limited

//et

Matthew Dumala, P.Eng., a Geological Engineer with Archer, Cathro &
Associates (1981) Limited, is the company's designated QP for this news
release within the meaning of National Instrument 43-101 and has
reviewed and validated that the information contained in the release is
consistent with that provided by the QPs responsible for the PEA.

On behalf of the Board of Directors
of ATAC Resources Ltd.
Graham Downs, President and CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS
THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS NEWS RELEASE.

Vanessa Pickering
Manager, Corporate Communications
ATAC Resources Ltd.
T: 604-687-2522 ext. 260
info@atacresources.com
______________________________________
_______________________________________________
TSX Venture closing price for ATC-V
Date: 2016/05/30
Closing Price: 0.71
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1615100020TS11615101214-07160720160531