Source	Marketwire
Date	05/03/2017
Time	09:01:30 PM

Company	 ML GOLD CORP.
Title	ML Gold Reports Additional Mineralized Zones Containing Visible Gold 
Identified in Palmetto Gold Project Drilling





    CDNX Symbol: MLG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ML Gold Corp.

TSX VENTURE SYMBOL: MLG
FRANKFURT SYMBOL: XOVN.F

May 4, 2017

ML Gold Reports Additional Mineralized Zones Containing Visible Gold Identified 
in Palmetto Gold Project Drilling


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 4, 2017) - ML Gold Corp. (TSX 
VENTURE:MLG)(FRANKFURT:XOVN.F) ("ML Gold" or the "Company") is pleased to 
provide an update on the Palmetto Gold Project in Esmeralda County, Nevada, 
within the Walker Lane mineral belt, where one core and one reverse circulation 
(RC) drill are operating to produce a maiden gold resource being conducted by 
engineering firm WSP Canada Inc.

To date, RC holes 1 through 4 have been processed and sent to ALS Minerals lab 
in Reno, Nevada for assaying. These holes are a combination of exploratory 
step-out and infill holes aimed to grow the resource estimate being completed 
following the drill program. ML Gold has received assay results for the first 
complete RC hole (PAL-17R01), and highlighted results are as follows:

/T/

----------------------------------------------------------------------------
From     To Interval   Gold Silver
Hole ID   Easting  Northing Azimuth Dip    (m)    (m)      (m)  (g/t)  (g/t)
----------------------------------------------------------------------------
UTM NAD 83 Z11
----------------------------------------------------------------------------
PAL-17R01  392515   4189508       0 -75  195.1  222.5     27.4   1.10   1.63
----------------------------------------------------------------------------
including                                211.8  219.5     7.62   3.56   3.07
----------------------------------------------------------------------------

/T/

This intersection in PAL-17R01 targeted an area down dip from the Discovery 
Zone's 3D computer generated mineralized shell, and did not twin any previously 
known intersections. This intersection, which includes 90 feet of greater that 
one gram material, extends the mineralization from within 40 metres (m) of 
bedrock surface to now at least 220 metres total depth. This hole confirms the 
mineralization is open to depth and will allow the 3D computer model to expand 
the volume of mineralized rock resulting in additional ounces in the resource 
estimate moving forward.

At present, the RC drill is on its 8th hole, an unplanned location in the 
Northwest Zone, not part of the original planned program, but added to test 
beneath an approximately 10 foot intercept of quartz veining with noted visible 
gold in the 7th RC hole. The intersection in hole 7 represents the first 
reported visible gold in the Northwest Zone, approximately 500 metres northwest 
of the Discovery Zone.

Concurrently, the core drill has completed its third hole of a program designed 
to confirm the geology, mineralization and physical rock properties for the 
anticipated resource estimate. Following the last update (see Company news 
dated April 6, 2017), the second core hole was drilled to a final depth of 
1,111 feet within the Discovery Zone and ended in mineralization after 
intersecting two additional zones below any previously known mineralized 
intercepts identified in the historic drilling. This further indicates that 
drilling in the Discovery Zone system has not found the "bottom" and asserts 
that the zones have to be tested even deeper. Logging and processing of the 
second core hole has been completed and samples are in transit to the ALS 
Minerals lab in Reno, Nevada. Visible gold was identified in at least one part 
of this hole.

Adrian Smith, President of ML Gold commented, "We are extremely pleased with 
the initial results in the first RC hole beneath the Discovery Zone. The hole 
suggests that robust gold mineralization continues to depth. Although awaiting 
assay information, the recently identified intersection containing visible gold 
in the Northwest Zone should further strengthen the multi-zone potential. We 
now have two adjacent gold systems on the property, it's very exciting, and we 
are anxiously awaiting results."

Quality Assurance/Quality Control

Sample preparation and analyses for this program were completed at ALS Minerals 
Lab in Reno Nevada. Gold was determined by 30g Fire Assay with Atomic 
Absorption Spectrophotometry (AAS) finish. Other elements were determined by 
Ultra Trace Aqua Regia digestion with Inductively Coupled Plasma Mass 
Spectrometry (ICP-MS) finish.

A comprehensive quality assurance/quality control program including duplicate 
samples, blanks and standards form part of ML Gold's sampling protocol in 
addition to the laboratory's own quality assurance program. The field program 
was supervised by ML Gold staff and contractors and the technical information 
in this news release has been prepared in accordance with Canadian regulatory 
requirements as set out in National Instrument 43-101, and reviewed by Adrian 
Smith, Director, and a Qualified Person as that term is defined in NI 43-101.

ABOUT ML GOLD CORP.

ML Gold Corp. is a Canadian listed Company, focused on creating shareholder 
value through discoveries and strategic development of mineral properties in 
Canada and the United States.

For additional information please visit the Company's website at 
www.mlgoldcorp.com.

ML GOLD CORP.

Andrew Bowering, Chairman

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE

This news release may contain certain "Forward-Looking Statements" within the 
meaning of the United States Private Securities Litigation Reform Act of 1995 
and applicable Canadian securities laws. When or if used in this news release, 
the words "anticipate", "believe", "estimate", "expect", "target, "plan", 
"forecast", "may", "schedule" and similar words or expressions identify 
forward-looking statements or information. These forward-looking statements or 
information may relate to future prices of commodities, accuracy of mineral or 
resource exploration activity, reserves or resources, regulatory or government 
requirements or approvals, the reliability of third party information, 
continued access to mineral properties or infrastructure, currency risks 
including the exchange rate of US$ for CDN$, changes in exploration costs and 
government royalties or taxes in Canada, the United States or other 
jurisdictions and other factors or information. Such statements represent the 
Company's current views with respect to future events and are necessarily based 
upon a number of assumptions and estimates that, while considered reasonable by 
the Company, are inherently subject to significant business, economic, 
competitive, political and social risks, contingencies and uncertainties. Many 
factors, both known and unknown, could cause results, performance or 
achievements to be materially different from the results, performance or 
achievements that are or may be expressed or implied by such forward-looking 
statements. The Company does not intend, and does not assume any obligation, to 
update these forward-looking statements or information to reflect changes in 
assumptions or changes in circumstances or any other events affections such 
statements and information other than as required by applicable laws, rules and 
regulations.

- 30 -

CONTACT INFO:

ML Gold Corp.
Investor Relations
(604) 669-2279
info@mlgoldcorp.com

INDUSTRY: Financial Services - Venture Capital
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=592582811