Source	MARKET NEWS
Date	05/04/2017
Time	05:54:36 AM

Company	 Marlin Gold Mining Ltd.
Title	Confirms 
Discovery Of New Gold Zone At Commonwea





    CDNX Symbol: MLN











Press Release





MARLIN GOLD MINING LTD ("MLN-V")
- Confirms Discovery Of New Gold Zone At Commonwealth Project

Marlin Gold Mining Ltd. ("Marlin" or the "Company") is pleased to
report drilling results from its wholly owned Commonwealth silver and
gold project in Cochise County, Arizona (the "Commonwealth Project").

On January 30, 2017 Marlin reported the "Footwall Zone" discovery
hole on Pearce Hill at the Commonwealth Project.  Hole 16CDDH06
intersected 2.91 g/t gold equivalent using a 160:1 silver to gold ratio
("AuEq") over 25.8 meters (2.72 g/t Au and 30 g/t Ag).  Since that
discovery hole, Marlin has drilled an additional 12 core holes deep
enough to test the Footwall Zone. Seven of these holes intersected AuEq
grades significantly higher than the M&I resource grade from the April
2014 NI 43-101 Technical Report, including 17CDDH24 which intersected
2.20 g/t AuEq over 25.7 meters (2.08 g/t Au and 19 g/t Ag).

The original interpretation of the Footwall Zone was that of a
parallel structure associated with the North Vein and part of the same
mineralized zone.  However, further drilling and geochemical analysis
has suggested that this is a distinct structure, with higher gold
values relative to silver, and formed at a different time and under
different chemical conditions.  This is consistent with the theory that
this district, which Marlin has consolidated for the first time in
modern history, is part of a larger hydrothermal system that has seen
multiple mineralizing events and has hosted a number of economic gold
and silver deposits.

Akiba Leisman, Executive Chairman and Interim CEO states that,
"based solely on the discovery hole, the interpretation of the Footwall
Zone was that of a high grade, but small target.  Now that we have
drill tested the Footwall Zone with 12 core holes, and hit significant
intercepts on seven of these holes, we believe the potential of this
target has increased substantially.  As a result, we will continue
drill testing down dip and along strike.  Additionally, the better
understanding of this new gold zone on Pearce Hill provides us an
analog that we can look for elsewhere on our approximately 3,600 acres
of privately owned land using targets developed from our geochemistry
and geophysics programs."

Click HERE for a cross section that highlights drill holes
16CDDH06 (previously released on January 30, 2017) and 17CDDH13, which
both intersected the Footwall Zone.

Click HERE for a cross section that highlights drill hole
17CDDH19, which intersected the Footwall Zone.

Click HERE for a cross section that highlights drill holes
17CDDH22 and 17CDDH24, which both intersected the Footwall Zone.

Click HERE for a plan view map of holes drilled deep enough to
test the Footwall Zone with corresponding grade x thickness values.

All holes drilled to date have been in oxide mineralization, which
can potentially be recovered through a heap leach process.  The
geometry of the Footwall Zone is variable and incompletely defined, but
based on current interpretations true widths of mineralized intercepts
are estimated to be 65% to 75% of the reported intercepts.

See below for a summary table of newly released drill holes.
Intercepts in bold intersected the Footwall Zone.

//st

Drill Hole(1)             From     To (m)   Length   AuEq       Au   Ag
(m)               (m)      (g/t)(2)   (g/t)(g/t)

17CDDH11                  94.48    102.36   7.88     0.60       0.28    51

and                       108.00   115.00   7.00     0.62       0.39    37

17CDDH12                  121.98   137.50   15.52    0.73       0.36    59

and                       140.30   161.00   20.70    0.71       0.45    42

and(3)                    222.80   228.43   5.63     0.78       0.74    7

17CDDH13                  2.00     8.00     6.00     0.96       0.37    95

and                       71.80    80.30    8.50     1.29       0.83    74

and(3)                    93.30    100.50   7.20     0.70       0.65    7

17CDDH14                  0.00     34.00    34.00    1.07       0.89    29

Including(4)   14.00    23.00    9.00     2.30       1.97    60

and                       37.00    43.76    6.76     0.36       0.31    7

17CDDH15                  18.00    29.30    11.30    0.95       0.83    19

and                       42.00    68.00    26.00    1.24       1.12    19

including(4)   46.00    60.00    14.00    2.00       1.88    21

and                       72.00    87.45    15.45    1.54       1.24    48

17CDDH16                  0.00     10.00    10.00    0.52       0.34    29

and                       37.40    45.00    7.60     0.61       0.20    65

and                       114.00   122.00   8.00     0.91       0.81    15

17CDDH17                  5.55     12.75    7.20     1.57       1.46    18

and                       34.00    43.00    9.00     0.44       0.24    32

and                       48.00    60.50    12.50    0.54       0.38    26

17CDDH18                  66.44    73.85    7.41     0.37       0.23    23

and                       112.00   126.00   14.00    2.95       2.79    26

including(4)   118.00   124.90   6.90     5.40       5.16    41

17CDDH19                  12.00    34.00    22.00    0.75       0.34    67

and                       38.00    56.00    18.00    0.56       0.17    63

and                       93.25    116.00   22.75    1.78       1.70    13

including(4)   102.00   112.00   10.00    3.50       3.37    13

17CDDH20                  48.00    84.79    36.79    0.63       0.25    61

and                       87.23    104.00   16.77    0.66       0.21    72

and                       110.00   122.00   12.00    0.87       0.58    47

and                       126.00   138.00   12.00    0.56       0.19    58

17CDDH21                  120.97   132.45   11.48    0.89       0.61    45

17CDDH22                  0.00     17.70    17.70    1.15       0.66    79

and                       30.17    41.40    11.23    0.63       0.22    65

and                       50.00    56.00    6.00     0.48       0.30    30

and                       67.00    77.00    10.00    0.53       0.35    30

and(3)                    96.90    107.00   10.10    1.40       1.34    10

17CDDH23                  24.00    42.00    18.00    0.38       0.23    24

17CDDH24                  40.90    58.00    17.10    0.49       0.20    47

and                       65.65    85.00    19.35    0.79       0.54    40

and                       112.00   137.70   25.70    2.20       2.08    19

including(4)   116.00   125.35   9.35     2.60       2.46    20

including(4)   130.00   137.70   7.70     3.60       3.43    24

//et

//st

(1)   Significant intercept defined as a minimum assay of 0.3 g/t AuEq
over a minimum 6-meter interval with no more than 2 meters of
internal dilution below 0.3 g/t AuEq.

(2)   Gold equivalent ("AuEq") values at a silver to gold ratio of 160:1.

(3)   Intercepts in italics for holes 17CDDH12, 17CDDH13 and 17CDDH22 are
included in this table because they are Footwall Zone intercepts,
but do not meet the definition of a "significant intercept" because
they are either shorter than 6 meters or have greater than 2 meters
of internal dilution.

(4)   Significant internal intercept defined as a minimum assay of 2.0
g/t AuEq over a minimum 6-meter interval with no more than 2 meters
of internal dilution below 0.5 g/t AuEq.

//et

Dr. Matthew D. Gray. C.P.G., of Resource Geosciences Incorporated,
a Qualified Person under the definitions of CSA NI 43-101, implemented
and supervised industry standard QA/QC protocols for the Commonwealth
Project drill sampling program including insertion of duplicate and
reference standard samples.  Dr. Gray has verified the reliability of
the drill sampling results reported in this press release.

Notes on Sampling and Assaying

Drill core was continuously sampled from inception to termination
of the drill hole. Sample intervals were typically two meters.  All
drill holes were started as large diameter PQ (8.5cm) core holes, and
were reduced to HQ (6.35cm) only where drilling conditions required.
Geologic and geotechnical data was captured into a digital database,
core was photographed, then one half split of the core was collected
for analysis and one half was retained in the core library. Samples
were kept in a secured logging and storage facility until such time
that they were received on site by representatives of Skyline Assayers
and Laboratories ("Skyline").  Sample preparation and analysis of pulps
was done in the Tucson, Arizona facilities of Skyline.  Gold was
analyzed by standard fire assay fusion, 30 gram aliquot, AAS finish,
with samples reporting greater than 10 grams per tonne gold re-assayed
by fire assay fusion with gravimetric finish.  Controls samples
consisting of duplicates, standards, and blanks were inserted into the
sample stream and analytical results of control samples confirmed
reliability of the assay data.

About Marlin Gold

Marlin is a growth-oriented gold and silver mining company focused
on the Americas.  The company owns two properties located in Sinaloa,
Mexico and Arizona, USA and a portfolio of royalties.  Marlin's
priority is to advance its properties toward commercial production and
enhance shareholder value through the growth of its wholly owned
subsidiary, Sailfish Royalty Corp.  Marlin is backed by a well-funded
investor with a successful track record in the resources sector.  The
La Trinidad Mine in Sinaloa, Mexico declared commercial production on
November 1, 2014 and is one of the highest-grade open pit heap leach
gold mines in Mexico.  A NI 43-101 mineral resource estimate and
preliminary economic assessment for the La Trinidad Mine and
Commonwealth Project can be found at www.sedar.com or at
www.marlingold.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as the term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary statement regarding forward-looking information

This news release contains 'forward-looking statements' within the
meaning of applicable securities laws. Forward-looking statements are
statements that are not historical facts and are generally, but not
always, identified by words such as the following: expects, plans,
anticipates, believes, intends, estimates, projects, assumes, potential
and similar expressions. Forward-looking statements also include
reference to events or conditions that will, would, may, could or
should occur, including, without limitation, the intended use of
proceeds. These forward-looking statements are necessarily based upon a
number of estimates and assumptions that, while based on management's
expectations and considered reasonable at the time they are made, are
inherently subject to a variety of risks and uncertainties which could
cause actual events or results to differ materially from those
reflected in the forward-looking statements, including, without
limitation: the risk that the anticipated effects of the equity
financing may not result in the outcomes predicted by management,
uncertainties related to raising sufficient financing to fund planned
work in a timely manner and on acceptable terms; changes in planned
work resulting from logistical, technical or other factors; the
possibility that results of work will not fulfill
projections/expectations and realize the perceived potential of the
Company's projects; uncertainties involved in the interpretation of
drilling results and other tests and the estimation of gold resources;
risk of accidents, equipment breakdowns and labour disputes or other
unanticipated difficulties or interruptions; the possibility of
environmental issues at the Company's projects; the possibility of cost
overruns or unanticipated expenses in work programs; the need to obtain
permits and comply with environmental laws and regulations and other
government requirements; fluctuations in the price of gold and other
risks and uncertainties, including those described in the Company's
current Annual Information Form filed on SEDAR at www.sedar.com. As a
result, readers are cautioned not to place undue reliance on these
forward-looking statements. The forward-looking statements contained in
this news release are made as of the date of this release. Unless
required by law, Marlin has no intention to and assumes no obligation
to update or revise any forward-looking statements, whether as a result
of new information, future events or otherwise.

NOT FOR DISTRIBUTION TO U.S. NEWSWIRE SERVICES OR FOR RELEASE OR
DISSEMINATION DIRECTLY, OR INDIRECTLY, IN WHOLE OR IN PART, IN OR INTO
THE UNITED STATES

TSX Venture closing price for MLN-V
Date: 2017/05/03
Closing Price: 0.72

TEL:  203-862-7059  Akiba Leisman, Executive Chairman and Interim CEO
Marlin Gold Mining Ltd.
EMAIL:  aleisman@marlingold.com
INTERNET:  http://www.marlingold.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712300010TS11712301085-05531220170504