Source	MARKET NEWS
Date	05/04/2017
Time	07:03:32 AM

Company	 Savary Gold Corp.
Title	Drilling 
Results





    CDNX Symbol: SCA











Press Release




[200/News Release]SCAVSAVARY GOLD CORPMAY 04 2017  07:01 AMDrilling 
Results --->@NEWS RELEASE
SAVARY GOLD CORP ("SCA-V;SVVYF-0")
- Drilling Results

Drilling Returns 13.05 g/t gold Over  Metres and 2.96 g/t Gold over 7
Metres at 75 Metres and 20 Metres from Surface, Respectively



Executive Summary:

-Results from last part of Phase 2 drill program (92-holes, 9,469
metres)

-Drilling is estimated to resume in mid-May - Phase 3 (~125-holes,
up to 8,000 metres)

-Summary of work done since the maiden resource in Q4/2015

Savary Gold Corp. ("Savary" or the "Company") is pleased to
announce the final set of drill results from its 9,496 metre, phase 2,
92-hole drill program that commenced at the end of January on the
Karankasso JV Project in south western Burkina Faso. This news release
presents results for 24 holes totalling 2,375 metres that were
completed between January 29 and March 30, 2017. The phase 3 drill
program, of approximately 125 holes totalling up to 8,000 metres, is
estimated to commence in mid-May.

A summary of select results, in the order they were drilled, are
presented below (see Figure for locations).

S-Nosa Zone area

-HE-RC-17-084 - 2.43 g/t gold over 7 metres

-HE-RC-17-085 - 13.05 g/t gold over 4 metres

-HE-RC-17-089 - 4.32 g/t gold over 3 metres (new)

Kueredougou West Zone area

-HE-RC-17-02 - 2.96 g/t gold over 7 metres

"The final part of our phase two drill program focussed on
follow-up and new target testing in the S-Nosa area as well as
expanding the mineral resource* footprint of the now 2,600-metre-long
Kueredougou West Deposit. At S-Nosa, we have begun to extend the
mineralized zone along strike and down dip with two good, gold-bearing
holes and intend to follow-up with additional holes. At Kueredougou
West, we have extended the zone to the north and south with a strong
intercept at the north end of the zone and will continue to step out
along strike." stated Don Dudek, President and CEO of Savary. Mr. Dudek
further noted "We are excited about our phase 3 drill program,
estimated to commence in mid-May. This program will follow-up all of
the new discoveries from the phase 2 program, continue to drill test
for extensions to our current resources and complete a first pass test
of all of the strongest gold-in-auger anomalies. Approximately 125 RC
and AC holes are planned for this part of the exploration program. Our
mandate is to continue to build value at the end of the drill bit."

Figure 1 - Karankasso JV Project - Locations of Kueredougou West
and S-Nosa 2017 Drill Intercepts.

Phase 2 of the program was completed at the end of April with 92
holes totalling 9,496 metres, drilled. A summary of significant results
from these latest holes, predominantly using 0.5 g/t gold cut-off, are
presented in Table 2 at the end of the release.

Project Advancements since Q4, 2015 Resource Estimate of In-pit
Inferred Mineral Resources of 671,000 ounces* grading 2.28 g/t gold in
six zones (Karangosso, Diosso South, West Trend, Kueredougou West,
Kueredougou, Kien East) using a 0.5 g/t gold cut-off (see Savary News
Release Oct. 8, 2015 and Figure 2, for zone locations)

//st



Zone                  Summary                 Details or Next Steps
Karangosso zone       ~75% increase in strike length
??zone extended from ~700 metres to 1,250 metres

??zone extended to depth below currently modeled in-pit

resource estimate

Diosso South Zone     ~120% increase in strike length
from ~860 metres to 1,900 metres ??Still open along
strike

---------------------------------------------------------------------------
-----------------------------------------------------------------
West Trend Zone       New area of gold mineralization
with three parallel lenses
discovered                     ??Currently 300
metres long and open
along strike and to
depth with more
testing planned

---------------------------------------------------------------------------

Kueredougou West Zone ~50% increase in strike length
from ~1,800 metres to 2,700
metres                         ??Still open along
strike

---------------------------------------------------------------------------

Serakoro 1 Main Zone  ~3,500-metre long mineralized
structure with 1.4 g/t gold to
5.17 g/t gold over 2 to eight
metres wide                    ??potential for
higher grade zone to
be tested

---------------------------------------------------------------------------

Serakoro 1 West Zone  Two new discoveries,
2.55 g/t gold over 17 metres
and 1.85 g/t gold over seven
metres                         ??associated with
2.0 and 1.6 km long
gold-in auger
anomalies,
respectively.
Follow-up holes
planned

---------------------------------------------------------------------------

S-Nosa Zone           expanding with two new
intercepts of 13.05 g/t gold
over 4 metres and 2.43 g/t gold
over 7 metres.                  ??Follow-up holes
planned

---------------------------------------------------------------------------

Six New               Targets are between 1.0
to 3.8 km long, gold-in auger
targets with gold values to
Gold-in-auger hole    2,211 ppb gold and only two
partially tested (Serakoro
1 West discoveries) to
drill targets date.             ??All of these
targets will be
tested in the Phase
3 program.

---------------------------------------------------------------------------

//et



S-Nosa Zone

New drill intercepts from this zone comprise 13.05 g/t gold over 4
metres and 2.43 g/t gold over 7 metres (see Figure). Both holes were
drilled as follow-up to a 2015 core hole that returned 1.34 g/t gold
over 11.6 metres. These holes are 100 metres apart, were drilled to
test a mineralized structure that trends 045 degrees azimuth and are
located approximately 425 metres east of the north end of the
Kueredougou inferred mineral resource estimate pit. Management believes
this mineralized direction is important as it is the first time that
strong gold mineralization was noted along this structural direction.
This mineralized trend correlates with a northeast-trending induced
polarization chargeability high and a northeast-trending airborne
vertical gradient magnetic high. Both of these geophysical trends
intersect the south end of the Kueredougou Zone trend where follow-up
drilling is planned during the phase 3, 2017 drill program.

The third intercept in the S-Nosa area, 4.32 g/t gold over 3
metres, was returned from a separate north and northeast trending
structure located 400 metres to the northwest of the S-Nosa Zone.

In this area of the property, there are at least six north- to
northeast-trending gold-mineralized structures, not including the
nearby Kueredougou Zone. The structures are associated with shallow
artisanal mining zones. A total of 7 short holes, totalling 582 metres,
were drilled to test five of the gold mineralized structures in the
S-Nosa Zone area. Additional evaluation of this structurally
complicated area is required.

Kueredougou West Zone

Highlights of this phase of the drill program include 2.96 g/t
gold over 7 metres in a 100 metre step out, along strike, at the north
end of the zone. Another hole, drilled 100 metres south of a previous
hole that returned 3.00 g/t gold over 4 metres, returned 0.98 g/t gold
over 4 metres approximately 40 metres from surface, within a larger,
lower grade, sericite-altered zone that returned 0.36 g/t gold over 19
metres. The wide alteration zone suggests reasonable potential for
additional gold mineralization.

The remainder of the holes drilled during the phase 2 drill
program were designed to add information both along and below the
current pit-constrained mineral resource estimate. These holes
intersected the gold-bearing lenses where expected generally returning
narrow gold-bearing intercepts that are believed to be supportive to
the overall resource, but will not materially add to it.

Additional holes are planned at both ends of the Kueredougou West
Zone. This zone has been traced for approximately 2,700 metres from an
original strike length of approximately 1,800 metres, an increase of
approximately 50% in strike length. Phase 3 drill holes will further
test a 1,000-metre gap between the Kueredougou Zone to the north where
the southern-most holes intersected 4.04 g/t gold over 5 metres and
12.8 g/t gold over 2 metres, and the Kueredougou West Zone, where the
northern-most hole intersected 2.96 g/t gold over 7 metres (see
Figure).
Kueredougou Zone

A recent review of artisanal mining activity at the north end of
the Kueredougou Inferred resource estimate pit indicated that the area
of artisanal mining has extended for an additional 300 metres north of
the current pit limits. Material being mined and added to the waste
pile is strongly sericite altered and contains 1 to 10% pyrite and
trace to 1% arsenopyrite. This area is part of a 600-metre drilling gap
at the northern end of the Kueredougou Zone, where the next hole, along
the trend, had returned 2.94 g/t gold over 15 metres (see Figure). Two
holes, 100 metres apart, are planned to further test the northern
extension of the Kueredougou Zone.

The Kueredougou Zone area has returned some of the highest grades
from drilling (to 83.35 g/t gold over 4 metres un-cut) on the
Karankasso Project and has always been considered to have some of the
most potential for higher grades. However, with the high grades, this
area is the most impacted by artisanal mining.

Phase 3 Drill Targeting

The Phase 3 drill program, of approximately 125 holes totalling up
to 8,000 metres, has been designed to both follow-up on extensions to
zones with a current pit constrained Mineral Resource estimate*,
follow-up new gold zones/drill intercepts and to test approximately 68
gold-in-auger anomalies containing )100 ppb gold. The gold-in-auger
anomaly targets comprise seven mineralized trends ranging from 1,000 to
3,800 metres long and one distinct Kueredougou West Trend area target.
A summary of the currently planned holes by area, including contingency
holes, is presented in Table 1, below.

Table 1 - Phase 3 drilling planned holes

//st

-----------------------------------------
Phase 3 Holes
---------------------------------------
# of  # of
holes metres
---------------------------------------
AC follow-up Gold-in-Auger
(RC drill with AC head     68    2856
adapter)
---------------------------------------
Diosso South               17    1069
---------------------------------------
Serakoro 1 West            9     910
---------------------------------------
Serakoro 1 Main            6     760
---------------------------------------
Kueredougou West           5     485
---------------------------------------
Kueredougou                3     360
---------------------------------------
S-Nosa                     3     240
---------------------------------------
West Trend North           4     295
---------------------------------------
Contingency                10    800
---------------------------------------
Totals                     125   7775
-----------------------------------------

//et

QA/QC Comments

Savary's procedure for handling reverse circulation drill chips
comprises initial riffle splitting of the rock chips from one metre
drill length samples into approximately 2.5 kilogram samples, as well
as description and logging into a database. A duplicate 2.5-kilogram
sample, prepared at the same time as the assay sample, is kept as a
reference for each sample. NQ-size core assay samples are first logged
into a database and then are sawn in half with half of the core
submitted for analysis; the length of the core samples depends on
logged geological controls with samples varying from 0.3 metres to 2.0
metres in length. A sample duplicate and assay blank was inserted
sequentially every 5 to 14 samples and an assay standard was inserted
every 29 to 34 samples. This results in 8% of the assayed samples being
reference/blank/control samples. Blanks and duplicates were
preferentially inserted in visually mineralized zones to better test
the assay results. This sampling procedure was periodically reviewed by
Savary's President and CEO, and the Company QP, Don Dudek, P. Geo. All
assay samples were collected at site by staff from SGS Burkina Faso SA
('SGS') from Ouagadougou, Burkina Faso where sample preparation and
analysis were performed. Each sample was dried, crushed to 75% passing
2 mm and then split to 1.5 kg by rotary splitter. This split was
pulverized to 85% passing 75 ?m. Fifty grams of the pulverized material
was analysed for gold via fire assay with an atomic absorption
spectroscopy (AAS) finish. SGS operates according to ISO 17025
standards and institutes a full Quality Assurance/Quality Control
(QA/QC) program consisting of insertion of internal blanks, standard
reference material, repeats and reject splits which in total account
for up to 25% of all determinations conducted. All standards and blank
control samples returned results within expected ranges.

About Savary Gold Corp.

Savary is a Canadian exploration company which, along with JV
partner Sarama Resources Limited, is focused on exploring and
developing the Karankasso Gold Project in Burkina Faso. Upon closing,
it is anticipated that the Karankasso JV Project will be approximately69.5% 
owned by Savary and 30.5% owned by Sarama Resources Limited
("Sarama") with Savary as operator. The Project is located within the
Birimian age, Hounde Greenstone Belt, which hosts Semafo's Mana mine,
Roxgold's Yaramoko Mine and additional gold deposits that are presently
subject to production decisions and extensive exploration efforts
(including Endeavour Mining's Hounde Project, Orezone's (acquired by
Sarama) Bondi Project and Sarama's/Acacia's South Hounde Project, which
is adjacent to Savary's property). The Project contains an Inferred
open pit constrained mineral resource estimate of 9.16 million tonnes
grading 2.28 g/t gold (Savary news release November 24, 2015). For
additional information please visit our website at www.savarygold.com.

* Open pit constrained Mineral resource estimate presented in
Savary news release dated October 8, 2015

Don Dudek, P.Geo., President and CEO of the Company and a
qualified person under National Instrument 43-101, has reviewed and
approved the scientific and technical information in this press
release.

SAVARY GOLD CORP.

On behalf of the Board

"Don Dudek"

President & Chief Executive Officer

For more information, please contact:

Don Dudek, President and CEO

T: 647-259-2097

E: info@savarygold.com; www.savarygold.com

Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These
statements include statements regarding the details of the potential
value growth of the JV, the upside of the property, the drill program,
the company's exploration plans and the timing of results, the focus on
existing drill targets and new targets. These statements are based on
current expectations and assumptions that are subject to risks and
uncertainties. Actual results could differ materially because of
factors discussed in the management discussion and analysis section of
our interim and most recent annual financial statement or other reports
and filings with the TSX Venture Exchange and applicable Canadian
securities regulations. We do not assume any obligation to update any
forward-looking statements, except as required by applicable laws.

Table 2 - Summary of Significant Intercepts

//st

------------------------------------------------------
Hole #       From To  Length Au g/t Target Area
----------------------------------------------------
HE-RC-17-001 55   58  3      0.53   Kueredougou West
----------------------------------------------------
HE-RC-17-001 136  138 2      1.39   Kueredougou West
----------------------------------------------------
HE-RC-17-001 146  153 7      0.91   Kueredougou West
----------------------------------------------------
incl.        152  153 1      2.86   Kueredougou West
----------------------------------------------------
HE-RC-17-002 6    8   2      1.17   Kueredougou West
----------------------------------------------------
HE-RC-17-002 20   27  7      2.96   Kueredougou West
----------------------------------------------------
incl.        21   24  3      6.45   Kueredougou West
----------------------------------------------------
HE-RC-17-003 18   20  2      1.47   Kueredougou West
----------------------------------------------------
HE-RC-17-003 33   34  1      1.52   Kueredougou West
----------------------------------------------------
HE-RC-17-003 60   61  1      0.74   Kueredougou West
----------------------------------------------------
HE-RC-17-004 35   37  2      0.52   Kueredougou West
----------------------------------------------------
HE-RC-17-004 38   39  1      2.74   Kueredougou West
----------------------------------------------------
HE-RC-17-004 48   52  4      1.22   Kueredougou West
----------------------------------------------------
HE-RC-17-005 78   79  1      0.54   Kueredougou West
----------------------------------------------------
HE-RC-17-005 83   85  2      1.69   Kueredougou West
----------------------------------------------------
HE-RC-17-005 115  116 1      0.66   Kueredougou West
----------------------------------------------------
HE-RC-17-074              NSV    Kueredougou West
----------------------------------------------------
HE-RC-17-075 129  130 1      0.6    Kueredougou West
----------------------------------------------------
HE-RC-17-076              NSV    Kueredougou West
----------------------------------------------------
HE-RC-17-077 32   33  1      0.96   Kueredougou West
----------------------------------------------------
HE-RC-17-077 39   40  1      0.55   Kueredougou West
----------------------------------------------------
HE-RC-17-077 43   44  1      0.55   Kueredougou West
----------------------------------------------------
HE-RC-17-077 47   51  4      0.98   Kueredougou West
----------------------------------------------------
HE-RC-17-078 32   33  1      0.30   Kueredougou West
----------------------------------------------------
HE-RC-17-078 43   45  2      0.48   Kueredougou West
----------------------------------------------------
HE-RC-17-079 33   35  2      0.79   Kueredougou West
----------------------------------------------------
HE-RC-17-080 85   86  1      0.40   Kueredougou West
----------------------------------------------------
HE-RC-17-081 79   80  1      0.99   Kueredougou West
----------------------------------------------------
HE-RC-17-081 82   84  2      1.32   Kueredougou West
----------------------------------------------------
HE-RC-17-082 56   59  3      1.09   Kueredougou West
----------------------------------------------------
HE-RC-17-084 50   51  1      0.52   South Nosa
----------------------------------------------------
HE-RC-17-084 69   71  2      0.76   South Nosa
----------------------------------------------------
HE-RC-17-084 75   90  15     1.34   South Nosa
----------------------------------------------------
incl         80   87  7      2.43   South Nosa
----------------------------------------------------
incl         83   87  4      3.37   South Nosa
----------------------------------------------------
HE-RC-17-085 73   76  3      1.49   South Nosa
----------------------------------------------------
HE-RC-17-085 79   80  1      0.93   South Nosa
----------------------------------------------------
HE-RC-17-085 95   99  4      13.05  South Nosa
----------------------------------------------------
incl         95   98  3      17.15  South Nosa
----------------------------------------------------
HE-RC-17-086 68   70  2      0.91   South Nosa
----------------------------------------------------
HE-RC-17-087 9    10  1      1.06   South Nosa
----------------------------------------------------
HE-RC-17-088 0    3   3      0.86   South Nosa
----------------------------------------------------
HE-RC-17-088 55   56  1      1.06   South Nosa
----------------------------------------------------
HE-RC-17-089 30   33  3      4.32   South Nosa
----------------------------------------------------
HE-RC-17-090              NSV    Kueredougou West
----------------------------------------------------
HE-RC-17-091 23   24  1      0.96   Kueredougou West
----------------------------------------------------
HE-RC-17-091 28   29  1      0.61   Kueredougou West
----------------------------------------------------
HE-RC-17-091 36   37  1      0.62   Kueredougou West
----------------------------------------------------
HE-RC-17-091 49   50  1      0.61   Kueredougou West
----------------------------------------------------
HE-RC-17-091 70   72  2      0.72   Kueredougou West
----------------------------------------------------
HE-RC-17-092 106  108 2      1.9    Kueredougou West
----------------------------------------------------
HE-RC-17-092 109  110 1      0.69   Kueredougou West
------------------------------------------------------

//et

* true widths are estimated at 65% to 80% of drilled widths
__________________________________________________
_______________________________________________
TSX Venture closing price for SCA-V
Date: 2017/05/03
Closing Price: 0.08
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712300031TS11712301510-07011720170504