Source	Marketwire
Date	05/01/2017
Time	05:01:22 AM

Company	 ATLANTIC GOLD CORPORATION
Title	Atlantic Gold Reports Additional Results From the Resource Definition 
Drill Programs at Fifteen Mile Stream and Cochrane Hill, and From Further 
Exploration Drilling at the Plenty Prospect





    CDNX Symbol: AGB











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

May 1, 2017

Atlantic Gold Reports Additional Results From the Resource Definition Drill 
Programs at Fifteen Mile Stream and Cochrane Hill, and From Further Exploration 
Drilling at the Plenty Prospect

HIGHLIGHTS INCLUDE:

Fifteen Mile Stream: 49m @ 2.37 g/t from 24m, 17m @ 3.49g/t from 60m, 24m @ 
1.65 g/t from 35m

Cochrane Hill: 16m @ 3.48 g/t from 51m, 6m @ 7.00g/t from 47m, 16m @ 1.63g/t 
from 77m, 17m @ 1.90 g/t from 202m

Plenty: 5m @ 5.68 g/t from 34m, 4m @ 4.97g/t from 14m, 13m @ 1.96 g/t from 95m 
and 3m @ 14.12g/t from 51m

VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 1, 2017) - Atlantic Gold 
Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is pleased to 
report assay results received from drilling programs on two gold deposits and a 
gold prospect: The Fifteen Mile Stream and Cochrane Hill deposits where 
resource definition drilling on 25m x 20m centres is underway with the 
objective of upgrading resources to measured and indicated categories, and at 
the Plenty prospect where previously reported high grade intersections are 
being drilled more systematically.

The Company plans to use the results from the drill programs to undertake 
further analysis to determine the economic viability of the above-noted 
deposits which would include analysis of the economics of processing these 
deposits at the Moose River Consolidated ("MRC") processing facility by way of 
a Pre-Feasibility Study.

New assay results from the three drilling programs are reported as follows:

/T/

1.  FIFTEEN MILE STREAM

/T/

Fifteen Mile Stream is located approximately 57km northeast of the central 
milling facility at Touquoy and is readily accessible by highway. Fifteen Mile 
Stream's current inferred mineral resources stand at 11.72 million tonnes at 
1.55 g/t Au for 584,000 oz. New assay results reported herein are from a 
further 16 holes of the ongoing resource definition diamond drilling program. 
At this time 140 holes for 15,737 of the planned 25,000m have now been drilled 
and one drilling rig is presently operating on the property.

Drilling Results:

The additional assay drill results continue to reflect those grades, widths and 
geometry of gold mineralization documented from the 1980s and 2011 drilling 
programs which support the current inferred resource estimate (see below). 
Mineralization occurs within argillites, greywackes and bedding-parallel quartz 
veins across the hinge zone and limbs of the E-W trending Fifteen Mile Stream 
(FMS) Anticline. The northern limb of the anticline dips moderately north, with 
the southern limb vertical to overturned (generally steeply north dipping). All 
holes are therefore declined to the south at various dips and hence true widths 
vary (see assay table below) depending on which limb of the anticline is 
intersected, and also depending on hole dip. Free gold is commonly observed, 
and in association with pyrrhotite and arsenopyrite.

Drilling across the hinge zone of the anticline is now underway. Owing to the 
location of certain wetlands, drilling has previously been conducted where 
ready access to dry or "upland" drill sites has been afforded such that 
intersections through the hinge zone of the anticline at Egerton-MacLean have 
to date been somewhat under-represented. Drilling from such sites with 
restricted access is now in progress. One of the notable intersections reported 
here - 49m @ 2.37g/t in hole FMS-17-104 - is from the hinge zone of the 
anticline (as is the previously reported intersection of 23m @ 5.4g/t in hole 
FMS-17-090).

In addition, it was previously reported that strong and shallow mineralization 
was being intersected along the southern limb of the anticline at 13250E to 
13400E. This position is now further strengthened by recent returns from holes 
FMS-17-097 and 098 (17m @ 3.49g/t from 60m, and 24m @ 1.65g/t from 35m depth 
respectively).

These shallow and widespread mineralized intersections across the limbs and 
core of this sub-horizontal anticlinal hinge zone are considered to be highly 
encouraging in the context of potential open pit extraction.

The accompanying cross sections and drill progress plan can be viewed here:
http://media3.marketwire.com/docs/27AprFMSDrill.pdf.

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017, March 1, 2017, March 16, 2017 and 
April 3, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to 0.5g/t Au
and up to 3m internal dilution)
------------------------------------
Approx.
Depth From   To Width true width    Grade
Hole id       East North  Dip  Az.   (m)  (m)  (m)   (m)        (m) (g/t Au)
----------------------------------------------------------------------------
FMS-17-089   12800 10080  -60  175   104   60   68     8          7     0.86
----------------------------------------------------------------------------
FMS-17-093   13500 10100  -60  175   131   40   48     8          8     0.60
----------------------------------------------------------------------------
and                                      57   59     2          2     4.04
----------------------------------------------------------------------------
and                                      72   73     1          1     71.3
----------------------------------------------------------------------------
and                                      82   83     1          1    16.35
----------------------------------------------------------------------------
and                                      87   89     2          2     2.36
----------------------------------------------------------------------------
and                                     103  125    22         18     1.10
----------------------------------------------------------------------------
FMS-17-096   13325 10080  -45  175   122   69   82    13         12     0.94
----------------------------------------------------------------------------
and                                      89  103    14         13     1.46
----------------------------------------------------------------------------
FMS-17-097   13350 10080  -45  175   131  8.7   24  15.3         15     0.90
----------------------------------------------------------------------------
and                                      60   77    17         15     3.49
----------------------------------------------------------------------------
(incl.                                   76   77     1          1    40.1)
----------------------------------------------------------------------------
and                                    84.8   92   7.2          6     0.82
----------------------------------------------------------------------------
FMS-17-098   13375 10070  -55  175   122   28   31     3          3     1.37
----------------------------------------------------------------------------
and                                      35   59    24         22     1.65
----------------------------------------------------------------------------
and                                      69   81    12          9     0.78
----------------------------------------------------------------------------
FMS-17-099   13375 10070  -45  175   101   26   30     4          4     1.85
----------------------------------------------------------------------------
and                                      34   54    20         19     0.85
----------------------------------------------------------------------------
and                                      60   69     9          8     0.89
----------------------------------------------------------------------------
FMS-17-100   13375 10095  -85  175   131   40   48     8          8     0.64
----------------------------------------------------------------------------
and                                     116  119     3        1.5     68.8
----------------------------------------------------------------------------
FMS-17-101   13375 10095  -75  175   152   14   23     9          9     0.68
----------------------------------------------------------------------------
and                                      27   45    18         18     0.71
----------------------------------------------------------------------------
and                                     134  152    18         12    0.81!
----------------------------------------------------------------------------
FMS-17-102   13375 10095  -65  175   134   21   24     3          3     1.56
----------------------------------------------------------------------------
and                                      29   34     5          5     0.92
----------------------------------------------------------------------------
and                                      38   52    14         14     0.76
----------------------------------------------------------------------------
and                                      98  106     8          5     0.99
----------------------------------------------------------------------------
and                                     111  126    15         10     0.77
----------------------------------------------------------------------------
FMS-17-103   13400 10120  -75  175   122   16   24     8          7     0.73
----------------------------------------------------------------------------
and                                      29   64    35         33     0.80
----------------------------------------------------------------------------
FMS-17-104   13400 10120  -60  175   200   24   73    49         45     2.37
----------------------------------------------------------------------------
(incl.                                   40   41     1          1    51.3)
----------------------------------------------------------------------------
(incl.
also                                    41   42     1          1   20.58)
----------------------------------------------------------------------------
and                                      88   89     1          1     4.45
----------------------------------------------------------------------------
and                                     111  122    11         10     1.19
----------------------------------------------------------------------------
and                                     127  145    18         15     0.71
----------------------------------------------------------------------------
and                                     154  163     9          7     1.22
----------------------------------------------------------------------------
FMS-17-105   13400 10046  -45  175    71   18   22     4          3     2.32
----------------------------------------------------------------------------
and                                      30   32     2          2     1.67
----------------------------------------------------------------------------
and                                      36   50    14         12     2.08
----------------------------------------------------------------------------
FMS-17-106   13450 10093  -65  175   182   22   26     4          3     0.90
----------------------------------------------------------------------------
and                                      52   88    36         24     0.92
----------------------------------------------------------------------------
and                                      95  109    14         10     1.87
----------------------------------------------------------------------------
and                                     120  135    15         10     1.44
----------------------------------------------------------------------------
and                                     150  153     3          2     1.58
----------------------------------------------------------------------------
FMS-17-107   13450 10030  -45  175    62   10   20    10         10     0.67
----------------------------------------------------------------------------
and                                      33   34     1          1     19.7
----------------------------------------------------------------------------
and                                      42   50     8          6     1.74
----------------------------------------------------------------------------
FMS-17-108   13500 10060  -45  175   113   11 22.1  11.1         10     1.62
----------------------------------------------------------------------------
and                                      33   41     8          7     1.62
----------------------------------------------------------------------------
and                                      50   59     9          8     1.22
----------------------------------------------------------------------------
and                                      64   68     4          3     1.10
----------------------------------------------------------------------------
and                                      80   85     5          4     0.95
----------------------------------------------------------------------------
FMS-17-111   13650 10140  -45  175    80   48   55     7          7     0.79
----------------------------------------------------------------------------

/T/

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection in the table above. Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Tonnes             Grade         Contained
Category                    (millions)          (g/t) Au          Au (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource                11.72              1.55           584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/
The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

/T/

2.  COCHRANE HILL

/T/

The Cochrane Hill Gold deposit is located within trucking distance 
(approximately 80km) to the central milling facility at Touquoy and is readily 
accessible by highway (based on a Preliminary Economic Assessment dated October 
14, 2014 prepared by Moose Mountain Technical Services). Mineral resources at 
Cochrane Hill currently comprise indicated resources of 4.5 million tonnes at 
1.8g/t Au for 251,000 oz. and inferred resources of 5.6 million tonnes at 1.6 
g/t Au for 298,000 oz.

New assay results reported herein are from a further eight holes of the ongoing 
resource definition diamond drilling program, these being the first assays 
returned from the second phase of the drilling program. This second phase has 
targeted potential extensions of mineralization to the west of the main body of 
mineralization and west of the step out holes on section 2775E across highway 
#7. Regulatory approval has been obtained to drill in this area which is 
largely covered by shallow wetland. A further nine lower priority holes have 
been added to this phase of the program to test for depth extensions beneath 
the last, deepest, encouraging intersection on each of nine cross-sections east 
of 3000E. This second phase of drilling will be completed in the coming week.

At this time 166 holes for 24,804m have now been drilled and three drilling 
rigs are presently operating on the property.

Drilling Results:

These new assay results come from two sections drilled at the eastern edge of 
the 200m gap, with best results (16m @ 3.48g/t and 6m @ 7.00g/t) at less than 
60m from surface. The geometry of the mineralization continues to be fairly 
predictable and continuous, as a reasonably discrete, tabular, 70 degrees 
north-dipping zone having a true width of approximately 25m. Mineralization is 
open at depth, notwithstanding economic parameters yet to be appropriately 
applied at the completion of this drilling campaign, though as noted above, a 
basal tier of deeper holes is being drilled to test further for such extensions.

The accompanying cross sections and drill progress plan can be viewed here: 
http://media3.marketwire.com/docs/27AprCochrDrill.pdf.

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: Dec 6, 2016, Jan 3, 2017, Jan 11, 2017, and Feb 2, 
2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to
0.5g/t Au and up to 3m internal
dilution)
-------------------------------
Depth   From     To  Width     Grade
Hole id   Easting Northing   Dip   Az.    (m)    (m)    (m)    (m)  (g/t Au)
----------------------------------------------------------------------------
CH-17-137    2925     3088   -45   171     82     36     42      6      0.88
----------------------------------------------------------------------------
and                                             60     65      5      0.96
----------------------------------------------------------------------------
CH-17-138    2950     3200   -60   171    242    202    219     17      1.90
----------------------------------------------------------------------------
CH-17-139    2925     3090   -60   171    121     47     53      6      7.00
----------------------------------------------------------------------------
(incl.                                          47     48      1     26.0)
----------------------------------------------------------------------------
and                                             61     73     12      1.73
----------------------------------------------------------------------------
CH-17-140    2950     3180   -60   171    224    160    164      4   2.00(i)
----------------------------------------------------------------------------
and                                            174    175      1      4.78
----------------------------------------------------------------------------
and                                            180    181      1      9.34
----------------------------------------------------------------------------
and                                            186    195      9      0.64
----------------------------------------------------------------------------
CH-17-141    2925     3090   -70   171    151     51     67     16      3.48
----------------------------------------------------------------------------
(incl.                                          51     52      1     40.0)
----------------------------------------------------------------------------
and                                             77     93     16      1.63
----------------------------------------------------------------------------
CH-17-142    2950     3160   -60   171    200    135    136      1      5.55
----------------------------------------------------------------------------
and                                            141    146      5      0.82
----------------------------------------------------------------------------
and                                            150    174     24      0.68
----------------------------------------------------------------------------
CH-17-144    2950     3140   -60   171    182    135    141      6      1.18
----------------------------------------------------------------------------
and                                            148    149      1      9.05
----------------------------------------------------------------------------
CH-17-145    2950     3220   -60   171    260    214    235     21      0.64
----------------------------------------------------------------------------
(i)Wholly or partly includes 50g fire assay on pulverised whole-sample (to
be screen fire assayed).

/T/

True width of the mineralization is approximately 80% of the down-hole width.

The current resource estimate for Cochrane Hill is tabulated below:

/T/

----------------------------------------------------------------------------
Tonnes             Grade         Contained
Category                    (millions)          (g/t) Au          Au (oz.)
----------------------------------------------------------------------------
COCHRANE HILL
----------------------------------------------------------------------------
Indicated Resource                 4.5               1.8           251,000
----------------------------------------------------------------------------
Inferred Resource                  5.6               1.6           298,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Cochrane Hill is quoted at a cut-off grade of 
0.5g/t. It has an effective date of August 1, 2014 and was prepared as part of 
a technical report in accordance with NI 43-101 by Mr. Neil Schofield, a 
principal of FSSI (Australia) Pty Ltd, released on August 14, 2014 on SEDAR.

/T/

3.  PLENTY

/T/

The Plenty prospect is located 300m south of the Company's Fifteen Mile Stream 
deposit. Plenty is one of several regional exploration targets selected for 
investigation, in parallel with Atlantic's ongoing resource definition drilling 
at Cochrane Hill and Fifteen Mile Stream. The immediate prospect is defined by 
an east-west trend of small historic mine workings dating to the late 1800s. As 
elsewhere in the Meguma Terrane of Nova Scotia these old workings were 
developed exclusively on quartz veins though the current exploration model 
encompasses the medium grade halo of disseminated mineralization within the 
adjacent wall rocks.

The new assay results reported here are from a further thirteen holes drilled 
on this property. In all, 21 holes for 2,272m have now been drilled by Atlantic 
on this prospect. At present the drilling rig has been deployed back to Fifteen 
Mile Stream and drilling will resume here once the current drilling campaigns 
at Fifteen Mile Stream and Cochrane Hill have been further advanced.

Drilling Results:

Results are tabulated below. These diamond core holes were drilled on nominal 
25m x 20m centres in the vicinity of high grade intersections (up to 13m @ 
21.8g/t) cut in several of the first eight holes drilled by Atlantic on this 
prospect. Results confirm the overall geometry - steep northerly dip and 
east-west trend - and continuity of the mineralization, though grades and 
widths are variable in this particular area. Mineralization is hosted both 
within well-defined argillites and bedding-parallel quartz veins and it is 
presently interpreted to extend eastward for about 350m where it abuts the 
Fifteen Mile Stream deposit against the Seigel Fault (refer to plan). This 350m 
gap, and the western extensions, are yet to be investigated. Gold in drill core 
is visible in places.

The accompanying cross sections and drill progress plan can be viewed here: 
http://media3.marketwire.com/docs/27AprPlenDrill.pdf.

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: January 25, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to
0.5g/t Au and up to 3m
internal dilution)
------------------------------
Depth   From    To  Width     Grade
Hole id     Easting  Northing  Dip  Az.    (m)    (m)   (m)    (m)  (g/t Au)
----------------------------------------------------------------------------
PL-17-009     12975      9860  -60  175    122     50    54      4   0.88(i)
----------------------------------------------------------------------------
and                                              92    93      1   46.5(i)
----------------------------------------------------------------------------
PL-17-010     12975      9860  -45  175    113     66    67      1      5.85
----------------------------------------------------------------------------
PL-17-011     12950      9840  -60  175    140     18    26      8      0.69
----------------------------------------------------------------------------
and                                              85    86      1      5.33
----------------------------------------------------------------------------
PL-17-012     12950      9820  -60  175    110     56    57      1      3.09
----------------------------------------------------------------------------
PL-17-013     12950      9800  -60  175     92     32    36      4      1.49
----------------------------------------------------------------------------
and                                              51    52      1      3.11
----------------------------------------------------------------------------
PL-17-014     12950      9788  -50  175     62     17    22      5      3.17
----------------------------------------------------------------------------
PL-17-015     12971      9820  -60  175     68     51    54      3     14.12
----------------------------------------------------------------------------
(incl.                                           53    54      1     23.8)
----------------------------------------------------------------------------
and                                              63    65      2      2.03
----------------------------------------------------------------------------
PL-17-016     12971      9820  -45  175     62     40    41      1      3.09
----------------------------------------------------------------------------
and                                              50    51      1     12.75
----------------------------------------------------------------------------
PL-17-017     12971      9800  -45  175     41     14    18      4      4.97
----------------------------------------------------------------------------
and                                              34    39      5      5.68
----------------------------------------------------------------------------
PL-17-018     12900      9840  -60  175    164     95   108     13      1.96
----------------------------------------------------------------------------
PL-17-019     12900      9820  -60  175    140                           NSA
----------------------------------------------------------------------------
PL-17-020     12900      9800  -60  175    122     54    65     11      1.42
----------------------------------------------------------------------------
PL-17-021     12900      9790  -50  175     92     42    45      3      1.97
----------------------------------------------------------------------------
and                                              49    55      6      0.61
----------------------------------------------------------------------------

/T/

/T/

(i)Wholly or partly includes 50g fire assay on pulverised whole-sample (to
be screen fire assayed).
NSA: No significant assays

/T/

True width of the mineralization is approximately 65% of the down-hole width.

Technical Disclosure

Fifteen Mile Stream

At Fifteen Mile Stream all assays are 50g charge fire assays conducted on 
whole-sample pulverized 1m samples of sawn, half NQ core with 1-in-10 duplicate 
assays and insertion of standards and blind blanks. Core recovery is estimated 
for each metre and averages greater than 97%, excluding occasional voids, 
usually less than 2m, representing historic underground workings. Wing samples 
to voids may be less than 1m to re-establish routine sampling on 1m intervals. 
Drill core in the hangingwall of the northern limb of the anticline where 
adjacent historic holes very clearly indicate this upper stratigraphy to be 
barren may not be sampled and assayed. Standards, blanks and duplicate assay 
results are acceptable.

Cochrane Hill
All core drilled at Cochrane Hill is assayed. All assays have been conducted on 
1m whole-sampled pulverized samples of sawn, half NQ core and, where 
mineralization is expected, assayed by total sample screen fire assay with 2x 
fines fire assays, and insertion of standards and blind blanks. In the 
hangingwall and footwall of expected mineralization samples are assayed by 50g 
charge fire assay with any mineralized samples (generally greater than 0.5g/t), 
and adjacent samples as appropriate, returned for screen fire assay. Core 


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

May 1, 2017

Atlantic Gold Reports Additional Results From the Resource Definition Drill 
Programs at Fifteen Mile Stream and Cochrane Hill, and From Further Exploration 
Drilling at the Plenty Prospect

HIGHLIGHTS INCLUDE:

Fifteen Mile Stream: 49m @ 2.37 g/t from 24m, 17m @ 3.49g/t from 60m, 24m @ 
1.65 g/t from 35m

Cochrane Hill: 16m @ 3.48 g/t from 51m, 6m @ 7.00g/t from 47m, 16m @ 1.63g/t 
from 77m, 17m @ 1.90 g/t from 202m

Plenty: 5m @ 5.68 g/t from 34m, 4m @ 4.97g/t from 14m, 13m @ 1.96 g/t from 95m 
and 3m @ 14.12g/t from 51m

VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 1, 2017) - Atlantic Gold 
Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is pleased to 
report assay results received from drilling programs on two gold deposits and a 
gold prospect: The Fifteen Mile Stream and Cochrane Hill deposits where 
resource definition drilling on 25m x 20m centres is underway with the 
objective of upgrading resources to measured and indicated categories, and at 
the Plenty prospect where previously reported high grade intersections are 
being drilled more systematically.

The Company plans to use the results from the drill programs to undertake 
further analysis to determine the economic viability of the above-noted 
deposits which would include analysis of the economics of processing these 
deposits at the Moose River Consolidated ("MRC") processing facility by way of 
a Pre-Feasibility Study.

New assay results from the three drilling programs are reported as follows:

/T/

1.  FIFTEEN MILE STREAM

/T/

Fifteen Mile Stream is located approximately 57km northeast of the central 
milling facility at Touquoy and is readily accessible by highway. Fifteen Mile 
Stream's current inferred mineral resources stand at 11.72 million tonnes at 
1.55 g/t Au for 584,000 oz. New assay results reported herein are from a 
further 16 holes of the ongoing resource definition diamond drilling program. 
At this time 140 holes for 15,737 of the planned 25,000m have now been drilled 
and one drilling rig is presently operating on the property.

Drilling Results:

The additional assay drill results continue to reflect those grades, widths and 
geometry of gold mineralization documented from the 1980s and 2011 drilling 
programs which support the current inferred resource estimate (see below). 
Mineralization occurs within argillites, greywackes and bedding-parallel quartz 
veins across the hinge zone and limbs of the E-W trending Fifteen Mile Stream 
(FMS) Anticline. The northern limb of the anticline dips moderately north, with 
the southern limb vertical to overturned (generally steeply north dipping). All 
holes are therefore declined to the south at various dips and hence true widths 
vary (see assay table below) depending on which limb of the anticline is 
intersected, and also depending on hole dip. Free gold is commonly observed, 
and in association with pyrrhotite and arsenopyrite.

Drilling across the hinge zone of the anticline is now underway. Owing to the 
location of certain wetlands, drilling has previously been conducted where 
ready access to dry or "upland" drill sites has been afforded such that 
intersections through the hinge zone of the anticline at Egerton-MacLean have 
to date been somewhat under-represented. Drilling from such sites with 
restricted access is now in progress. One of the notable intersections reported 
here - 49m @ 2.37g/t in hole FMS-17-104 - is from the hinge zone of the 
anticline (as is the previously reported intersection of 23m @ 5.4g/t in hole 
FMS-17-090).

In addition, it was previously reported that strong and shallow mineralization 
was being intersected along the southern limb of the anticline at 13250E to 
13400E. This position is now further strengthened by recent returns from holes 
FMS-17-097 and 098 (17m @ 3.49g/t from 60m, and 24m @ 1.65g/t from 35m depth 
respectively).

These shallow and widespread mineralized intersections across the limbs and 
core of this sub-horizontal anticlinal hinge zone are considered to be highly 
encouraging in the context of potential open pit extraction.

The accompanying cross sections and drill progress plan can be viewed here:
http://media3.marketwire.com/docs/27AprFMSDrill.pdf.

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017, March 1, 2017, March 16, 2017 and 
April 3, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to 0.5g/t Au
and up to 3m internal dilution)
------------------------------------
Approx.
Depth From   To Width true width    Grade
Hole id       East North  Dip  Az.   (m)  (m)  (m)   (m)        (m) (g/t Au)
----------------------------------------------------------------------------
FMS-17-089   12800 10080  -60  175   104   60   68     8          7     0.86
----------------------------------------------------------------------------
FMS-17-093   13500 10100  -60  175   131   40   48     8          8     0.60
----------------------------------------------------------------------------
and                                      57   59     2          2     4.04
----------------------------------------------------------------------------
and                                      72   73     1          1     71.3
----------------------------------------------------------------------------
and                                      82   83     1          1    16.35
----------------------------------------------------------------------------
and                                      87   89     2          2     2.36
----------------------------------------------------------------------------
and                                     103  125    22         18     1.10
----------------------------------------------------------------------------
FMS-17-096   13325 10080  -45  175   122   69   82    13         12     0.94
----------------------------------------------------------------------------
and                                      89  103    14         13     1.46
----------------------------------------------------------------------------
FMS-17-097   13350 10080  -45  175   131  8.7   24  15.3         15     0.90
----------------------------------------------------------------------------
and                                      60   77    17         15     3.49
----------------------------------------------------------------------------
(incl.                                   76   77     1          1    40.1)
----------------------------------------------------------------------------
and                                    84.8   92   7.2          6     0.82
----------------------------------------------------------------------------
FMS-17-098   13375 10070  -55  175   122   28   31     3          3     1.37
----------------------------------------------------------------------------
and                                      35   59    24         22     1.65
----------------------------------------------------------------------------
and                                      69   81    12          9     0.78
----------------------------------------------------------------------------
FMS-17-099   13375 10070  -45  175   101   26   30     4          4     1.85
----------------------------------------------------------------------------
and                                      34   54    20         19     0.85
----------------------------------------------------------------------------
and                                      60   69     9          8     0.89
----------------------------------------------------------------------------
FMS-17-100   13375 10095  -85  175   131   40   48     8          8     0.64
----------------------------------------------------------------------------
and                                     116  119     3        1.5     68.8
----------------------------------------------------------------------------
FMS-17-101   13375 10095  -75  175   152   14   23     9          9     0.68
----------------------------------------------------------------------------
and                                      27   45    18         18     0.71
----------------------------------------------------------------------------
and                                     134  152    18         12    0.81!
----------------------------------------------------------------------------
FMS-17-102   13375 10095  -65  175   134   21   24     3          3     1.56
----------------------------------------------------------------------------
and                                      29   34     5          5     0.92
----------------------------------------------------------------------------
and                                      38   52    14         14     0.76
----------------------------------------------------------------------------
and                                      98  106     8          5     0.99
----------------------------------------------------------------------------
and                                     111  126    15         10     0.77
----------------------------------------------------------------------------
FMS-17-103   13400 10120  -75  175   122   16   24     8          7     0.73
----------------------------------------------------------------------------
and                                      29   64    35         33     0.80
----------------------------------------------------------------------------
FMS-17-104   13400 10120  -60  175   200   24   73    49         45     2.37
----------------------------------------------------------------------------
(incl.                                   40   41     1          1    51.3)
----------------------------------------------------------------------------
(incl.
also                                    41   42     1          1   20.58)
----------------------------------------------------------------------------
and                                      88   89     1          1     4.45
----------------------------------------------------------------------------
and                                     111  122    11         10     1.19
----------------------------------------------------------------------------
and                                     127  145    18         15     0.71
----------------------------------------------------------------------------
and                                     154  163     9          7     1.22
----------------------------------------------------------------------------
FMS-17-105   13400 10046  -45  175    71   18   22     4          3     2.32
----------------------------------------------------------------------------
and                                      30   32     2          2     1.67
----------------------------------------------------------------------------
and                                      36   50    14         12     2.08
----------------------------------------------------------------------------
FMS-17-106   13450 10093  -65  175   182   22   26     4          3     0.90
----------------------------------------------------------------------------
and                                      52   88    36         24     0.92
----------------------------------------------------------------------------
and                                      95  109    14         10     1.87
----------------------------------------------------------------------------
and                                     120  135    15         10     1.44
----------------------------------------------------------------------------
and                                     150  153     3          2     1.58
----------------------------------------------------------------------------
FMS-17-107   13450 10030  -45  175    62   10   20    10         10     0.67
----------------------------------------------------------------------------
and                                      33   34     1          1     19.7
----------------------------------------------------------------------------
and                                      42   50     8          6     1.74
----------------------------------------------------------------------------
FMS-17-108   13500 10060  -45  175   113   11 22.1  11.1         10     1.62
----------------------------------------------------------------------------
and                                      33   41     8          7     1.62
----------------------------------------------------------------------------
and                                      50   59     9          8     1.22
----------------------------------------------------------------------------
and                                      64   68     4          3     1.10
----------------------------------------------------------------------------
and                                      80   85     5          4     0.95
----------------------------------------------------------------------------
FMS-17-111   13650 10140  -45  175    80   48   55     7          7     0.79
----------------------------------------------------------------------------

/T/

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection in the table above. Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Tonnes             Grade         Contained
Category                    (millions)          (g/t) Au          Au (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource                11.72              1.55           584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/
The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

/T/

2.  COCHRANE HILL

/T/

The Cochrane Hill Gold deposit is located within trucking distance 
(approximately 80km) to the central milling facility at Touquoy and is readily 
accessible by highway (based on a Preliminary Economic Assessment dated October 
14, 2014 prepared by Moose Mountain Technical Services). Mineral resources at 
Cochrane Hill currently comprise indicated resources of 4.5 million tonnes at 
1.8g/t Au for 251,000 oz. and inferred resources of 5.6 million tonnes at 1.6 
g/t Au for 298,000 oz.

New assay results reported herein are from a further eight holes of the ongoing 
resource definition diamond drilling program, these being the first assays 
returned from the second phase of the drilling program. This second phase has 
targeted potential extensions of mineralization to the west of the main body of 
mineralization and west of the step out holes on section 2775E across highway 
#7. Regulatory approval has been obtained to drill in this area which is 
largely covered by shallow wetland. A further nine lower priority holes have 
been added to this phase of the program to test for depth extensions beneath 
the last, deepest, encouraging intersection on each of nine cross-sections east 
of 3000E. This second phase of drilling will be completed in the coming week.

At this time 166 holes for 24,804m have now been drilled and three drilling 
rigs are presently operating on the property.

Drilling Results:

These new assay results come from two sections drilled at the eastern edge of 
the 200m gap, with best results (16m @ 3.48g/t and 6m @ 7.00g/t) at less than 
60m from surface. The geometry of the mineralization continues to be fairly 
predictable and continuous, as a reasonably discrete, tabular, 70 degrees 
north-dipping zone having a true width of approximately 25m. Mineralization is 
open at depth, notwithstanding economic parameters yet to be appropriately 
applied at the completion of this drilling campaign, though as noted above, a 
basal tier of deeper holes is being drilled to test further for such extensions.

The accompanying cross sections and drill progress plan can be viewed here: 
http://media3.marketwire.com/docs/27AprCochrDrill.pdf.

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: Dec 6, 2016, Jan 3, 2017, Jan 11, 2017, and Feb 2, 
2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to
0.5g/t Au and up to 3m internal
dilution)
-------------------------------
Depth   From     To  Width     Grade
Hole id   Easting Northing   Dip   Az.    (m)    (m)    (m)    (m)  (g/t Au)
----------------------------------------------------------------------------
CH-17-137    2925     3088   -45   171     82     36     42      6      0.88
----------------------------------------------------------------------------
and                                             60     65      5      0.96
----------------------------------------------------------------------------
CH-17-138    2950     3200   -60   171    242    202    219     17      1.90
----------------------------------------------------------------------------
CH-17-139    2925     3090   -60   171    121     47     53      6      7.00
----------------------------------------------------------------------------
(incl.                                          47     48      1     26.0)
----------------------------------------------------------------------------
and                                             61     73     12      1.73
----------------------------------------------------------------------------
CH-17-140    2950     3180   -60   171    224    160    164      4   2.00(i)
----------------------------------------------------------------------------
and                                            174    175      1      4.78
----------------------------------------------------------------------------
and                                            180    181      1      9.34
----------------------------------------------------------------------------
and                                            186    195      9      0.64
----------------------------------------------------------------------------
CH-17-141    2925     3090   -70   171    151     51     67     16      3.48
----------------------------------------------------------------------------
(incl.                                          51     52      1     40.0)
----------------------------------------------------------------------------
and                                             77     93     16      1.63
----------------------------------------------------------------------------
CH-17-142    2950     3160   -60   171    200    135    136      1      5.55
----------------------------------------------------------------------------
and                                            141    146      5      0.82
----------------------------------------------------------------------------
and                                            150    174     24      0.68
----------------------------------------------------------------------------
CH-17-144    2950     3140   -60   171    182    135    141      6      1.18
----------------------------------------------------------------------------
and                                            148    149      1      9.05
----------------------------------------------------------------------------
CH-17-145    2950     3220   -60   171    260    214    235     21      0.64
----------------------------------------------------------------------------
(i)Wholly or partly includes 50g fire assay on pulverised whole-sample (to
be screen fire assayed).

/T/

True width of the mineralization is approximately 80% of the down-hole width.

The current resource estimate for Cochrane Hill is tabulated below:

/T/

----------------------------------------------------------------------------
Tonnes             Grade         Contained
Category                    (millions)          (g/t) Au          Au (oz.)
----------------------------------------------------------------------------
COCHRANE HILL
----------------------------------------------------------------------------
Indicated Resource                 4.5               1.8           251,000
----------------------------------------------------------------------------
Inferred Resource                  5.6               1.6           298,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Cochrane Hill is quoted at a cut-off grade of 
0.5g/t. It has an effective date of August 1, 2014 and was prepared as part of 
a technical report in accordance with NI 43-101 by Mr. Neil Schofield, a 
principal of FSSI (Australia) Pty Ltd, released on August 14, 2014 on SEDAR.

/T/

3.  PLENTY

/T/

The Plenty prospect is located 300m south of the Company's Fifteen Mile Stream 
deposit. Plenty is one of several regional exploration targets selected for 
investigation, in parallel with Atlantic's ongoing resource definition drilling 
at Cochrane Hill and Fifteen Mile Stream. The immediate prospect is defined by 
an east-west trend of small historic mine workings dating to the late 1800s. As 
elsewhere in the Meguma Terrane of Nova Scotia these old workings were 
developed exclusively on quartz veins though the current exploration model 
encompasses the medium grade halo of disseminated mineralization within the 
adjacent wall rocks.

The new assay results reported here are from a further thirteen holes drilled 
on this property. In all, 21 holes for 2,272m have now been drilled by Atlantic 
on this prospect. At present the drilling rig has been deployed back to Fifteen 
Mile Stream and drilling will resume here once the current drilling campaigns 
at Fifteen Mile Stream and Cochrane Hill have been further advanced.

Drilling Results:

Results are tabulated below. These diamond core holes were drilled on nominal 
25m x 20m centres in the vicinity of high grade intersections (up to 13m @ 
21.8g/t) cut in several of the first eight holes drilled by Atlantic on this 
prospect. Results confirm the overall geometry - steep northerly dip and 
east-west trend - and continuity of the mineralization, though grades and 
widths are variable in this particular area. Mineralization is hosted both 
within well-defined argillites and bedding-parallel quartz veins and it is 
presently interpreted to extend eastward for about 350m where it abuts the 
Fifteen Mile Stream deposit against the Seigel Fault (refer to plan). This 350m 
gap, and the western extensions, are yet to be investigated. Gold in drill core 
is visible in places.

The accompanying cross sections and drill progress plan can be viewed here: 
http://media3.marketwire.com/docs/27AprPlenDrill.pdf.

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: January 25, 2017.

/T/

----------------------------------------------------------------------------
Significant Intervals
(greater than or equal to
0.5g/t Au and up to 3m
internal dilution)
------------------------------
Depth   From    To  Width     Grade
Hole id     Easting  Northing  Dip  Az.    (m)    (m)   (m)    (m)  (g/t Au)
----------------------------------------------------------------------------
PL-17-009     12975      9860  -60  175    122     50    54      4   0.88(i)
----------------------------------------------------------------------------
and                                              92    93      1   46.5(i)
----------------------------------------------------------------------------
PL-17-010     12975      9860  -45  175    113     66    67      1      5.85
----------------------------------------------------------------------------
PL-17-011     12950      9840  -60  175    140     18    26      8      0.69
----------------------------------------------------------------------------
and                                              85    86      1      5.33
----------------------------------------------------------------------------
PL-17-012     12950      9820  -60  175    110     56    57      1      3.09
----------------------------------------------------------------------------
PL-17-013     12950      9800  -60  175     92     32    36      4      1.49
----------------------------------------------------------------------------
and                                              51    52      1      3.11
----------------------------------------------------------------------------
PL-17-014     12950      9788  -50  175     62     17    22      5      3.17
----------------------------------------------------------------------------
PL-17-015     12971      9820  -60  175     68     51    54      3     14.12
----------------------------------------------------------------------------
(incl.                                           53    54      1     23.8)
----------------------------------------------------------------------------
and                                              63    65      2      2.03
----------------------------------------------------------------------------
PL-17-016     12971      9820  -45  175     62     40    41      1      3.09
----------------------------------------------------------------------------
and                                              50    51      1     12.75
----------------------------------------------------------------------------
PL-17-017     12971      9800  -45  175     41     14    18      4      4.97
----------------------------------------------------------------------------
and                                              34    39      5      5.68
----------------------------------------------------------------------------
PL-17-018     12900      9840  -60  175    164     95   108     13      1.96
----------------------------------------------------------------------------
PL-17-019     12900      9820  -60  175    140                           NSA
----------------------------------------------------------------------------
PL-17-020     12900      9800  -60  175    122     54    65     11      1.42
----------------------------------------------------------------------------
PL-17-021     12900      9790  -50  175     92     42    45      3      1.97
----------------------------------------------------------------------------
and                                              49    55      6      0.61
----------------------------------------------------------------------------

/T/

/T/

(i)Wholly or partly includes 50g fire assay on pulverised whole-sample (to
be screen fire assayed).
NSA: No significant assays

/T/

True width of the mineralization is approximately 65% of the down-hole width.

Technical Disclosure

Fifteen Mile Stream

At Fifteen Mile Stream all assays are 50g charge fire assays conducted on 
whole-sample pulverized 1m samples of sawn, half NQ core with 1-in-10 duplicate 
assays and insertion of standards and blind blanks. Core recovery is estimated 
for each metre and averages greater than 97%, excluding occasional voids, 
usually less than 2m, representing historic underground workings. Wing samples 
to voids may be less than 1m to re-establish routine sampling on 1m intervals. 
Drill core in the hangingwall of the northern limb of the anticline where 
adjacent historic holes very clearly indicate this upper stratigraphy to be 
barren may not be sampled and assayed. Standards, blanks and duplicate assay 
results are acceptable.

Cochrane Hill
All core drilled at Cochrane Hill is assayed. All assays have been conducted on 
1m whole-sampled pulverized samples of sawn, half NQ core and, where 
mineralization is expected, assayed by total sample screen fire assay with 2x 
fines fire assays, and insertion of standards and blind blanks. In the 
hangingwall and footwall of expected mineralization samples are assayed by 50g 
charge fire assay with any mineralized samples (generally greater than 0.5g/t), 
and adjacent samples as appropriate, returned for screen fire assay. Core 
recovery is estimated for each metre and averages greater than 98%. Standards 
and blanks assay results are acceptable.

Plenty

All core drilled at Plenty is assayed. All assays have been conducted on 1m 
whole-sample, pulverized samples of sawn, half NQ core and, where 
mineralization is expected, assayed by total sample screen fire assay with 2x 
fines fire assays, and insertion of standards and blind blanks. In the 
hangingwall and footwall of expected mineralization samples are assayed by 50g 
charge fire assay with any mineralized samples (generally greater than 0.5g/t), 
and adjacent samples as appropriate, returned for screen fire assay. Core 
recovery is estimated for each metre and averages greater than 98%. Standards 
and blanks assay results are acceptable.

The individual drill hole assay results underlying the mineralized 
intersections listed in the all assay tables above have been verified by 
detailed checking against the original assays sheets. The lengths and average 
grades of each intersection have also been checked against the drill hole assay 
logs. Sample preparation and assaying of all samples is conducted at the 
Sudbury and Vancouver laboratories of ALS Canada Ltd, an entity having no other 
relationship with the Company.

Results and updates from this drilling program will be reported progressively.

Wally Bucknell, Director of Exploration to the Company and a Qualified Person 
as defined by National Instrument 43-101 ("NI 43-101") has reviewed and 
approved the contents of this news release.

Further updates will be provided in due course and as new results come to hand.

On behalf of the Board of Directors,

Steven Dean, Chairman and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements:

This release contains certain "forward looking statements" and certain 
"forward-looking information" as defined under applicable Canadian and U.S. 
securities laws. Forward-looking statements and information can generally be 
identified by the use of forward-looking terminology such as "may", "will", 
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans" or 
similar terminology. Forward-looking statements and information are not 
historical facts, are made as of the date of this press release, and include, 
but are not limited to, statements regarding discussions of future plans, 
guidance, projections, objectives, estimates and forecasts and statements as to 
management's expectations with respect to, among other things, the activities 
contemplated in this news release and the timing and receipt of requisite 
regulatory, and shareholder approvals in respect thereof. Forward-looking 
statements in this news release include, without limitation, statements related 
to proposed exploration and development programs, grade and tonnage of material 
and resource estimates.
These forward looking statements involve numerous risks and uncertainties and 
actual results may vary. Important factors that may cause actual results to 
vary include without limitation, the timing and receipt of certain approvals, 
changes in commodity and power prices, changes in interest and currency 
exchange rates, risks inherent in exploration estimates and results, timing and 
success, inaccurate geological and metallurgical assumptions (including with 
respect to the size, grade and recoverability of mineral reserves and 
resources), changes in development or mining plans due to changes in 
logistical, technical or other factors, unanticipated operational difficulties 
(including failure of plant, equipment or processes to operate in accordance 
with specifications, cost escalation, unavailability of materials, equipment 
and third party contractors, delays in the receipt of government approvals, 
industrial disturbances or other job action, and unanticipated events related 
to health, safety and environmental matters), political risk, social unrest, 
and changes in general economic conditions or conditions in the financial 
markets. In making the forward-looking statements in this press release, the 
Company has applied several material assumptions, including without limitation, 
the assumptions that: (1) market fundamentals will result in sustained gold 
demand and prices; (2) the receipt of any necessary approvals and consents in 
connection with the development of any properties; (3) the availability of 
financing on suitable terms for the development, construction and continued 
operation of any mineral properties; and (4) sustained commodity prices such 
that any properties put into operation remain economically viable. Information 
concerning mineral reserve and mineral resource estimates also may be 
considered forward-looking statements, as such information constitutes a 
prediction of what mineralization might be found to be present if and when a 
project is actually developed. Certain of the risks and assumptions are 
described in more detail in the Company's audited financial statements and MD&A 
for the year ended December 31, 2016 on the SEDAR website at www.sedar.com. The 
actual results or performance by the Company could differ materially from those 
expressed in, or implied by, any forward-looking statements relating to those 
matters. Accordingly, no assurances can be given that any of the events 
anticipated by the forward-looking statements will transpire or occur, or if 
any of them do so, what impact they will have on the results of operations or 
financial condition of the Company. Except as required by law, the Company is 
under no obligation, and expressly disclaim any obligation, to update, alter or 
otherwise revise any forward-looking statement, whether written or oral, that 
may be made from time to time, whether as a result of new information, future 
events or otherwise, except as may be required under applicable securities laws.

- 30 -

CONTACT INFO:

Atlantic Gold Corporation
Maryse Belanger
COO
+1 604 689-5564
Fax: 604 566-9050
info@atlanticgoldcorporation.com
www.atlanticgoldcorporation.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=592260725