Source	Marketwire
Date	05/03/2017
Time	04:01:53 AM

Company	 ANFIELD GOLD CORP.
Title	Anfield Announces an Updated NI 43-101 Mineral Resource Estimate for its 
Coringa Project





    CDNX Symbol: ANF











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Anfield Gold Corp.

TSX VENTURE SYMBOL: ANF

May 3, 2017

Anfield Announces an Updated NI 43-101 Mineral Resource Estimate for its 
Coringa Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 3, 2017) - Anfield Gold Corp. 
("Anfield" or "Company") (TSX VENTURE:ANF) has completed an updated mineral 
resource estimate on its Coringa Project ("Coringa" or "Project") located in 
the Para State of Brazil. The updated mineral resource estimate is based on 
approximately 25,200 metres of infill drilling, which concluded in March 2017, 
and prior drilling completed by Magellan Minerals (which was acquired by 
Anfield in 2016). The mineral resource estimate is comprised of an Indicated 
Mineral Resource of 726 thousand tonnes at an average grade of 8.4 grams per 
tonne ("gpt") gold and 17 gpt silver, containing 195 thousand ounces of gold 
and 396 thousand ounces of silver. In addition, there is an Inferred Mineral 
Resource of 1.3 million tonnes at an average grade of 4.3 gpt gold and 5.1 gpt 
silver, containing 181 thousand ounces of gold and 215 thousand ounces of 
silver. The Indicated Mineral Resource estimate is based on drill results from 
three veins at Coringa, Serra, Meio and Galena, and is expected to form the 
basis for a feasibility study.

Anfield commissioned this more rigorous mineral resource estimate to obtain an 
improved resource model on which to base the initial years of mine production. 
The updated mineral resource estimate incorporates increased drilling 
information and more refined data inputs; in addition, more constrained 
assumptions have been used to classify mineral resources when compared to prior 
mineral resource estimates. While this updated mineral resource estimate has 
resulted in a reduction from the previous mineral resource estimate prepared 
for Coringa(1), Anfield remains confident in its ability to expand Coringa's 
mineral resource base through additional drilling from surface and from 
underground, once below surface development work is initiated.

(1) Technical report prepared by Snowden Inc. entitled "Magellan Minerals Ltd. 
- Coringa Mineral Resource NI 43-101 Technical Report, Project No. V1491" dated 
May 13, 2015.

Coringa Mineral Resource Estimate Summary:

/T/


----------------------------------------------------------------------------
Tonnes Gold Grade Silver Grade Contained Gold Contained Silver
Zone    (000's)    (g/t)       (g/t)         (koz)           (koz)
----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Serra      488       7.5        16.1           117             253
----------------------------------------------------------------------------
Meio      160      10.7        20.7           55              106
----------------------------------------------------------------------------
Galena      78       9.4        14.7           24              37
----------------------------------------------------------------------------
Total      726       8.4        17.0           195             396
----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Serra      262       4.3         8.7           36              73
----------------------------------------------------------------------------
Meio      229       4.2         6.1           31              45
----------------------------------------------------------------------------
Galena      63       3.4         3.5            7               7
----------------------------------------------------------------------------
Mae de Leite  244       5.9         2.6           46              20
----------------------------------------------------------------------------
Come Quieto   253       4.5         7.5           37              61
----------------------------------------------------------------------------
Valdette    249       3.0         1.0           24               8
----------------------------------------------------------------------------
Total     1,301      4.3         5.1           181             215
----------------------------------------------------------------------------
Notes: Base case cut-off grade is 2g/t gold. Minimum thickness is 0.8 m
horizontal.
Mineral resources are not mineral reserves because the economic
viability has not been demonstrated.
Totals may not add due to rounding.

/T/

Estimates of mineral resources are made using a three-dimensional block model 
with a nominal block size of 1x5x2 metres. Grade estimates for gold and silver 
are based on the geology, drill hole spacing and geostatistical analysis of the 
drill hole sample data. The mineralized vein domains are interpreted using 
sample grades and geologic information based on a minimum horizontal thickness 
of 0.8 metres. The effects of potentially anomalous high-grade sample data, 
composited to 0.5 metre intervals, are controlled using both traditional 
top-cutting as well as limiting the distance of influence during block grade 
interpolation. The grade models have been validated using a combination of 
visual and statistical methods. Blocks in the model estimated using three or 
more drill holes drilled on a maximum 50-metre grid pattern are included in the 
Indicated category. Blocks within a maximum distance of 100-metre from a drill 
hole are included in the Inferred category. The estimate of mineral resources 
demonstrates relatively continuous zones of mineralization that are considered 
amenable to underground extraction methods. Mineral resources are not mineral 
reserves as the economic viability has not been demonstrated.

The Company is progressing work on a feasibility study to assess the optimal 
mine plan, plant configuration and throughput rate based on the above mineral 
resource estimate; it expects the study to be completed by July 2017. The 
existing equipment on site, including the two ball mills purchased from Troy 
Resources, affords management flexibility as it assesses different engineering 
and development options, including implementation of a staged production 
ramp-up.

Pre-construction activities at site permissible under Anfield's current permits 
are continuing in anticipation of the receipt of our Trial Mining Operating 
License and Vegetation Suppression and Fauna Capture authorizations. Management 
continues to work with the Secretaria de Estado de Meio Ambiente e 
Sustentabilidade (SEMAS) and the Instituto Nacional de Colonizacao e Reforma 
Agraria (INCRA) to receive these authorizations. Following which, construction 
activities are expected to take approximately nine to twelve months to complete.

On April 21, 2017, the Company commenced approximately 500 metres of drilling 
at the Galena vein, intended to add to the existing 24 thousand ounces of gold 
in the Indicated category. Results from this drill program are anticipated by 
the third quarter of this year.

Marshall Koval, Anfield's Chairman and CEO, commented: "Although the infill 
drill results did not yield as large an indicated mineral resource estimate as 
anticipated, we remain committed to advancing Coringa forward to production. 
Our team in Brazil is prepared to begin full construction activities at Coringa 
as soon as the required permits are received."

Quality Assurance

All Anfield sample assay results have been independently monitored through a 
quality control / quality assurance ("QA/QC") program including the insertion 
of blind standards, blanks and the reanalysis of duplicate samples at a second 
umpire laboratory. The results of the QA/QC program and the resampling program 
indicate that the sample database is of sufficient accuracy and precision to be 
used for the generation of mineral resource estimates.

Qualified Persons

Robert Sim, P.Geo., a Qualified Person as defined by National Instrument 43-101 
Standards of Disclosure for Mineral Projects ("NI 43-101"), is responsible for 
the estimate of mineral resources presented in this news release and has 
reviewed, verified and approved the contents of this news release as they 
relate to the mineral resource estimate. Leo Hathaway, P.Geo, Chief Geological 
Officer and the Qualified Person as defined by NI 43-101 for the Project has 
reviewed, verified and approved the contents of this news release as they 
relate to the other scientific and technical information contained herein.

About Anfield Gold

Anfield Gold Corp. (TSX VENTURE:ANF) is a Vancouver, Canada based precious 
metal exploration and development company focused on the development of the 
Coringa Project located in Para State, Brazil. Anfield's strategic plan also 
includes the acquisition of other gold projects with the goal of becoming a 
mid-tier gold mining company.

Further details are available on the Company's website at 
https://anfieldgold.com

Anfield Gold Corp.

Marshall Koval, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

Certain statements and information herein, including all statements that are 
not historical facts, contain forward-looking statements and forward-looking 
information within the meaning of applicable securities laws. Often, but not 
always, forward-looking statements can be identified by the use of words such 
as "plans," "intends," "will" "are expected" or variations of such words and 
phrases. Forward looking statements or information in this press release 
include, but are not limited to, the mineral resource estimate; the preparation 
of, and timing to completion of, a feasibility study for the Project; Anfield's 
strategic plan to acquire other gold projects with the goal of becoming a 
mid-tier gold mining company; Anfield's ability to expand Coringa's mineral 
resource base through additional drilling; Anfield's plans for further drilling 
at the Project; the timing to complete construction at the Project and timing 
of drill results from the further drilling occurring at the Galena vein. In 
making the forward-looking statements in this release, Anfield has applied 
certain factors and assumptions that are based on information currently 
available to Anfield as well as Anfield's current beliefs and assumptions 
(including Anfield's belief in the accuracy of the mineral resource estimate). 
Although Anfield considers these beliefs and assumptions to be reasonable based 
on information currently available to it, they may prove to be incorrect, and 
the forward-looking statements in this release are subject to numerous risks, 
uncertainties and other factors that may cause future results to differ 
materially from those expressed or implied in such forward-looking statements.
Such risk factors include, among others, that mineral resources may never 
become mineral reserves and do not demonstrated economic viability, Anfield may 
not be able to achieve the base case during actual mining at the Project, 
additional drilling and exploration may determine that there is no potentially 
viable mine plan for the Project, risks associated with the business of 
Anfield, risks related to reliance on technical information provided by 
Magellan Minerals Ltd. as related to the Project; risks relating to exploration 
and potential development of the Company's projects; risks related to obtaining 
the permits and approvals necessary to develop and commission the Project on 
terms that are acceptable to Anfield; risks related to Anfield identifying 
suitable acquisition targets; business and economic conditions in the mining 
industry generally; the supply and demand for labour and other project inputs; 
prices for commodities to be produced and changes in commodity prices; changes 
in interest and currency exchange rates; risks relating to inaccurate 
geological and engineering assumptions (including with respect to the tonnage, 
grade and recoverability of mineral resources); risks relating to unanticipated 
operational difficulties (including failure of plant, equipment or processes to 
operate in accordance with specifications or expectations, cost escalation, 
unavailability of materials and equipment, government action or delays in the 
receipt of government approvals, industrial disturbances or other job action, 
and unanticipated events related to health, safety and environmental matters); 
risks relating to adverse weather conditions; political risk and social unrest; 
changes in general economic conditions or conditions in the financial markets; 
and changes to business and economic conditions in the mining industry 
generally. Although Anfield has attempted to identify important factors that 
could cause actual results to differ materially from those contained in 
forward-looking information, there may be other factors that cause results not 
to be as anticipated, estimated or intended. There can be no assurance that 
such information will prove to be accurate, as actual results and future events 
could differ materially from those anticipated in such statements. Accordingly, 
readers should not place undue reliance on forward-looking information. Anfield 
does not undertake to update any forward-looking information, except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Anfield Gold Corp.
Scott Hicks
604  646-1884
Fax: 604  687-7041

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=592476846


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Anfield Gold Corp.

TSX VENTURE SYMBOL: ANF

May 3, 2017

Anfield Announces an Updated NI 43-101 Mineral Resource Estimate for its 
Coringa Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 3, 2017) - Anfield Gold Corp. 
("Anfield" or "Company") (TSX VENTURE:ANF) has completed an updated mineral 
resource estimate on its Coringa Project ("Coringa" or "Project") located in 
the Para State of Brazil. The updated mineral resource estimate is based on 
approximately 25,200 metres of infill drilling, which concluded in March 2017, 
and prior drilling completed by Magellan Minerals (which was acquired by 
Anfield in 2016). The mineral resource estimate is comprised of an Indicated 
Mineral Resource of 726 thousand tonnes at an average grade of 8.4 grams per 
tonne ("gpt") gold and 17 gpt silver, containing 195 thousand ounces of gold 
and 396 thousand ounces of silver. In addition, there is an Inferred Mineral 
Resource of 1.3 million tonnes at an average grade of 4.3 gpt gold and 5.1 gpt 
silver, containing 181 thousand ounces of gold and 215 thousand ounces of 
silver. The Indicated Mineral Resource estimate is based on drill results from 
three veins at Coringa, Serra, Meio and Galena, and is expected to form the 
basis for a feasibility study.

Anfield commissioned this more rigorous mineral resource estimate to obtain an 
improved resource model on which to base the initial years of mine production. 
The updated mineral resource estimate incorporates increased drilling 
information and more refined data inputs; in addition, more constrained 
assumptions have been used to classify mineral resources when compared to prior 
mineral resource estimates. While this updated mineral resource estimate has 
resulted in a reduction from the previous mineral resource estimate prepared 
for Coringa(1), Anfield remains confident in its ability to expand Coringa's 
mineral resource base through additional drilling from surface and from 
underground, once below surface development work is initiated.

(1) Technical report prepared by Snowden Inc. entitled "Magellan Minerals Ltd. 
- Coringa Mineral Resource NI 43-101 Technical Report, Project No. V1491" dated 
May 13, 2015.

Coringa Mineral Resource Estimate Summary:

/T/


----------------------------------------------------------------------------
Tonnes Gold Grade Silver Grade Contained Gold Contained Silver
Zone    (000's)    (g/t)       (g/t)         (koz)           (koz)
----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Serra      488       7.5        16.1           117             253
----------------------------------------------------------------------------
Meio      160      10.7        20.7           55              106
----------------------------------------------------------------------------
Galena      78       9.4        14.7           24              37
----------------------------------------------------------------------------
Total      726       8.4        17.0           195             396
----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Serra      262       4.3         8.7           36              73
----------------------------------------------------------------------------
Meio      229       4.2         6.1           31              45
----------------------------------------------------------------------------
Galena      63       3.4         3.5            7               7
----------------------------------------------------------------------------
Mae de Leite  244       5.9         2.6           46              20
----------------------------------------------------------------------------
Come Quieto   253       4.5         7.5           37              61
----------------------------------------------------------------------------
Valdette    249       3.0         1.0           24               8
----------------------------------------------------------------------------
Total     1,301      4.3         5.1           181             215
----------------------------------------------------------------------------
Notes: Base case cut-off grade is 2g/t gold. Minimum thickness is 0.8 m
horizontal.
Mineral resources are not mineral reserves because the economic
viability has not been demonstrated.
Totals may not add due to rounding.

/T/

Estimates of mineral resources are made using a three-dimensional block model 
with a nominal block size of 1x5x2 metres. Grade estimates for gold and silver 
are based on the geology, drill hole spacing and geostatistical analysis of the 
drill hole sample data. The mineralized vein domains are interpreted using 
sample grades and geologic information based on a minimum horizontal thickness 
of 0.8 metres. The effects of potentially anomalous high-grade sample data, 
composited to 0.5 metre intervals, are controlled using both traditional 
top-cutting as well as limiting the distance of influence during block grade 
interpolation. The grade models have been validated using a combination of 
visual and statistical methods. Blocks in the model estimated using three or 
more drill holes drilled on a maximum 50-metre grid pattern are included in the 
Indicated category. Blocks within a maximum distance of 100-metre from a drill 
hole are included in the Inferred category. The estimate of mineral resources 
demonstrates relatively continuous zones of mineralization that are considered 
amenable to underground extraction methods. Mineral resources are not mineral 
reserves as the economic viability has not been demonstrated.

The Company is progressing work on a feasibility study to assess the optimal 
mine plan, plant configuration and throughput rate based on the above mineral 
resource estimate; it expects the study to be completed by July 2017. The 
existing equipment on site, including the two ball mills purchased from Troy 
Resources, affords management flexibility as it assesses different engineering 
and development options, including implementation of a staged production 
ramp-up.

Pre-construction activities at site permissible under Anfield's current permits 
are continuing in anticipation of the receipt of our Trial Mining Operating 
License and Vegetation Suppression and Fauna Capture authorizations. Management 
continues to work with the Secretaria de Estado de Meio Ambiente e 
Sustentabilidade (SEMAS) and the Instituto Nacional de Colonizacao e Reforma 
Agraria (INCRA) to receive these authorizations. Following which, construction 
activities are expected to take approximately nine to twelve months to complete.

On April 21, 2017, the Company commenced approximately 500 metres of drilling 
at the Galena vein, intended to add to the existing 24 thousand ounces of gold 
in the Indicated category. Results from this drill program are anticipated by 
the third quarter of this year.

Marshall Koval, Anfield's Chairman and CEO, commented: "Although the infill 
drill results did not yield as large an indicated mineral resource estimate as 
anticipated, we remain committed to advancing Coringa forward to production. 
Our team in Brazil is prepared to begin full construction activities at Coringa 
as soon as the required permits are received."

Quality Assurance

All Anfield sample assay results have been independently monitored through a 
quality control / quality assurance ("QA/QC") program including the insertion 
of blind standards, blanks and the reanalysis of duplicate samples at a second 
umpire laboratory. The results of the QA/QC program and the resampling program 
indicate that the sample database is of sufficient accuracy and precision to be 
used for the generation of mineral resource estimates.

Qualified Persons

Robert Sim, P.Geo., a Qualified Person as defined by National Instrument 43-101 
Standards of Disclosure for Mineral Projects ("NI 43-101"), is responsible for 
the estimate of mineral resources presented in this news release and has 
reviewed, verified and approved the contents of this news release as they 
relate to the mineral resource estimate. Leo Hathaway, P.Geo, Chief Geological 
Officer and the Qualified Person as defined by NI 43-101 for the Project has 
reviewed, verified and approved the contents of this news release as they 
relate to the other scientific and technical information contained herein.

About Anfield Gold

Anfield Gold Corp. (TSX VENTURE:ANF) is a Vancouver, Canada based precious 
metal exploration and development company focused on the development of the 
Coringa Project located in Para State, Brazil. Anfield's strategic plan also 
includes the acquisition of other gold projects with the goal of becoming a 
mid-tier gold mining company.

Further details are available on the Company's website at 
https://anfieldgold.com

Anfield Gold Corp.

Marshall Koval, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

Certain statements and information herein, including all statements that are 
not historical facts, contain forward-looking statements and forward-looking 
information within the meaning of applicable securities laws. Often, but not 
always, forward-looking statements can be identified by the use of words such 
as "plans," "intends," "will" "are expected" or variations of such words and 
phrases. Forward looking statements or information in this press release 
include, but are not limited to, the mineral resource estimate; the preparation 
of, and timing to completion of, a feasibility study for the Project; Anfield's 
strategic plan to acquire other gold projects with the goal of becoming a 
mid-tier gold mining company; Anfield's ability to expand Coringa's mineral 
resource base through additional drilling; Anfield's plans for further drilling 
at the Project; the timing to complete construction at the Project and timing 
of drill results from the further drilling occurring at the Galena vein. In 
making the forward-looking statements in this release, Anfield has applied 
certain factors and assumptions that are based on information currently 
available to Anfield as well as Anfield's current beliefs and assumptions 
(including Anfield's belief in the accuracy of the mineral resource estimate). 
Although Anfield considers these beliefs and assumptions to be reasonable based 
on information currently available to it, they may prove to be incorrect, and 
the forward-looking statements in this release are subject to numerous risks, 
uncertainties and other factors that may cause future results to differ 
materially from those expressed or implied in such forward-looking statements.
Such risk factors include, among others, that mineral resources may never 
become mineral reserves and do not demonstrated economic viability, Anfield may 
not be able to achieve the base case during actual mining at the Project, 
additional drilling and exploration may determine that there is no potentially 
viable mine plan for the Project, risks associated with the business of 
Anfield, risks related to reliance on technical information provided by 
Magellan Minerals Ltd. as related to the Project; risks relating to exploration 
and potential development of the Company's projects; risks related to obtaining 
the permits and approvals necessary to develop and commission the Project on 
terms that are acceptable to Anfield; risks related to Anfield identifying 
suitable acquisition targets; business and economic conditions in the mining 
industry generally; the supply and demand for labour and other project inputs; 
prices for commodities to be produced and changes in commodity prices; changes 
in interest and currency exchange rates; risks relating to inaccurate 
geological and engineering assumptions (including with respect to the tonnage, 
grade and recoverability of mineral resources); risks relating to unanticipated 
operational difficulties (including failure of plant, equipment or processes to 
operate in accordance with specifications or expectations, cost escalation, 
unavailability of materials and equipment, government action or delays in the 
receipt of government approvals, industrial disturbances or other job action, 
and unanticipated events related to health, safety and environmental matters); 
risks relating to adverse weather conditions; political risk and social unrest; 
changes in general economic conditions or conditions in the financial markets; 
and changes to business and economic conditions in the mining industry 
generally. Although Anfield has attempted to identify important factors that 
could cause actual results to differ materially from those contained in 
forward-looking information, there may be other factors that cause results not 
to be as anticipated, estimated or intended. There can be no assurance that 
such information will prove to be accurate, as actual results and future events 
could differ materially from those anticipated in such statements. Accordingly, 
readers should not place undue reliance on forward-looking information. Anfield 
does not undertake to update any forward-looking information, except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Anfield Gold Corp.
Scott Hicks
604  646-1884
Fax: 604  687-7041

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=592476846